## Slide 1: Analysis of 19F MRI images (WP2, Task 2.3)

## Slide 2
Evaluate bio-distribution of fluorinated tracers in patients
Proposal: MRI with 19F
Absence of intrinsic signal in living tissues allows in vivo visualization of exogenous fluorinated tracers
- Suffers from low Signal to Noise Ratio (SNR)
Our strategy:
- SNR optimization (new RF antenna, SDR technology, digital
signal processing)
- optimization of the image analysis: Task 2.3
Goals

## Slide 3
Analysis Tasks
Currently 19F images are extremely coarse because of low SNR
Noise reduction
- Recent developments in deep learning neural network (DNN) based
denoisers show promising results in noise reduction tasks
Registration with 1H images
- Together with 19F images 1H high resolution images can be taken
=> Better estimate of the 19F noise from the correspondence with
1H image
- Need automatic registration methods => DNN methods
Automated Segmentation of anatomical structure in 1H MRI
- Can help to study tissue-specific noise correlation
- Can also be done with DNN

## Slide 4
First-step: in-vitro measurement
Aim of the measurement:
- try denoising and study noise correlation 19F-1H (Stefano)
- study resolution
Plan for measurements:
- wait for 19F probe
- at least 400 images are needed for AI algorithms
- 2 campaigns of 200 images (13 days each)
- each measurement can be taken at 3 different times to
see if we can extrapolate signal@maximum

## Slide 5
First-step: in-vitro measurement
Phantom material
- tests with material suitable for 3D printer underway
to check NMR compatibility (Silvio&Silvia)
Poliossimetilene: (CH2O)n , DELRIN
Cloruro di polivinile : (C2H3Cl)n PVC
Polimetilmetacrilato: (C5O2H8)n METACRILATO
Acrilonitrile-butadiene-stirene, Acido polilattico and somilar
Phantom shape
- different shape under consideration (concentric tubes.., singular
tubes divided in 4 sectors..)
Solutions under study
- 19F with different concentrations in blood or physiological solution