## Slide 1: Neptune-Pavia
WP2: imaging and quantification

## Slide 2: Neutron autoradiography
Imaging and quantification of 10B distribution in a biological sample can be obtained by neutron autoradiography:
sensitive film
10B
n
Li
α
θ
sample
Charged particles leave latent tracks on the sensitive film that are made visible by chemical attack (etching)

## Slide 4: Cell cultures treatment and samples preparation
AND
BPA (Boronophenylalanine)

## Slide 5
1. Cells are seeded and allowed growing for 24 h in proper medium.
2. Boron-enriched medium is delivered to cells.
3. At the end of the time of contact (4 h) the 10B containg medium is replaced and cells are washed three times in PBS, trypsinized, harvested and centrifuged in boron deprived medium and counted.
4. Cells are layered on mylar disks for neutron autoradiography
Cell cultures treatment and samples preparation
OR
BPA (Boronophenylalanine)
Notes: 5

## Slide 7
Irradiation and etching - Quantification
PPM
TRACK DENSITY
Low neutron fluence, low etching with PEW solution
Quantification of boron distribution in the
dried pellet of cells. It evidences how many PPM of 10-B are present inside cells, averaging over the entire sample.
NOTE that boron NOT internalized by cells is not counted here because cells have been washed before measurement!

## Slide 8: Ex-vivo tissues I – Qualitative neutron autoradiography
Histology
Autoradiography
Autoradiography
Histology

## Slide 9: Ex-vivo tissues II – Quantative neutron autoradiography

## Slide 10
Ex-vivo tissues III – Alpha Spectrometry
mylar support
detector
thermal n flux 2 ·109 cm-2 s-1
tissue sample with 10B
collimator
The holder is remotely rotated to acquire the spectra
of the calibration sample (superficial 10B implantation
in Si, by NIST), the background (bare mylar disk)
and 10 tissue samples without opening the TC

## Slide 11
Reconstruction of boron concentration from the analysis of the absorbed spectrum in an energy range where only alpha particle contribute. Coupled with imaging, A.S. can discriminate between healthy tissue and tumour.
#
keV
healty tissue
tumor
background
α
p+ from 14N(n,p)14C
7Li