## Slide 1: Scanning status in Japan
2019.02.1
Atsuhiro UMEMOTO

## Slide 2: Contents
Improvement of scanning speed
Evaluation of elliptical fitting analysis
Detector study for calculating DM cross-section
Surface run at Nagoya with Equatorial telescope

## Slide 3: Improvement of Scanning speed
Kobayashi developed a new algorithm for improving the PTS3 scanning speed.
( the detailed was shown in previous kobayashi’s slide)
And the algorithm was installed in PTS2.
① Optimization of surface recognition
In new algorithm, the surface position of next view
is predicted by using the current surface position.
The starting Z position can be tuned and
the slope of sample surface is corrected.
 | N of all trial | 1 | 2
before | 1778 | 415 | 417
after | 1042 | 951 | 35
992 view scanning by PTS2
Our scanning uses surface recognition using Au40nm. If the surface is recognized, the scanning goes next
Step(elliptical fitting and image saving). If not, scanning repeats surface recognition at same position.
Total scanning time 992view | before | 76min 10sec
 | after | 58min 30sec

## Slide 4: Improvement of Scanning speed
Each image filter processing before elliptical fit was speed up with GPU stream.
③ Stage control and elliptical fitting (w/ image saving) were parallelized.
after
before
before
After
-1 s
-0.15s
Scan condition: 4MB image × 96 layer. Sample: FAN113gf 0day after MAA (F.D. = 0.12/(10um)^3 w shrink)
Same area was selected for scanning speed check.
The difference of two
scanning methods is
only stage movement.
+ 1.62 s
Estimation: the number of retake (surface recognition) is reduced In the new method.
The size of scanning data access to HDD per unit time is increased.
⇒ HDD always needs to work, the treatment efficiency will be worse.
Process time when surface recognition is success

## Slide 5: Improvement of Scanning speed
Before
Image save
As BMP
After
Image save
As BMP
After
Image save
As PNG
After
w/o Image save
*PNG image
= 1.4 MB/layer
Because it has
enough time to
move and wait stage
Process time when surface recognition is success

## Slide 6
 | Ready to scan | Image filter | Elliptical fit and image save | Total/view
Before | 0.26 ±0.01 (s) | 1.67 ±0.09 (s) | 1.15±0.79 (s) | 3.08 ± 0.79(s)
After BMP | 0.09 ±0.14 (s) | 0.61 ±0.01 (s) | 2.78±1.64 (s) | 3.48 ± 1.65(s)
After PNG | 0.09 ±0.15 (s) | 0.61 ±0.01 (s) | 1.81±0.23(s) | 2.51 ± 0.28(s)
After wo image | 0.26 ±0.11 (s) | 0.62 ±0.03 (s) | 0.63±0.03 (s) | 1.50 ± 0.12(s)
Current scanning, the image is required for eye-check, additional image solution etc..
We decide to save scanning image as PNG.
⇒ SSD is better for speed up of image saving than HDD.
The scanning will be changed that does not save images
after understanding the both signal and noise characteristics. (April or May)
 | Effective scan speed include surface recognition
Before | 76min 10sec / 992views
After BMP | 58min 30sec / 992views
After PNG | 42min 30 sec / 992views
After wo image | 26min 10sec / 992views

## Slide 7: Current scanning
①
②
③
④
Optical mark by 400 nm Au
0
-15
1
2
12
26
27
31
59
47
X(mm)
3
23
y(mm)
Image of Optical mark
112 um
area1 | 9.9×17 mm2 =17200 views | *2.3 TB PNG Image and txt file
area2 | 14.9×17 mm2 =25800 views | 
area3 | 20.9×17 mm2 =36120 views | 
area4 | 12×18 mm2 =18381 views | 
The position of optical mark was recorded.
The scanning area was separated into four
(to save each scanning image to different HDDs)
Total=97501 views
PTS2 scanning. Data is being analyzed now.
FAN113gf (DM search at surface lab -20℃ for 1month)

## Slide 8: Time log
Chart: Scanning Log
| 43441.002083333326 | 43441.043749999997 | 43441.085416608796 | 43441.127083275453 | 43441.168749942131 | 43441.210416608796 | 43441.25208327546 | 43441.293749942124 | 43441.335416608796 | 43441.37708327546 | 43441.418749942139 | 43441.460416608796 | 43441.50208327546 | 43441.543749942131
area1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1
area2 | 2 | 2 | 2 | 2 | 2 | 2 | 2 | 2 | 2 | 2 | 2 | 2 | 2 | 2 | 2 | 2 | 2 | 2 | 2 | 2
area3 | 3 | 3 | 3 | 3 | 3 | 3 | 3 | 3 | 3 | 3 | 3 | 3 | 3 | 3 | 3 | 3 | 3 | 3 | 3 | 3 | 3 | 3 | 3 | 3 | 3 | 3 | 3
miss | 4 | 4 | 4 | 4
area4 | 4 | 4 | 4 | 4 | 4 | 4 | 4 | 4 | 4 | 4 | 4 | 4 | 4 | 4 | 4 | 4 | 4 | 4
12/7 0:03
12/7 14:03
12/7 15:00
12/8 10:30
12/8 13:30
12/9 15:25
12/9 15:45
12/9 19:36
12/10 9:57
25800 views
17200 views
36120 views
18381 views
area1 | 14 hours / 17200 views | 2.93 sec/view
area2 | 19.5 hours / 25800 views | 2.72 sec/view
area3 | 25.92 hours /36120 views | 2.59 sec/view
area4 | 14.5 hours /18381 views | 2.84 sec/view
Total = 81hours and 54 minutes（loss time 8hours and 7minutes）
Effective Scanning time= 73 hours 47min /97501 views.
If all area of views (except surface) are available for data analysis
(112um)^2×（64 layer×0.3125um/0.6）×10^-12×97501×3.44 = 0.14 g / 3.07 days ⇒ 1 g /22days

## Slide 9: PTS2 and PTS3
 | Maximum Speed (w image saving) | Maximum Speed (w/o image saving)
PTS2 | <16.6 g/year | <27.0g/year
PTS3 | <22.0 g/year | <32.0g /year
PTS2+3 | <38.6 g/year | <59.0 g/year
We need more study to use scanning data of both PTS2 and PTS3.
The difference of detection efficiency, angular resolution and fog density should be understood.
We are going to operate PTS2 and PTS3 scanning in this May.

## Slide 10: Elliptical fitting
We used a Image filtering and “rectangle recognition method” to get minor, major, ellipticity and track angle in previous, but this was much affected by the digitized pixel.
2017/02~04 BG run in LNGS
0.035 g Scanning data of FAN085gf4
- Ellipticity cut >=2.0
Anisotropic angular distribution
We developed a new elliptical fitting method using image frequency .

## Slide 11: Elliptical Fitting by FFT
Bicubic
DFT
Filtering
IDFT
51 pixel ( 2.8 um)
102 pixel ( 2.8 um)
Elliptical Fitting
by using brightness
distribution
(Minor, Major, Ellipticity) =
(4.1506 9.59089 2.31072)
Not online

## Slide 12: Ag40 nm spherical
Brighter event was selected by brightness parameters and image eye-check was done.
52 events selected by Max brightness 160<=Max<=200, Mean brightness 65<=mean<=105
FFT
rectangle
FFT
rectangle
digitized

## Slide 13: Carbon 100 keV ion w 10 degree implant
FAN113gf NIT-70nm
Camera X-axis pixel arrangement was beam direction(90d)
FFT
Elli>=1.25
rectangle
Elli>=1.25
rectangle
Elli>=1.25
Camera was rotated about 45d by manually.
⇒beam direction became 135d
FFT
Elli>=1.25

## Slide 14: Detection efficiency and angle by FFT
FAN113gf NIT-70nm
FAN113gf DM search area1
Selection parameter
- Absolute (minor - 3.89) < 4 × 0.24
- elli>= 1.75
- 100<=Max –BG brightness <= 150
- 30<=Mean –BG brightness <= 75
- 35<=number of Pixel<=75
Selection parameter
- Absolute (minor - 3.89) < 4 × 0.24

## Slide 15: Carbon ion efficiency by FFT
The event was recognized as two separated grain, then in current system
it was judged as noise (like a dust).
The higher kinetic energy, those events got increased ⇒ need a tracking method.
200 keV carbon track
Signalellicut – Maskellicut
2.8 um
Signalall – Maskall
Effi=

## Slide 16: Carbon ion efficiency by FFT
I estimated the efficiency
if tracking methods was available
It is not easy to develop a tracking program soon.
After finishing the current data analysis, I will try developing .

## Slide 17: Detection efficiency of Nuclear recoil
It is important to understand the relation between Ellipticity and track length.
We evaluated the detection efficiency of only Carbon ion with Elliptical fitting.
Our DM target nuclei are {C,N,O,Ag,Br}.
⇒ we will estimate the detection efficiency of all target nuclei from the result of
carbon efficiency using the relation between track length and ellipticity.
The systems between DM search and ion implantation are different.
⇒ Ion data has the tracks which are scattered out from NIT. Those events are negligible in the case of DM search ( interaction is occurred inside of NIT)
Detection efficiency should be converted to DM search system.

## Slide 18: Cross-section Limit
To calculate the DM cross-section, we have to understand the “Recoil Energy”, “Emulsion track length”, and “Ellipticity”.
Recoil track length
Converted from the relation
track length and recoil energy
by SRIM.
↓
Emulsion track length is decided by
the crystal formation and crystal
sensitivity of NIT.
NIT Param..
Crystal size = 44 nm
Crystal density = 10000 /um3
Crystal sensitivity ~ 100% (30keV Carbon)
Recoil Energy ERecoil
calculation can be done
when DM mass and velocity
are assumed.
Detectable in experiment
Ellipticity , event rate
ERecoil⇔Remulsion
Remulsion⇔ Ellipticity

## Slide 19: Our detection process
Recoil track
Erecoil
Rrecoil
Remulsion
After development
Optical observation
Ellipticity
Rrecoil
Remulsion
Optical simulation by PSF
Add
Crystal formation
Elliexperiment
Comparison

## Slide 20: Our detection process
Recoil track
Erecoil
Rrecoil
Remulsion
After development
Optical observation
Ellipticity
Rrecoil
Remulsion
Optical simulation by PSF
Add
Crystal formation
Elliexperiment
Comparison
Ellisimulation
PSF

## Slide 21: SRIM+NIT+Optical Simulation
The relation between track length and ellipticity is studied using SRIM simulation with a virtual emulsion detector and optical simulation.
The virtual emulsion and SRIM calculation were done by Asada.
- the size of crystal has a distribution like actual AgBr crystal.
- track range by SRIM is determined as the length from start point to end point.
Optical image was calculated by Fresnel equation by Shiraishi.
⇒elliptical fit and get parameters.
SRIM calculation
X
Y
ion
start
end
NIT. face-centered cubic lattice and random walk

## Slide 22: NIT70 nm C100 keV 10degree implantation
2D track length
ー SRIM = 340 nm
● Crystal = 334 nm
As a first test, 3 latent image specs were generated at random point in each AgBr crystal
2D track angle
ー SRIM = 112 degree
● Crystal = 112 degree
0 degree
180 degree
90 degree
2D track length
ー SRIM = 340 nm
● grain = 394 nm
2D track angle
ー SRIM = 112 degree
● grain = 112 degree
X(depth)
Y(beam angle)
Y(beam angle)
Z
X(depth)
Z
All grain diameter are same
= 48 nm
4/3*(24)^3*pi = 1/3* 70nm Volume

## Slide 23: Track length
SRIM and the end of crystal
SRIM and the end of grain

## Slide 24: NIT70 nm
2D track length
ー SRIM = 340 nm
● Crystal = 334 nm
2D track angle
ー SRIM = 112 degree
● Crystal = 112 degree
0 degree
180 degree
90 degree
2D track length
ー SRIM = 340 nm
● grain = 394 nm
2D track angle
ー SRIM = 112 degree
● grain = 112 degree
FFT elliptical fitting
Minor : 3.50747
Major : 5.70059
Elli : 1.62527
Track angle : 112.721
Each grain was set as apertures with R=48 nm.
The optical image was generated (NA1.4 and λ=510 nm)
1.87 um

## Slide 25: C100 keV ion comparison
ー PTS2data
ー simulation
The fog event was subtracted using mask in PTS2 data.
The relation between track range(kinetic energy ) and ellipticity seems to be found.

## Slide 26: Ellipticity and SRIM ,grain length

## Slide 27: Equatorial telescope
We tested a prototype of equatorial telescope for DM directional detection.
New nano. tracker (SIGHTRON company) was used.
Portable equatorial telescope
60×98×44 mm , 400g
Power supplied from socket with USB
Guaranteed temperature -10 ~ 40℃
http://www.sightron.co.jp/sightron/sightron_products25/
From WEB page
New nano. tracker

## Slide 28: Equatorial telescope setup
Our telescope consists of
- Camera platform for setting NIT toward CYGNUS
- Reflector plate and photoreflector (QTR-1A) to
monitor telescope running
- Microcomputer for data taking of photo reflector
QTR-1A
Turntable
6 cm
Camera platform
Earth axis
CYGNUS
Reflector plate
Light absorber (black tape)

## Slide 29
Arduino
2019/01/11/15:03
2019/01/11/17:01
Equatorial telescope rotates the camera platform with reflector plate.
QTR-1A catches emitted light by itself when the reflector plate comes upward of QTR-1A.
Then the output voltage of QTR-1A becomes lower.
- Reflector plate is not square in this test, so we can get the time difference of output voltage
and it has the relation with the telescope movement.
“arduino” (a kind of microcomputer) operates QTR-1A and also records output voltage in time as a text file.
QTR-1A circuit

## Slide 30: Test at room temperature
As day passes,
the reflector plate came
3~4 minutes earlier.
⇔ relation with the
earth diurnal rotation
Data taking in a minute
Light absorber (black tape)
I checked if the tape
worked as light absorber
in this test .
The tape was come
upward of QTR-1A in
this time region.
I checked the reflector plate
came on the QTR-1A sensor by eyes.

## Slide 31: Test at -10 degree
Thermostatic chamber
electronics
Temperature sensor

## Slide 32
-10℃
The shape of Vout in -10 degree was almost same as that of room test.
Room temperature
-10℃
Room temperature

## Slide 33: Plan and summary
Scanning speed is enough to do 1 gram DM search. (Only PTS2)
The angular resolution was improved by FFT elliptical fitting and DM directional search can be done with equatorial telescope(⇒ BG event has flat distribution).
DM cross-section will be calculated using ellipticity and SRIM.
Our important task is rejecting dust events.
The number of dust event generated by development process can be reduced by tuning the pAg in NIT gel production. I would like to produce this NIT and set it on the equatorial telescope at surface-lab.
Brightness and Phase-contrast information
NIT70 should be better than NIT40 for rejecting dust (it has to be evaluated )