## Slide 1
The Clock/Sync Distribution & a Streaming Readout TDC
William Gu
Streaming Readout IV
22-24 May 2019, Camogli
1. JLAB Trg/Clk/Sync/Busy overview
2. Clock recovery study
3. VETROC streaming TDC
4. ReadOut interfaces test
5. Prototype board
6. Summary

## Slide 2
1. JLAB HallB/D Trg/Clk/Sync/Busy overview
~60
Trigger etc.
Clock
Sync
FiberMeas
FiberMeas
Not_used
Not_used
Acknowledge/Busy
TS/TD
TI (front end)
MTP Fiber assignment:
TS
SD
TD (up to 16)
TI
FronEnd Readout electronics
Same clock for the system;
Frontend electronics is Synced to one clock period (4 ns);
Delay adjustment on TI to compensate for the fiber delays;
Clock jitter: several ps
(TS) Trigger
Supervisor
(TD) Trigger
Distribution
(TI) Trigger
Interface
FrontEnd
TDC/ADC
Signal Distribution
VXS backplane
Signal Distribution
VXS backplane
MTP fibers

## Slide 3
2. Clock Recovery Study
2.1 Low jitter clock can be recovered
Mellanox
(10 GBE)
Xilinx KCU105
(UltraScale Kintex)
Recovered clock to Tektronix DPO7254
Mellanox
10 GBE
Xilinx KCU040 312.5 MHz
Tektronix DPO7254
Clock result:
Period: 3.2000ns, Frequency: 312.50 MHz
Std Dev: 3.28 ps, 320.2 KHz
P_P: 29.3ps, 2.86 MHz
Enabling the Mellanox TX, Std Dev  3.30 ps
Enabling the KCU040 TX, Std Dev  6.42 ps
Single pulse period measurement: Std Dev: 6~7 ps
DPX mode (200 GSps): 700~900 fs
Fiber
Co-ax/copper

## Slide 4
2. Clock Recovery Study
2.2 OneTwo clock recovery
Xilinx KCU1500 6.25 Gbps
VETROC
Xc7a200
312.5/2
VETROC
Xc7a200
312.5/2
Clock result:
Period: 6.4000ns, Frequency: 156.25 MHz
Std Dev: 10.02 ps, 244.6 KHz
P_P: 85ps, 2.08 MHz
Single pulse period meas.: Std Dev: 7.5 ps
DPX mode (200 GSps): 778 fs
*VETROC FPGA  Scope: long LVCMS, then differential PCB traces. 312.5 MHz impossible
QSFP transceivers/Fiber
Xilinx Aurora-64B66B
& Aurora-8b10b

## Slide 5
2. Clock Recovery Study
2.3 Clock wandering probem
Trigger on the VETROC_A recovered clock, the VETROC_B recovered clock width P_P is about 200ps !
All these four channels are reconstructed KCU1500 clock
Ch#1 and Ch#2 have narrow spread as ch#2 is the trigger source
Ch#3 and Ch#4 have wide spread (~200ps)
Ch#2: Width: 6.4ns, Std Dev: 1.71ps
Ch#4: Width: 6.4ns, Std Dev: 2.54ps
The phase between Ch#1/2 and Ch#3/4 are changing (within a clock cycle) when re-link, though the phase is pretty stable. This is caused by the CDR clock devision.
Ch#1: VETROC_A, MGT#2 RxClk, single-ended probe
Ch#2: VETROC_A, MGT#3 RxClk, differential probe
Ch#3: VETROC_B, MGT#2 RxClk, single-ended probe
Ch#4: VETROC_B, MGT#3 RxClk, differential probe

## Slide 6
2. Clock Recovery Study
2.3 Clock wandering probem (continued)
The difference between two reconstructed clocks.
The width of the difference of the two reconstructed clocks from the SAME vetroc board is measured to be (one differential probe):
  Width: 336 ps
  Std Dev: 3.75 ps
The width of the difference of the two reconstructed clocks from two VETROC boards is measured (two differential probes with scope math) to be:
  Width: ~472/822 ps (mean 458/781 ps)
  Std Dev: ~35/50 ps (p_p ~210/347 ps)
  (Positive/Negative, not precise meas.)

## Slide 7
2. Clock Recovery Study
2.3 Clock wandering probem (continued)
Fundamental problem: TIE (Total Interval Error), not jitter. The TIEs are asynchronous among the recovered clocks.
The recovered clock depends on the data protocol (consecutive number of 1s or 0s in the data stream)
ADC measurement effects:
Clock Jitter affects the measurement precision;
The TIE effect is not critical
TDC measurement effects:
The TIE affects the measurement precision (channel to channel alignment, unless a precision common signal is used as the time reference);
The jitter effect is not critical as the jitter is much smaller than the TDC measurement precision
Data transmission effects:
Clock Jitter affects the data transmission;
The TIE effect is not critical
A typical clock recovery circuit

## Slide 8
2. Clock Recovery Study
2.4 Clock/Sync distribution tree
Something? (10GBE TCP/IP etc.)
Clock
Sync
FiberMeas /Data/Backpressure
FiberMeas / Streaming Data
Streaming Data
Streaming Data
Streaming Data
Computer (Event ID)
Detector (front end)
MTP Fiber assignment:
Clock extraction,
Clock cleanup,
Sync etc.
It is not expensive ($50 for a 40 Gbps optic transceiver) to keep QSFP (easy) for Clock/Sync distribution and streaming data readout
Dedicated clock to keep the edge information (low jitter, no wandering), but, we will keep an eye on the LpGBT development at the LHC

## Slide 9
3. VETROC Streaming TDC
3.1 TDC measurement principle
The edges of the pulse is measured against the system clock:
precision part: phase in the clock (using Xilinx FPGA carry chain delay and clock registers);
coarse part: number of clock cycles since system reset (T_zero) (a synchronous counter)
Ch_In
Calib_In
Calib_sel
Carry Chain
33x4 units
DoubleClock
500MHz
FD
Register
132
FD
FD
FD
FD
FD
FD
FD
FD
FD
FD
FD
FD
FD
FD
FD
FD
FD
FD
FD
Rising/Falling edge finder
Pipelined edge position encoder
Rising edge
Falling Edge
Detect the edge phase (relative to the 250 MHz clock)
Fine_Time(5:0)
Free running timer,
(one timer for all channels)
FineTDC(7:0)
Coarse Time
Fine Time
TDC data/Data Valid
“ZERO”
suppressed
Fine_Time(5:0)
One CLB
One CLB
One CLB
One CLB
Clock
250MHz
Rising edge
Falling edge
Edge
Detected
Valid
SYNC
(T_zero)

## Slide 10
3. VETROC Streaming TDC
3.2 VETROC Streaming TDC
Ext_Calib_In
4*6.25 Gbps
Streaming outputs
32-channels LVDS inputs
VME 64
xc7A200 FPGA
Ref_Ch_In
32-channels LVTTL inputs
32-channels LVDS inputs
32-channels LVTTL inputs
Data Format (128 bits)
Bits (127-124) (123:104) (103:78) (77:52) (51:26) (25:0)
TYPE Timer Ch#A Ch#B Ch#C Ch#D
Timer(28:9)
( 25:20 : 19:8 : 7 : 6 : 5 : 0 )
CH# Coarse_time Clk250 pulse Fine_time
0-63 Time(11:0) edge edge ~35ps
Bit(127:124) decoding:
0x8 for channels 1-32;
0x9 for channels 33-64;
0xA for channels 65-96;
0xB for channels 97-128;
0xF for reference channels
For reference channels, the full 48-bit timer is included, which keeps the unique time for about 290 hours after SYNC.

## Slide 11
3. VETROC Streaming TDC (backup slide)
3.2 VETROC Streaming TDC – 128 TDC channels with extra reference channels
Ch#1 data(19:0)
Ch#2 data(19:0)
Ch#4 data(19:0)
Merged data(127:0)
128(wide) x 1024(deep)
Channels 1-4
Merges the eight
Streams to one (127:0)
(round robin)
And buffer in memory
Two 41, empty control
One 21, timer control
Ch#32 data(19:0)
Data merging and Clock domain transition.
MGT (4*6.25Gbps)
QSFP fiber
Ch#3 data(19:0)
Timer(47:0)
Clock 250 MHz
Timer(11:0)
Timer(28:9)
Merged data(127:0)
128(wide) x 1024(deep)
Channels 5-8
Channels 29-32
/20
/20
/20
/20
/20
/128
Clk 250 MHz
Ch#33-64, 65-96, 97-128
Ref_Ch
128
128
3x128
Aurora_8b10b
Edge separation: <2.5ns;
LSB: ~35ps;
TimeStamp: ~10 days;
Streaming rate: ~2.5 Gbyte/s
Channel count: 128
Computers do not recognize the AURORA data stream

## Slide 12
4. Streaming Readout:
4.1 10-GBE test using KCU105 eval board
10 GbE to a Mellanox card
(UDP) and skip the 802.2 header:
Reached: ~1.1 GByte/s (sustained)
(from ifconfig ?trusted?)

## Slide 13
4. Streaming Readout:
4.2 xDMA PCIe3x8 test using KCU1500 accelerator card
Using Xilinx’s PCIe DMA driver, and modified test software:
QSFPs: Aurora 8-lane, 8x10 Gbps, 64b66b encoding, loopback through fiber
Achieved on the computer:
Computer (memory)  KCU1500: 5600 MB/s
AND KCU1500  Computer (memory): 5200 MB/s.

## Slide 14
4. Streaming Readout:
4.3 TCP/IP readout (INDRA lab setup)
KCU1500
In ALKAID
MLX 10_GBE
in INDRA-S2
ARISTA
7170-32C
VETROC TDC
In VXS crate
ARISTA 7170-32
KCU1500
VETROC TDC
MLX 10GBE
Aurora
8b10b
TCPIP
10 GBE
TCPIP
10 GBE
Graham’s
Stream_Router
~400 Mbyte/s
20 gb/s

## Slide 15
4. Streaming Readout:
4.4 KCU1500 functional diagram
StreamTDC
QSFP (4x6.25gbps)
TX
RX
10 GBE
10 GBE
10 GBE(TCP/IP)
PCIe3x8(xdma)
Aurora
20 gbps
FIFO
Double
Reg(31:0)
D2(31:0)
D3(31:0)
OUT
IN
IN
IN
IN
DB(127:0)
10 GBE
Mon(127:0)
Duplicate
Merge
QSFP
RX
D1(31:0)
Playback
ROM
computer
QSFP
TX
10 GBE
ARISTA 7170
MLX 10GBE/Computer
Data_Sel
* The Data flows are in parallel

## Slide 16
5. Prototype board:
5.1 STDCpcie
Two QSFPs
(2x4x10 GbE
Or 2x40 GbE
Or others)
PCIe3x8 (64 Gb/s)
32 LVDS inputs
+ 10MHz clock
32 LVDS inputs
+ SYNC
XCKU040-2
12-layer, PCIe x8 or VME (~3U)
PRELIMINARY
Clock, Sync
Combining the VETROC streaming readout TDC and the KCU105 into one:
64-CH Streaming TDC with standard interfaces (PCIexpress_Gen3 and Ethernet_10GBE)

## Slide 17
5. Prototyping board:
5.2 STDCpcie Status
This board will be able to test:
  Standalone 64-channel streaming TDC (~20ps) with up to eight 10 GBE interfaces;
  64-channel TDC  PCIe Gen3 x8 interface;
  Sync/clock/Readout test of many boards (system) with the proposed fiber assignment (sec. 2.4);
  8x MGT (1 Gbps ~ 16 Gbps)  PCIe3 x8;
  4x MGT (1 Gbps ~ 16 Gbps)  4x 10 GbE;
  Serial link beyond 10 Gbps (PCIe GEN4, 25_GBE/100_GBE) with more advanced FPGAs;
The board is ready to be manufactured: the PCB is fully routed and DRC checked; budget secured.

## Slide 18
6. Summary:
The CLOCK/SYNC distribution is feasible
  The dedicated clock distribution tree is better and easier, and cost manageable;
  The SYNC can be accomplished with the fiber length measurement, and delay compensation;
  We will keep an eye on the CLOCK/SYNC developments (LpGBT etc.);
The STREAMING READOUT is feasible
  A 128-ch Streaming TDC is tested;
  Some readout interfaces are tested;
Several (prototype) boards will be manufactured for CLOCK/SYNC/StreamingTDC test
Thank You