## Slide 1: Studies on MS Performance with 2009 Cosmics Data
Several people involved:
Igor: See yesterday presentation
Ahmimed, Eve, Niels, Peter, Egge: two presentations in this meting
Fabio: this talk

## Slide 2: MRATF publication on 2008-2009
Draft 1 of the paper attached to the agenda: it contains many performance studies based on cosmic data analysis
http://agenda.infn.it/getFile.py/access?contribId=0&amp;resId=0&amp;materialId=paper&amp;confId=1821

## Slide 3: Outline
Introduction on Sagitta and Momentum Resolution for BARREL
  Alignment Expectations: sagitta mean values
  “Expected” Sagitta and P resolution
Sagitta studieds on Cosmics
  Sagitta resolution vs P(ID)
Momentum Studies on Cosmic
  Uses ID as reference
Conclusions

## Slide 4: Introduction: Sagitta Resolution
Sagitta Resolution contributions from 2 terms
  ss(P) = K0/P + K1
  K0 Multiple Scattering ~ L/4 x 13.6(MeV) √(x/X0)
  K1 Intrinsic resolution:
    [tube-resol.+alignment+calibration+ cham-geometry…] ~ 60um
  Does NOT depend on B-field and Energy-Loss before MS
     Study part of P MS resolution contribution

## Slide 5
Published on NIM A: Measured in H8 Large Sector (only BML material)
  K0 = 9 mm x GeV  √x/X0 ~ 0.5
  K1 = 50 mm (Perfect alignment + very limited region)
100 GeV  ~90 mm

## Slide 6: What do we expect in ATLAS: Barrel ?
K0 Multiple Scattering much larger in Small Sectors:
  Small sectors:
    √(x/X0) ~1.5  Small
    L ~ 6.0 m  Small
  Large Sectors
    √(x/X0) ~0.7  Large
    L ~ 4.5 m  Large
  K0Large ~ 11 mm x GeV
  K0Small ~ 28 mm x GeV
K1 cosmics dominated by alignment + calibrations + … ?
  Use recent run 121737 (July) to measure it
Small
Peter Kluit

## Slide 7: Expected Alignment Performance
Alignment based on straight tracks from Run 113860 + Optical in Relative Mode
Igor Checks on Run 121737
On average <sag> for sectors 37 and 1115
Single towers ~ 50-250um
Igor Potrap
Optical Relative corrections for run 121737 (both runs have B-field OFF) ~0.3-1 mm
Pierre-Francois

## Slide 8: Sagitta Resolution: Method description
Use run 121737 - Toroid=OFF + Solenoid=ON:
  Pm measured by ID
  Alignment from Tracks (run ) + optic-relative mode
  Measure sagitta resolution for I-M-O segments measured in MS vs Pm and fit for K0 and K1

## Slide 9: Sagitta run 121737: MS segments
Used calibration ntuples
  Re-processed by Kevin with new Constants from Tracks(113860)+OpticalRelative
Select segments from MOORE: quality cuts have impact on results !:
  N-MDT hits ≥ 5 (BM, BO)
  N-MDT hits ≥ 7 (BI)
  N-RPC hits ≥ 3
  Chi-2 < 1.
  ==1 Segment same sector in I, M and O (Top Sectors)
  Processed ~3.3 M events RPCwBeam Stream

## Slide 10: Sagittas run 121737
Select Inner Detector Tracks (loose quality)
  |d0|< 1000 mm
  |z0|< 1000 mm
  Chi-2/ndf < 5.
  N-hits>100
  Pm = [P(ID)+ 3 GeV] to take into account E-loss
3.3M events Left  1000 muons
Make 5 bins in P: Bin Center  <P>
Fit sagitta resolution (single Gaussian fit OK) in each P bin

## Slide 11: Large Sector: 3, 5 and 7
K0  12± 1 mm GeV
K1 Intrinsic ~180 ± 40um

## Slide 12: Large Sector: 5 ONLY
K0  12 ± 1 mm GeV
K1 Intrinsic ~160 ± 80 um

## Slide 13: Small Sectors: 2, 4, 6 and 8
K0  24 ± 3 mm GeV
K1 Intrinsic  ~ 390 ± 80 um
Poor Fit !

## Slide 14: Conclusions on sagitta resolution
Multiple Scattering term look reasonable
Intrinsic term at the level of 150-300 mm
  Best sector5: ~100-150 um
On COSMICS: quality requirement on segments very important (correct t0-refit, outliers,..): intrinsic term going down from 250 to 150 um just changing cut on segment c2
Waiting for FINAL reprocessing of run 121737 with better calibration to converge on a single number

## Slide 15: Momentum scale and resolution
Method:
  Run 121080 Toroid=ON + Solenoid=ON
  Pt(m) measured by ID as reference
  Plot the relative difference [Pt(MS)-Pt(ID)]/Pt(ID)
  Study MS Pt-resolution vs Pt after subtracting expected ID resolution

## Slide 16: Expected in ATLAS: From CSC notes
10 GeV 5%  E- Loss fluctiations
100 GeV 4%  Mul. Scatt.
1 TeV 12%  s(s) ~ 60um
-------------------------------
Crude Parameterization:
Res. = P0 Pt + P1 + P2/Pt
Intr. MS E-loss
-------------------------------
E-Loss ~ 0.450 GeV
MS ~ 3.5%
Intrinsic Sagitta ~ 60um
|h| < 1.5

## Slide 17: P resolution: Naïve estimate 1
To simplify assumed Barrel Pt ~ P
Error on B neglected (<1% ?)

## Slide 18: P resolution: Naïve estimate 2

## Slide 19: Results from Cosmics run 121080
Use DP3D produced from AOD by Fabrizio Petrucci run 121080  2M ID-cosmic stream events
Track selection (all sectors accepted):
  MS - MuonBoySA tracks at IP:
    Pt > 4 GeV ; 23>nMDT>16; nRpcPhi>2 ;
    |d0| < 1m ; |z0| < 1m , chi2/ndf < 2 ; |h|<1
  ID tracks:
    Pt>2 GeV; nTRT>16; n(SCT+Pixel)>6 ; |h|<1
    |d0| < 0.5m ; |z0| < 0.75m , chi2/ndf < 1 ; q=(90±25)°
15K Muons selected:
  Fit s(P)/P in 8 Pt bins with single-Gaussian fit

## Slide 20
Run 121080
Reasonable Fit: 2 sigma core
Some non gaussian tails

## Slide 21: <[Pt(MS)-Pt(ID)]/Pt(ID)>
Mean-Pt=Pt-SCALE Agreement with ID at <1% up to 100 GeV !

## Slide 22
s([Pt(MS)-Pt(ID)]/Pt(ID)
Before Subtracting ID resolution

## Slide 23: ID resolution
* ID resolution: 2,5% up to 50 GeV - 3% at 60 GeV - 5% at 100 GeV – 7% 200 GeV
BUT for “LONG track” they claim scale as L2  factor 4 SMALLER  Negligible

## Slide 24: Resolution FIT: All sectors
- Energy Loss Error = 300 ± 40 MeV
- MS = 4.1 ± 0.1 %
Intrinsic resolution = (4.6 ± 0.7) x 10-4  ~40% @ 1 TeV
Up to 50 GeV very close to expected Performance !

## Slide 25: Resolution FIT: Sector 5+13
- Energy Loss Error = 270 ± 30 MeV
- MS = 4.1 ± 0.1 %
- Intrinsic resolution = (4.0 ± 0.8) x 10-4  40% @ 1 TeV Only a factor 2 w.r.t. CSC ?
Cut on Phi ID Track

## Slide 26: Conclusions 1
Sagitta studies in Barrel:
  Alignment concept in Barrel tested for runs 121737 seems to work at least at 50-300 mm (for movements ~0.2-1mm)
  Resolution Approaching 150-200 mm at high-Pt for some sectors: probably alignment is NOT the only contribution (calibrations, segment reconstruction quality, ..)
  Resolution still quite large for small sectors (not understood) ?
P-scale in agreement with ID at 1-2% level: OK at this stage

## Slide 27: Conclusions 2
P-resolution:
  E-loss term seems better than expected (200 MeV)
  MS term of the order of 3-4% : OK
  Sector-5 Intrinsic term approaching 150 um or better
  For several sectors compatible with 200um
  For cosmics quality of segments and tracks play a role: still margin for improvements – optimization of recons. Parameters
  Still very difficult to KNOW and/or to USE right calibration and alignment in reconstruction !
  Below 40 GeV very close to NOMINAL performance but for limited detector region

## Slide 28: Spare Slides

## Slide 29: Sagitta analysis from Igor: RPC time corrections+ better r(t)
Igor: Sector 5
Single hits instead of segment: K0 sagitta should be smaller: better then my result

## Slide 30: Sagitta analysis from Igor: RPC time corrections+ Better r(t)
Igor: Sector 4 and 6 side C only
Single hits instead of segment: K0 sagitta should be smaller: better then my result

## Slide 31: Results from Igor Sector 5
Hit resolution 150um  s(s) intrinsic ~100um  better calibration used HERE !
Kevin reprocessing this run with correct calibrations now
Igor Potrap

## Slide 32: Egge Fits Sectors 3, 5 and 7
K0 =16 ± 1 mm  90% x/X0
K1 =250 ± 12 mm
Fit quality NOT perfect but acceptable

## Slide 33: Dependency on track quality: Niels
s=4.9%

## Slide 34: Dependency on track quality: Niels
s=3.2%

## Slide 35
Same Analysis on 91890 !!! Only Optical Absolute Alignment Corrections !!!
E-loss 380 MeV
Fit insensitive to MS (6% error)
Intrinsic term 36 times larger than Nominal  1.8 mm