## Slide 1: HERMES: An ultra-wide band X and gamma-ray transient monitor on board a nano-satellite constellation
F. Fuschino INAF/OAS & INFN Bologna
on behalf HERMES collaboration

## Slide 2: The discovery of GRBs by the Vela satellites
Advanced Vela equipped with silicon
photodiode sensors with millisec
timing: ~10deg positions
Modularity —> improved performances
First 6 Vela equipped with X-ray and γ-ray detectors with limited timing capabilities: rough positions
First launch 1963 (6 satellites)
Last Advanced Vela launch 1970 (6+6 satellites)
In operation till 1985

## Slide 3: InterPlanetary Network
First IPN 1976
4-6 spacecrafts. Baseline ~ 1 AU
Second IPN ~1990
PVO, Ulysses, CGRO, Wind
Third IPN 2000
~ 20 spacecrafts
Localisations: arcmin-deg
Main disadvantage: long data acquisition ~days

## Slide 4: The multimessenger revolution
Advanced Ligo/Virgo provide position with accuracy
~ tens deg
Large volumes difficult to survey at optical λ.
Tens/hundreds/thousands optical transients.
Best strategy:
~ all sky prompt search for transients at high energies. Negligible probability to find an uncorrelated HEA transient at the time of GWE

## Slide 5: Mission concept
HERMES constellation of cubesat
2016: ASI funds for detector R&D
2018: MIUR funds for Technological pathfinder (Progetti premiali 2015) – 3nsat
2017 progetti premiali 2016 proposal for Scientific Pathfinder – 3+3nsat
2018 H2020 Space proposal
Disruptive technologies: cheap, underperforming, but producing high impact. Distributed instrument, tens/hundreds of simple units
Current
Current
Future
Next Step

## Slide 6: Mission concept
cΔt
Baseline
GRB front
+
=
σCCF~10μs
σPos~10arcsec
if <B>~7000km, N~100
Measure GRB positions through delays between photons arrival times:
σPos = σCCF x c / <B> / (Nx(N −1− 2)1/2

## Slide 7: Requirements
Arcmin-arcsec positions of ~a few dozen GRB/yr;
Prompt(minute) localisation;
Sub-μs timing;
Δt/ΔE~3μs/100keV 30μs/1MeV—> MQG~Mplanck (quantum Astronomy);
≈hundreds of satellites (final constellation);
a ≥50cm2 detector per satellite;
total collecting area ≥1m2 (final constellation);
Energy range 3-2000 keV;
Temporal resolution ≈100ns;
Attitude reconstruction < a few m;
Download full burst info in minutes;

## Slide 8: Spacecraft
solar
panels
payload: detector, electronics
AOCS,
reaction wheel
power management batteries
Lavagna+2017
3Ucubesat – simplest basic
configuration ~ 50cm2 detector

## Slide 9: Payload
Scintillator cristal (GAGG) + Photo detector (SDD)
3-2000 keV
~50 cm2 coll. area
a few sr FOV
Temporal res. ≈100 ns
Power < 4W
~1.8kg

## Slide 10: HERMES efficiency
Feasible only with
SDDs & Low Noise FEE
Dual Simultaneous Functionality for SDDs:
Solid State Detector
for Low Energy X-rays
Scintillator readout system
for Higher Energy X/g-rays

## Slide 11: Ce:GAGG Cerium-doped Gadolinium-Aluminum-Gallium Garnet
Yoneyama+2018
• Light output: 40 – 60 ph/keV
• No intrinsic background
• Not hygroscopic
• Decay time ~90 ns
• High density (6.63 g/cm3)
• Peak emission at 520 nm
• Hardness: 8 Mohs scale
• Energy resolution ~ 5% @ 662 keV
Ce:Gd3(GaxAl1-x)5O12 (x=1-5, typ.=3)
Available from industry since ~2014
1x1x3cm
Very promising literature radiation tests
Planned further test to better understand
Afterglow effects
Measured @ Bo-Lab ~23 e-/keV
Measured @ Bo-Lab ~30 e-/keV
1x1x3cm
10krad 70MeVp+

## Slide 12: SDD within Collaboration
Largest SDD
ever built (~ 80cm2)
6’’ Silicon wafers
Single cell SDD
with 900 mm2 sensitive area
Low anode capacitance (few tens of fF)
Low leakage current (tens of pA/cm2)
SDD Quantum Efficiency (QE) > 80%
Funded by INFN – P.I. Prof.A.Vacchi
Notes: Tecnologia SDD principio di funzionamento e caratteristiche e FEE giusta
Descrizione redsox come temi di apllicazione
Dal disegno al prodotto finito

## Slide 13: Collaboration
Design, production &
costs funding
Integration SDD & FEE
Nuclear Physics
and
Synchrotron light
applications
Extremely Low Noise
Front End Electronics
Design and production
High Energy
Astrophysics
applications
The

## Slide 14: The HERMES Front-End-Electronics
32 parallel channels
~ 0.5 mW / channel
ENC ~ 15 e- r.m.s.  185eV @5.9keV (-30°C)
The Heritage :VEGA ASIC (LOFT –M3 Phase-A)
TWO separated dies:
VE (single channel ~ 0.9x0.6mm)
Premplifier
Shaper (first stage)
GA (32ch ~ 16.5x2.5mm)
Shapers (second stage)
Discriminators
Sample & hold
32ch multiplexer
Post-layout simulations guarantee
ENC ~ 15 e- r.m.s. with 1mW/channel (VE+GA)
Europractice submission 24.05
AMS CMOS 0.35mm
Coordinated by Bertuccio (poliMi) & Malcovati (UniPV)
Ahangarianabhari+2014
Campana+2014

## Slide 15: SDD design & arrangement (FEE board)
Gross area ~ 91.95 cm2
Effective Area ~ 54.01 cm2
12 SDD arrays;
120 channels (120 VE);
4 GA;
EXTERNAL FRAME
VE chips
GA chips
Flat Cables
Crystal coupled
with 2ch SDD
X-rays  single
g-rays double
Rigid-Flex PCB

## Slide 16: BEE board (block diagram)
32ch / GA
ADC ≥ 11bit
FPGA-based Control Logic
Time Marking
Channel Adressing
Event Data Genrator (Single/double)
PDHU I/F
GA ch 1-32
GA ch 96-128

## Slide 17: BEE deadtime effects
With 32ch readout blocks
ADC non yet selected
Power VS. deadtime Tradeoff

## Slide 18: PDHU
PDHU The ISIS on-board computer (iOBC)
Dimensions: 96 x 90 x 12.4mm (incl. FM daughter board) Mass 100g with EM daughter board Power Consumption: 400mW average
Scientific data processing (trigger logic), Scientific RMs, HKs, TCs,
P/L configuration, operative modes, TM generation, I/F with OBDH…
trigger logic:
continuous comparison background rate
VS
current rate on different timescales (sub-ms to tens of secs)

## Slide 19: Preliminary Thermal results
Sun Array T
SVM T
Worst (hot) case temperature of SA and SVM in polar orbits are similar to equatorial results
PLM T

## Slide 20: Preliminary lifetime estimation
SPENVIS + AP8MIN derived p+ flux
Leakage Currrent increase with the
Non-Ionizing Energy Loss
Annealing parameters
from Moll+02

## Slide 21: Programmatics
Progetto Premiale 2015 (Technological pathfinder – 3nsat) – Coordinated by ASI
KO May 2018 (in few week)
PDR T0+9
CDR+QR T0+15 QM—> PFM1
AR T0+24 —> PFM2+PFM3
Launch mid 2020 (VegaC maiden flight or Vega)
NEXT: Scientific pathfinder – 3+3nsat; towards FULL Constellation

## Slide 22: HERMES people
Burderi, Fiore, Negri, Vacchi, Pirrotta, Puccetti, Carpentiero, Lavagna, Lunghi, Labanti, Fuschino, Campana, Morgante, Feroci, Evangelista, Ambrosino, Piazzolla, Del Monte, Di Cosimo, Malcovati, Grassi, Bertuccio, Gandola, Ahangarianabhari, Fiorini, La Rosa, Sottile, Santangelo, Tenzer, Bayer, Guzman, Pliego, Puehlhofer, Diebold, Amelino-Camelia, Riggio, Sanna, Di Salvo, Iaria, Celletti, Nava, Bongiorno, Piranomonte, Antonelli, Papitto, Della Valle, Capozziello, De Laurentis, Pucacco, Costa, Amati, Frontera, Rosati, Baldazzi, Rignanese, Zampa, Rachevski, Rashevskaya, Scarano, Gambino, Calderini, Ubertini, Natalucci, Pacciani, Rapisarda, Rubini, Di Salvo, Zaccheo, Perelli, Gronchi, Arzano, D’amico, Palmisano, Ghirlanda, Ghisellini, D’Avanzo ….
HERMES is open to ideas and collaboration
Want to be involved? Send an e-mail
fabrizio.fiore@inaf.it
burderi@dsf.unica.it