## Slide 1: Measuring the Gravitational constant with Atom interferometry for Novel fundamental physics Test (MEGANTE)
Gabriele Rosi
Consiglio di Sezione
04/03/2019

## Slide 2: Outline
Introduction to Atom Interferometry (AI)
The history: INFN MAGIA experiment (2002-2014)
Geometry free determination of the gravity gradient with AI
An improved G determination using cold atoms
MEGANTE: testing gravity measuring G
Conclusions and prospects: the new apparatus at INFN FI
G. Rosi MEGANTE

## Slide 3: Atom Interferometry
G. Rosi MEGANTE

## Slide 4: Atom Interferometry for gravity measurement
Ingredients:
A source of Cold Atoms (~ μ K or less)
(the sample must be slowly expanding and weakly interacting )
A laser system to cool the sample and to manipulate
the wavepacket
Atom Interferometry can measure accelerations
We use Cold Atoms as free falling microscopic masses
Quantum features of matter allow to improve the sensitivity
(not just a time-of-flight measurement in the “classical way”)
G. Rosi MEGANTE

## Slide 5: Atom / light Interferometry: the analogy
Once you have an atomic two level system you can make the analogy with light looking at the Rabi’s population oscillations scheme
Interaction time τ [1/Ω]
P1-2
π
π/2
|1 ›
|2 ›
π /2 pulse works like a beamsplitter
momentum transfer
π pulse works like mirror;
momentum transfer
state |2>
state |1>
Mirror
beamsplitter
interference
fringe
Optical interferometer
Atom interferometer
SPLIT
RECOMBINE
REFLECT
G. Rosi MEGANTE

## Slide 6: Atom Interferometry: theory
ω1
ω2
Δω=ωHF
Two hyperfine states are coupled by two photon RAMAN Transition
using two couterpropagating beams
frequency difference must be equal to hyperfine states separation
Momentum recoil and arms separation
|1>
|2>
z
t
We need to couple two long-lived states
Why RAMAN: we need large momentum recoil (arms separation)
SPLIT
G. Rosi MEGANTE

## Slide 7: Atom Interferometry: theory
Wave function PHASE evolution
|1>
|2>
If
Population on final State depends
On the interferometer phase
GRAVITY BREAKS
THE SIMMETRY
fringes
varying RAMAN laser’s phase
z
t
totally symmetric
evolution
G. Rosi MEGANTE

## Slide 8: MAGIA
Misura Accurata di G mediante Interferometria Atomica

## Slide 9: The big G issue
“The wide disagreement among recent measured values of G must cast some doubt on our abilities in this crucial area of small-force measurement and in other areas where similar techniques are used. This is an unsatisfactory situation” [*]
Macroscopic probe (detailed modelling)
Mechanical influences hard to control (gravity is weak!)
Two-centuries old concept
«Classical»» Instruments
[*] Outcome of the Royal Society meeting ‘The Newtonian constant of gravitation, a constant too difficult to measure?’ (2014)
G. Rosi MEGANTE

## Slide 10: MAGIA - the procedure
G
SOURCE MASSES
Well-characterized tungsten cylinders
PROBE MASSES
Cold, freely falling 87Rb atoms
MEASUREMENT METHOD
Raman atom interferometry (local acc.)
Spatial & temporal differential scheme
CALCULATION of gravitational attraction
G. Rosi MEGANTE

## Slide 11: MAGIA - the idea
G. Rosi MEGANTE

## Slide 12: MAGIA - the experimental sequence
G. Rosi MEGANTE

## Slide 13: MAGIA - the apparatus
LASER SYSTEM
Manipulate 87Rb atoms
G. Rosi MEGANTE

## Slide 14: MAGIA - the apparatus
LASER SYSTEM
Manipulate 87Rb atoms
OPTICAL FIBERS
Transport light
G. Rosi MEGANTE

## Slide 15: MAGIA - the apparatus
LASER SYSTEM
Manipulate 87Rb atoms
OPTICAL FIBERS
Transport light
VACUUM SYSTEM
Long interaction times
G. Rosi MEGANTE

## Slide 16: MAGIA - the apparatus
LASER SYSTEM
Manipulate 87Rb atoms
OPTICAL FIBERS
Transport light
VACUUM SYSTEM
Long interaction times
SOURCE MASSES*
Gravitational field
*G. Lamporesi, A. Bertoldi, A. Cecchetti, B. Dulach, M. Fattori, A. Malengo,, S. Pettorruso, M. Prevedelli, G.M. Tino, Source Masses and Positioning System for an Accurate Measurement of G, Rev. Scient. Instr. 78, 075109 (2007)
G. Rosi MEGANTE

## Slide 17: The G measurement
Features:
Source masses modulation time: 30 mins
Integration time:
more than 100 hours over 2 weeks (July 2013)
Sensitivity: 3x10-9 g/Hz1/2
Final sensitivity: ~ 10-11 g
G = 6.67191(77)stat(62)sys× 10-11 m3 Kg-1 s-2
G. Rosi MEGANTE

## Slide 18: Systematic
Error budget:
Most of the entries are evaluated through MonteCarlo simulation of the experiment, evaluating
the derivative of Φ with respect to each parameters
Final inaccuracy: 92 ppm
Limiting parameters: atomic samples dimensions, source masses position (Radial), Coriolis Effect
G. Rosi MEGANTE

## Slide 19: Current status
6.67191(77)stat(62)sys× 10-11 m3 Kg-1 s-2
G. Rosi MEGANTE

## Slide 20: Current status
6.67191(77)stat(62)sys× 10-11 m3 Kg-1 s-2
“Although the final uncertainty is not presently competitive, determinations of G using atom interferometry could be more competitive in the future.”
How to improve? Two ways:
Improve the cold atoms technology using the same method
Change the method maintaining the same technology
G. Rosi MEGANTE

## Slide 21
Cancelling gravity gradients
The tidal forces on the atoms in a uniform gravity field and gradient modify the wavepacket trajectories. The gravimetric phase shift is
φ = keffgT2 + keffΓzz(z0 + v0T)T2
z0, v0 initial atomic position and velocity.
The error on z0 and v0 is one of the major sources of noise and systematics:
For WEP tests at 10-15 level is required a control on z0 and v0 of 1 nm and 0,3 nm/s.
In the AI determination of G[1] one of the major sources of systematic error arises from the limited control on the thermal cloud degrees of freedom.
[1] G. Rosi, F. Sorrentino, L. Cacciapuoti, M. Prevedelli & G. M. Tino, “Precision measurement of the Newtonian gravitational constant using cold atoms”, Nature 510, 518-521 (2014).
G. Rosi MEGANTE

## Slide 22
Cancelling gravity gradients
Readapting the effective wave vector keff of the π pulse it is possible to compensate the effect of Γzz[1]
Δkeff = (ΓzzT2/2)keff
φ no longer depends on z0 and v0.
This procedure simulates the effect of a gravity gradient on the atomic trajectories. We implement it to measure gravity gradients, gravity curvature
[1] A. Roura, Phys. Rev. Lett. 118, 160401 (2017).
G. Rosi MEGANTE

## Slide 23
For the three gravity gradiometers (1-2, 2-3, 1-3) we measure the linear dependence Φ(Δν) vs Δν (Φ gradiometric phase)
We simultaneously interrogate three clouds with the Raman interferometer for two source masses configurations. During the π pulse the frequency of the Raman lasers is changed by Δν*.
Gravity gradient is traslated into a frequency!*
Cancelling gravity gradients
G. Rosi MEGANTE

## Slide 24
Final results*:
 | Γ23 [10-6 s-2] | Γ12 [10-6 s-2] | Γ13 [10-6 s-2]
Far | -3,32 ± 0,02 | -3,48 ± 0,01 | -3,40 ± 0,01
Close | 0,497 ± 0,006 | -4,87 ± 0,01 | -2,193 ± 0,006
Measurements also provide gravity gradient sign.
As expected Γ13 = (Γ12 + Γ23)/2.
Measured cloud distances and gravity curvature in close configuration:
d23 = (307,2 ± 0,3)mm d12 = (308,6 ± 0,4)mm
ξclose = (Γ23 - Γ12)/d = (1,743 ± 0,004) x 10-5 m-1s-2
Far configuration
Close configuration
*D’amico et al. PRL 2017
Cancelling gravity gradients
G. Rosi MEGANTE

## Slide 25
A new experimental strategy for G*
F
C
The value of the gravity constant can be retrieved by measuring the corresponding modulation of the gravity gradient and thus of the zero crossing frequency Δν0 :
The measurement is independent by the atomic sample size and velocity distribution if the gravity gradient produced by the source mass is perfectly linear
*G. Rosi, Metrologia (2018)
- Advantages: “easy” to implement (same technology of MAGIA, no need of ultra-cold atomic samples)
- Disadvanges: need of a large source mass
G. Rosi MEGANTE

## Slide 26
Another approach: the gravitational AB effect
The idea: determine G by probing the gravitational potential produced by a given source mass while the force acting on the wave-packets is zero*
Interferometer phase:
*Hohensee et al., PRL, 2012
G. Rosi MEGANTE

## Slide 27
Another approach: the gravitational AB effect
=
- Advantages: phase accumulates at Compton frequency rate => light and small source masses
- Disadvanges: need of ultracold (1 nK or less) and small (< 1 mm) atomic samples; technique not yet experimentally demonstrated
G. Rosi MEGANTE

## Slide 28
MEGANTE
MEasuring the Gravitational constant with Atom interferometry for Novel fundamental physics TEest

## Slide 29
A unique apparatus for independent measurements of G towards the puzzle solution & precision tests of gravity to unveil new physics scenarios
MEGANTE
G. Rosi MEGANTE

## Slide 30
TASK 1
Target relative accuracy on G: < 10-5
Investigation of the gravitational force
A unique apparatus for independent measurements of G towards the puzzle solution & precision tests of gravity to unveil new physics scenarios
MEGANTE
G. Rosi MEGANTE

## Slide 31
TASK 1
Target relative accuracy on G: < 10-5
Investigation of the gravitational force
A unique apparatus for independent measurements of G towards the puzzle solution & precision tests of gravity to unveil new physics scenarios
TASK 2
Target relative accuracy on G: ~10-5
Investigation of the gravitational potential
MEGANTE
G. Rosi MEGANTE

## Slide 32
TASK 1
Target relative accuracy on G: < 10-5
Investigation of the gravitational force
A unique apparatus for independent measurements of G towards the puzzle solution & precision tests of gravity to unveil new physics scenarios
TASK 3
Precision test of gravity searching for dark energy signatures due to Chameleon scalar fields
TASK 2
Target relative accuracy on G: ~10-5
Investigation of the gravitational potential
MEGANTE
G. Rosi MEGANTE

## Slide 33
Statistics
T=0.22 s, d=0.23 , ΔΓ=5x10-6 s-2, keff = 1.6x107
5 μrad on phase for 10 ppm on G! (9 times better than MAGIA):
More atoms (less shot noise)
Larger keff
Stationary point with vertical coordinates
Focus on task 1
12 stacks of tungsten cylinders (diameter 10 cm, height 0.6 m) => 4 tons of source masses to lift up!
Acceleration (10-6 m/s2)
Vertical coordinate z (m)
0
1
-3.0
3.0
Statistics:
G. Rosi MEGANTE at LNF

## Slide 34
Focus on task 2
The idea: determine G by probing the gravitational potential produced by a given source mass while the force acting on the wave-packets is zero (Gravitational Aharonov-Bohm effect1 ).
MEGANTE experimental strategy:
State-of-art atom optics for wave packet manipulation 2
+
Source mass design to allow
gradiometric configuration
1 Hohensee et al., PRL, 2012 2 Kovachy et al., Nature, 2015
Issue: Small potential from the source mass in a large gravitational field
Solutions:
Gradiometer baseline fixed by splitting a single atomic sample
Systematics from initial position fluctuation attenuated by the common local value of second derivative of the potential
Source mass grav. potential
Vertical coordinate z
Atom optic laser
Atom optic laser
G. Rosi MEGANTE

## Slide 35
Focus on task 2
z (m)
Phase (T=1s)
ΔU
Gradiometric phase
Gravitational red shift!
Gradiometer displacement (m)
Relative shift on Φ (ppm)
2
4
High immunity from sample size and position!
G. Rosi MEGANTE

## Slide 36
Newtonian ISL test
Several theories (involving extradimensions) predict deviations from the Newtonian law of Gravitational according to the Yukawa formula
The quantity (GF/GAB-1) can be used as a null test to improve the current constrains in the 0.01-1 m range!
G. Rosi MEGANTE

## Slide 37
  Λ sets the strength of the self-interaction/Dark energy scale;
  M determines the coupling between the chameleon and matter;
n=1
n=1
Low density
High density
From Burrage C, Sakstein J. Tests of chameleon gravity. Living Reviews in Relativity. 2018
Chameleon gravity
Chameleon is a hypothetical scalar particle recently postulated as a dark energy candidate.
Its main characteristic consists to have a coupling mechanism which gives to the scalar field a value depending on the local density of matter:
G. Rosi MEGANTE

## Slide 38
MEGANTE experimental strategy:
Source mass designed to modulate the Chameleon field φC:
Opposite value of second derivative of the potential
Larger systematic effects due to the cloud position jittering!
Target relative accuracy on G: 100 ppm
Source mass grav. potential
Vertical coordinate z
Internal
pair
External
pair
Atom optic laser
Atom optic laser
Focus on task 3
G. Rosi MEGANTE

## Slide 39
Expected results
Complete exploration of M parameter for Λ~2.4 meV (<= cosmic acceleration)
G. Rosi MEGANTE

## Slide 40
The Roadmap
Starting date: 1st of February 2019
G. Rosi MEGANTE

## Slide 41
Location
G. Rosi MEGANTE

## Slide 42
Conclusions
Lab space (50 m2 for 7 m of maximum height)
Building equipped with a crane
Design of the vacuum system
Design of the laser system
Preliminary Monte Carlo simulation of the system
Infrastructure design
Source mass handling system design (4-5 tons to be lifted for 4 m)
Air conditioning of the room (0.1 °C)
Open points:
Need of the Engineering Support
for Experimental Apparatus (SPAS)
of the LNF
G. Rosi MEGANTE