## Slide 1
Nuclear emulsions:
status of the analysis
A. Alexandrov, G. De Lellis, A. Di Crescenzo, G. Galati, A. Iuliano, A. Lauria, M. C. Montesi, A. Pastore, V. Tioukov
Università di Napoli “Federico II”, INFN Napoli, INFN Bari

## Slide 2: Analysis On-Going
 | Oxygen 200 MeV/n | Oxygen 400 MeV/n
Carbon | GSI1 | GSI3
Polyethylene | GSI2 | GSI4
Target
Beam

## Slide 3
797 μm
590 μm

## Slide 4: Efficiency Plate by Plate (All Tracks)
Plate Id | eff all tracks | eff Oxy
1 | 100.0% | 100.0%
2 | 100.0% | 100.0%
3 | 100.0% | 100.0%
4 | 86.8% | 86.6%
5 | 93.8% | 94.0%
6 | 98.0% | 99.8%
7 | 72.2% | 22.9%
8 | 96.4% | 99.6%
9 | 92.9% | 93.5%
10 | 93.4% | 93.3%
11 | 91.2% | 91.8%
12 | 92.2% | 91.8%
13 | 92.1% | 92.2%
14 | 92.4% | 89.8%
15 | 89.7% | 88.8%
Plate Id | eff all tracks | eff Oxy
16 | 92.8% | 91.2%
17 | 100.0% | 100.0%
18 | 89.9% | 85.0%
19 | 93.5% | 92.9%
20 | 94.8% | 94.2%
21 | 89.5% | 77.2%
22 | 93.1% | 94.0%
23 | 93.9% | 92.5%
24 | 95.6% | 94.5%
25 | 93.7% | 94.8%
26 | 97.3% | 98.8%
27 | 100.0% | 100.0%
28 | 100.0% | 100.0%
29 | 100.0% | 100.0%
30 | 100.0% | 100.0%
Mean Efficiency all = 94%
Mean Efficiency Oxy = 91%

## Slide 5: Track Efficiency by Angle
To be improved…
Signal Region
Angle (rad)
Efficiency

## Slide 6: Oxygen Counting

## Slide 7: Oxygen Counting
Our scanning software is not optimized for such ionizing particles
The grains along the oxygen trajectory are not separated and on a straight line
Oxygen grains created by the same particle are associated with close segments

## Slide 8: Oxygen Counting
Segments with ΔRxy<1.5 μm && Δθ<0.04 rad are replaced by a single segment that combines properly all the information
Notes: couples->Draw("s.eX:s.eY", "TMath::Abs(eX-62000)<797&&TMath::Abs(eY-48000)<590&&Theta()<0.04", "COLZ")

## Slide 9: Oxygen Counting
Before
After
Notes: couples->Draw("s.eX:s.eY", "TMath::Abs(eX-68000)<797&&TMath::Abs(eY-51000)<590&&Theta()<0.04", "COLZ")

## Slide 10: Oxygen Counting
Beam: 19375 Oxygen ions
Reconstructed base tracks with θ<0.04 rad rad on Plate 1: 18778
Efficiency ~ 97%

## Slide 11: MicroTracks
PLATE 1
PLATE 30
X - Y microtrack distributions
Slope X microtrack distributions

## Slide 12: Signal vs Cosmic Rays Separation
Cosmic Rays
Signal
Angle (rad)
Volume
Notes: couples->Draw("s.eVolume:Theta()>>h(200,0,1,200,1500,14000)", "", "COLZ")

## Slide 13: All Oxygen Vertices

## Slide 14: Vertexing - Example
3 cm
470 μm

## Slide 15: Comparison with Simulation
MonteCarlo Simulation was converted into the raw data files format and underwent the tracking reconstruction
Flat efficiency was set at 94%
4 mrad smearing was applied on angles
No misalignment was simulated
No cosmic rays or background were simulated

## Slide 16: Comparison with Simulation
Selection: incoming particle with θ<0.04 rad
Vertex probability>0.5
MC normalized to data

## Slide 17: Comparison with Simulation
Selection: incoming particle with θ<0.04 rad
Vertex probability>0.5
MC normalized to data

## Slide 18: Comparison with Simulation
Selection: incoming particle with θ<0.04 rad
Vertex probability>0.5
MC normalized to data

## Slide 19: Comparison with Simulation
Selection: incoming particle with θ<0.04 rad
Vertex probability>0.5
MC normalized to data

## Slide 20: Next Steps
Improve tracking efficiency
Vertices manual check and one by one analysis to better understand interactions characteristics and validate the analysis
Continue emulsion scanning and microscope tuning

## Slide 21
Back Up Slides

## Slide 22
Emulsion spectrometer design
Vertexing
alternated layers of emulsions and target (C or C2H4)
Charge identification
only emulsion layers
Momentum measurement
and isotope identification
alternated layers of emulsions and passive material (plastic, tungsten and lead)
beam
10 cm
12 cm
C (C4H4) layer
1000 (2000) μm
Emulsion film
300 μm
Polyethylene
1000 μm
Tungsten
500 μm
Tungsten
900 μm
Lead
1000 μm
Notes: The Emulsion Cloud Chamber detector is made of three sections:
SECTION 1: alternated layers of emulsion films and target (C/C2H4)
Vertex detector
Tracking of all charged particles
SECTION 2: emulsion films only
Charge identification for low Z fragments
SECTION 3,4,5: alternated layers of emulsion films and passive material
Momentum measurement by range and Multiple Coulomb Scattering (MCS)
Isotopic identification

## Slide 23: Detector Structure
S1
S2
S3
S5
S4
S6
S1
S2
S3
S5
S4
S6
 | Oxygen 200 MeV/n | Oxygen 400 MeV/n
S1 | C (30x1mm) / C2H4 (30x2mm) + 29 emu | 
S2 | Emu (36) | 
S3 | Polyethylene (10x1mm)+10emu | 
S4 | W (10x0.5mm)+10emu | 
S5 | W (15x0.9mm)+15emu | 
S6 | Pb (20x1mm)+20emu | Pb (40x1mm)+40emu
S1
S2
S3
S5
S4
S6
S2
S3
S5
S4
S6
S1

## Slide 24: Comparison with Simulation
Selection: incoming particle with θ<0.04 rad
Vertex probability>0.5
RAW Data = Data before replacing fragmented
oxygens with a single segment

## Slide 25: Comparison with Simulation
RAW Data = Data before replacing fragmented
oxygens with a single segment
Selection: incoming particle with θ<0.04 rad
Vertex probability>0.5

## Slide 26: Comparison with Simulation
RAW Data = Data before replacing fragmented
oxygens with a single segment
Selection: incoming particle with θ<0.04 rad
Vertex probability>0.5

## Slide 27: Comparison with Simulation
RAW Data = Data before replacing fragmented
oxygens with a single segment
Selection: incoming particle with θ<0.04 rad
Vertex probability>0.5