## Slide 1
COSMO-SkyMed data for territory monitoring
luca.fasano@asi.it

## Slide 2
COSMO-SkyMed first generation

## Slide 3
3
4 X-band SAR satellites constellation day/night all weather
Dual system
Operational for many years
On demand system + background
High performance, flexibility and reactivity
Possibility to expand to external partner/users (partner-UGS / CUT), giving the capabilities for:
  Acquisition Request
  Satellite data acquisition, also by local antenna
  Data processing and distribution
  Archiving and cataloguing
COSMO-SkyMed first generation
The largest Italian investment in Space Systems for Earth Observation
Commissioned and funded by ASI and the Italian Ministry of Defense
2007
2016
8 giu 2007
CSK PFM
9 dic 2007
CSK FM2
2008
2009
2010
2011
2012
2013
2014
2015
25 ott 2008
CSK FM3
5 nov 2010
CSK FM4
2017
2018
2019
CSG PFM
CSG FM2

## Slide 4
Orbital characteristics:
sun synchronous:
Inclination 97.86°;
Revolutions/day 14.8125;
Orbit Cycle 16 days ;
Eccentricity 0.00118;
Semi Major Axis 7003.52 km;
Nominal Height 619.6 km.
CSK1
CSK2
CSK3
CSK4
67,5°
Day
1
2
3
4
5
6
7
8
9
10
11
12
13
14
15
16
17
CSK1
CSK1
CSK3
CSK2
CSK4
Interferometric revisit:
Space Segment

## Slide 5: Ground Segment

## Slide 6: CSK Data Policy
Civilian Domain (75%)
AD
partner
Institutional Users (managed by ASI)
Commercial Users (managed by e-Geos)
Defence Domain (25%)
Absolute Priority
07/03/2007: COSMO-SkyMed National Data Policy and Resources Sharing (DPRS) (ASI – AD)
General principles of the national policy for the distribution of COSMO-SkyMed civil component data
COSMO-SkyMed System Utilization Guidelines
Details of Civilian data distribution and control
License
 | APPLICANTS | SpotLight2 | StripMap | ScanSAR
A | Natural or legal persons, to whom it is prohibited to provide any kind of COSMO-SkyMed product | No | No | No
B | Special cases. Countries whose users can be granted use of SL2 limited to their national territory | Own territory only | Yes | Yes
C | Particular combination of applicant country – requested area to be submitted to OICI assessment | Case by case assessment (by OICI) | Yes | Yes
D | All other cases not falling within the case studies as set forth in the lines “A”, “B” and “C” of this table | Yes | Yes | Yes

## Slide 8
COSMO–SkyMed Applications
Highways
Subsidence phenomena
Building
Landslides
Mining activities
Oil&Gas
Vessel detection
Analysis and monitoring of soil deformations
Railway
infrastructures
Volcanic phenomena
Pipelines
Earthquakes
Bridges

## Slide 9
Monitoring the Stability of St. Peter's Basilica
Buildings Monitoring

## Slide 10: Landslides Monitoring
Areas with landslide risk
Railway
Ground monitoring near a railway with COSMO data by e-GEOS for the Russian Railway company
analisi
Covering the AoI with COSMO-SkyMed Stripmap
Area of interest
Black Sea

## Slide 11: Post seismic Analysis: L’Aquila Earthquake - 2009
analisi

## Slide 12
COSMO-SkyMed second generation

## Slide 13
The Second Generation (CSG) is the follow on system to COSMO- SkyMed (CSK)
The first satellite is scheduled to be launched in 2019
Operational continuity/preserve
Performance improvements/enhance
Phase C
Nov.2017
CDR
Phase D
NOW
Manifacturing / AIT
Phase E1
Phase E2
Launch/Commis./Operations
VEGA-C(Korou SC)
2020
SOYUZ(Korou SC)
COSMO-SkyMed second generation

## Slide 14: …in Ground Segment
The Ground Segment (GS) upgraded in order to:
  manage, control, and utilise a System with such an increased performance
  ensure the full architectural integration between the ‘old’ CSK and the new CSG
  Other System improvements:
  Very urgent / Last Minute Planning Services
  Dynamic Resources Management and new Planning Algorithms
A Satellite Platform enhanced in terms of:
  augmented electrical power (i.e. 40% more) - to sustain the imaging performances
  A new Avionics Subsystem (AVS) - for a very high satellite agility
  an increased propulsion fuel tank capacity - for a prolonged operative lifetime.
A renewed Payload Data Handling and Transmission (PDHT) design that significantly improves the performances of the PDHT currently in use in CSK, in terms of:
  data reception rate from SAR (x 4)
  on-board data storage capacity (x 2)
  space-to-ground data transmission throughput (x 2)
…in Space Segment
Improvements

## Slide 15: SAR improvements
A brand-new design of the Synthetic Aperture Radar (SAR) instrument, capable to make the space resolution of the “narrow field images” finer than CSK, while providing multi-polarization.
Stripmap
Spotlight
Multi Burst ScanSAR
Quad Pol
Spotlight
  Spotlight 2A - best resol
  Spotlight 2B – same swath of CSK
  Spotlight 2C – less power cons.
Stripmap
  HIMAGE
  Ping Pong
  Quadpol
ScanSAR
  ScanSAR-1
  ScanSAR-2
Standard Modes
Non-Standard Modes
Operational
DI2S Spotlight 2B
Theatre Spotlight 2x
Spotlight

## Slide 16
Thanks to the agility of CSG platform (Control Moment Gyro attitude actuator), the satellite will be able to acquire while manoeuvring.
Spotlight acquisitions on a Theatre scenario are similar to standard Spotlight acquisitions, apart from a non-zero Doppler azimuth.
Theatre Acq mode

## Slide 17
DI2S spotlight technique exploits the SAR capability to work at doubled PRF, in order to simultaneously acquire two different images.
The swath is reduced, but the resolution and other performances are maintained.
DI2S Acq mode

## Slide 18: NOT STANDARD ACQ. MODES
Along track
Across track
CSG Theatre mode:
  The platform agility allows to perform pitch maneuvers
  More images in a theatre region can be acquired
CSG DI2S:
  The SAR instrument capabilities allows to acquire two targets almost simultaneously (using double PRF)
  The swath is reduced in range
A Quad-Pol mode introduced
CSG HIMAGE mode:
Improved resolution
Separation between spotlight images is ~100 km
CSG Spotlight standard mode:
CSG Improvements in Acquisition Modes

## Slide 19: CSG New User Services
  Very Urgent. Asynchronous requests: they can be inserted until little time before commands uplink
  Last Minute Planning. An orbital segment is «booked». If it is planned, the user can insert the real request until little time before commands uplink
  Near Real Time. High priority in receiving data from external station and in processing
Very Urgent
Last Minute Planning

## Slide 20: CSG Standard Products
Level | Code | Sample Information | Projection
1A | SCS_B | focused data, Hamming weighted and radiometrically equalized | Slant Range / Azimuth (Zero-Doppler)
 | SCS_U | focused data, unweighted and not radiometrically equalized | 
 | SCS_F | focused data, apodized and radiometrically equalized (only available in the Spotlight case) | 
1B | DGM_B | detected, multilooked (despeckled), Hamming weighted | Ground (WGS84 Ellipsoid) / Azimuth (Zero-Doppler)
 | DGM_F | detected, apodized (only available in the single-look Spotlight case) | 
1C | GEC_B | detected, multilooked | UTM (-80≤ lat < 84°) UPS (otherwise) OR Geodetic LatLon
 | GEC_F | detected, apodized (only available in the single-look Spotlight case) | 
1D | GTC_B | backscattering coefficient, multilooked, | UTM (-80≤ lat < 84°) UPS (otherwise) OR Geodetic LatLon Projected onto a reference elevation surface
 | GTC_F | backscattering coefficient, apodized (only available in the single-look Spotlight case) | 
2 types of production:
Standard Delivery: the mode associated to the distribution of Precision Product (in terms of their geolocation accuracy)
Fast Delivery: near-real time production mode, hence originating lower geolocation accuracy products
Level 1A
Level 1B
Level 1C
Level 1D

## Slide 21
Thank You!
Roberto Formaro
ASI
Head of Technology and Engineering Department
roberto.formaro@asi.it
For further information visit www.prisma-i.it
Thank You