## Slide 1
From very large to compact small accelerators
Prof. Luigi Palumbo
University of Rome “La Sapienza” and INFN, Italy
Retreat Fisica Particelle Elementari
Assisi June,18 2019

## Slide 2: Contents
- High Luminosity LHC
- Future Circular Colliders
- Limits of rf accelerating structures
- High frequency high gradient RF
- Plasma wave acceleration
- Compact linear accelerators for medical and industry
- Compact proton sources

## Slide 3
Luigi Palumbo
Mauro Migliorati
Andrea Mostacci
Luca Ficcadenti
Massimo Petrarca
Bruno Spataro
Post-Doc:
Luigi Faillace
Danilo Quartullo
Mostafa Behtouei
Accelerators phisycs and techonology team 2019:
Master thesis students:
Francesco Latini (2016) Diego Ferrazza (2016)
Giacomo Mazzacano (2017)
Matteo Pandolfi (2018)
Alberto Cutone (2018)
Debora Ventura (2018)
Paola Racano (2018)
Leandro Intelisano (2019)
Fabio Bosco (2019)
Jordan Arnesano (2019)
…...
.....
Permanent staff:
PhD student:
Serena Persichelli
Letizia Ventura
Giorgia Favia
Danilo Quartullo
Eleonora Belli
Marco Marongiu
Lucia Giuliano
Lorenzo Teofili
Fabio Cardelli
Francesco Filippi
Massimiliano Scisciò
Anna Giribono

## Slide 4: Livingston curve for accelerators

## Slide 5: VERY LARGE accelerators projects:
Need of new Large Colliders beyond LHC ?
Physics requests:
a) Increase the Luminosity HL-LHC
b) Increase the energy ILC, FCChh, FCCee

## Slide 6: Relevant parameters list of HL-LHC

## Slide 7: MICA experiment: Hi-Lumi and FCCee activities (M. Migliorati et al.)
A collaboration agreement was signed between SBAI Department and CERN for High Luminosity LHC and injector chain.
A Memorandum of understanding was signed between SBAI Department and CERN for FCCee.

## Slide 8: MICA experiment: Hi-Lumi LHC activity
We coordinated the evaluation of the impedance model of the CERN Proton Synchrotron with both theoretical studies and beam measurements.
We also studied different instabilities occurring in the machine

## Slide 9: MICA experiment :Impedance studies for the Hi-Lumi LHC
Beam
Rail
Shielding cylinder
Holder
Mechanical motor to move the shielding cylinder up and down
Mechanical motor to move the rail left and right
Tank
The goniometer is a device for beam collimation planned to be used in operation in the CERN LHC from 2021.
It uses a silicon crystal to bent halo particles with a rad accuracy.
Request from High-Lumi project: assess the impact of the goniometer coupling impedance on beam stability.
CAD model in CST simulations (external and internal views)
Frequency [GHz]
Re Z []
Measurement
Simulation
Longitudinal impedance
EM simulations and bench measurements performed to evaluate the impedance.
  The complexity of the internal features of the goniometer makes simulations difficult.
  Measurements can be affected by artifacts and uncertainties.
Collaboration between Sapienza SBAI Department and CERN for this study.
Crystal

## Slide 10: Crystal at Hi-Lumi LHC (Gianluca Cavoto)
  Review of all the experimental results obtained with crystal at SPS, LHC and with H8 test beams
Crystal collimation
  LHC, in operation
  HL-LHC
Future applications under study
  Crystal-aided SPS extraction (BDF)
  LHC crystal extraction (ALICE and LHC-b)
  MDM (and EDM) with crystals (LHC-b)
  UA9 double crystal experiment on SPS
  The future after the future: MDM of τ (!)

## Slide 11: LHC crystal extraction
Non-resonant and parasitic extraction
  Intercept the LHC beam halo with a bent crystal

## Slide 12
MICA experiment: activity FCCee (Migliorati)

## Slide 13: Relevant parameters of FCCee

## Slide 14
Luminosity challenges(*)
Luminosity cannot be fully demonstrated before the project implementation
Luminosity is a feature of the facility not the individual technologies
Have to rely on experiences, theory and simulations
Foresee margins
FCC-ee is based on experience from LEP, DAPHNE, KEKB, PEP II, superKEKB, …
Gives confidence that we understand performance challenges
New beam physics occurs in the designs,
e.g. beamstrahlung is unique feature of FCC-ee
Identified and anticipated in the design, should be able to trust simulations
The technologies required are improved versions of those from other facilities
(*) See C. Biscari, and L. Rivkin, P. Burrows, F. Zimmermann, Open Symposium towards updating the European Strategy for Particle Physics
May 13-16, 2019, Granada, Spain
FCC-ee challenges

## Slide 15
Maturity(*)
Do not see a feasibility issue with technologies or overall design
But more hardware development and studies essential to ensure that the performance goal can be fully met
E.g. high power klystrons, strong-strong beam-beam studies with lattice with field errors, …
RF technology(*)
Accelerator Technologies are ready to go forward for construction in few years
SRF accelerating technology is well matured for the realization including cooperation with industry but represents a challenge for high-Q SRF cavity at < GHz and for Nb Thin-film Coating
Continuing R&D effort for higher performance is very important for future project upgrades. Energy efficiency (RF efficiency) is also important
High synchrotron radiation constraint
(*) See C. Biscari, and L. Rivkin, P. Burrows, F. Zimmermann, Open Symposium towards updating the European Strategy for Particle Physics
May 13-16, 2019, Granada, Spain
FCC-ee challenges

## Slide 16
Impedance and instability studies for FCC-ee
Evaluation of the frequency-dependent impedance due to resistive wall in the multilayer case
Effect of coating on the microwave instability threshold
Our group is responsible of single beam collective effects for the FCC-ee machine:
MICA experiment: FCC-ee activity (1/2)

## Slide 17
Measurements of SEY at different thickness to determine a minimum effective coating mitigating e-could instabilities with low impact on the resistive wall impedance
A coating of 100-200 nm with NEG can help to reduce the RW impedance and, at the same time, guarantee a reasonable performance in terms of pumping and electron cloud mitigation
MICA experiment: FCC-ee activity (2/2)
NEG materials consisting of Titanium (Ti), Vanadium (V), Zirconium (Zr) it achieves a homogeneous surface

## Slide 18
Linear Collider projects (CLIC, ILC)
Reach the highest collision energy
Reach the highest luminosity
With a reduced power consumption and a minimum cost
BDS = Beam Delivery System
RTML = Return To Main Linac
e+ target
e-

## Slide 20
ILC (International Linear Collider) e+ e-

## Slide 21
ILC parameters
Parameter | Symbol | ILC | Unit
Center of mass energy | Ecm | 500 | GeV
Main Linac RF Frequency | fRF | 1.3 | GHz
Luminosity | L | 2 | 1034 cm-2 s-1
Luminosity (in 1% of energy) | L99% | 1 | 1034 cm-2 s-1
Linac repetition rate | frep | 5 | Hz
No. of particles / bunch | Nb | 20 | 109
No. of bunches / pulse | kb | 1312 | 
Overall two linac length | llinac | 22 | km
Proposed site length | ltot | 31 | km
Beam power / beam | Pb | 10.8 | MW
Wall-plug power to beam efficiency | ηwp-rf | 9.4 | %
Total site AC power | Ptot | 230 | MW
Transverse horizontal emittance | γεx | 8000 | nm rad
Transverse vertical emittance | γεy | 40 | nm rad
Horizontal IP beam size before pinch | σ*x | 640 | nm
Vertical IP beam size before pinch | σ*y | 5.7 | nm
Beamstrahlung energy loss | δB | 2.4 | %

## Slide 22
A tremendous amount of challenging parameters
Accelerating gradient ( G = 100 MV/m)
Beam emittance production and preservation (ge n = 5 nm.rad at Damping ring exit)
Very low break down rate in the accelerating cavities (BDR < 10-7)
Ground motion and stability requirements
Positron flux ( 1.1 1014 e+/s => 20 times more than the SLC machine produced)
Beam size at IP (sy = 1 nm)
Power consumption ( ~ 600 MW)
Cost (several billions of €, $, CHF,…..)
+ many others; none will be discussed in this seminar; only the beam size at IP is illustrated in the next slide

## Slide 23: Accelerating structures and EM spectrum
23
800MHz
110GHz
3MHz
1.3GHz
3GHz
450GHz
future
dielectric
6GHz
11GHz

## Slide 24: C-band R&D for GBS-ELI

## Slide 25
LWFA
Accelerating field limits

## Slide 26: R&D to reach high gradient RF at high frequency (Bruno Spataro et al.)
Using material with a higher fusion temperature
Avoiding the device heating at high temperature as done in conventional brazing
R&D on material
R&D on fabrication techniques
R&D on material
R&D on fabrication techniques
Sintered Molybdenum (Bulk)
[NIM-A-657 (2011)]
- Electroplated [NIM-A-657 (2011)]
Electroforming [JINST, March 8, 2016]
Electron Beam welding (EBW) [JINST, September 19, 2018]
Tungsten inert gas welding (TIG)
      [JINST, September 19, 2018]
Molybdenum sputtering
[study in progress in Osaka]

## Slide 27: Demetra experiment
The MOTIVATION :
The research project is devoted to the R&D of key components for existing accelerators and for the next generation of accelerators. New technologies are necessary to achieve the Multi-TeV energies of future linear colliders, x-ray FELs, etc.
Approach :
To study new materials and manufacturing techniques including single and multi-layer surfaces with precision-controlled properties
To use in high brilliance photo-injectors to compensate the beam longitudinal phase-space distorsion, enhanced by the bunch compression of the acceleration process
To gain know-how in vacuum microwave technologies

## Slide 28: Innovative compact braze-free joints structures at LNF (1/2)
Motivations:
Avoids high tempersture processes.
Cells joined together by means of specifically designed and proprietary screws which ensure good vacuum and RF contacts.
Use the Electron beam welding (EBW) and Tungsten Inert gas (TIG) processes.
Remarkable improvements of the RF perfomance
Strong costs reductions
JINST, September 19, 2018

## Slide 29: Innovative compact braze-free joints structures at LNF (2/2)
Ultra-High Field Cryogenic Radiofrequency Cu structures with a lower breakdown probability (S and X band experimental results)
S Band
Cu@45K
Emax = 250 MV/m
(surface electric field)
Cryocooler system
X Band
Cu@45K
Emax = 500 MV/m
(surface electric field)
PRAB 22, 023403 (2019)

## Slide 30: W Band Structures - Demetra experiment
electron
beam
RF out
M. Dal Forno et al. (SLAC) – INFN/LNF
Eacc = 300 MV/m
Esup = 1.5 GV/m
First 110 GHz Open Structure
High- Gradient Acceleration structure at 110 GHz at MIT
Moving Forward to Test @ MIT, Target 1 MW - Eacc > 400 MV/m
Split-Cell Structure with Mode Converter and Cavities
E. Nanni et al. (SLAC) - INFN/LNF
output horn
10 cm
PRAB [19, 011301 (2016)]
PRAB [19, 051302 (2016)]
NIMA [59852 (2018)]
PRAB [21, 091301 (2018)]
Conf. Series 874, (2017) 012039
IOP Conf. Series:
PRAB [19, 111301 (2016)]
Mode launcher, snake shape, and converter from TE11 to TM01 mode.

## Slide 31: Accelerating field limits (original)
LWFA

## Slide 32
Laser-driven electron acceleration
Laser-driven electron acceleration has made its breaktthrough on tens of TW laser systems in 2004 and reaching 1 GeV in 2006

## Slide 33
Summary of self-injection
Laser-driven electron acceleration has made its breaktthrough on tens of TW laser systems in 2004 and reaching 1 GeV in 2006
Reliable production of >200 MeV electron bunches with ≈mrad divergence.
Stability, spectral width and energy control (vs density) in progress.

## Slide 34: Nel 2014 presso la struttura FACET (Facility for Advanced Accelerator Experimental Tests) del laboratorio SLAC (Stanford Linear Accelerator Center), negli Stati Uniti, è stato realizzato il primo esperimento in cui un pacchetto di elettroni pilota crea l’onda di plasma che, a sua volta, accelera efficientemente un secondo pacchetto. Questo esperimento ha raggiunto risultati record dimostrando la possibilità di ottenere un’efficienza di trasferimento di energia tra i due pacchetti di elettroni del 30%, con un guadagno di energia di circa 1,6 GeV su 36 cm di lunghezza di plasma (un gradiente di energia di circa 4,4 GeV/m), e una dispersione media di energia del 2%.
Presso il Lawrence Berkeley national laboratory si studia la possibilità di utilizzare una successione di stadi di accelerazione basati su una combinazione di queste nuove tecniche laser-plasma per accelerare, fino a energie di 10 GeV, un pacchetto di elettroni su una distanza dell’ordine del metro. In tal modo si potrebbe costruire un collisore lineare elettroni-positroni con energia di 1 TeV (per fascio) costituito da soli 100 moduli di accelerazione al plasma, riducendo quindi drasticamente la dimensione complessiva della macchina rispetto ai progetti basati su una tecnologia standard, come ILC.
FACET

## Slide 35: In principle, there are several methods to create the high-quality multi-GeV electron beams by plasma acceleration proposed for EuPRAXIA. In the first place, the plasma wakefield can be driven by a high-power laser pulse (Laser Wakefield Acceleration – LWFA) or by a moderate energy electron beam (Plasma Wakefield Acceleration – PWFA). The first technique requires a laser system able to deliver pulses of around 100 fs duration in the petawatt regime; the second employs either a radiofrequency (RF) electron linac or a laser wakefield accelerator providing 0.5 – 1.0 GeV electrons in ultrashort bunches of a few femtoseconds. Secondly, the accelerated particle beam may come from the plasma electrons trapped in the back of the wake (internal injection) or from an external electron beam, precisely timed to arrive at the plasma structure on the peak of the longitudinal electric field in the forward direction (external injection). The external electron beam, in turn, may come from a radiofrequency linac or a preceding laser wakefield accelerator. Finally, the electrons may be accelerated up to the final energy in a single plasma structure or in a sequence of plasma structures where the electrons accelerated in the first stage are injected in a second stage for further acceleration. The EuPRAXIA study is considering all possible combinations between these schemes at the moment, in order to reach its baseline parameters. In total, there are nine different scenarios, of which the most promising ones will be selected in 2019:​
EUPRAXIA: (European Plasma Research Accelerator with eXcellence In Applications)

## Slide 36: SPARC_LAB Sources for Plasma Accelerators and Radiation Compton with Lasers And Beam
laser input line
300 TW, < 25 fs
Ti:Sa laser
External Injection into plasma
SL_EXIN
Plasma Wakefield
Acceleration (COMB beams)
SL_COMB
High Brightness electron beam
from SPARC

## Slide 37: Plasma acceleration experiments @ SPARC_LAB
laser input line
300 TW, < 25 fs
Ti:Sa laser
External Injection into plasma
SL_EXIN
Plasma Wakefield
Acceleration (COMB beams)
SL_COMB
High Brightness electron beam
from SPARC

## Slide 38
laser input line
300 TW, < 25 fs
Ti:Sa laser
External Injection into plasma
SL_EXIN
Plasma Wakefield
Acceleration (COMB beams)
SL_COMB
High Brightness electron beam
from SPARC
Plasma acceleration experiments @ SPARC_LAB

## Slide 39
Courtesy of
M. Ferrario (INFN), IPAC 2019
Sparc_Lab recent results

## Slide 40: TERA (Terahertz ERA): CALL INFN-CSN5 2018-2020 (S.Lupi – M. Petrarca et al.)
The aim of the TERA project is to build a synergic interdisciplinary collaboration among different INFN sections and external institutions with the final goal to push forward a strong R&D activity on THz technology with particular regard to THz acceleration.
Benefit of THz radiation:
Small time jitter (fs level and below)
Easy control of phase (long wavelength vs nowadays optomechanical and electronic capabilities)
kHz repetition rate
Bfield beyond actual device (2kT/m) and Efield up to 1GV/m

## Slide 41
Higher field gradient up to ~ 1GV/m
pC charge level
Accelerating structure design optimization
Staging of structures
Terahertz accelerator modules easily fit into two fingers.© DESY/Heiner Müller-Elsner
NATurE PHoToNiCS | VOL 12 | JUNE 2018 | 336–342 |
Outlook of THz for accelerators

## Slide 42: Compact accelerators and sources: applications

## Slide 43
22
Surface contaminant (H2O)
Bulk Target (Al)
-
-
-
-
-
-
-
- -
- -
- -
- -
- -
-
-
-
+ -
+ -
+ -
+ -
H+ ion
Bulk Target (Al)
Surface contaminant (H2O)
e
-
fewfew
IIλλ22
Ultra-intense short pulse laser proton beams are generated on hundreds of TW systems and make their breakthrough in 2000 achieving up to 60 MeV from µm targets.
Year 2000
Properties:
High number (~1013)
High energy (~60 MeV)
Produced in short time (~ ps)
Laminar (100 times be\er than conventional accelerator)
Target Normal Sheath Acceleration
LaserHdriven proton sources
Laser:
J / ~1 ps (>10 TW)
>1018 W cm-2 m2

## Slide 44
LaserHdriven proton acceleration
Scaling laws indicate that higher: power systems should generate ions suitable for many applications
ELI Whitebook

## Slide 45
Tomorrow ?
Today

## Slide 46: Laser-driven X-ray sources @ ELI Beamlines
LUX/XFEL
X-rays from relativistic e-beams
Harmonics (gas)
Plasma sources

## Slide 47
Small accelerators for industrial applications
The technology is based on the MicroLinac (originally developed at SLAC), an X-band linear accelerator powered by an inexpensive and commonly available magnetron.
1 MeV MicroLinac for industrial radiography
2 MeV MicroLinac, with mobile phone shown
for scale.

## Slide 48
Small accelerators for medical applications:
FLASH therapy
Ultra-High dose in very short pulse resultes more efficiently than conventional RT in the cancer cure.