## Slide 1: Software spettrometro
30/10/2009

## Slide 2: Structure
DAQ (Visual C++)
Reconstruction
Root
Simulation(mathematica/ GEANT)

## Slide 3: DAQ [Silvia]
Open questions:
  Format of the output
    One ADC/channel
    Event time stamp?
    How to merge several PMTs?  authomatic up to 5
  Which granularity? One histo per shot? Integrate several shots?
  Will need to display each single shot for online monitoring
Name: SPCDaq.c

## Slide 4: DAQ
Proposal:
  Write a root tree with timestamp and array with ADC reading of N channels
  Alternatively, write an histogram per shot named with the timestamp  drawback: no room for other variables
Need to test technical feasibility of either solutions  Silvia

## Slide 5: Simulation [Nadia]
Mathematica based
  Verify shape of y(p) for several values of theta  do something a bit better than just taking +/- 2 mrad  would be better translated into c++
  Write a program to emulate the output of the DAQ starting from the parametrizations from the mathematica file
    Input:
      text (or root) with exact positions of fibers
      Configuration file (text) to be able to specify characteristics of the beam (energy spectrum, pointing characteristics, angular divergence)
    Output:
      Data in same format as DAQ
Name: SPCFastSimu.c
Name: SPCMath.nbk

## Slide 6: Simulation (II)
Geant based code:
  Simultaneous generation of a large number of particles
  Simulation of the response of each particle
Input:
  Spectra from PIC simulations
  Text (or root) file with exact positions of fibers
Output:
  Same structure as DAQ
Name: SPCFullSimu

## Slide 7: Reconstruction [Francesco]
Inputs:
  Root file with observed spectra in DAQ format
  Root file with PECs
    How many and which needed to interpolate to the correct quantities?
    Need to account for variations in beam pointing
    B field can be accounted for by just rescaling momentum
  File or Database with conditions (magnetic field, beam direction, interaction point, RMS, …)
  File or Database with calibrations(gains & efficiencies), xtalk
Output:
  Unfolded spectrum in root file
  Notes:
    Need to include Xtalk and calibrations
    might not need objects in code
Name: SPCReco

## Slide 8: Scripts
Will need scripts to sincronize the DAQ and Reco and display in root:
  shot by shot monitoring
  Reconstruction of the whole set of events
  Statistical analysis (will need an ad-hoc program)

## Slide 9: Top priorities
SPCFastSimu  Ric
SPCFullSimu  Nadia
SPCDaq Silvia
SPCReco  Francesco
All these programs need subdirectory by itself in svn
Write clear README for each