## Slide 1
Experimental activity #2: Photocathode RF Gun
Overview:
This device is used a particles source in high brightness electron Linacs
Description of Photocathode RF Gun System and working principle
Theory of Resonant cavities and Multi-cells structures
Tuning of a cavity: Slater theorem and bead drop technique
Example of a real RF Gun
Overwiew of the measurement activity

## Slide 2
Experimental activity #2: RF Photocathode Gun
  An RF Gun is an electron source that generates very low emittance pulsed beams. The electron bunches are generated by photoelectric effect.
  Very short laser pulses hit a metallic cathode, which is embedded in an electromagnetic accelerating structure.
  It is a Standing Wave (SW) structure realized by two coupled resonant cavities.
  The emitted electron bunches are confined by a solenoidal magnetic field and accelerated by an oscillating electric field on the gun axis.
  Picosecond laser pulses and RF fields are synchronized for efficient acceleration.
  The ratio of the number of electrons emitted per incident photon is called Quantum Efficiency (Qe) which is a function of the photon energy. For metals, the minimum energy photons are typically in the ultraviolet range (λ(Cu) < 267nm).
klystron
Drive Laser
Master Oscillator
Electron beam
Solenoid
RF signal
Cathode

## Slide 3
Standing Wave structures: Resonant cavities
A Resonant cavity is a (almost) closed conductor enclosing an empty volume where the electromagnetic fields can only exists in the form of particular spatial conformations (resonant modes) whose components, including the accelerating field Ez , rigidly oscillate at some specific frequencies characteristic of the mode (Standing Waves).
Real cavities are lossy. Surface currents dissipate energy, so that a certain amount of RF power must be provided from the outside to keep the accelerating field at the desired level. If the external excitation is turned off, fields inside the cavity decay exponentially with a time constant characteristic of any given mode.
beam
Electric field
Reflection coefficient

## Slide 4
Cavities and multi-cell cavities
Cylindrical cavity or pillbox operating at the TM010 accelerating mode. This mode has a longitudinal electric field in the centre of the cavity which is suitable for particle acceleration.
Usually to have a more efficient acceleration more cavities (N) are coupled together.
The N-cells structure obtained behaves like a system composed by N oscillators coupled together.
Each single-cell mode degenerates in a set of N possible coupled oscillation modes of the whole system, characterized by a cell-to-cell phase advance given by:
SW multi-cell cavities are designed to use the last mode (for acceleration (.

## Slide 5
Slater Theorem
For a cavity on resonance, the electric and magnetic stored energies are equal. If a small perturbation is made on the cavity wall, this will generally produce an imbalance of the electric and magnetic energies, and the resonant frequency will shift to restore the balance. The Slater perturbation theorem describes the shift of the resonant frequency, when a small volume ΔV is removed from the cavity of volume V. The general result is
Where U is the total stored energy.
This theorem can be used also to measure the field profiles in the cavity by inserting a perturbing object and measuring the frequency shifts while moving it along selected paths. The theorem mathematical expression is different in this case and form factors need to be introduced because field lines are strongly deformed in this case, while they are almost unperturbed when the boundary is slightly deformed.

## Slide 6
Bead Drop Measurement
bead
Nylon wire
Network Analyzer
1-port Reflection measurement
If the perturbing object (bead) is a perfectly conducting sphere the values of the form factors are:
If a sphere of radius a is moved along the beam axis of a cavity the E field profile and the R/Q of a resonant accelerating mode can be estimated according to:
Probe
Sign of the E-field profile (it takes into account the phase variation of the field )
R
Q

## Slide 7
ELI-NP RF photocathode gun
1.6 cell photoinjector of the BNL/SLAC/UCLA type with new features:
elliptical shaped irises with larger aperture
Symmetric port to compensate the dipole field component
coupling hole rounded to reduce the pulsed heating
cooled cathode
fabrication without brazing using the clamping gasket technique
RF frequency | GHz | 2.856 | 
Rep. Rate | Hz | 100 | 
Working Mode | π mode (SW) |  | 
Max Rf input power | MW |  | 16
RF peak field at the cathode | MV/m |  | 120
Average dissipated power | kW |  | 1.5
Unloaded Q factor | 14500 |  | 
Coupling coefficent β | 3 |  | 
Working temperature | °C |  | 33 -34
Filling time | ns |  | 420
Shunt Impedance | MΩ/m |  | 1.64
Type of cathode | copper |  | 
waveguide
pumping port
cathode
Beam tube
cells
RF gun
Solenoid
Cathode
Input Waveguide

## Slide 8
Experience overwiew
RF Gun characterization in reflection with Network Analizer
  Calibration
  Localize the two resonating modes measuring the S11 (NA settings: fstart=2.8GHz fstop=2.86GHz)
  Estimate the frequency separation between the two modes.
  Measure the resonant frequency and the S11|fres and compute the coupling factor β for the two modes (NA settings: fcenter=fres span=4MHz) (NOTE: the π-mode is overcoupled β > 1, the 0-mode is undercoupled β < 1)
RF Gun characterization in transmission with Network Analizer
  Measure the S21 of the device and using the «Bandwidth» function (Marker Search -> Bandwidth) measure the Loaded Quality Factor QL
  Compute the Unloaded Quality Factor Q0 and the External Quality Factor Qext
Longitudinal electric field profile measurement with “bead-drop” technique (mode π):
  Ticks drawn on the nylon wire are equally spaced every 5 mm
  Fill a spreadsheet with: bead position (z [m]) and measured fres
  Compute and plot (f-fres)/fres vs z and finally Ez vs z

## Slide 9
R/Q calculation:
  From the spreadsheet, compute R/Q
  (Note: The spherical bead radius is a=0.0018m, ε=8.85418781762E-12, c=299792458 m/s)
Filling/Decay time measurement (time domain with realistic RF pulse)
  The filling or decay time, is the time for the energy stored in the cavity with loaded Q = QL to build to 1/e of its saturation point
  Connect the RF signal generator through a switch and an amplifier to the Gun and read the output probe through the oscilloscope
5V
100Hz, few us pulses
switch
scope
  Measure the filling time τ of the gun. Compare it with the one evaluated from QL.
(OPTIONAL) Longitudinal electric field profile measurement with “bead-drop” technique (mode 0)
  Repeat the procedure of point 3 for the 0 mode
fπ
15V

## Slide 10
Useful Formulae
Accelerating voltage on axis
Loaded Q factor
External Q factor
Unloaded Q
Cavity filling time
Coupling coefficient β
R/Q and Accelerating field from the perturbation measurement

## Slide 11
Main Parameters | 0-mode | π-mode
Res. frequency | 2814.3 GHz | 2855.7 GHz
Freq. separation | 41 MHz | 
Input coupling coeff. (β) | 0.9 | 1.86
QL | 4700 | 3600
Q0 | 9000 | 10400
Qext | 9900 | 5600
R/Q factor | ≈117 Ω | -
Filling time | ≈360 ns | -
cathode
½ cell
Full cell
Beam pipe
Vacuum tube
Input waveguide
Solutions
General measurement
settings:
fstart = 2.8 GHz
fstop = 2.86 GHz
Single mode measurement
settings:
fcenter = fres
fspan = 4 MHz