## Slide 1
ESS & PIP II
Paolo Michelato
per il gruppo SCRF
Paolo Michelato

## Slide 2: What’s going on at LASA on Superconducting Cavities?
European XFEL
2010
2020
2015
PIP R&D
PIP construction
2025
Superconducting cavities, cryomodules and ancillaries
ESS preconstruction
ESS construction
TRASCO
ADS
SNS
PDS-XADS
MAX
MYRRHA

## Slide 3: The European XFEL facility and SC accelerator
The European X-ray Free Electron Laser
  17.5 GeV light source user facility
  Photon energy 0.24-24 keV
  Pulse duration ~ 10-100 fs
  Pulse energy few mJ
  1.4 ms RF pulses at 10 Hz
  10 Hz (27 000 b/s)
  5 beamlines / 10 instruments
  Start version with 3 beamlines and 6 instruments
Experimental Hall
Beam Dumps
Undulators
Collimation
Bunch
Compressor
Linear Accelerator
Injector
Photon Beam Lines
Electron Beam
Distribution
2.1 km
  The XFEL SC accelerator
  800 SC-RF TESLA-type cavities, couplers & tuners
  101 cryomodules, 26 RF stations
  e- beam 1.35 mA nom., up to 500kW beam power
  Bunch length: 600 ms (2700 pulses inside)
  2 years of cavity / cryomodules tests / tunnel installation
Superconducting
Cavities & tuners
Cryomodules
3.9 GHz 3rd Harmonic Cryomodule
European XFEL Italian Contribution (based on INFN know how): 33 Meuro (2005)
All components produced by Italian Industry

## Slide 4: INFN LASA Contribution to ESS
INFN LASA In-Kind contribution for 11.6 M€.
  Fabrication of 36 cavities in the industry, including treatments, tuning and He tank following a
  Built to Print strategy.
  Cavities delivered ready for the cold test.
    Analogous strategy as for the XFEL successful experience
  Cold test in a qualified infrastructure (DESY).
  Delivery at CEA ready for the cryomodule assembly.
Series cavities production at the industry:
    First cavity, ready for the cold test by November 2018
    Cold test at DESY and CEA delivery: December 2018
    Delivery rate: 2 cav/3 weeks
LASA contribution
ESS Parameters | 
Max Energy | 2 GeV
Average beam power | 5 MW
Peak beam power | 125 MW
Peak beam current | 62.5 mA
Pulse length | 2.86 ms
Repetition rate | 14 Hz
Energy from SC sections | 96 %

## Slide 5: INFN-LASA ESS Medium beta cavities: from design to series
HOM analyses
Cell shape design
Dumb-Bells
INFN LASA ESS cavity prototype MB001 qualification at 2.0 K
ESS specs:
Eacc >16.7 MV/m
Q0> 5109
Cold test @ LASA
Cavity tuning
INFN R&D on ESS prototypes
  INFN design, plug compatible with ESS cryomodule.
  Know how transfer to the industry
  Built prototypes at industry with same procedures as for series.
  Final handling and test done in the qualified infrastructure at LASA.
  Successful result well over specification

## Slide 6: INFN-LASA ESS cavities production workflow

## Slide 7: INFN-LASA ESS cavity production
Niobium Procurement
Ca. 4000 kg of Nb sheets delivered in 3 batches
Eddy current scanning of sheets at DESY
All semi-finished products (tubes, MC, PU, etc.) at Zanon
Raw material at Nb vendor site
Sheet eddy current scanning at DESY
Cavity Fabrication
Nb sheets are deep drawn to form the half cell
Half cells are EB welded to form the Dumb Bell
All parts are EB welded together to form the cavity.
Surface treatment: BULK BCP (200 mm removal)
Heat treatment @600°C for Hydrogen degassing
Inner surface Visual inspection
Field flatness tuning
The He-Tank is the welded to the cavity
Final BCP (20 mm)
Cavity is shipped to DESY
EC
EC
PC
PC
IC
ID
PD
CD
EGP
EGC
Cavity after welding
Dressed cavity ready for shipment

## Slide 8: INFN ESS cavities production strategy

## Slide 9: INFN-LASA ESS QA/QC and document flow
Document and data management developed in the framework of collaboration
≈ 100 documents /cavity
Total of > 4000 documents to be:
  Exchanged among:
  EZ – INFN – ESS - CEA
  Managed and stored with INFN ALFRESCO DMS
  Analyzed for statistics, deviations, guidance and feedback for production
Trends figure
Dashboard

## Slide 10: INFN-LASA ESS cavities testing
  Cavity are mostly tested at DESY AMTF facility
  Two cavities tested at a time in the same cryostat
  Q vs Eacc curve acquired at 2 K temperature
  External radiation measurement (counter, NaI scintillator)
ESS specification asks for Q0 = 5·109 at Eacc = 16.7 MV/m.
The most of cavities largely overcome 20 MV/m gradient with limited or absent field emission. Also Q0 > 1010 at nominal gradient.
Vertical insert
Cryostat cover
ESS SPECS

## Slide 11: Status and time schedule of the INFN-LASA series cavities for ESS
4 cavities successfully tested, delivered at CEA, integrated in the Module M-1, under assembly at CEA
3 cavities under test at DESY, to be sent at CEA within mid of July for module M-2
3 additional cavities will be delivered at DESY within July end to be tested, for M-2 and M-3.
2 cavities to be delivered to LASA for additional cold test in the next 2 months
A total of 21 cavities welded at Ettore Zanon, under processing for surface treatment.
All subcomponents (half cells, terminal cell, etc.) already deep drawn

## Slide 12: Activity at Ettore Zanon for ESS
Test of deep drawing dies
Half cell deep drawing
Cavity integration in He tank
Cu DumbBell
Deep drawing dies
Nb tubes for end group
Cavity tuning machine
Nb sheets water cut
Nb sheets deep drawn
Co.Co.De for HC and DB RF measurements
Bulk BCP

## Slide 13: The PIP-II project
World-leading beam power to the neutrino programs
> 1 MW proton beam up to 120 GeV using Booster and Main Injector.
Modern 800 MeV superconducting linac of CW-capable components, initially operated in pulsed mode.
Low-Beta (LB650, b=0.61) cryomodule: recently reviewed to host 4 650 MHz, 5-cells cavities instead of 3 as in the former design.
RT
SC
LASA contribution

## Slide 14: INFN & PIP-II
A long-term fruitful Collaboration exists between Fermilab and INFN.
  A first agreement between DoE and Italian Ministry of Education, University and Research (MIUR) in July 2017 quote high power proton accelerators.
  Green light in 2018 from MIUR for an Italian participation to the realization of PIP-II through an in-kind contribution mediated by INFN LASA.
  INFN-LASA is today expected to build the 650 MHz cavities required by the low-beta section of the front-end linac, as signed by US Department of Energy and Italian MIUR on December 4th 2018.
December 4th, 2018, the U.S. DOE and Italy’s MIUR agreement signed

## Slide 15: INFN & PIP-II
INFN - LASA firstly provided a novel RF design for the LB650 cavities, fully plug compatible with the Fermilab technical interfaces and performances specifications.
  This cavity design has been chosen for PIP-II LB650 as the best compromise between CW and pulsed operation performances
INFN-LASA contribution is expected to cover the needs of LB650 section, and this includes:
  40 SC cavities (36 plus contingency) delivered as ready for string assembly, equipping 9 cryomodules.
  Qualification via vertical cold-test through a qualified cold-testing infrastructure acting as a subcontractor. INFN-LASA will cover a limited number of cavity tests.
  Compliance to the PIP-II Technical Review Plan, the procedure issued by Fermilab in order to meet PIP-II technical, schedule and budget commitments.
  Engagement of INFN-LASA and Fermilab technical teams to ensure that final cavity design properly interfaces with external components.
PIP-II LB650 Project Specifications | 
Acc. Gradient | 17.5 MV/m
Q0 | 2.3 1010
RF rep rate | 20 Hz to CW
Beta | 0.61

## Slide 16: INFN PIP-II Cavity Design
INFN LB650 for PIP-II, cold cavity | 
βgeometric | 0.61
Frequency | 650 MHz
Number of cells | 5
Iris diameter | 88 mm
Cell-to-cell coupling, kcc | 0.95 %
Frequency separation π-4π/5 | 0.57 MHz
Eq. diameter - IC | 389.8 mm
Eq. diameter - EC | 392.1 mm
Wall angle – Inner & End cells | 2 °
Effective length (10*Lhc) | 704 mm
Optimum beta βopt | 0.65
Epeak/Eacc @ βopt | 2.40
Bpeak/Eacc @ βopt | 4.48 mT/(MV/m)
R/Q @ βopt | 340 Ω
G @ βopt | 193 Ω
Inner cells stiffening radius | 90 mm
External cells stiffening radius | 90 mm
Wall thickness | 4.2 mm
Longitudinal stiffness | 1.8 kN/mm
Longitudinal frequency sensitivity | 250 kHz/mm
LFD coefficient kext at 40 kN/mm | -1.4 Hz/(MV/m)2
Pressure sensitivity kext at 40 kN/mm | -11 Hz/mbar
Maximum Pressure VM stress at 50 MPa | 2.9 bar
Maximum Displacement VM stress at 50 MPa | 1.5 mm
INFN LB650 RF Design rationales:
Cell coupling kcc optimized assuming TESLA-type cavity as a reference, of the quantity N2/(βkcc), where N is number of cells, β relative velocity. It models field-flatness sensitivity to cell frequency errors.
End Cell frequency tuning achieved by increasing the diameter of the whole terminal cell thus preserving its round shape and symmetry.
Maximize G factor while preserving sidewall angle at 2° avoiding potentially negative value during the cavity field flatness tuning stage.
Achieve a large frequency separation between π and 4/5 π modes.
Single stiffening rings at both end and inner cells, preserving manufacturing quality and tunability with respect to a double stiffener.
Example of EM analyses performed: Dipole HOM at 1678 MHz showing partial reflections in the FPC

## Slide 17: INFN & PIP-II – from Design to Manufacturing
In order start validating cavity design, fabrication procedures and surface treatments, several prototype cavities are being realized:
5 single-cell cavities, 3 already manufactured and 2 soon to be delivered
2 complete 5-cell cavities, fully compliant to the current state of cavity interfaces as per Fermilab specifications. Delivery expected after summer 2019.
  Eddy Current scanning of Nb sheets ongoing now at DESY.
INFN prototype as designed
End-group stage
5 delivered single-cell cavities
Surface inspection of copper mockup

## Slide 18: INFN-LASA and Fermilab joint agenda items
Electro-Polishing RF surface treatment: specific tools are being developed and the process recipe is being optimized for the PIP-II geometry with steep cell walls.
  The difference in size and shape requires a careful optimization of treatment parameters and electrode geometry with respect to 1.3 GHz tesla-shaped cavities
  First step: successful results with test EP removal at the prototypes vendor premises on a single-cell cavity.
Prototypes shared with Fermilab, surface treated and qualified by means of vertical cold-tests in both infrastructures early 2020.
In-depth characterization of magnetic flux expulsion performances of the Niobium material of these prototypes at the VTS facility at FNAL.
Jacketing and dressing of at least one multi-cell prototype to conclude this phase with an horizontal test with power coupler by late 2020.

## Slide 19: Infrastruttura criogenica e test RF

## Slide 20: Superconducting cavities testing facilities
Bunker with vertical LHe cryostat, f 700 mm, 4500 mm depth, can hold large SC cavities as 500 MHz
Sub-cooling system for superfluid helium, up to 1.5 K. Cooling power 40 W a 2.0K
2 Cold inserts for cavity testing
RF generators: 700 MHz, 1.3 and 3.9 GHz, with related accessories as PLL, power meters, etc.
Associated infrastructures
  ISO4 clean room (9 m2)
  High Pressure Rinsing facility
  Slow pumping Slow venting system
  UP water production plant (100 l/h)
Chart: Temperature (K)
| 2 | 1.9 | 1.8 | 1.7 | 1.6 | 1.5
Cooling Power (W) | 41 | 28 | 17 | 9.3 | 4.6 | 2

## Slide 21: Cryogenic infrastructure
Helium Liquefier: LINDE TCF100 (second hand in 1983)
  40 l/h with LN2
  Manual operation
  Refurbishment for automatic operation under way
Liquefier compressor: Sulzer, dry, 4 pistons
Recovery compressors: 100 m3/h
He purifier Linde, single column
He gas inventory: 4000 Nm3
LHe storage dewar: 4000 l
Balloon: 100 m3
On line He gas analysis: H2O, O2, N2

## Slide 22: Cryogenic infrastructure – workload
Helium Liquefier operation is fully enslaved to experiments and to the maintaining infrastructure as dewars cold (about 400 h/year for this purpose).
SC RF cavity processes 2300 liters of LHe for each test.
SC Magnet processes 1200 liters of LHe for each test.
Typical annual running figures.
  Running time, last 5 Y: between 1000 and 2000 h/y, depending on experiments.
  Discontinuous operation for the liquefier: typically 80 – 100 h for a single liquefaction cycle, every 3 - 5 weeks and up to 20 cycles per year.
  LHe produced per year: ∼ 40000 l
  Losses for physiological leaks, about 5-7 LHe liters per day. Remedy under way.
Limited man power and no turnover!
  Typically one person runs the liquefier
  Support available from groups and lab General Services (3 more peoples)
  No margin available if more plant intense use is foreseen as for next years
year | SRF tests | SCM tests | LHe purchased (l) | LHe cost (€/l) no VAT
2015 | 5 | 2 | 2700 | 8.10
2016 | 5 | 2 | 3600 | 8.50
2017 | 2 | 2 | 4500 | 9.10
2018 | 2 | 2 | 2700 | 11.8
2019 | 3 (5 tot) | 4 (5 tot) | (3600) | (13 or more?)
2020 | 5 | 5 | (> 4000) | ?
2021 | 3 | 5 | (> 4000) | ?
2022 | 3 | 5 | (> 4000) | ?

## Slide 23: Cryogenic infrastructure: status and upgrade
Warm helium gas management, from recovery to 200 bar storage
  Contract awarded to Linde for a fully automized and remotely controllable gas panel with embedded process and operator safety measures.
Helium liquefier status: in operation, limited degraded in performances, LHe transfer efficiency reduced.
  Assessment of TCF100 status by LINDE to happen soon. Then just two options are available. Only limited maintenance is possible only on heat-exchangers (60 k€).
  Revamping: keeping the existing cold-box and upgrade the full control chain, both hardware (pneumatic actuators) and software (PLC) to a modern unit. No guarantee on coldbox lifetime! 350 k€ + VAT, 6 months lead time, 4 weeks installation time
  Buying a new liquefier (60 l/h). 1.2 - 1.5 M€ + VAT, including piping and electrical installation 8 months lead time, 6 weeks installation time

## Slide 24: Personale
 | Ricercatori e tecnologi |  |  |  | Tecnici |  |  |  |  | 
 | TI |  |  |  | TI |  |  |  |  | 
 | Angelo Bosotti |  |  |  | Massimo Bonezzi |  |  |  |  | 
 | Paolo Michelato |  |  |  | Massimo Fusetti |  |  |  |  | 
 | Laura Monaco |  |  |  |  |  |  |  |  | 
 | Carlo Pagani |  |  |  | Calcolo (Pietro Spada) |  |  |  |  | 
 | Rocco Paparella |  |  |  | Progettazione e officina (Carlo Uva) |  |  |  |  | 
 | Daniele Sertore |  |  |  | Servizi generali (Luca Imeri, Mauro Quadrio) |  |  |  |  | 
 | TD |  |  |  | TD |  |  |  |  | 
 | Alessio D'Ambros |  |  |  | Vito Vizziello |  |  |  |  | 
 | Michele Bertucci |  |  |  |  |  |  |  |  | 
 | Giorgio Fornasier |  |  |  |  |  |  |  |  | 
 | Tommaso Grimaldi |  |  |  |  |  |  |  |  | 
 | Sandeep Mohanty |  |  |  |  |  |  |  |  | 

## Slide 25: Photocathodes for High Brightness Photoinjectors
LASA is providing high QE Cs2Te photocathodes since ‘90s (more than 150 photocathode produced) to different labs for high brightness RF electron gun operation, representing the state of the art in this field.
  DESY (FLASH, PITZ, REGAE)
  E-XFEL
  APEX (LBNL)
  FAST (FNAL)
  LBNL for the LCLS II commissioning
VT installation
Cs2Te Production & Transfer
Cs2Te Production
Cs2Te Transfer
Preparation Chamber at LASA
1998
1999
2000
2001
2002
2003
2004
2005
2006
2007
2008
2009
2010
“New diagnostic”
2011
2013
2015
2016
13 mm
10 mm
5 mm

## Slide 26: New Collaborations on photocathodes
Shanghai Tech University (MoU signed with INFN in Feb 2019)
  Interest for a complete photocathode systems based on Cs2Te for RF Gun
  Interest for a complete modified photocathode systems based on Cs2Te for 500 kV DC Gun
DESY Zeuthen (cost sharing with INFN LEAPh)
  Established a reproducible procedure to grow alkali antimonide compounds (green sensitive) on INFN plugs
  Development (design and construction) and of a new photocathode system for visible light sensitive photocathode (base pressure in the low 10-11 mbar)
New Pumping System based on D2000 NexTorr (SAES)

## Slide 27: Photocathode Stress test for CW operation (BriXSinO)
The operation of photocathodes at 1 MHz as SHINE, LCLS II, MariX, and even more at the 100 MHz repetition rate foreseen for BriXs is a challenge for the present photocathodes and lasers.
INFN supported a photocathode stress test, funding the buying of a first part of the 100 MHz BriXSinO laser system.
We plan a stress test for Cs2Te photocathodes at LASA in our DC gun with a dedicated laser (tender in progress)
  Laser: 10 W in IR and 0.5 W in UV @ 100 MHz
  DC Gun: 100 kV (max), 8 mm gap
  Photocathode charge (QE=5 % @ 254 nm): 50 pC
*
HP10
Uscita alternativa per cross correlatore
l/2
A
PBS
LBO
Dic1
Sistema telescopico 2
BBO
Dic2
*
Sistema telescopico 3
Shaping
Sistema telescopico 4
T
BS-UV
delay
BBO
UV-det
BS-diag
«CCD»
*
*
PC
Oscilloscopio
a-BBO
Foc-CC

## Slide 28: Spare slides

## Slide 29: Cryoplant layout

## Slide 30: Lifetime and extracted charge in pulsed operation
Extracted charge: 3.1 C
D time=439 days
Extracted charge: ~ 20 C
D time > 3 years
Pulsed operation
800 ms, 1 MHz, 10 Hz
73.3 Dark Current Evolution
73.3 QE Evolution

## Slide 31: Lifetime and extracted charge in CW operation
CW operation
1 MHz

## Slide 32: Photocathodes for High Brightness Photoinjectors
LASA photocathode systems are UHV systems and consist of a preparation system, a transport box (suitcase) and a transfer system for insertion of the photocathodes into the gun.
The systems have been installed in many labs and several suitcases (> 10) are available for photocathode exchange between the labs.
The upgraded version of the suitcase is based on SAES NexTorr pump, allowing shipping by plane.
Final Tuning
VT installation
Preparation Chamber at LASA
Transport Box
Preparation Chamber
DESY FLASH
New transport box

## Slide 33: Cs2Te growth studies and stability
  Cs2Te growth studied by XPS (in collaboration with UniModena)
    Different compounds identified before formation of the correct stochiometric ratio
  On-line monitoring of reflectivity and spectral response allows achieving stable and reproducible photoemissive films.
  Deposition stable and reproducible also changing Te film thickness both in QE and in reflectivity
A. di Bona et al., JAP80(1996)3024
Hg lamp
Filter wheel
Shutter
Remote controller
Photocurrent signal
Prep. chamber viewport
Photodiode
Reflected power
Incident power

## Slide 34: Cs2Te R&D
Intensive R&D activity has supported the production process aiming in deeper understanding of the physical properties of the materials
  Optical properties
  Photoemission model
  Thermal Emittance
Cs2Te
4th harmonic (l = 264 nm)
eth = 0.5 ± 0.1 mm mrad
for 1 mm rms spot radius
5th harmonic (l = 211 nm)
eth = 0.7 ± 0.1 mm mrad
for 1 mm rms spot radius
Rs
Rp
Vacuum
Molibdenum
Cs2Te
n | k | s [nm] | thickness [nm]
1.75 | 0.356 | 0 | 38.5