## Slide 1: Proposal of a compact Inverse Compton X-ray Source for advanced radiological imaging
Overview of Compton Sources (ICS) and Applications
Paradigms for Compton Sources (Linac – based, Storage ring – based, Energy Recovery Linac – based, Linac+FEL – based)
Brilliance Chart (ICS, bremsstrahlung, FELs, Light Sources, etc)
STAR @ UniCal
BoCXS for Bologna metropolitan area
Luca Serafini – INFN-Milan and University of Milan
luca.serafini@mi.infn.it
Massimo Placidi – Università di Bologna – massimoplacidi@icloud.com
Seminar Outline

## Slide 2: Inverse Compton Sources, Overview, Theory, Main Technological Challenges – Photonic Colliders
New Generation of X/g ray beams via electron-photon beam collisions for advanced applications in medicine/biology-material science/cultural heritage/national security and fundamental research in nuclear physics and high energy physics (e-g, g-g colliders, pol. e+ beams, hadron. physics, etc)
Inverse Compton Sources (ICS) are e-/photon colliders aimed at producing secondary beams of photons
Several Test-Facilities world-wide: after a decade of machine test&development we are entering the era of User Facilities in X-ray imaging and g-ray Nuclear Physics and Photonics

## Slide 3
Courtesy A. Variola
STAR
ICS are the most effective “photon accelerators” (boost twice than FELs)
“4g2 boost effect”
HigS
ELI-NP
CALA

## Slide 4: Existing and planned Thomson sources
From THOMX Conceptual Design Report, A.Variola, A.Loulergue, F.Zomer, LAL RT 09/28, SOLEIL/SOU-RA-2678, 2010
STAR (Calabria) Linac 20-100 5.1010 (100 Hz) 18
ELI-NP-GBS Linac+Laser-Recirc 0.2-20 MeV 1012 (100 Hz) 18

## Slide 5
highly asymmetric compact*
electron-photon colliders
secondary photon beams via large
lorentz boost of c.m. reference frame
*10 m, 10 M$
MeV/GeV’s electrons
eV’s photons
w/o laser recirculator 5.1010 ph/s
w laser recirculator 1012 ph/s
up to 1012 ph/s
with MW-class FP
optical cavities

## Slide 6
MariX/BriXS Program at Universita’ degli Studi di Milano and INFN
Courtesy V. Petrillo
1013 - 1014 ph/s
with 100 mA e- beams

## Slide 7
After 1 year of hard work...
CDR has been published and
available for download at
www.marix.eu

## Slide 9
Executive Summary
published on NIM-A

## Slide 10
BriXS & MariX FEL based on bubble arc compressor:
we use twice the same 1.5 GeV SC CW Linac
1.5-1.8 GeV
3.-3.6 GeV
3.2-3.8 GeV
Compton
Compton
BriXS: 20-180 keV mono-chromatic X-rays up to 5.1012 photons/sec in 5% bdw
Elettra-like
A relativistic-doppler antenna
A boosted e-g
Collider

## Slide 13: 3rd-4th Generation Light Sources
Synchrotron light sources: < 50 keV, > 50 ps (100 m, 300 M$)
X-ray FEL (LCLS): energy ≤25 (50?) keV, 1-100 fs (1 km, 1 G$)
New approach: inverse Compton scattering (ICS) 20-200 keV , sub-ps, (10 m , 10 M$) – sometimes called Laser Synchrotron since a laser pulse substitutes the magnetic undulators
The critical frequency of synchrotron radiation is
B

## Slide 14
1-25 GeV
electrons
100-0.5 Å
photons
cm und. period lu
FEL’s and Thomson/Compton Sources common mechanism: collision between a relativistic electron and a (pseudo)electromagnetic wave
20-150 MeV electrons
0.8 m laser l
20-500 keV
photons
3 km
20 m
The Classical E.M. view (Maxwell eq.): Thomson Sources as synchrotron radiation sources with electro-magnetic undulator

## Slide 15
FEL resonance condition
(magnetostatic undulator )
Example : for lR=1A, lw=2cm, E=7 GeV
(electromagnetic undulator )
Example : for lR=1A, l=0.8mm, E=25MeV
Example : for hn=10 MeV, l=0.4mm, E=530 MeV
laser power
laser spot size
L. Serafini et al., Proceedings of the SPIE,
Volume 6634, article id. 66341G (2007)
Violation of Energy-Momentum Conservation !!

## Slide 16
FELs (pure g2)
Thomson
X-rays
Nuclear
Photonics
X/g
[MeV]
Te [MeV]
1 GeV
1 TeV
Polarized
Positrons
D
g-g Colliders
Ecm [MeV]
0.511
1.533

## Slide 17: Quantum Model: a look at what happens in the Center of Mass reference system (kinematics)
Lab ref.
c.m. ref.
Recall some Basics

## Slide 18
Courtesy M. Gambaccini
300 mrad
60 mrad

## Slide 19
Recap
(exact analytical formula, no approximations)
cos
cos

## Slide 20
Recap
(exact analytical formula, example 250 MeV electrons against hnL=1.2 eV photons)

## Slide 21
Recap
(exact analytical formula, example 250 MeV electrons against hnL=1.2 eV photons)

## Slide 25
Compact machine
10x10 m2
In operation since
early 2015
An ICS based X-ray User Facility in operation in Germany

## Slide 26
Measured 1.5.1010 ph/sec with 20 mA
measured

## Slide 27
Measured 5.1010 ph/sec with 20 mA
measured

## Slide 28
Conventional X-ray tube for mammography
Spatial resolution ~100 mm
High Flux ~107 g/(mm2s) equivalent to ~5.1011 g/s over 20x20 cm2 area.
65 cm
Great example of Radio-logical imaging applied to mass screening over population: mammography
Low energy photons in the spectrum are absorbed by tissue, delivering radiation dose without bringing informations to detector. Risk of inducing secondary tumors increases without increasing the benefit of detecting early tumors
Absent in
Thomson
Source
X-ray
spectrum!

## Slide 29
3 cm thick in vitro human breast tissue
a) SR digital image
Energy 17 keV
Scan step 100 mm
MGD 1 mGy
b) SR digital image
Energy 20 keV
Scan step 100 mm
MGD 0.33 mGy
Conventional
X-ray tube 26 kVp
MGD 1 mGy
Mammography with Mono-chromatic X-rays at 20 keV has been proven
far superior in Signal-to-Noise-Ratio w.r.t. conventional mammographic tubes,
with a considerably lower radiation dose to the tissue

## Slide 30
Compact Thomson X-ray Sources could be located inside hospitals to diagnose
and treat patients directly at the hospital site (unlike Synchrotrons…)

## Slide 31
Phase Contrast Imaging made possible
by small round source spot size (< 20 mm)

## Slide 32
courtesy of A. Bravin (ESRF)
Bio-Medical Advanced Imaging with Mono-chromatic X-rays, demonstrated at
Synchrotrons, is possible also with High Flux Thomson X-ray Sources
in 20 keV-100 keV energy range

## Slide 33
Bio-Medical Advanced Imaging with Digital Subtraction of Mono-chromatic
X-ray shots are also possible with High Flux Thomson X-ray Sources with
picosecond to millisecond time resolution

## Slide 34
accepted for publication on Physics in Medicine and Biology
MariX-RAD CSN5-INFN
Resp. Naz. Paolo Cardarelli
Univ. di Ferrara

## Slide 35
MariX-RAD CSN5-INFN - Resp. Naz. Paolo Cardarelli - Univ. di Ferrara

## Slide 37
comprehensive overview recently presented at the PAHBB-2016 Workshop (see https://conferences.pa.ucla.edu/hbb/index.html) by A. Variola (INFN-LNF)

## Slide 38: Advancing Thomson X Ray Sources for Bio/Medical Imaging Applications and Matter Science

## Slide 39
Accelerator and Equipments
in ELI-NP Building
100 m, 100 M$ scale
A g-ray User Facility in construction in
Romania: ELI-NP-GammaBeamSystem

## Slide 40: Optical system: laser beam circulator (LBC) for J-class psec laser pulses focused down to mm spot sizes
Circulator principle
2 high-grade quality parabolic mirrors
  Aberration free
Mirror-pair system (MPS) per pass
  Synchronization
  Optical plan switching
    Constant incident angle = small bandwidth
PARAMETERS = OPTIMIZED ON THE GAMMA-RAY FLUX
Laser power = state of the art
Angle of incidence (φ = 7.54°)
Waist size (ω0 = 28.3μm)
Number of passes = 32 passes
2.4 m
30 cm
Electron beam is transparent to the laser (only 109 photons are back-scattered at each collision out of the 1018 carried by the laser pulse)
courtesy K. Cassou

## Slide 42
Laser pulse round-trip is about 16 nsec. A fresh electron bunch must be transported and focused at the IP every 16 nsec, for 32 round trips (total of 480 nsec -> need long flat RF pulse)
g-ray beam time structure: micro-pulses carrying about 105 photons within the bandwidth (0.3%-0.5%) with 0.8 psec pulse duration, in trains of 32 micro-pulses, repeating at 100 Hz (10 msec train-to-train separation)
courtesy K. Cassou

## Slide 43
109 Authors, 327 pages
published today on ArXiv
http://arxiv.org/abs/1407.3669

## Slide 44
Rivaling with Synchr. Light Sources for energies above 50 keV

## Slide 45
FLASH
12.4
1.24
0.124
l (nm)
Thomson/Compton Sources
Brilliance of Lasers and X-ray sources
BELLA
ELI
Outstanding X/g photon beams
for Exotic Colliders

## Slide 46
highly asymmetric compact*
elecron-photon colliders
secondary photon beams via large
lorentz boost of c.m. reference frame
*10 m, 10 M$
MeV/GeV’s electrons
eV’s photons

## Slide 47
STAR – Southern europe Thomson source for Applied Research
is a good example of research infrastr. based on X-ray beam lines for a regional facility to be built in an developing region/country
10 m

## Slide 52
STAR Hangar and Bunker

## Slide 53
Stato Bunker STAR a Gennaio 2016

## Slide 54
Stato Bunker STAR a fine Maggio 2017

## Slide 59
Commissioning will start soon - first beams expected within end of 2019