## Slide 1
High transparent neutron beam profile monitor: beam image quality test
Vincenzo Variale, INFN-Ba
Meeting n_TOF, 20/06/2019
Catania

## Slide 2
The results show a partial beam profile slightly off axis;
A test with the small collimator should be planned (The test has been done with the big collimator  neutron beam spot, d=8 cm, larger than the monitor sensitive area, d=2.5 cm) ;
In order to verify the image quality of the device, some test with a proper ‘mask’ and/or reference objects (like wires ..) in front to the monitor (the Al foil) should be planned.
Partendo dalle conclusioni della presentazione del CERN  La statistica molto bassa
non permetteva nessuna valutazione sulla qualità dell’ immagine:

## Slide 3
Neutron
beam
The converter is an Al foil of 14 m with
a 1.6 m deposite of 6Li
Accelerating Grids
Stainless steel
Plastic
Ph
Deflecting Grids
In attesa del fascio si propongono dei tests per caratterizzare la qualità dell’immagine prodotta dal monitor.
Vincenzo Variale INFN-Bari, N_TOFmeeting, Catania 2019
Deflecting Grids
MCP and
Phosphor screen

## Slide 4: Monitor montato sulla flangia
a)
c)
b)
The vacuum chamber;
The Electrostatic Mirror mounted on the CF flange where there is also the ‘MCP assembly’;
c) The monitor mounted inside the vacuum chamber.
Notice no hindrance along the beam axis;
Beam axis

## Slide 5: Monitor test with a source
The neutron converter Al foil (the old one was dameged)
The a source mounted in the vacuum chamber
Zoomed a source view
a)
b)
c)

## Slide 6: Maschera proposta
Per controllare le dimensioni sia sull’asse orizzontale che su quello verticale si propone una croce:
Per attaccarla alla griglia:
Nota: per un test co sorgente a la maschera
potrebbe essere di alluminio per un test
con sorgente di neutroni?

## Slide 7
Montaggio su specchio Elettrostatico
Dalla forma della croce sul fosforo e quindi sulla ‘CCD camera’ si dovrebbero
ricavare informazioni sulla qualità dell’immagine ottenibile col dispositivo.