## Slide 1: Background rate simulation for EcoGas set up @ GIF++
Andrea Gelmi (University and INFN Bari (IT))
21/06/2019

## Slide 2
GIF++ GEOMETRY
z
x
Dorothea Pfeiffer (“The radiation field in the Gamma Irradiation Facility GIF++ at CERN”, arXiv:1611.00299v3 8 June 2017)

## Slide 3
Ecogas setup @ GIF++
To obtain more precise results, others set up present in the GIF++ upstream area have been simulated to take into account the possible backscattering:
CMS iRPC behind ecogas chambers
CMS-RPCs TROLLEY-1 (6 chambers) behind ecogas trolley

## Slide 4
Layer n° | Material | Density [g/cm3] | Thickness [mm]
1 | Aluminium | 2.69 | 0.500
2 | Aluminium core | 0.5 | 5
3 | Aluminium | 2.69 | 0.500
4 | C10H8O4 PET | 1.37 | 0.188
1 | C6H10O5 cellulose | 0.3 | 1
6 | Copper | 8.96 | 0.380
7 | C10H8O4 PET | 1.37 | 0.188
8 | C10H8O4 PET | 1.37 | 0.188
9 | EVA (10%etylene + 90%vinyl acetate) | 0.934 | 0.150
10 | Graphite | 1.7 | 0.001
11 | HPL | 1.4 | 2
12 | Gas gap | 3.569 | 2
13 | HPL | 1.4 | 2
14 | Graphite | 1.7 | 0.001
15 | EVA (10%etylene + 90%vinyl acetate) | 0.934 | 0.150
16 | C10H8O4 PET | 1.37 | 0.188
17 | C10H8O4 PET | 1.37 | 0.188
18 | Copper | 8.96 | 0.380
CMS-RPC geometry has been used for all detectors

## Slide 5
SIMULATION DETAILS
Number of simulated events per ABS: 5*108
Source activity:
spring 2015
Spring 2019 = 4 years later T= sec
half life
/N simulated = 24500
To compare the rate simulated and measured:
Rate simulated * (
2 day cpu
High statistics <1%

## Slide 6
SIMULATION DETAILS
Simulation performed using Geant4.9.6
• Physics List: G4EmLivemorePhysics()
• Energy Threshold in Geant4 are expressed in terms of range. Used standard Geant4 cuts : Gammas 1 um
In the GEANT simulation the number of events with a signal in the detector has been defined when a charged particle interact in a gas volume.
= if ((particleCharge !=0) && (edep !=0) && (volName == "GasGap1") || (volName == "GasGap2"))
Has been assumed that each produced charged particle generates a signal in the readout strips on arriving at the gas gaps. If more than one charged particles reaches the gas gap, only the first one is assumed to produce a signal.
Statistical uncertainty: BINOMIAL DISTRIBUTION

## Slide 7
Charged particles threshold
From previous CMS-RPC experience:
Optimal charged particles threshold > 100 keV
iRPC
GIF++ experiments results vs simulation results
For ECOGAS simulation a “simulated threshold” cut = 2 is directly
applied on the hit rate, taking into account the previous results (discrepancy)
*More results in backup

## Slide 8
BACKGROUND RATE
Cluster rate normalized for the detector surface.
Good agreement between simulated rate and rate measured @ GIF++ (CMS-GT 2mm)

## Slide 9
SENSITIVITY
S(ABS) = (ABS)
RPC sensitivity increases @ low ABS due to the different gammas energy distribution 
@ low ABS more gammas at nominal energy (662 kev)
Double gap RPC have sensitivity ~ 2 times higher

## Slide 10
INCIDENT PARTICLES
Knowing the incident gamma flux, one could rescale it using a “specific sensitivity” (optimized for the detector and electronics) and better define the hit rate

## Slide 11
BACK UP
SLIDES
Some results from the CMS iRPC simulation and comparison with real data @ GIF++

## Slide 12
GIF++ Irradiator
ID scan | ABS upstream
2363 | 4.6
2361 | 6.9
2360 | 10
2364 | 15
2359 | 22
2370 | 33
2356 | 46
2374 | 69
2358 | 100
2371 | 150
2357 | 220
2372 | 316
2362 | 460
2365 | 1000
Source Cs137
Nominal energy gammas = 662 keV
Filter | Material | ABS
A1 | Empty | 1
A2 | Pb | 10
A3 | Pb | 100
B1 | Empty | 1
B2 | Al | 1.5
B3 | Pb | 100
C1 | Empty | 1
C2 | Pb | 2.2
C3 | Pb | 4.6
Aluminium support

## Slide 13
The gammas interact with the materials present in the GIF++:
lead (absorbtion filters, collimators, lense),
steel (absorbtion filters frame, source capsule, floor),
aluminium (absorbtion filters),
concrete (surrounding bunker enclosure).
absorption filters
source
source
collimator
lens
absorption filters
absorption filters
lens
GIF++ Irradiator
Notes: Thickness lens: 0.01-3.47 mm
Thickness collimators: 0.05 – 26.68 mm

## Slide 14
Uniform gammas incident distribution
X-Y distribution: electrons creation and electrons ionization.
GIF++ photons spatial distribution
X-Y gammas incident
X-Y electrons creation-ionization
The ± 37° panoramic collimators and the angular correction lens allow to replace the dependence of the photon current by a uniform current in each X-Y plane. This is confirmed by the G4simulation gammas incident distribution.

## Slide 15
GIF++ photons energy distribution: not monoenergetic!
GIF++ nominal photons energy 662keV
P2 80 keV
Pb atom de-excitation
P1 184 keV
Compton scattering (Tmax)
13
11.6
82
For γ energies of 662 keV or below, the main processes are Compton scattering and photoelectric Effect.
GIF++ photons energy spectrum
Notes: Clearly visible in the spectra are the back-scatter peak at 184 keV and the characteristic 82 Pb K-shell X-ray peaks around 80 keV

## Slide 16
GIF++ photons energy spectrum

## Slide 17
GIF++ photons energy spectrum
For energies of 662 keV or below, the main processes are Compton scattering and photoelectric Effect.
13
11.6
82
The photons arrive already at the attenuation filters with low energy component, the source capsule and the irradiator collimator already cause an amount of scattering that broadens the spectrum.

## Slide 18
Kinetic energy distribution of Compton scattered electrons
Tmax is known as the
Compton Edge
Why the photons pick (p1) at ~ 200 keV ?
GIF++ photons energy spectrum

## Slide 19
photoelectric
Why the photons pick (p2) at ~ 100 keV ?
Pb
The gammas with energy of 0-300 keV have an high probability to interact by photoelectric effect. The X-rays emitted because of the Pb atom de-excitation from K-shell have an energy around 80 keV.
GIF++ photons energy spectrum

## Slide 20
Rate GIF++ vs G4 simulation

## Slide 21
Sensitivity GIF++ vs G4 simulation

## Slide 22
Rate GIF++ vs simulation
γ energy cuts
e- energy cuts
N events with an electron that ionizes in one of the two gas gaps or both

## Slide 23
Discrepancy GIF++ vs simulation
γ energy cuts
e- energy cuts

## Slide 24
SIMULATION DETAILS
Incident particles (TOP,BOT, TOTAL):
Number of particles,
Particle Data Group,
ID,
Parent ID,
Kinetic energy,
X position,
Y position,
X-Y position,
Z position,

## Slide 25
SIMULATION DETAILS
Charged particles (GAP1, GAP2, TOTAL):
Number of particles,
Particle Data Group,
ID,
Parent ID,
Kinetic energy,
X position creation,
Y position creation,
X-Y position creation,
Z position creation,
X position interaction,
Y position interaction,
X-Y position interaction,
Z position interaction,

## Slide 26
SIMULATION DETAILS
Charged particles (GAP1, GAP2, TOTAL):
X-Y creation vs interaction,
Z creation vs interaction,
Creation Compton vs Photoelectric,
Interaction mcs vs ion vs eBrem,
Energy deposited,
Sensitivity.