## Slide 1: Overview of channeling in bent crystals
University of Ferrara and INFN - Italy
Vincenzo Guidi
guidi@fe.infn.it

## Slide 2: Outline
Orientational coherent interactions in bent crystals
Experiments with bent crystals at different energies and particles
Summary

## Slide 3: Orientational coherent interactions in bent crystals
Channeling is the confinement of charged particles traveling through a crystal within atomic planes or strings
Channeling occurs as the trajectory of particles forms an angle lower than the critical angle [1]
[1] J. Lindhard, K. Dan. Vidensk. Selsk. Mat. Fys. Medd. 34 (1965) 14.
Planar Channeling
Axial Channeling

## Slide 4: Planar phenomena
(a) Straight Crystal
(b) Bent Crystal
Volume reflection was predicted by Taratin and Vorobiov in 1988

## Slide 5: Positive- vs. negative-particle dechanneling
Channeled negative particles are dechanneled faster than positive ones due to higher probability to suffer incoherent scattering with nuclei.
Ultra thin bent crystals are required for efficient deflection of negative particles

## Slide 6: Channeling and volume reflection in a bent crystal
Bent crystals can be used in an accelerator for particle beam manipulation:
  extraction of particles from the circulating particle beam;
  collimation of the beam;
  focusing
  splitting
With short bent crystals (~ mm), it is possible to deflect ultra-high-energy particles in CERN (SPS or LHC) with angles (100 µrad – 1mrad) achievable by 1000 Tesla magnets having a similar size.
[1] Tsyganov (1976)
[2] Taratin and Vorobiov (1988)
~θbending [1]
~θcritical [2]
θbending

## Slide 7: Labs for channeling experiments
SPS
LHC
2 MeV
0.195 – 0.855 GeV
3-10 GeV
120-270 GeV
400 GeV
7 TeV
INFN exp.
Since 2003
NTA_HCCC
Coherent
Icerad
Chanel
Axial
CRYSBEAM
UA9

## Slide 8: Sub-GeV electrons
CHANEL exp. & X1 experiments
195-855 MeV electrons
Mainzer Mikrotron – University of Mainz (Germany)
195-855 MeV

## Slide 9: Quasi-mosaic crystals fabrication
G. Germogli, A.Mazzolari et al., Nucl. Instr. Meth. B 355 (2015)

## Slide 10
<111>
<211>
Crystal bending and characterization
FOGALE TMAP 4: thickness measurement
Quasi-mosaic crystal [1]:
Anticlastic curvature suppressed due to strong bending along principal direction
Panalytical X’pert Pro x-rays: bending angle estimation
Crystal mounted onto bending holder
[1] Y. M. Ivanov, JETP Lett. (2005).

## Slide 11: Experimental setup at the MAinzer MIkrotron
855 MeV electron beam characteristics:
Beam-Spot size σhor = 200 µm,
Beam Divergence σ'hor = 70 µrad
Beam-Spot size σvert = 70 µm,
Beam Divergence σ'vert = 30 µrad
Crystal parameters:
T = 30.5 µm
Rqm = 33.5 mm
(111) Bent planes
U0= 23 eV
θc= 220 µrad
D. Lietti et al. Rev. Sci. Instr. 86 (4), 045102 (2015)

## Slide 12: Experimental results on beam steering
(a) Angular scan for deflected beam distribution: (1) and (6) nonchanneling regime; (2) channeling; (3) dechanneling; (4) volume reflection; and (5) volume capture.
(b) Crystal aligned with the beam: multiple scattering causes dechanneling and rechanneling.;
(c) crystal is not aligned with respect to the beam, but the beam trajectory becomes tangent to the atomic planes inside the crystal bulk. VR or the competitive process of volume capture occurs.
A. Mazzolari et al., Phys. Rev. Lett. 74 (2014) 2740

## Slide 13: Experimental results on beam steering
CHANNELING
VOLUME REFLECTION
Θinc~450 µrad Deflection =191±10 µrad
Fraction of reflected is 76.7±1.1%
Θinc ~ 0 µrad Deflection = 910±5 µrad
Fraction of channeled is 20.1±1.2%
First experimental observation of efficient steering of negative particles in the sub-GeV energy range
A. Mazzolari et al., Phys. Rev. Lett. 74 (2014) 2740

## Slide 14: GeV electrons
T513 exp. & CHANEL exp.
3.35-14 GeV electrons
Stanford Linear Accelerator Center– Menlo Park, California (USA) in collaboration with Aarhus University (Denmark)
3.35 -14 GeV

## Slide 15
The crystal was mounted in a scattering chamber in the End Station A Test Beam. A Newport AG-PR100 precision rotational stage allowed rotation of the crystal with step sizes nominally down to 5 µrad. A YAG screen with a camera 13 m downstream of the crystal provided the main diagnostics detecting the effect of the crystal on the beam.
Experimental setup at SLAC
http://estb.slac.stanford.edu

## Slide 16
Experimental results
6.3 GeV electrons
3.35 GeV electrons
Comparison with Monte Carlo simulation through
DYNECHARM++ code
Channeling efficiency: 24%
Channeling efficiency: 22%
U Wienands et al., Phys. Rev. Lett. 114 (2015) 074801

## Slide 17: Deflection efficiency vs. beam energy
TN Wistisen et al. A study of Channeling, Volume Reflection and Volume Capture of 3.35-14.0 GeV Electrons in a bent Silicon Crystal, SLAC-PUB-16435 (submitted to Physics Letters B)
T513 crystal: Si (111), 60.0 µm thick, bending angle = 402 µrad
CHANNELING
VOLUME REFLECTION

## Slide 18: Hundreds-GeV beams
UA9 & H8RD22 collaborations
INFN CHANEL and AXIAL experiments
120 GeV/c e-, 150 GeV/c π-, 400 GeV/c p
SPS and SPS-extracted lines H4 & H8
120-400 GeV/c

## Slide 19: Crystal fabrication
Anisotropic etching:
Etching rate on different silicon planes for KOH 20% at 40 °C
LPCVD deposition of silicon nitride thin layer
Crystalline surfaces
Silicon nitride patterning
[1] S. Baricordi et al., Journal of Physics D: Applied Physics 41 (24), 245501
[2] S. Baricordi et al., Applied Physics Letters 91 (6), 061908
Notes: Non altero la qualità cristallina originaria

## Slide 20: Crystal bending
A primary curvature is imparted by mechanical external forces, which result in a secondary (anticlastic) curvature.
The mechanical holder imparts a primary strain and can be set far apart from the beam hence reduceing unwanted interaction with the beam.
Beam
JAP 107 (2010) 113534

## Slide 21: Experimental Setup on CERN-SPS external beamline (H8-H4)
Spatial resolution
~5 μm
Angular Resolution
~1 μrad
Goniometer resolution
~1 μrad
Double sided silicon detectors* DsX (300μm)
High-precision goniometer
Notes: SISTEMA DI TRACCIAMENTO X e Y
POSIZIONE Z DATA DA POSIZIONE RIVELATORI
NECESSARI 3 DETECTOR -> COSTRUZIONE ANGOLO DI DEFLESSIONE
SUFFICIENTI 3 DETECTOR -> MENO DIFFUSIONE MULTIPLA
DISTANZA 10 m fra DETECTOR per CALCOLO ANGOLO
RISOLUZIONE SPAZIALE 5 MICRON-> ANGOLARE 0.5 MICRORAD

## Slide 22
Planar case: 400 GeV/c protons
Unperturbed beam
Channeling
Dechanneling
Volume reflection
Volume capture
Unperturbed beam
W. Scandale et al.,PRL 98 (2007) 154801
Deflection angle: full bending angle, i.e. 170 µrad
Efficiency: ~ 70 - 80%
Limited angular acceptance
Deflection angle: 13.5 µrad
Efficiency: > 95%
Large angular acceptance equal to the bending angle
Channeling
Volume reflection
Notes: 22

## Slide 23: The concept of multiple VR
A multistrip is a crystal for multiple VR
θref
θref
θref
V. Carassiti Rev. Sci. Instrum. 81, 066106 (2010)
V. Guidi et. al., J. Appl. Phys. 107, 113534 (2010).

## Slide 24: Observation of MVR
Deflection angle: 109 rad
Efficiency: 94%
It combines wide acceptance with very high efficiency
Installation of a unit in the SPS by CERN
PLB 688 (2010) 284
JINST 7 (2012) P04002

## Slide 25
MVR in one crystal
V. Tikhomirov PLB 655 (2007) 5
MVR from different planes of one bent crystal becomes possible when particles move at a small angle with respect to a crystal axis
Potential along [111] direction in silicon crystal
Notes: 25

## Slide 26
MVROC observation
Amplification of deflection angle of a factor 5
Deflection efficency as high as 84%
PRB 682 (2009) 274

## Slide 27: Crystal assisted beam collimation
A “smart target” which kicks all particles in only one direction
a) multi-stage collimation system: an amorphous material spread the primary halo so that it can be intercepted by a secondary collimator.
b) crystal-assisted collimation: a curved crystal deviates the halo directly to the primary absorber.
c) Essential tool for halo collimation in the LHC with 7 TeV protons

## Slide 28
The UA9 experiment at
Super Proton Synchrotron
The high deflecting power of short bent crystal can be exploited in the collimation systems of LHC
The UA9 experiment investigates the possibility of using bent silicon crystals as primary collimators for HE protons and ions
Notes: 28
Aggiungi qualche commento

## Slide 29
Halo loss rate due to nuclear inelastic interactions of 120 GeV/c protons/Pb ions in the aligned crystal results to be smaller of up to 5-6 times for protons and up to 3 times for Pb ions than for its amorphous orientation.
Channeled efficiency was ~ 80-85% for protons and 74% for Pb ions by intercepting the deflected beam with another collimator located between the crystals and the absorber.
Channeling
VR
Amorphous orientation
Amorphous orientation
[1] W. Scandale et al. PLB 692 (2010) 78
[2] W. Scandale et al. PLB 703 (2011) 547
Collimation of protons
Notes: 29
Aggiungi qualche commento

## Slide 30
Collimation of lead ions
Collimation of 120 GeV/c per charge lead ion beam
Deflection by 170 urad with efficiency up to 74% like for 120 GeV/c protons
Loss rate due to nuclear inelastic interaction drops by factor of 3 (6 for protons)

## Slide 31: TeV beams
Extension of UA9 exp. to LHC
6.5 TeV/c protons
Large Hadron Collider
6.5 TeV/c

## Slide 32: LUA9: Crystal channeled the 6.5 TeV proton beam in the LHC
Nov 6th 2015: Beam steering via channeling in a bent crystal in the LHC.
FERRARA Si strip crystal installed in the LHC

## Slide 33
Beam losses vs. orientation
Operation at injection 450 GeV
Operation at 6.5 TeV
UA9: Crystal channeled the 6.5 TeV proton beam in the LHC
W. Scandale et al. PLB 758 (2016) 129

## Slide 34: Summary
Coherent interactions in bent crystals are powerful tools to manipulate the trajectories of particle beams
Such technique works over several decades of particle energies, particle’s charge and mass
Several orientational effects can be used for particle steering

## Slide 35
Thank you for your attention