## Slide 1: Status-of-art LHC machine crystal simulations
D. Mirarchi, A. Fomin, S. Redaelli, W. Scandale
Workshop on electromagnetic dipole moments of unstable particles
Milano, 4th October 2019

## Slide 2
Outline
LHC Collimation and layout conceptual idea
Layout design
Operational scenario
Expected performance
Conclusions

## Slide 3
Outline
LHC Collimation and layout conceptual idea
Layout design
Operational scenario
Expected performance
Conclusions

## Slide 4
The LHC: biggest and most powerful particle accelerator ever built
What does it mean?
Introduction
And in HL-LHC stored energy increased to ~ 700 MJ
Very sensitive machine, several constrains for operations with high intensity beams!
Highly efficient collimation system needed for a safe beam disposal at any time!
LHC design 360 MJ
USS carrier (Nimitz-class)
At ~5.2 knots
Stored energy
15-50mJ/cm3
Ladybug at same speed
Quench limit

## Slide 5
LHC collimation system
Multi-stage cleaning with about 50 collimators per beam,
Circulating
beam
Primary halo
Secondary halo
Tertiary halo
+ hadronic shower
Protection
Devices
(TCD)
Primary
Collimators
(TCP)
Secondary
Collimators
(TCSG)
Absorbers
(TCLA)
Tertiary
Collimators
(TCT)
Bottleneck
IP
Arc
Insertion
two dedicated insertions
Warm
Cold
Cold
Movable collimators: ensure required performance along the entire cycle
At 6.5 TeV/c: ~2 mm gap with 5 mm resolution!
Beam

## Slide 6
Conceptual idea
Beam halo deflected by a bent crystal (Crystal 1) : aperture Crystal 1 > TCP
Interaction products channelled by a second bent crystal (Crystal 2)
Dedicated absorber to intercept deflected halo that did not interact with target
Deflected halo impacts on a target
Double channelling scheme proved at SPS by UA9!
Channelling of secondary halo proved at LHC!
Deflected halo by Crystal 1
Shadow
Crystal 2
Second channelling by Crystal 2!
A. Natochii
D. Mirarchi, Workshop on electromagnetic dipole moments of unstable particles

## Slide 7
Outline
LHC Collimation and layout conceptual idea
Layout design
Operational scenario
Expected performance
Conclusions

## Slide 8
Main goals and constraints
Maximise the proton on target (PoT) while keeping the losses on superconducting magnets below standard collimation losses
Maximise number of Lc at the exit of Cry2, given the acceptance of the detector
Main constraints:
Space availability
Enhance the displacement of channelled halo and channelling efficiency of multi-turn halo
Clearance between deflected halo and machine aperture & circulating beam
Avoid the possibility to get hit by the beam during an asynchronous dump
Absorption efficiency of interactions products
Main goals:

## Slide 9
Simulation tools
Semi-analytical tools developed for quick evaluation of feasible layouts
Complete multi-turn simulations using SixTrack
Dedicated routine to treat interactions in bent crystals
Benchmarked in the energy range from 180 GeV/c to 6.5 TeV/c
6D and fully chromatic tracking taking into account interaction with collimators and aperture model of the machine
Prediction of expected density of protons lost with accuracy of 10 cm over 27 Km!

## Slide 10
Optimized layout in IR8
Natural choice: use of LHCb detector given its asymmetric orientation (Beam 1 direction)
5 mm long target of W (can be tuned depending on experimental needs)
Bending angle Cry2 = 14 mrad, length = 7cm: send decay products into LHCb acceptance
Bending = 150mrad
Length = 1.2cm
R = 80 m
Cry1
can be revised as a function of the operational scenario
Angular cut ~60 mrad
4 LHC-type collimators

## Slide 11
Optimized layout in IR3
Still Beam 1 orientation: possible debris from absorbers goes to IR4 rather than to ALICE
Warm insertion as opposed to the superconducting magnets present in IR8
Angular cut ~20 mrad
Mirror layout in Beam 2?
Same parameters as crystals in LHC!
Bending = 50mrad
Length = 4mm
R = 80 m
Cry1
Bending angle Cry2 = 5 mrad, length = 7.5 cm (avoid double channelling of 6.5 TeV protons)
Drift space of about 70 m to fit a dedicated experimental apparatus
5 mm long target of W (can be tuned depending on experimental needs)

## Slide 12
Outline
LHC Collimation and layout conceptual idea
Layout design
Operational scenario
Expected performance
Conclusions

## Slide 13
Operational scenario definition
Observable: is the loss pattern affected by the insertion of the Cry1+target+Cry2 assembly?
YES: limit on maximum stored intensity
NO: measurements during standard physics operations could be allowed
Parasitic operations
Dedicated operations
LHC running configuration in 2018 used
Dedicated optics would imply dedicated operations
ATLAS
ATLAS
ALICE
dp/p Coll.
RF
CMS
Dump
b Coll.
LHCb
TCP
TCSG
TCLA
IR7-DS

## Slide 14
Maximum stored intensity
Several configuration tested: Cry1 from 5s to 8s with 1s step
IR8 layout:
Cry1 at 5 s
(as IR7-TCPs)
Losses compatible only with dedicated operations
(i.e. maximum ~250 bunches)
Cry1 at 6 s
Losses compatible with parasitic operations (i.e. ~2500 bunches)
IR3 layout:
Cry1 at 5 s
(as IR7-TCPs)
Losses always compatible with parasitic operations
(i.e ~2500 bunches)

## Slide 15
Outline
LHC Collimation and layout conceptual idea
Layout design
Operational scenario
Expected performance
Conclusions

## Slide 16
Expected PoT
Loss sharing H/V planes
Flux of proton lost taking into account burn-off in 4 IPs
Fraction on impacts on the Cry1
Cry1 channeling efficiency
IR8 layout
IR3 layout
Cry1 at 5 s excluded for both layouts due to machine protection constraints
Values at 5 s to be considered as the asymptotic performance reach

## Slide 17
Lc channeling efficiency
Impacting distribution of protons on the target from SixTrack
Decay of Lc in the Cry2 taken into account as:
Distribution of Lc emerging from target obtained with Pythia8.240
Cry2 acts like a spectrometer:
Dechanneling length linear in
Critical channeling angle
Expected channeling efficiency of Cry2

## Slide 18
Expected Lc yield in a 10h fill
Significantly larger integrated yield of Lc in IR3
For both layouts Cry1 at 5s to be considered as the asymptotic performance reach
~70 Lc
~104 Lc
Total Lc production in 5mm long W target
Decay in the target
Lc spectrum
Lc channeling efficiency
Integrated PoT over 10h

## Slide 19
Optimized operational scenario
Main question: what is the minimum settings achievable for the Cry1?
  Avoid to become primary collimation stage
  Avoid high cold losses for both channeling and amorphous orientation
  Avoid dump on losses in case of lifetime drops
Both layout could be used in parasitic mode and full machine with Cry1 at 5.5 s!
~10 Lc
~200 Lc
Expected PoT(t) rate
Expected Lc yield in a 10h fill

## Slide 20
Margins and further constraints
Increased target length
To be studied in detail increase of losses in the machine (bkg to the detector, etc…)
Factor 2 in bunch in intensity in HL-LHC (hard to scale tails pop. and diffusion rate, i.e. PoT)
Germanium crystals
To be studied in detail increase of Lc channeling efficiency
Selective bunch train excitation in the vertical plane
To be studied in detail luminosity loss in main experiments
Challenging conditions in HL-LHC (Crab-Cavities failure, optics correction, …)
Allowed Cry1 settings may be larger than the 5.5 σ considered in these studies
Maximum sustainable PoT rate during operations and failure scenarios to be defined
LHCb experiment is operated at levelled luminosity: dynamic setup changes

## Slide 21
Outline
LHC Collimation and layout conceptual idea
Layout design
Operational scenario
Expected performance
Conclusions

## Slide 22
Conclusions
Studies for fixed-target experiments on-going in the Physics Beyond Collider framework
Design of two possible layouts finalized
IR8 to profit ot the LHCb detector
IR3 to overcome intrinsic limitations in IR8
Paper accepted for publication on EPJC
Expected PoT(s) with optimized scenario ~106 p/s, leading to ~10(200) Lc per fill in IR8(IR3)
Intrinsic limitations in IR8:
Bending of Cry2 of at least 14mrad (LHCb acceptance)
Proximity to IP8 leads to large angular cut of absorbers and Cry1 bending
Main limitation of IR3:
Dedicated detector to be built (70 m of available longitudinal space)

## Slide 23
Outline
Thank you for your attention!

## Slide 24
Outline
BACKUP

## Slide 25
Further considerations
Controls:
Crystals and target inserted only in SB and to be considered as VELO and XRP
Static limits on position to safely dump if devices accidentally moved
Impedance:
Optimized design needed for all components to be inserted with high intensity beams
Vacuum:
Present IR7 goniometers already compliant with all constraints
Operations:
Same commissioning, validation and operations as XPRs
ecloud:
Present IR7 goniometers never exposed to 25ns beams: SEY meas. recommended
Background to experiments:
No impacts expected on loads on TCTs
Assessment of local losses under the responsibility of LHCb

## Slide 26
Code Benchmarking
Crystal routine physics:
D. Mirarchi, et al, “Crystal implementation in SixTrack for proton beams.”, CERN Yellow Reports: Conference Proceedings (CERN, 2018). URL https://cds.cern.ch/record/2646800
NIMB 355, 378 (2015)
Examples of benchmarking:
Coherent effects
Nuclear interactions
NIMB 355, 378 (2015)
At the SPS extraction line (180 GeV/c & 400 GeV/c)
In the SPS and LHC rings (270 GeV/c, 450 GeV/c, 6.5 TeV/c)
Angular scan at 6.5 TeV/c
LHC: CERN-THESIS-2017-424
SPS: CERN-THESIS-2015-099

## Slide 27
Channeling efficiency in LHC (I)
450 Z GeV/c lead beams

## Slide 28
Channeling efficiency in LHC (II)
6.5 Z TeV/c lead beams

## Slide 29
Channeling efficiency in LHC (III)
~50 urad bending
4 mm long
~65 urad bending
4 mm long
Too close to critical bending radius!
Known poor nuclear channeling description in the routine for these extreme bendings

## Slide 30
Cry1 channeling efficiency

## Slide 31
Integrated PoT
IR8
IR3

## Slide 32
Local losses Cry1 at 5s in IR8

## Slide 33
Source of losses with Cry1 at 5s in IR8
Main limitations:
Large angular cut from TCSGs due to large b
Significant single diffractive production in the Cry1 due to required length

## Slide 34
Lc spectrum

## Slide 35
Impacts distribution on target

## Slide 36
LHC running conditions
Sharing losses H/V planes
Flux of proton lost taking into account burn-off in 4 IPs
Fraction on impacts on the Cry1
CH eff. of the Cry1
Assuming 2018 running conditions and:
t = 200h
tBO = 20h
256 bunches with 1.1x1011 p per bunch for Cry1 in IR8 at 5 s
2556 bunches with 1.1x1011 p per bunch for all other scenarios
Fill length = 10 h
Estimated protons lost in IR7 during 2017 using RadMon ~ 1.7e15
Estimated protons lost in IR7 during 2017 using formula above ~ 1.6-2.1e15

## Slide 37
LHC parameters in 2018