## Slide 1: Production of Electrodes for the ‘small FTM’
Piet Verwilligen INFN Bari 18-06-2019

## Slide 2: Reminder: Design of the small FTM
Main Idea:
- well isolated low noise detector to demonstrate the FTM principle: time resolution vs number of layers
- Make small area prototype, with only 2 electrodes: top & bottom
- Go back as much as possible to the design of the original prototype (with resistive kapton XC)

## Slide 3: Mechanical Design Internal Foil holder

## Slide 4: Mechanical Design External + Internal holder

## Slide 5: Disks to be produced by EP-DT-EF-MPT Workshop
Both disks:
  rdisk = 19 mm
  Cu electrode with «tongue» r1=16mm, r2=18mm
«Amplification foil» (2x)
  DLC covered Polyimide (50um)
  Active Area: ractive = 10 mm
  50um holes at 140um pitch
  Top hole diam: 50um, bottom hole diam: 70um
«Drift foil» (4x)
  Resistive Kapton XC (25um)
Cu ring (5um thick) r1=16 mm, r2=18mm
DLC Coated (USTC) 50um thick Polyimide rdisk = 19 mm
Yellow: active (holes) ractive = 10 mm Orange: plain DLC
Resistive Kapton XC

## Slide 6: Disks to be produced by EP-DT-EF-MPT Workshop
Both disks:
  rdisk = 19 mm
«Readout foil»
  Plain 50um polyimide foil
  Central Cu disk (ractive = 10 mm)
  Central via that allows to solder wire at the bottom side of the readout foil
«Insulation foil»
  Mylar
  As thin as reasonably possible: 5-10um
50um thick Polyimide rdisk = 19 mm
Cu (readout) 5um ractive = 10 mm with central via to solder wire
Mylar (5-10um)

## Slide 7: Detection Concept: Single detection layer of FTM
Outline of a Single Detection layer for the small FTM
I want to make the detector with 2 layers of 5mm drift
Spacers made by INFN-Bari
Important to have via on top and bottom Readout foil
If signal can be picked-up and discriminated then I will go to 4 layers of 2.5mm; 8 layers of 1mm; …
I would like to order:
  2 x Readout foil
  4 x Drift foil
  2 x Amplification foil
  2 x thin Mylar disk
Design is very simple, DXF available, need conversion to GERBER
Mylar Isolation (thin)
Top Readout (PI)
Drift Electrode (XC)
Mylar Isolation (thin)
Bottom Readout (PI)
Bottom Electrode (XC)
Amp Electr (DLC + PI)
Gas Gap (5mm)
Signal Wire (to SMA)
Signal Wire (to SMA)