## Slide 1
SLICE
(Soc eLectronIcs Compact dEtector)
Sviluppo di rivelatori All-In-One (detector,elettronica ,DAQ) utilizzando sistemi su circuiti integrato (SoC) commerciali di ultima generazione.
INFN Roma: Valerio Bocci (Resp Nazionale),Francesco Iacoangeli
INFN Roma2: Davide Badoni (Resp Locale), Matteo Salvato, Mattia Scagliotti
Particle
Detector
photon
Detector
Analog
conditioning
SoC
Trasmission
Layer
Formatted DATA
SLICE Valerio Bocci 2019

## Slide 2
The first scintillator detector All in One in literature using a microcontroller as main component (2014, V.Bocci ,G.Chiodi, F. Iacoangeli L. Recchia) DOI: 10.1109/NSSMIC.2014.7431252
Scintillator
SiPM
ArduSiPM Shield+Arduino Due
Suitable for any SiPM with bias voltage 10-90 Volt ,any size (1x1,3x3,6x6 …mm)
< 1 ns time resolution with internal analog discriminator
25 ns Time resolution with internal TDC
12 bits Internal peak hold ADC
All-in-One system, scintillator,SiPM,power supply,DAQ.
Synchronizable with GPS Clock (25 ns precision timestamp)
2.5 watt, <200 grams , few cm3 volume (shrinkable)
Simple Interface with PC (USB),Storage (SD Card),IOT(WiFi)
ArduSiPM as starting point
Application :
Chirone Surgery Probe (Gr5), UA9 beam monitor(Gr1)
Low Price
(now 350 € ,prevision in large quantity < 150 €)
Tecnology Transfer 2016
Now (2019) around 100 unit around the world.
Main application: School,University Lab, Beam test,Outreach.
Many schools projects:
Used from winners of CERN BL4S 2017
Measuraments of cosmic ray flux using light balloon up 33.5 Km, EOS Project 2018, MoCRiS OCRA project 2019.
SLICE Valerio Bocci 2019

## Slide 3
Non solo particelle, sviluppi interdisciplinari :
rivelatori portatili di reazioni di bioluminoscenza/chemiluminoscenza
Prof Elisa Michelini (Univ Bologna) Dr. Marcello D’Elia (Direttore Aree Laboratori forensi Polizia di Stato)
«ArduSiPM platform to detect different bioluminescent proteins and chemiluminescent reactions with very promising results».
SLICE Valerio Bocci 2019
ArduSiPM
Porta campioni
SiPM
3 mm
3 mm
21.2 mm3

## Slide 4
ASIC Way: Readout of detectors using ASIC (Application Specific Integrated Circuit)
Pro:
1) Custom design, fitting perfectly the application .
2) Many channels integration
Contro
1) High design and development cost .
2) Expensive production and high cost CAD needed
3) Strong dependence from technology and foundry, minimum quantity production.
SLICE way: Readout of detectors using generic mixed design (Analog/Digital) SoC (System On Chip) as main element.
Pro:
General application but custom use with different firmware.
Very low price also for single piece (<5 euro)
Free software or low cost development software.
Internal clock can be used for timing measuraments (order of nanoseconds).
Cheap Picoseconds scale TDC available as small external peripheral now (on chip in the future)
The best technology available in the market.
CPU Inside and many internal communication interface (WiFi, Ethernet, Bluetooth)
One channel modularity (maximum scalability)
Contro:
Need conditioning of analog signal.
Software optimization is not easy, there is a need for a deep knowledge of the functionality of the chip.
Low speed ADC and DAC (changing with technology trend)
Number of channels limited from peripherals available
SLICE Valerio Bocci 2019

## Slide 5: Goal of SLICE: Investigate and characterize commercial available chips for All-in-one platfom detector.
Chip Scale Atomic Clock
GPS time receiver
Analog signal conditioning
Generic SOC
10 ps RMS TDCs
Clock Reference Chip
SoC ,Analog Chip,GPS SoC, Oled Display
Accurate TDC from the market
Very low power data radio transmission
SLICE Valerio Bocci 2019

## Slide 6
SLICE Valerio Bocci 2019
SoC ,LoRa, Chip Scale Atomic Clock,TDC Platforms
Chip Scale Atomic Clock
Chip Scale Atomic Clock
Evaluation Board
TDC Evaluation Boards
SoC Evaluation Boards
LoRAWan Gateway

## Slide 7
Analog Circuits
Controlled DC-DC converter
Time Over Threshold
Fast Discriminator
SLICE Valerio Bocci 2019
Chips and evaluation Boards

## Slide 8
S13362-3050DG (3x3 mm2 , 3600 pixel)
S13362-1350DG (1,3x1,3 mm2 ,667 pixel)
Integration test with SiPMs
S13360-3050CS (3x3 mm2 , 3600 pixel)
S13360-1350CS (1,3x1,3 mm2 ,667 pixel)
MPPC Module C13366 as reference
Photo counting module for TE-cooled MPPC
High voltage power supply
Amplifier
Temperature control circuit
Low threshold comparator
Digital output for external scaler
MPPC 13360 serie with low dark count and crosstalk (3%)
Thermoelectric cooled MPPC 13362 series
with reduced dark count and crosstalk
Dark Box testbench
Laser Pulse module
SLICE Francesco Iacoangeli 2019

## Slide 9
INFN Roma1 Valerio Bocci (Resp Nazionale/Locale). 1 FTE
INFN Roma2 Davide Badoni (Resp Locale). 0.6 FTE
Anagrafica
SLICE Valerio Bocci 2019

## Slide 10
INFN Roma1
INFN Roma2
SLICE Valerio Bocci 2019

## Slide 11
SLICE Valerio Bocci 2019

## Slide 12
Materiali 2020
Evaluation Boards per SOC, Analog, TDC
Evaluation Boards e gateway LoRA
Referenza temporale con CSAC (Chip Scale Atomic Clock)
SiPMs ,Scatola test SiPMs , SiPM reference Electronics
Consumo vario
PCBs
SLICE Valerio Bocci 2019

## Slide 13
Valutazione diversi SoC : Microchip, STM, Infineon, Esprissif
Test TDC commerciali ai Picosecondi
Test Stabilità oscillatori per ottimizzazioni tag temporali e utilizzo del Chip Scale Atomic Clock
Test di Configurazioni analogiche
Test trasmissioni dati radio a bassa potenza (LoRA, Wifi,gold, Low power Bluetooth)
Test SiPM + Scintillatori
Attività 2020:
SLICE Valerio Bocci 2019