## Slide 1
Mu2e Calorimeter electronics
MUSE Network General Meeting
October 23th 2019
F. Spinella
INFN Pisa

## Slide 2: Talk overview
Calorimeter electronics scheme
Front End electronics
DIRAC spec, architecture and design
DIRAC qualification tests
Dirac cooling
Module 0
Slice test
Dirac V2

## Slide 3: Calorimeter design
SiPM + Holder + FEE
Calorimeter disks
CsI + SiPM + Holder + FEE
CsI crystals
UV-extended SiPMs
DIRAC + Mezzanine
CRATE
High granularity → 1348 undoped CsI crystals (3.4x3.4x20 cm3)
Crystals arranged in 2 disks (inner/outer radius 37.4 cm / 66 cm, separation between disks 75 cm)
1 crystal coupled to 2 UV-extended SiPMs (14x20 mm2 area) → 2696 electronic channels
SiPM packed in a parallel arrangement of 2 groups of 3 cells biased in series
DAQ crates located inside the cryostat to limit the number of pass-through connectors

## Slide 4: Why a digitizer?
Calorimeter
Disk0 Disk1
Typical 1.7 µs Mu2e event
Pile Up Example (Front End output)
Very intense particle flux expected in the calorimeter
We need high-sampling rate digitizers to resolve pile-up

## Slide 5: Which requirements? (1)
Digitization requirements = function (calorimeter requirements)
Particle-Id:
  σt < 500 ps @ 100 MeV
  σE/E <10% @ 100 MeV
We require the additional contribution due to the digitization procedure itself to be:
  σt < 200 ps @ 100 MeV
Analog input waveform and calorimeter digitization scheme:
  Sampling frequency and number of ADC readout bits impact time and energy resolution
  Thresholds impact the total data throughput and Energy resolution
Zero suppression: acquire only samples in blue and red regions
Red region needed for time and pedestal calculation
Blue region for energy

## Slide 6: Which requirements? (2)
Simulation results show that a digitizer with:
  Sampling frequency of 200 MHz
  ADC with 12 bits resolution
Matches the calorimeter requirements on time and energy resolution
Time resolution versus sampling frequency and ADC-bits
Energy resolution versus sampling frequency and ADC-bits
Energy is reconstructed from the total number of ADC counts
Energy resolution (FWHM/2.35) for Conversion Electrons (~105 MeV)
Time is reconstructed by fitting the leading edge
Time resolution for Conversion Electrons (~105 MeV)

## Slide 7: Which requirements? (3)
System located inside the cryostat → Harsh Environment:
  Magnetic field of 1 T and 10-4 Torr vacuum
  Total Ionizing Dose (TID):
    0.2 krad/yr (from simulation)
    12 Safety factor (requested from collaboration)
    5 years data taking
    TID 12 krad
  Neutron flux 5x1010 1 MeV (Si)/yr (from simulation)
Mechanical constraints → DAQ crates located inside the cryostat:
  Limited space → 20 ADC channels/board
  Limited access for maintenance → Highly Reliable Design mandatory

## Slide 8: Calorimeter electronics scheme
Crate x10
FEE x10 / board
Waveform Digitizers (DIRAC) x8
FPGA
DC/DC
ADC
CsI Crystal
CsI Crystal
Disks x2
(MPPC x2 / FEE)
ADC
ADC
ADC
ADC
ADC
ADC
ADC
ADC
ADC
DC/DC
DC/DC

## Slide 9: Front End Electronics
FE boards connected to SiPMs to provide:
  Amplification
  Local linear regulation of the bias voltage
  Monitoring of current and temperature
  Test pulse
Mezzanine boards:
  20 FE boards controlled by 1 Mezzanine Board (MB) → SiPM LV and HV distributed by an ARM controller
  Differential signals from 20 FE boards sent to MB and then to 1 DIRAC
DIRAC:
  sampling, processing and data transmission to the Mu2e DAQ

## Slide 10: DIRAC v1 architecture
ADC
FPGA
SoC
Optical
Receiver
ADC
ADC
ADC
ADC
1
2
3
9
10
FE
FE
FE
FE
FE
Mezzanine Board
1
2
3
19
20
DC/DC
&
LDO
Jitter Cleaner
Optical
Receiver
20

## Slide 11: DIRAC v1 design
After an intense campaign of tests:
ADC: ADS4229 (Texas Instruments®)
FPGA (SoC): SM2150T (Microsemi®)
DC-DC: LTM8033 (Linear Thecnologies®)
LDO: MIC69502 (Micrel®)
Jitter Cleaner: LMK04828 (Texas Instruments®)
Optical Transceiver: RJ-5G-SX (Cotsworks®)
PCB specs:
Material: FR408-HR
Layers: 16
Dimensions: 233x165 mm
Thickness: 2.127 mm
Differencial lines: 100 Ω
Single ended lines: 50 Ω

## Slide 12: DIRAC qualification tests
  Several test campaigns were performed:
    Total Ionizing Dose (TID) → requested 12 krad:
      ƳELBE @HZDR
        γ from Bremsstrahlung (0<E<14MeV)
        Extimated dose ≈ 20 krad/h @ 600µA
        Single components test
      Calliope @ENEA
        Co60 source
        Dose in function of distance: Max 2krad/h, requested 1krad/h
        Full board test
    Magnetic Field (B):
      LASA @INFN Milano (1T)
    Neutron irradiation test
      FNG @INFN
        Total neutron flux of 1.2 x10^12 n 1 MeV (Si) / cm^2
        Total neutron flux of 6x10^11 n 1 MeV (Si) / cm^2
        DCDC test

## Slide 13: ƳELBE facility
Photons is produced per Bremsstrahlung by the electron beam hitting a niobium foil in the accelerator hall
Nominal beam conditions: 17 MeV electrons, 600uA, 12.4 um niobium radiator foil
Simulated dose rate ≈ 18.6 krad/h
Active dosimetry used to confirm simulated dose rate

## Slide 14: Calliope facility
Gamma rays at 1.17 and 1.33 MeV from Co60.
3.7x10^15 Bq of activity.
Isotropic source, flux scales with r^2
DIRAC

## Slide 15: LASA facility
z
y
x
Uniform magnetic field up to 1.2 T
We tested different orientations of the DCDC with respect to the magnetic field
Same setup of the radiation tests

## Slide 16: FNG facility
Up to 10^11 14 MeV neutrons/s
almost isotropic source, flux scales with r^2
calibrated at 3% level using alpha particles
Frascati Neutron Generator (FNG) is a linear electrostatic accelerator in which up to 1 mA D+ ions are accelerated onto a Tritium target
r
D+T +n

## Slide 17: DIRAC: TID test results
Input waveform →4.5@10MHz, readout waveform:
LTM8033 and MIC69502 Vout(rad;t)
Conclusions:
41 h beam time
Nominal Dose Rate ≈ 1krad/h
TID ≈ 41krad
No evidence of broken components up to 35 krad
After 41 krad SM2 ARM does not restart after power cycle
DCDC converters voltage increase: ≈ 20% @ 41 krad, no recover if no beam CHANGE IN V2
LDO small increase, fast recover if no beam

## Slide 18: Tests in magnetic field results
Test conditions:
View X (parallel to B)
Vin 28V, Vout 2.5V
Variable load
Switching frequency
Efficiency quite low (still acceptable), higher if Vin lower
Test conditions:
View X (parallel to B)
Vin 28V, Vout 3.3V
Variable load
Constant frequency
Vout constant

## Slide 19: LTM 8033 Neutrons tests
  Test conditions:
  Neutrons over DCDC up to 1.2E12 1MeV-eq-Neutrons/cm2
  DCDC Vout (loaded with 1 ohm resistor):
    Measured before irradiation
    Measured after the test
  Negligible change …
6x10^11 n 1 MeV (Si) / cm^2

## Slide 20: DIRAC cooling (1)
General cooling requirements:
  Maximum temperatures must not be exceed during operation → the max electronic components temperature is set to half specified values → set max temp = 60 0C
  The cooling system must be robust and reliable
  Leak less cooling system
  All component must be compatible with magnetic field
  All parts must have a low outgassing rate for operating in vacuum
  Components must be radiation hard
A compact crate with 9 slots designed → house the boards and provides their cooling
  The cooling channels are milled on the lateral walls of the crate and sealed with a welded covers

## Slide 21: DIRAC cooling (2)
DIRAC estimated power 20W
8 DIRAC/crate + MB → 200 W/crate
Vacuum environment → the heat generated from the components is removed through:
  Thermal plate (Cu) pre-formed (radiator)
  Thermal Interface Material (TIM): thermal grease
  Bridge resistors (Beryllium Oxide)
  Card Lok Retainer (CALMARK® Series 265)
The electronic components modeled in three regions: top cover, junction and bottom cover
TIM allows the thermal contact between the top cover and the thermal plate
Card Lok
Bridge resistors
DIRAC + Cu Thermal plate
TIM

## Slide 22: Module-0
Large scale EMC prototype:
  51 CsI crystals
  102 Mu2e SiPMs
  102 FEE boards
  1 DIRAC board handle 20 channels
Mechanics and cooling system similar to the final ones (vacuum and low T)
Goals:
Validate the acquisition chain → Slice Test
Test integration and assembly procedures

## Slide 23: Slice test
Calorimeter electronics readout chain test using cosmic rays
Module-0 equipped with FE boards
SIPMs cooled @18°C (external chiller)
1 DIRAC v1 (16 channels) + 1 MB
Firmware → Preliminary version
External trigger → Cosmic ray coincidence

## Slide 24: Slice test firmware
Firmware:
Initializes ADCs and Jitter Cleaner
Synchronizes clock phases
Digitizes 20 channels @ 200 MHz (DDR)
Stores 250 samples for channel, with an initial buffer of 60 before the trigger (1.2 µs) without zero suppression
External trigger → 2 plastic scintillator paddles coupled PMTs placed over and below the Module-0 (outside the vessel)
Binary data output through UART interface @ 1 Mbs (event rate 5Hz enough for cosmics)
DAQ software:
Written in python and C++, based on ROOT libraries
Transforms the received binary data in a standard rootopla containing:
  The waveform
  Reconstructed quantities like pedestals, charge and time
Online monitor

## Slide 25: Slice test results
An example of the resulting waveform (Fig.A) and the distribution of the peak amplitude versus the integrated charge (Fig.B) is shown
Fig.B: Energy distribution deposited by cosmic rays (ADC counts)
Fig.A: Resulting waveform

## Slide 26: DIRAC v2
  Changes due to radiation resistance:
    FPGA: Microsemi PolarFire® MPF300 (FGC1152, 300K LE, 512 user IO, 20.6 Mbits RAM) was M2S150
    Optical tranceiver: CERN VTRX ( radhard up to 1Mrad) was Cotswork RJ-5G-SX
    DCDC converters: Texas Instruments® LMZM33606 was Linear Technology LTM®8033
  Changes due to changes in specifications:
    Clock chain encoded in the data
    Readout point-to-point (only one optical driver)
    CAN BUS
    DDR3 bigger
  DIRAC V2 status:
    TID, neutrons and B tests performed to validate all new components
    Single channel test to verify MPF300/ADS4229 compatibility
    Prototype should arrive in November

## Slide 27: DIRAC v2 design

## Slide 28: DIRAC v2 PCB
Design @ INFN Pisa: COMPLETED
Routing @ CERN: COMPLETED
PCBs under PRODUCTION
The boards assembled (2 prototypes) will be ready in November

## Slide 29: Conclusions
A waveform digitizer designed to operate in hostile environment has been presented
The DIRAC is designed to sample @200 MHz differential signals coming from the FEE of the DAQ of the electromagnetic calorimeter of the Mu2e experiment
The presence of vacuum (10-4 Torr), high magnetic fields (1T) and radiation (Non-Ionizing Energy Loss 5x1010 n/cm2 @ 1 MeVeq (Si)/y and Total Ionizing Dose 12 Krad) makes the environment particularly harsh and the design of the board very challenging
A slice test on Module 0 has been performed and it validated the acquisition chain
A new version V2 has been designed to strenghten the radiation hadrness