## Slide 1: Ricostruzione dell’energia di elettroni e fotoni in ECal
Due metodi di calibrazione :
Calibration Hits (CH): ATL-ARG-PUB-2007-012,2007; ATL-LARG-INT-2008-001,2008
Longitudinal Weights (LW): Expected performance of the ATLAS experiment-I Performance
N.B. Entrambi I metodi sono stati elaborati per energie >20 GeV
Le performance sono state applicate anche a 5 e 10 GeV
Entrambi I metodi sono disponibili in Athena. CH e’ il default.
Attivita’:
Nota congiunta sulle Performace (98% ok)
Studio dell’ effetto di un aumento di X0 davanti al criostato (tracker)
  In attesa dei files
  (??)Ottimizzazione performance 5-20 GeV. Energie inferiori (???)
  Richiede nuove simulazioni (Es: 15, 12.5, 7.5)
(??)Estensione dei CH al crack ( 1.425-1.55)
(??)Nuovi coefficienti ( dipendera’ dai risultati)

## Slide 2
electtroni
Fotoni non convertiti
Fotoni convertiti

## Slide 3
5 GeV
10 GeV

## Slide 4
η | 1/sin(Θ) | 1/cos(Θ)
0.7 | 1.25 | 1.65
1.3 | 1.97 | 1.16
2.0 | 3.76 | 1.04
η=0.7
η=1.3
Pixel Barrel 1-2-4%
SCT Barrel
1→3%
2→6%
4→12%
TRT Barrel - TRT EC
3 - 6 - 10%
SCT services
2.5 - 5 - 7.5 %
Pixel Barrel-EC
1-3-4%
Pixel EC service
0.6→1.2%
1.2→2.4%
2.4→4.8%
v
Proposed new geometry tag

## Slide 5
η | E | Position | ΔX0 | Additional tags
0.7 | 25; 50 GeV | Pixel Barrel | 1, 2, 4% | 3
 |  | SCT Barrel Cone of increasing material along z | 1-3, 2-6, 4-12 % | 3
 |  | TRT Barrel-TRT EC (constant z) | 3, 6, 10% | 3
1.3 | 25; 50 GeV | Pixel Barrel | 1, 2, 4% | 3
 |  | SCT services at R=55cm | 2.5, 5.0; 7.5% | 3
2.0 | 50; 100 GeV | Pixel Barrel-EC (constant z) | 1, 3, 4% | 3
 |  | Pixel EC services. Cone increasing material along z . | 0.6-1.2, 1.2-2.4, 2.4-4.8 | 3
 |  | SCT services at R=55cm | 1, 2.5, 5% | 3
The aim is to obtain a relation dE vs dX0 and decide what to do given dX0.and to study the effect of material on shapes (IsEM) and compute selection efficiencies.
New simulations with additional material in the cryostat (ΔX0=0.1 & 0.2%) are ongoing.
Summary of the proposed new simulations
Each tag with:
Δη= 0.1, Δφ =π/2
no vertex spread
2 Energies
80k events
Ideal geometry sample will be simulated for reference
Total runs: 2Ex(8x4) Tag=64 jobs