## Slide 1
Luca Serafini – INFN-Milan and University of Milan –
on behalf of MariX-C.D.R. Collaboration
The Challenge: sustainable CW coherent X-ray FEL & ICS
MariX: Conceptual Design Report of a Multi-disciplinary Advanced Research Infrastructure for the generation and application of X-rays
The Opportunity
MariX Seminar – Laboratori Naz. del Sud - INFN - Nov. 13th, 2019

## Slide 2
Linea ferroviaria Mi-Torino
Autostrada A7 Como-Varese
MIND : Milan INnovation District

## Slide 3
MAX-Lab
ESS Neutron
PETRA-III
X-FEL, FLASH
SOLEIL
LLB
DIAMOND
ISIS - CLF
ESRF
ILL, LETI
ALBA
SLS, SwissFEL
Elettra FERMI
MYRRHA
ANKA
SPARC DAFNE
SOLARIS
Infrastrutture di Ricerca Analitiche aperte
all’utenza internazionale che operano in Europa e sedi LERU
Da PSE Landscape Analysis ESFRI Roadmap 2016
LERU members
Courtesy Giorgio Rossi – former Chair ESFRI
Analytical Machines as User Facilities in Europe and League of European Research Universities:
a 400 km void around Univ. of Milan

## Slide 4
Scientific Case for a low jitter CW FEL was conceived by Giorgio Rossi, Giacomo Ghiringhelli, Ezio Puppin, Francesco Stellato/Silvia Morante, Bruno Paroli, Martino Bolognesi: Linear Spectroscopy in 0.2-8 keV at femtosecond time scale
Clinical Case for ICS monochromatic X-ray Source delineated by metropolitan Milan Hospitals: San Raffaele, Niguarda, Istituto Naz. dei Tumori, in collaboration with Ferrara and Naples Univ.
Design of a High Sustainability CW combined FEL & ICS X-ray Source for UniMi Scientific Campus spanning 0.2-180 keV (delivering 200kW to 2 MW sustainable beam power to client, cfr. Fermi 100 W, LCLS 2 kW )
Multi-disciplinary Advanced Research Infrastructure
for the generation and application of X-rays: MariX C.D.R.

## Slide 5
Compton X-ray photon beam: 1012 - 1013 hn/s (@ 100 MHz) in 5% Dn/n, 20-180 keV, tunable, polarized, st = 2 psec, 10 mm round source spot size, mrad divergence
FEL fully coherent diffraction limited X-ray photon beam: 108-10 hn/pulse @ 1 MHz
in 0.05% Dn/n, 0.2-8 keV, st < 50 fsec, 1016 hn/s
FEL Spectrum
2.5 GeV, lw=12 mm
Compton spectrum
FP @ 400 kW, 10 mA,
e- beam 1 MW
2.6.1012 photons/s
The Mission: coherent femto-second X-rays @ (0.2-8) keV, and ultra-high brilliance hard X-rays @ 20-180 keV
LCLS, 1 Angstrom
15 GeV, lw=2.5 cm

## Slide 6
Letter of Intent signed in July 2017 by University of Milan Rector (Prof. G. Vago) and INFN President (Prof. F. Ferroni)
The mandate to CDR collaboration team: Twin Source of FEL coherent X-rays in 0.2-8 keV range up to 1017 photons/s and ICS hard X-rays in 20-180 keV range up to 1013 photons/s
MariX CDR completed in March 2019 by 96 authors, belonging to INFN, University of Milan and 18 more Universities/Institutions (Politecnico di Milano - Sincrotrone Elettra), also thanks to INFN support for 3 fellowships and R&D funds for BriXSino
MariX Conceptual Design Report : Main Steps
MariX Seminar – Laboratori Naz. del Sud - INFN - Nov. 13th, 2019

## Slide 7
After 1 year of hard work...
CDR has been published and
available for download at
www.marix.eu
The Product: Conceptual Design Report

## Slide 9
Executive Summary
published on NIM-A

## Slide 11
Machine Team: A. Bacci, A. Bosotti, F. Broggi, S. Cialdi, C. Curatolo (INFN-PD), S. DiMitri (ST),
I. Drebot, A. Esposito (LNF), D. Giove, G. Galzerano (PoliMi/CNR), P. Michelato, L. Monaco,
R. Paparella, V. Petrillo, F. Prelz, E. Pinotti (PoliMi), M. Placidi (Univ. BO), E. Puppin (PoliMi),
A.R. Rossi, D. Sertore, V. Torri
Fellows: D. GiannottiINFN, L. FaillaceINFN, M. Rossetti ContiINFN, S. CapraUniMi
PhD/Master Students: F. Canella, M. Opromolla, C. Paulin, M. RuijterINFN,
S. SamsamICTP, E. Suerra

## Slide 12
Synchrotron Radiation sources
500 MHz repetition
nJ pulse energy; ≈50ps
105-6 photons x (5)x108pulses
Linear response regime:
Imaging and spectroscopy (perturbation theory)
Free Electron Laser sources
10Hz-27kHz repetition
mJ pulse energy; ≈50fs
1012-13 photons x
101-3-(6)pulses
Ultrafast Non-linear response regime
Imaging, flash+destroy
Laser-HHG UV-Soft X
MARIX+FEL (10 keV)
1 MHz repetition
100nJ pulse energy; ≈50fs
108-11 photons x 106pulses
Ultrafast Linear response
Courtesy Giorgio Rossi
DLSR: vertical emittance 2-8 picorad,
horizontal emittance 200-300 picorad
MariX: vertical/horizontal
emittance 45 picorad
⇒ Round vs. Flat beams

## Slide 13
High resolution low dose Radio-logical Imaging (<100 mm) with mono-chromatic X-rays up to 150 keV: mammography, 2 color angiography, radio-therapy with auger electrons on cis-platine, CAT 3D imaging of Cult.Herit./Archeological/Paleontological samples
Time resolved spectroscopy with fs coherent X-rays up to 8 keV @ 1 MHz rep rate: catalisys and chemistry in solvents, structure of nano-objects from coherent diffraction, bio-chemistry @ atomic and fs scale, pump&probe spectroscopy of strongly correlated materials, magnetism, superconductivity, topological materials, materials under strong spin-orbit interaction. Protein Crystallography with single-shot imaging (flash-and-destroy)
Scientific/Clinical Case: 2 Research Fields
enabled by MariX originality (Compton+FEL in CW)

## Slide 14
Courtesy Giorgio Rossi

## Slide 15
Comparison between X-FELs
Electron Beam Energy to radiate at ~ Angstrom
FEL | Radiation Wavelength (A) | Electron Beam Energy (GeV) | Linac Length (m)
LCLS | 0.5 | 14.3 | 1000.
PSI | 1.0 | 5.8 | 500.
EuXFEL | 0.15 | 17.5 | 1700.
LCLS II | 2.4 | 4.0 | 650.
MariX | 1.5 | 3.8 | ???? < 200
lR = lw (1+aw2)/ 2g2 , lw ÷ 1.2-3 cm

## Slide 16
Injector
Superconductiong Linac: 13 XFEL crio-modules Compr Undulator
100 MeV 1.6-1.8 GeV
Traditional
FEL layout
l=7 Ang
MariX
layout
Arc
compr
Injector
Linac1: 11 XFEL crio-modules
3.4-3.8 GeV 2.8-3.2 GeV 1.4- 1.6 GeV
l=1.5 Ang
Linac2
0
100m
200m
300m
400m
500m
dV/dz=17 MV/m
In quest of High Sustainability we had to conceive a new kind of machine:
the Two-Way Linac (TWL)
All Accelerators are one way – the beam propagates in one direction (ERL too)
MariX uses the CW Linac twice – forward and backward
Only Standing Wave RF Cavities can accelerate particles in both directions!

## Slide 17
Acceleration in opposite directions through a Linac
(two-way acceleration)
is possible if:
RF fields can accelerate in both directions
(Standing Waves can do it)
2) Focusing effective in both directions and weakly energy dependent
(RF focusing and/or solenoids)
3) No bunch crossing –> Twice the Linac Length < Bunch separation
4) RF fields must be on for a time longer than
bunch back-and-forth travel time (CW recommended)
5) Orbit position must not be dependent on magnetic rigidity
(no two-way through dipoles, except bifurcations)
MariX Seminar – Laboratori Naz. del Sud - INFN - Nov. 13th, 2019

## Slide 18
Modo risonante TM010-p ad Onda Stazionaria
k
phase velocity = c
n=1.3 GHz ; l=0.23 m
Standing RF Waves
9 celle = 4.5 l = 1.04 m

## Slide 19
E0 sin(kz)cos(wt-f0) =
(1/2) E0 sin(kz-wt+f0) + (1/2) E0 sin(kz+wt-f0)
standing wave
forward traveling wave,
synchronous to z = ct
backward traveling wave,
synchronous to z = -ct
ampiezza della componente
di onda viaggiante sincrona
rispetto all’elettrone

## Slide 20
RF Focusing effective only in Standing Wave RF Cavities
a lesson we learned long time ago
RF transport matrix

## Slide 21
RMS Envelope Equation for laminar beams: a path towards the Invariant
Envelope Theory for High Brightness el. beams (1997, L.S and J.Rosenzweig)
1.1

## Slide 22
RF (ponderomotive) Focusing
~ 1 Standing
~ 0 Traveling

## Slide 23
Two-pass 2-way region
The Super Conductive Main Linac
Ten Tesla like cryomodules: max grad 16 MV/m, 8 cavity per cryomodules
Chirp for AC-compression is given injecting @ + 6° from RF crest.
5 T solenoid
We rely only on second order focusing, symmetric back-and-forth: Rf focusing and solenoid foc.
Notes: Adiabatic focsing

## Slide 24: The beam dynamics
Linac 1 1st pass TL Arc compressor TL Linac 1 2nd pass Linac2
Envelopes
Emittances
All the beam dynamics simulations have been done with ELEGANT by
Alberto Bacci and Marcello Rossetti Conti
MariX Seminar – Laboratori Naz. del Sud - INFN - Nov. 13th, 2019

## Slide 25
AC – matching line
Not trivial 10 quads matching line with 2 SOLUTIONS
SOL. 1: «going bunch» match perfectly at the DIPOLE entrance
SOL. 2: «the coming back bunch» control bunch envelopes avoiding disastrous emit degradation by chromatic aberrations @ the 5T SOLENOID
going
coming

## Slide 26: Source layout 5: The arc compressor
One DBA
14 Double Bending Achromats Elettra-like
30°
R=41 m
R56=35 mm
dipole
quad
sextupole
Study of the arc compressor done by
M. Rossetti Conti
MariX Seminar – Laboratori Naz. del Sud - INFN - Nov. 13th, 2019

## Slide 27: Beam dynamics 1: before the arc, Q=50 pC
Longitudinal phase space
here
<E>=1.5 GeV
Ipeak=16 A
sz=360 mm
DE/<E>=7 10-4
enx,y=0.2 mm
sx=6 mm
Transverse phase space
Beam dynamic study made by A. Bacci
MariX Seminar - Univ. of Pisa - Dept.of Physics – Sept. 25th, 2019

## Slide 28
Beam dynamics 2: after the arc, Q=50 pC
here
Ipeak=1600 A
sz=20 mm
DE/<E>=3.6 10-4
sx=52mm
en,x=1 mm
sy=14.5 mm
en,y=0.2 mm
Longitudinal phase space
Transverse phase space
Centro Brasileiro de Pesquisas Fisicas, Rio de Janeiro, May 2nd, 2019

## Slide 29
In Publication on Phys. Rev. AB

## Slide 30
500 m
Next generation CW FELs like LCLS-II are km-long: not enough space in new UniMi Campus

## Slide 31
100
200
300
400
m

## Slide 32
Ezio Puppin – CDR convener for Civil Engineering and
Infrastructure Systems

## Slide 33
200 kW underground beam dump @ 3.8 GeV

## Slide 35
UliX1 l=2.8 cm aw<2.5
from 100 eV to 4KeV
General considerations on MariX FEL
UliX2 l=1.2 cm aw<0.8
from 2 KeV to 8 KeV
ULIX2
ULIX1
1) For emitting with continuity from 100 eV to 8 KeV:
Lmod=2.8 m
Ldrift=56 cm
Undulator
module
Quadrupole
BPM
Phase Shifter
Lquad=20 cm
Beam
pipe
Lmod=1.2 m
Ldrift=24 cm
Undulator
module
Quadrupole
BPM
Phase Shifter
Lquad=8 cm
Beam pipe
Nominal electron beam

## Slide 36
FEL simulations
With ELEGANT simulations we obtained
an electron beam with parameters very
similar to the nominal ones
0.5-0.35
Sirius like, ESRF-upgrade like

## Slide 38
SASE1: water window (2.77 nm) ULIX1, lw=2.8 cm
I=1.5 kA
emit=0.35 um
DE/E=3.6 10-4
aw=2.5
dt=10-3 fs
Spectrum
30 m
 | 16pC | 50 pC
e-En (GeV) | 3.2 | 3.2
Und l_w, L(cm,m) | 3 , 25 | 5, 25
Ph-en (keV) | 0.45 (2.8nm) | 0.45 (2.8nm)
Rep rate | 1 MHz | 1 MHz
Energy | 21 mJ | 156 mJ
Numb per shot | 3 1011 | 2.2 1012
Bandwidth (%) | 0.1 | 0.15
Pulse duration (fs) | 3 | 10
N/ s (s-1) | 3 1017 | 2.2 1018
S dens(N/shot/%bw) | 1.7 1012 | 1.5 1013
Radiation size mm | 0.15 | 0.07
Divergence mrad | 2.5 10-2 | 1.810-2
Tot. S. d. (N/s/%bw) | 1.7 1018 | 1.5 1019
Coherence | Single Spike | SASE
Power
30 m
Q=16 pC
Q=50 pC
Growth
Q=50 pC
SASE
Q=16 pC
Single Spike

## Slide 39
SASE2: linear spectroscopy (4.17 Å), ULIX2, 1.2 cm
Growth
Spectrum
60 m
Power
60 m
 | 50 pC | 8 pC
e-En (GeV) | 3 | 3
Und lw, L(cm,m) | 1.2 60 | 1.2 60
Ph-en (keV) | 3 | 3
Rep rate (MHz) | 1 | 1
Energy (mJ) | 42 | 2.5
Numb per shot | 8.75 1010 | 5.4 109
Bandwidth (%) | 0.45 | 0.8
Pulse duration (fs) | 6.6 | 1.2
N/ s (s-1) | 8.75 1016 | 5.4 1015
S dens(N/shot/%bw) | 1.94 1010 | 6.7 108
Tot. spect dens. | 1.94 1016 | 6.7 1014
Radiation size mm | 0.135 | 0.14
Divergence mrad | 4 10-2 | 4.3 10-2
Coherence | SASE | Single Spike
I=1.5 kA
emit=0.35 um
DE/E=3.6 10-4
aw=0.6
dt=10-3 fs
Q=50pC
Q=8pC
Q=8pC
Quasi Single spike
Q=50pC
SASE
50 pC
50 pC
16 pC
16 pC
Spectrum
60 m

## Slide 40
SASE3: single shot imaging (1.5 Å), ULIX2, 1.2 cm
Growth
Spectrum
60 m
Power
60 m
e-En (GeV) | 3.8
Und (cm,m) | 1.2 60
Ph-en (keV) | 9.25
Rep rate | 1 MHz
Energy | 3.3 uJ
Numb per shot | 2.5 109
Bandwidth (%) | 0.3
N/ s (s-1) | 2.5 10 15
Spectral dens(N/shot/1%bw) | 0.8 109
Radiation size mm | 0.1
Divergence mrad | 15 10-3
Tot. spect dens. (N/s/1%bw) | 8 10^14
Coherence | SASE
Q=50 pC, SASE
I=1.5 kA
emit=0.35 um
DE/E=3.6 10-4
aw=0.64
dt=10 fs
SASE spikes undersampled
in the graph (but not in the calculus)

## Slide 41
Seeded pulses for linear spectroscopy (3-6 Ang):
three options
Multi-Cascade Seeded by HHG in gas at 13 nm
Multi-Cascade seesed by a FEL Oscillator at 13 nm, MoSi mirrors
Regenerative Amplifier with diamond mirrors
1 MHz, Optical line by Alberto Tagliaferri
Possible only at low repetition rate
Possible at 0.5 MHz

## Slide 42
after ∼ 10 m
SASE/seed
competition
maximum
coherence
1st option: Cascade with HGG in gas at 13.6 nm; 5x3 at 9 Ang
2.7 nm
0.9 nm
0.9 nm
Final
spectrum
Final
temp. distr.
Seed needed:
15 nJ@13.6 nm
E(mJ)

## Slide 43
2nd option: Cascade with Oscillator at 13.6 nm
Undulator length: best value 4.4 m
The Mo/Si mirrors, quasi normal incidence
At the exit of the oscillator
Temp. Distr.
Spectrum
The oscillator

## Slide 44
z (m)
E (J)
2° option: Cascade 5x5 (5.4 Ang) with Oscillator at 13.6 nm
Temp distr
Spectrum
Temp distr
Spectrum

## Slide 45
3rd option: Regenerative amplifier at 4 Ang with Diamond mirrors
3 Diamond mirrors, 1 beam splitter,
quasi normal incidence @ 3 KeV
Round trip number
Photon number/shot
Fluctuations are due to the different electron microscopy
from shot to shot

## Slide 46
3° option: Regenerative amplifier at 4 Ang with Diamond mirrors
SASE
Spectrum
Temp. distr.
Reg. amplifier
l(nm)
s(mm)
Round trip number
Round trip number

## Slide 47
Comparison between X FELs, photons per second,
Electron Beam Energy to radiate at ~ Angstrom
FEL | Pulse per second
LCLS | 120 Hz
SACLA | 30-60 Hz
FERMI | 10-50 Hz
PAL | 30-60 Hz
PSI | 100 Hz
EuXFEL | 27 kHz
LCLS II | 1 MHz
MariX | 1MHz
lR = lu / 2g2
MariX Seminar – Laboratori Naz. del Sud - INFN - Nov. 13th, 2019

## Slide 48
BriXS: an example of high sustainability. High power 2 MW beam delivered to user with only 200 kW power consumption/dissipation with outstanding beam quality (larger than storage rings, same current)

## Slide 50
Inverse Compton Sources rivaling in Average Brightness with Synchrotron Light Sources at photon energies above 80-100 keV
I.C.S.
STAR
ELI-NP-GBS

## Slide 51
Fonte dei grafici: SwissFEL Science Case
BriXS Compton Source
Clinical/Scientific Case
enrolling
Ercolano’s
papyri

## Slide 53
MariX-RAD CSN5-INFN (FE, MI, NA)
Resp. Naz. Paolo Cardarelli - Univ. di Ferrara and INFN-FE

## Slide 55
6 M€, TDR within 2019
20 mA, 100 MHz, 10 MeV
> 60% energy recovery

## Slide 56
Bdw = 5% , Flux = 4.1012 ph/s

## Slide 57
MariX 2-Phases (M€)
BriXS 82.5
MariX-FEL 685.3
cmp. LCLS-II > 1 G€
XFEL > 1 G€

## Slide 58
Operational Costs (M€/year) Footprint (m2) (€/kwh)
MariX 45.5 (18 A/C) 35.000 0.234
LCLS 110
XFEL 120
SIRIUS 35 68.000 0.11
MariX Seminar – Laboratori Naz. del Sud - INFN - Nov. 13th, 2019

## Slide 59
FEL @ 7.4 keV - beam 50 pC @ 3.8 GeV, Nph = 8.5.1015 s-1 , efficiency = 5.3 .10-5
2) FEL @ 1.6 keV - beam 50 pC @ 1.8 GeV, Nph = 2.4.1017 s-1 , efficiency = 6.8 .10-4 3) ICS @ 180 keV - beam 200 pC @ 100 MeV, 95% recovery, Nph = 5 .1012 s-1, efficiency = 1.4.10-6
MariX efficiency in transforming electron beam power into radiation
MariX Seminar – Laboratori Naz. del Sud - INFN - Nov. 13th, 2019

## Slide 60
MariX/BriXS/BriXSino – the Italian way towards sustainable high power e- (e+) accelerators (MW and multi-MW class)
A new genetic line in accelerator zoology (2-way 2-pass)
Both are strategic motivations for INFN (BriXSino aims at filling an Italian void in this field)
Why Milano: unique overlap among expertise in accelerator & laser physics and technology, like High Brightness Beams/FEL/ICS Physics - SC/RF technology - High QE photocathodes - High Power Optical FP cavities, and a qualified User Community in Synchro-tron Light and FELs, with the endorsement in MariX-CDR and BriXS-EoI from IRCCS San Raffaele, Niguarda, Istituto Nazionale dei Tumori
conclusions

## Slide 61
MariX Seminar – Laboratori Naz. del Sud - INFN - Nov. 13th, 2019

## Slide 62
800 kW
150 kW

## Slide 66
MariX-RAD CSN5-INFN - Resp. Naz. Paolo Cardarelli - Univ. di Ferrara

## Slide 68
Comparison between X FELs, photons per second
Normal conducting
Super conducting
FEL | Pulse per second
LCLS | 120 Hz
SACLA | 30-60 Hz
FERMI | 10-50 Hz
PAL | 30-60 Hz
PSI | 100 Hz
EuXFEL | 27 kHz
LCLS II | 1 MHz
MariX | 1MHz
MariX Seminar – Elettra - Trieste - July 12th, 2019

## Slide 69
Comparison between X FELs, photons per second
FEL | Pulse per second
LCLS | 120 Hz
SACLA | 30-60 Hz
FERMI | 10-50 Hz
PAL | 30-60 Hz
PSI | 100 Hz
EuXFEL | 27 kHz
LCLS II | 1 MHz
MariX | 1MHz
MariX Seminar - Univ. of Padova - Dept.of Physics - July 17th, 2019

## Slide 70
Temporal pulse structure
MariX
FEL | Pulse per second
LCLS | 120 Hz
SACLA | 30-60 Hz
FERMI | 10-50 Hz
PAL | 30-60 Hz
PSI | 100 Hz
EuXFEL | 27 kHz
LCLS II | 1 MHz
MariX | 1MHz
Room
temperature
linacs
Superconducting
linacs
MariX Seminar – Elettra - Trieste - July 12th, 2019

## Slide 71
Citta’ Studi
Ateneo
Centro Brasileiro de Pesquisas Fisicas, Rio de Janeiro, May 2nd, 2019

## Slide 72
La scala sub-nanometrica (piccole molecole), la scala 1-10 nm (proteine e complessi), la scala 10-100 nm (organelle, virus), la scala micrometrica (cellule) sono suscettibili di imaging con la diffrazione coerente con l=0.2 nm)
Coherent diffraction imaging with 2 Angstrom (6 keV) X-rays is ideal for proteins (1-10 nm) and viruses (100 nm)
Fonte dei grafici: SwissFEL Science Case
MariX Free Electron Laser Scientific Case
Centro Brasileiro de Pesquisas Fisicas, Rio de Janeiro, May 2nd, 2019

## Slide 73
Coherent Diffraction Imaging di nanoscristalli e macromolecole
MariX Free Electron Laser Scientific Case
Centro Brasileiro de Pesquisas Fisicas, Rio de Janeiro, May 2nd, 2019

## Slide 74
Research areas and techniques: photon energy, number and time
Fine analysis of matter at/under the nanometer scale
relies on X-rays produced by
Synchrotrons
or
FELs.
Research areas (yellow)
and techniques (blue)
mapped onto
(photon energy-
photon number)
Processes
vs
(photon number
-time duration)
Courtesy of G. Rossi
Centro Brasileiro de Pesquisas Fisicas, Rio de Janeiro, May 2nd, 2019

## Slide 75
There is the need of a source:
Low cost, contained dimension
Reaching 8 keV
Low flux/shot: 107-109 ph per shot
Large rep rate: up to 1 MHz
Possibly large coherence degree.
Research areas (yellow)
and techniques (blue)
mapped onto
(photon energy-
photon number)
A source for bridging the gap between Synchrotrons and FELs
Region of the
linear spectroscopy
Courtesy of G. Rossi
Centro Brasileiro de Pesquisas Fisicas, Rio de Janeiro, May 2nd, 2019

## Slide 76
Centro Brasileiro de Pesquisas Fisicas, Rio de Janeiro, May 2nd, 2019
3.8 GeV electron energy to FEL-radiate at 8 keV (1.5 Angstrom) with 1.2 cm undulator period
Super-conducting RF Cavities at TESLA frequency (1.3 GHz) can safely operate up to 17 MV/m
accelerating gradient in CW (continuous wave) mode (to be compared with 25 MV/m of
XFEL in pulsed mode)
This means 3.8 / 0.017 = 224 m active RF Cavity length. Typical filling factor of SC Linacs is 0.5, implying toal effective legnth of about 450 m just for the main SC Linac. Let’s add spaces for
Injectors (30 m), transfer lines (20 m), magnetic compressors (50 m), matching line (20 m), undulator (80 m), photon beam lines (100 m), it rounds up to about 800 m. As a matter of fact LCLS-II is a km long.
How can we fit the whole FEL source into a
500 m long Campus available footprint ??
TOTAL LENGTH BUDGET FOR MariX

## Slide 77
General considerations
To achieve continuous tunability from 100 eV to 8 KeV
we need two undulators
2) All components must operate up to 1 MHz repetition rate
Max 50 pC bunch charge - beam dump constraints at 3.8 GeV
(50 microampere, about 200 kW average beam power)
Beam optics in two-way section at arc-entrance-exit must operate in
both directions - second order optics adopted (RF-solenoid, no quads!)
Lengths have been chosen to avoid collisions between bunches
  (1 MHz – 1 microsec – 300 m bunch separation)
Centro Brasileiro de Pesquisas Fisicas, Rio de Janeiro, May 2nd, 2019

## Slide 78
Some general considerations
For emitting up to 8 KeV we need such an electron beam:
-0.3
Centro Brasileiro de Pesquisas Fisicas, Rio de Janeiro, May 2nd, 2019

## Slide 79
Two-pass 2-way region
The two-way Linac II passage
5 T solenoid
Notes: Simulation done with Elegant

## Slide 80
Two-pass 2-way region
Last energy adjustment LINAC-2
Focusing triplet

## Slide 81: Beam dynamics 3: at the undulator, 30 pC
Longitudinal phase space
Transverse phase space
1500
Ipeak=1500 A
sz=20.6 mm
<E>=3.2 GeV
DE/<E>=3.6 10-4
en,x=0.33 mm
sx=34.5 mm
en,y=0.2 mm
sy=14.5 mm
here
Collimator
Centro Brasileiro de Pesquisas Fisicas, Rio de Janeiro, May 2nd, 2019

## Slide 82: FEL seeding: search for coherence and stability
The single spike regime leads to an
increase of coherence of the single
shot, but gives no improvement in
stability.
This last is achieved only with seeding
techinques.
Direct seeding impossible.
Among all the seeding techniques we have individuated only those with quite
short installations.
We selected three different methods for producing truly coherent X rays pulses:
a harmonic cascade seeded by the harmonics in gas of a IR laser;
a similar cascade but seeded by a FEL oscillator
a regenerative amplifier in the X-rays.
Centro Brasileiro de Pesquisas Fisicas, Rio de Janeiro, May 2nd, 2019

## Slide 83: Cascaded case: which wavelength, how much energy?
Seed level
10-20 nJ
with the power associated to the shot noise level:
lrad=4-10 Ang= lseed /n
n=15-30
lseed= 12 nm
Seed wavelength:
Seed energy:
Centro Brasileiro de Pesquisas Fisicas, Rio de Janeiro, May 2nd, 2019

## Slide 84: 1) Cascade with High Harmonic Generation
A consistent spectral power is needed to overcome the shot noise level at lowering wavelengths
Radiation at around 13nm (H59-63), starting from a Ti:Sa laser at 800nm, has been obtained with two methods at Riken, based on the interaction with a Ne gas
From M. Artioli et al., EuPRAXIA@SPARC Lab CDR (2017)
From M. E. Couprie et al., Seeding FEL with high harmonics in gas, Nanobeam 35° ICFA (2005)
Centro Brasileiro de Pesquisas Fisicas, Rio de Janeiro, May 2nd, 2019

## Slide 85: 1) Cascaded operation with HGG as seed, fresh bunch
λ = 12.7-13.6nm (H59-63)
E = 10-15nJ
σ ∼ 2µm (rms)
Pmax = 1-1.5MW
Duration ∼ 30fs (rms)
Seed
Examples of possible HGHG up-shift frequency conversions
A delay line between the modules shifts each stage output to a fresh portion of the e-beam (fresh bunch injection)
1° Mod
2° Mod
Radiator
Centro Brasileiro de Pesquisas Fisicas, Rio de Janeiro, May 2nd, 2019

## Slide 86
Cascade 5x3
after ∼ 10m
after ∼20m
after ∼ 10m
SASE/seed
competition !
Seed at λ = 13.6nm
Centro Brasileiro de Pesquisas Fisicas, Rio de Janeiro, May 2nd, 2019

## Slide 87
after ∼ 10m
SASE/seed
competition
maximum
coherence
Cascade 5x3 at 9 Ang
2.7 nm
0.9 nm
0.9 nm
Centro Brasileiro de Pesquisas Fisicas, Rio de Janeiro, May 2nd, 2019

## Slide 88: with the real MariX beam
Centro Brasileiro de Pesquisas Fisicas, Rio de Janeiro, May 2nd, 2019

## Slide 89
Cascade performances to be compared with its SASE counterpart
Quasi-Gaussian temporal profile, with increased shot-to-shot stability
Degree of temporal coherence increased by one order of magnitude
Natural synchronization with the laser
Number of photons per pulse reduced by one order of magnitude
Competition SASE -seeded
Lower Repetition Rate (100 kHz? Determined by the HGG device)
τc∼13fs=10 τc,SASE
Q=50pC
Q=8pC
Advantages:
Problems:
Centro Brasileiro de Pesquisas Fisicas, Rio de Janeiro, May 2nd, 2019

## Slide 90: 2) Cascade with a FEL oscillator as seed
λ = 13.6nm (H59)
E = 10-20nJ
σ ∼ 2µm (rms)
div = 55µrad
size = 100µm
From Q. Huang et al., High efficiency structured EUV multilayer mirror for spectral filtering of long wavelengths, Optical Society of America (2014)
Developments in EUV multi-layer coatings allow the use of Mo/Si-like mirrors at λ = 13.6 nm with reflectivities up to 75%, depending on the angle of incidence and polarization.
After twelve rounds
Centro Brasileiro de Pesquisas Fisicas, Rio de Janeiro, May 2nd, 2019

## Slide 91: Results of the 5x3 cascade compared …
Higher shot-to-shot stability
Lower SASE effect
Higher coherence
Courtesy of Michele Opromolla,
See Master Thesis published on www.marix.eu
Centro Brasileiro de Pesquisas Fisicas, Rio de Janeiro, May 2nd, 2019

## Slide 92
3) Regenerative amplifier
Chart: E (eV)
3 diamonds mirrors and 1 beam splitter
Beam intradistance 300 m
SASE growth
Incidence angle 3.092° from normal
Diamond
mirror
Diamond
mirror
Diamond
mirror
Beam splitter
SASE Spectrum
at 25 m
l=4,16 Ang
=3%
ESASE(25m)=6mJ
Eseed=180 nJ
Centro Brasileiro de Pesquisas Fisicas, Rio de Janeiro, May 2nd, 2019

## Slide 93: Cascades with harmonics in gas
Centro Brasileiro de Pesquisas Fisicas, Rio de Janeiro, May 2nd, 2019

## Slide 94
Cascades with Oscillator
Centro Brasileiro de Pesquisas Fisicas, Rio de Janeiro, May 2nd, 2019

## Slide 95
Comparison between X FELs, photons per shot
SASE
Self seeding
Single spike
seeded
Centro Brasileiro de Pesquisas Fisicas, Rio de Janeiro, May 2nd, 2019

## Slide 96
Comparison between X FELs, photons per shot
SASE
Self seeding
Single spike
seeded
MariX
MariX
seeded
Centro Brasileiro de Pesquisas Fisicas, Rio de Janeiro, May 2nd, 2019

## Slide 97
MariX with bubble arc compressor
1.5-1.8 GeV
3.-3.6 GeV
3.2-3.8 GeV
Dump& post FEL users
Intra-bunch time separation : 1 micro-second, 300 m
Beam time structure: 1 MHz repetition rate, single bunch CW

## Slide 98
BriXS & MariX FEL based on bubble arc compressor:
we use twice the same 1.5 GeV SC CW Linac
1.5-1.8 GeV
3.-3.6 GeV
3.2-3.8 GeV
Compton
Compton
BriXS: 20-180 keV mono-chromatic X-rays
up to 5.1012 photons/sec in 5% bdw
Elettra-like
A relativistic-doppler antenna
A boosted e-g
Collider

## Slide 99
BriXS: MariX Compton Source
1.5-1.8 GeV
3.-3.6 GeV
3.2-3.8 GeV
Compton
Compton
BriXS: 20-180 keV mono-chromatic X-rays
up to 5.1012 photons/sec in 5% bdw
Elettra-like
A boosted Collider
e-g as I.C.S.
(in regime Thomson)

## Slide 100
Centro Brasileiro de Pesquisas Fisicas, Rio de Janeiro, May 2nd, 2019

## Slide 101
Centro Brasileiro de Pesquisas Fisicas, Rio de Janeiro, May 2nd, 2019

## Slide 102
A quite complex machine from BD point of view
Centro Brasileiro de Pesquisas Fisicas, Rio de Janeiro, May 2nd, 2019

## Slide 103
The common beamline or BriXs linac layout
Centro Brasileiro de Pesquisas Fisicas, Rio de Janeiro, May 2nd, 2019

## Slide 104
One Wing of BriXS WP – NO remarkable open questions
Energy Recovery Linac re-injection: deceleration or recovery mode
Energy Recovery Linac exit: acceleration
15 m
30 m
22.5 m
10 m
Compton Interaction Point
Centro Brasileiro de Pesquisas Fisicas, Rio de Janeiro, May 2nd, 2019
Notes: Mettere le dimensioni della stanza

## Slide 105
We are planning to build a small scale BriXS demonstrator at INFN-Milano LASA: BriXsino
Centro Brasileiro de Pesquisas Fisicas, Rio de Janeiro, May 2nd, 2019

## Slide 106
Centro Brasileiro de Pesquisas Fisicas, Rio de Janeiro, May 2nd, 2019
Thanks for your Attention!
luca.serafini@mi.infn.it
Obrigado pela vossa Atenção

## Slide 107
Centro Brasileiro de Pesquisas Fisicas, Rio de Janeiro, May 2nd, 2019

## Slide 108
Centro Brasileiro de Pesquisas Fisicas, Rio de Janeiro, May 2nd, 2019

## Slide 110
σs = 3.96μm
(Cf ≈ 64.9)
The compressor performances (output emittance= 0.5 um)
Peak current evaluation
(Cf ≈ 64.9) x (Ip=25A) = 1650 A

## Slide 112
Apex MARIX & BriXS working points
TExit [KeV] | Qb [pC] | Tlaser [ps] (plateau) | σx_laser [mm] | εn,t /σx [µm/1mm] | σz [um] | εn [µm] | Δγ [KeV] | T [MeV]
BriXS |  |  |  |  | Inj. exit |  |  | 
830 | 200 | 48 | 420 | 0.5 | 1000 | 0.85 | 5 | 6.7
MARIX |  |  |  |  | Inj. exit |  |  | 
830 | 50 | 40 | 200 | 0.5 | 460 | 0.36 | 7.0 | 6.4
GUN Parameters
@ injector exit
APEX
lCLS-II
buncher 1.3 GHz
booster-I & compressor 1.3 GHz
booster-II 1.3 GHz
High harmonic
cavity 3.9 GHz
total length 4.0 m
L. Faillace map scheme

## Slide 113
Apex MARIX & BriXS injector dynamics
Very good performances for the both Working Points
@ 6.5 MeV

## Slide 114
Dogleg & ERL WP @ 200 pC. GIOTTO optimization
Fully restored in cylindrical symmetry
GIOTTO Genetic Algorithm optimization
Emittance oscillation tuning
Bunch Longitudinal compression
Full energy spread compensation
100MeV target energy

## Slide 115
Most of the story began with BriXS E.o.I. (2015)
downloadable at
https://www.researchgate.net/publication/308793009_BriXS_BRIght_and_compact_X-ray_Source_Expression_of_Interest_1
BriXS-EoI-2.3.pdf (Oct. 2016)

## Slide 116
Firmatari

## Slide 117
Courtesy A. Variola
STAR
Le Sorgenti Thomson/Compton sono gli “acceleratori di fotoni” piu’ efficaci
“4g2 boost effect”
HigS
ELI-NP
CALA

## Slide 118
1-25 GeV
electrons
100-0.5 Å
photons
cm und. period lu
FEL’s and Thomson/Compton Sources common mechanism: collision between a relativistic electron and a (pseudo)electromagnetic wave
20-150 MeV electrons
0.8 m laser l
20-500 keV
photons
3 km
20 m
The Classical E.M. view (Maxwell eq.): Thomson Sources as synchrotron radiation sources with electro-magnetic undulator

## Slide 122
macchina compatta 10x10 m2
In operazione dai primi del 2015

## Slide 123
Flusso misurato
1.5.1010 fotoni/s con 10 mA
measured
Righe spettrali
mono-cromatiche
e accordabili

## Slide 124
Imaging a Contrasto di Fase (risoluzione spaziale < 80 μm)

## Slide 126
Sorgente Convenzionale per Mammografia: tubo RX.
Risoluzione spaziale richiesta ~100 mm Alto Flusso ~107 g/(mm2s) equivalente a ~5.1011 g/s su un’area di 20x20 cm2.
65 cm
ESEMPIO NOTEVOLE DI IMAGING PER SCREENING DI MASSA: MAMMOGRAFIA
Parte di bassa energia dello spettro di fotoni X che viene assorbita dai tessuti ed aumenta il rischio secondario di indurre tumori, abbassando il rapporto rischio-beneficio dello screening di massa sulla popolazione femminile > 40 anni
Assente nello
spettro X
delle Sorgenti
Thomson!

## Slide 127
3 cm thick in vitro human breast tissue
a) SR digital image
Energy 17 keV
Scan step 100 mm
MGD 1 mGy
b) SR digital image
Energy 20 keV
Scan step 100 mm
MGD 0.33 mGy
Conventional
X-ray tube 26 kVp
MGD 1 mGy
La Mammografia con Raggi X Mono-cromatici a 20 keV e’ gia’ stata dimostrata
essere di gran lunga superiore nel rapporto Segnale-Rumore rispetto ai tubi
Mammografici convenzionali, con una dose di radiazione ai tessuti di gran lunga inferiore (esperimenti alle facilities di Luce di Sincrotrone)

## Slide 128
Portare i pazienti in Ospedale non al Sincrotrone…
realizzare un Sincrotrone-equivalente (Sorgente Thomson)
che possa funzionare all’interno dell’Ospedale
Basso rate di pazienti diagnosticati al Sincrotrone, in pratica solo i dubbi falsi positivi
vengono indirizzati al Sincrotrone a valle della diagnostica con strumenti convenzionali

## Slide 130
K Edge imaging per Beni Culturali, XRF, realizzato a ESRF
Courtesy A. Variola

## Slide 131
Courtesy R. Agostino

## Slide 132
Courtesy R. Agostino

## Slide 133
Courtesy R. Agostino

## Slide 135: Inverse kinematics of a relativistic (massive) particle Ep = gMpc2 (g >>1) colliding quasi head-on (q ≈p ) with a photon EL=hnL
Recall some Basics
lab ref. frame
Assumptions:
‘ = particle rest ref. frame
c.m. ref.
frame
X: particle recoil

## Slide 136: Example: Inverse Compton scattering
X=0 electron: relativ. mirror
(Thomson regime)
X>>1 symmetric collider
Eph = energy of scattered photons as function of scattering angle q*
in c.m. ref. frame
0 momentum
exchange
full momentum
exchange
Compton edge

## Slide 137
FELs (pure g2)
Thomson
X-rays
Nuclear
Photonics
X/g
[MeV]
Te [MeV]
1 GeV
1 TeV
Polarized
Positrons
X
g-g Colliders
Ecm [MeV]
0.511
1.533
X

## Slide 138: Example: Inverse Compton scattering
cos
example 250 MeV electrons against hnL=1.2 eV photons
High sensitivity of Lorentz Boost to scattering angle q is the origin
of secondary beam phase space dilution (emittance, en. spread)

## Slide 139
From particle-particle to
beam-beam collisions
courtesy of D. Moncton
negligible diffraction
0 crossing angle
electrons
laser
Laser pulse length matched to focus size (Rayleigh length).
Laser pulse too long for small focus size.

## Slide 140
Single electron-photon spectra
What happens when we scatter beams of electron against beams of photons?

## Slide 141
See C. Curatolo, PhD Thesis, Univ. of Milan, 2016 (and references therein)
Electron beam emittance and energy spread spread out the c.m. propagation so to generate a “beam” of c.m. ref. frames

## Slide 142
Electron-photon Collider Spectra

## Slide 143
Courtesy C. Barty - LLNL

## Slide 145: Bandwidth due to collection angle, laser and electron beam phase space distribution
;
;
etc
angular spread due to scattering angle and angular spread due to single electron incoming angle (emittance) are treated symmetrically
cos

## Slide 146
scales like en in low recoil regime,
while it scales like en/X1/2 in high recoil regime
4th order variational expansion over rms phase space
distribution of two colliding beams
(assumed gaussian, spectral distribution of scattered photon treated exactly)
broad-band lasers/photon beams
are acceptable in high recoil regime

## Slide 152
Collisore elettrone-fotone altamente
asimmetrico e compatto* (cfr. LHC)
Fascio secondario di fotoni prodotto grazie al grande boost di Lorentz del sistema di riferimento del centro di massa elettrone-fotone (cfr. LHC, simmetrico, zero boost di Lorentz)
*10 m, 10 M$
Elettroni con energia nel range 10-100 MeV collidono contro fotoni laser con energia nel range 1-3 eV
Nuova Generazione

## Slide 156
Per una review omni-comprensiva delle applicazioni delle sorgenti Thomson/Compton si veda la present. di A. Variola (INFN-LNF) al PAHBB-2016 Workshop (https://conferences.pa.ucla.edu/hbb/index.html)
Radio-terapia con raggi X monocromatici del glioblastoma cerebrale, basato su attivazione Auger di cisplatino nelle cellule tumorali. Gli elettroni Auger attivati mediante K-edge dai fotoni X depositano radiazione solo all’interno del tumore.

## Slide 157
FLASH
12.4
1.24
0.124
l (nm)
Thomson/Compton Sources
Brilliance of Lasers and X-ray sources
BELLA
ELI
Outstanding X/g photon beams
for Exotic Colliders

## Slide 158
Rivaling with Synchr. Light Sources for energies above 50 keV

## Slide 159
Dump
3 MeV
+ 6~8 MeV
BriXsinO
3 MeV

## Slide 160
Dump
3 MeV
+ 6~8 MeV
BriXsinO
3 MeV

## Slide 161
Dump
3 MeV
+ 6~8 MeV
BriXsinO
3 MeV
L=1m;
V=5 MV;
f=1.3 GHz;

## Slide 162
Gun
Dumping
Variant with Pac-Man 1800 bending
RF
Optical table
Such bending magnets are using in the medical linacs
2 MeV
~8 MeV

## Slide 163
THz CW FEL for biological imaging
Kurchatov interest in collaboration

## Slide 166
Acceleration in opposite directions through a Linac
(two-way acceleration)
is possible if:
RF fields can accelerate in both directions
(Standing Waves can do it)
2 ) Focusing must be effective in both directions and weakly energy dependent (RF focusing and/or solenoids)
3) No bunch crossing –> Twice the Linac Length < Bunch separation
4) RF fields must be on > back-and-forth bunch travel time
(CW recommended)