## Slide 1
vendittozzi@aerospace.unb.br
07 November 2019
INFN Frascati (Rm) - Italy
Cristian Vendittozzi
Mimic Nature, seeking for intelligent engineering system

## Slide 2
Biomimetic
2
07/11/2019 INFN, Frascati (Rm)
Introduction
Basic definitions
My interpretation and focus
Case studies
Aerospace applications
STRUCTURE

## Slide 3
07/11/2019 INFN, Frascati (Rm)
I am associate professor at the Aerospace Engineering course at the University of Brasilia (Brazil).
I holds a Master degree in Aerospace Engineering, a Ph.D. in Materials and Raw Materials Engineering, both from Sapienza, Rome University (Italy).
Currently he I am dealing with the development of highly distributed optical fiber sensor systems for the monitoring of critical parameters in aerospace structures, the Intelligent monitoring of environmental disasters and the study and development of foldable systems that can be used for space applications.
For 2019, I am invited Scholar at CIRA (The Italian Aerospace Research Centre) to deepen concepts related to morphing and adaptive structures.
I have strong interest in biomimetic, trying to couple what I learned previously with the idea of developing a meta-material that can be printed (3D) and that can be able to change shape if properly stimulated (+ 1D).  A 4D material that is able to feel the changes taking place in the operating environment and to react by adapting itself (by morphing) to the new conditions.
Few words about me …
https://fga.unb.br/cristian
http://lattes.cnpq.br/0016059435687196
https://orcid.org/0000-0003-0793-4052

## Slide 4
07/11/2019 INFN, Frascati (Rm)
FGA/UnB Gama Faculty campus
FUP/UnB Campus in Planaltina (DF)
FCE/UnB Campus in Ceilândia (DF)
UnB main campus
«Darcy Ribeiro», Brasìlia (DF)
… and about my faculty.
http://fga.unb.br/
~35 km

## Slide 5
British English Dictionary definition:
(of a human-made product) imitating nature or a natural process
Collins English Dictionary.
Copyright © HarperCollins Publishers
07/11/2019 INFN, Frascati (Rm)
What is Biomimetic?
And, what does biomimicry mean?

## Slide 6
What is Biomimetic?
And, what does biomimicry mean?
07/11/2019 INFN, Frascati (Rm)
Biomimetic refers to an interdisciplinary field in which principles from engineering, physics, chemistry and biology are applied to the synthesis of materials, synthetic systems or machines ant to the definition of human processes that have functions that mimic biological systems and processes.

## Slide 7
… it is, science inspired by nature!
Easier? From an engineer’s point of view… it is a kind of reverse engineering about nature’s models and practices.
07/11/2019 INFN, Frascati (Rm)
What is Biomimetic?
And, what does biomimicry mean?

## Slide 8
Giant Water Lily Lotus
Background texture of a Giant Amazon water Lily leaf (Victoria Amazonia)
Inspiration for topological optimization

## Slide 9
Giant Water Lily Lotus
Crystal Palace, giant glass-and-iron exhibition hall designed by Sir Joseph Paxton, built in Hyde Park, London, that housed the Great Exhibition of 1851, it survived until 1936.
Crystal Palace
07/11/2019 INFN, Frascati (Rm)

## Slide 10
07/11/2019 INFN, Frascati (Rm)
HOOKS
LOOPS
VELCRO
Hook-and-loop fastener
BURDOCK/ARCTIUM LAPPA
In 1941, the Swiss engineer George de Mestral coming back from a hunting trip noticed a lot of burdock seeds and flowers clung to his clothes and his dog’s fur.
He tried to reproduce the geometry to create a Hook-and-loop fastener, made of two strip of fabric, mimicking the burdock behavior.
In 1955 he patented his invention naming it as Velcro.
(combining velour – velvet - and crochet - hook)

## Slide 11
1989 The San'yō Shinkansen
high-speed bullet train (Series 100)
170 mi/h (273,59 km/h)
07/11/2019 INFN, Frascati (Rm)
Extremely noisy!
Shinkansen Series 500 “birdwatching” inspired design

## Slide 12
Shinkansen 100 pantograph
Shinkansen 500 pantograph
The pantograph, that connects the train to its power source, vibrated and made a loud noise.
The owl has a concave face capable of absorbing sound. Its body has ample down to absorb fluttering sounds.
Tiny serrations on its primary feathers minimize the vortex generated by movement.
The pantograph was reshaped like an owl's wing
including small serrations,
which resulted in no vibrations and a quieter impact for residents near the tracks.
07/11/2019 INFN, Frascati (Rm)

## Slide 13
Shinkansen 100 pantograph
Shinkansen 500 pantograph
The pantograph, that connects the train to its power source, vibrated and made a loud noise.
The body of the Adelie Penguin is shaped like a spindle which allows it to move effortlessly through water to catch fish.
The pantograph's supporting shaft was reshaped like a penguin's body to lower its wind resistance.
The supporting frame for the pantograph had a high degree of wind resistance resulting in aerodynamic noise.
07/11/2019 INFN, Frascati (Rm)

## Slide 14
07/11/2019 INFN, Frascati (Rm)
The shape of the Kingfisher's head and beak allow it to glide through the air and precisely dive into water to snag fish.
It is considered the most efficient animal on earth to transition from low pressure (air) to high pressure (water).
“Half of the entire Sanyo Shinkansen Line (from Osaka to Hakata) is made up of tunnel sections.
When a train rushes into a narrow tunnel at high speed, this generates atmospheric pressure waves that gradually grow into waves like tidal waves. These reach the tunnel exit at the speed of sound, generating low-frequency waves that produce a large boom and aerodynamic vibration so intense that residents 400 meters away have registered complaints.”
Tomohiro Kobayashi
(Project Coordination Director )
 No more bang!
When the train would enter a tunnel, a loud bang would occur due to the fixed air volume of the tunnel and the sudden increase in pressure from the exiting train.
The nose of the Shinkansen train was reshaped in the form of the Kingfisher’s beak to eliminate the sudden pressure increase.
GOAL!
This shape has enabled the 500-series to reduce air pressure by 30%, electricity use by 15%, and allowing a more comfortable ride, even though speeds have increased by 10% over the former series.

## Slide 15
And … what about aerospace applications?
From the myth of Icarus to the wing of the Leonardo Da Vinci ornithopter, the yearning for flying was always - obviously - inspired by that of birds.
07/11/2019 INFN, Frascati (Rm)

## Slide 16
07/11/2019 INFN, Frascati (Rm)
Flapping wing vs. fixed wing
Slats
Three slotted inner flaps
Three slotted outer flaps
Spoilers
Spoilers-Air brakes
Winglet
Low Speed Aileron
Hight Speed Aileron
Flap track fairing
Krüger flaps
The primary purpose of aircraft wings is to produce the required lift to maintain the aircraft in the air. As lift is related to the wet surface of the wing

## Slide 17
07/11/2019 INFN, Frascati (Rm)
07/11/2019 INFN, Frascati (Rm)
17
Landing
sequence
APPROACH
ROUNDOUT
FLARE
TOUCH DOWN
The fixed wing configuration is optimized for only one flight phase

## Slide 18
07/11/2019 INFN, Frascati (Rm)
Source: Concilio A., et Al., “An Adaptive Trailing Edge”, pp.517-545, in Morphing Wing Technologies, edited by Concilio A., Dimino I., Lecce L., Pecora R., 2017, ISBN: 978-0-08-100964-2, 978 pages, Publisher: Butterworth-Heinemann (UK), DOI: 10.1016/B978-0-08-100964-2.00017-4.
a.concilio@cira.it
Adaptive structures
Adaptive - Finger like - trailing edge
Seeking for morphing solutions for aerodynamic surfaces for:
the extension of the flight envelope and
the improvement of the performance at different regimes.

## Slide 19
Nature has always been used as a source
of inspiration in aerospaceengineering applications.
Bamboo groove.
Tall and thin stems
Aircraft fuselage frames and formers
designed for reducing buckling risk
07/11/2019 INFN, Frascati (Rm)
Notes: A former is a transverse structural component of the shell fuselage of an aircraft. Its function is to maintain the shape of the fuselage section, decrease the length of the stringers reducing buckling and to transfer, introduce and redistribute the internal and external loads. This is how aircraft engineers design aircraft fuselages, copying, more or less unconsciously, what nature has been doing for a few million years

## Slide 20
HONEYCOMB
Hexagons are the most efficient way to fill a space with the least amount of material.
Honeycomb structural materials are commonly made by layering a honeycomb material between two thin layers that provide strength in tension.
Honeycomb materials are widely used where flat or slightly curved surfaces are needed and their high specific strength is valuable.

## Slide 21
LOTUS EFFECT
From self-cleaning surfaces ...
Lotus leaves exhibit extreme water-repellent properties.
Their surfaces are Superhydrophobic and self-cleaning due to hierarchical roughness and the presence of wax tubules on the leaf surface.
07/11/2019 INFN, Frascati (Rm)
This phenomenon is of interest in various applications, including self-cleaning windows, exterior paints for buildings, navigation ships, textiles, solar panels, and applications requiring antifouling and a reduction in fluid flow.

## Slide 22
07/11/2019 INFN, Frascati (Rm)
F. Piscitelli, et Al., On a simplified method to produce hydrophobic coatings for aeronautical applications, Applied Surface Science 472, 71–81, 2019.
DOI: 10.1016/j.apsusc.2018.04.062
f.piscitelli@cira.it
Ice accretion on aircraft leads to difficulties in aircraft flight control due to weight increase and change in weight distribution. Conventionally these difficulties are overcome using anti-icing or de-icing products, such as freezing depressants and heating devices.
A more cost effective way to solve these problems would be to use ice repellent surfaces (ice-phobic).
LOTUS EFFECT
… to anti icing systems

## Slide 23
From Ladybugs to Origami-Like folding devices
Images are courtesy of Prof. Kazuya Saito (Tokyo University),
Source: Investigation of hindwing folding in ladybird beetles by artiﬁcial elytron transplantation and microcomputed tomography.
DOI: 10.1073/pnas.1620612114
At take off, ladybug deploys its wings from beneath the elytra, in 1/10 s.
When it lands, it folds it back in 2/10 s.
LADYBUG & ORIGAMI PATTERN
07/11/2019 INFN, Frascati (Rm)

## Slide 24
60 ft (18.3 m)
15 ft (4.6 m)
10.6 103 ft3 (300 m3)
STOWING VOLUME LIMITATIONS
07/11/2019 INFN, Frascati (Rm)
Since the beginning of the Space era, one of the major issues faced by space systems engineers has been mass and volume reduction due to launch vehicle storage limitations and for launch cost reduction.

## Slide 25
SPACE DEBRIS MITIGATION
Ensuring orbit decay within 25 years.
(IADC Space Debris Mitigation Guidelines)
LEO (Low Earth Orbits)
is the most densely populated orbital region
is the region that is seeing the fastest growth.

## Slide 26
SPACE DEBRIS MITIGATION
07/11/2019 INFN, Frascati (Rm)
Preliminary design of a Modular Deployable Deorbiting System (MDDS) based on an Origami Deployable Drag Sail (ODDS) to be used as a lightweight passive system in a 3U CubeSat platform.
The purpose is to obtain the lowest possible packaging volume given the sail surface extension that allows the orbital decay.
Reducing the volume of the stowed sail, designing a deployment system with a highest
Packing-Ratio (PR)
η=S/V
of deployed surface (S) to stowed volume (V)
Speeding up the sail deployment, minimizing the risk of failure during this phase

## Slide 27
07/11/2019 INFN, Frascati (Rm)
Drag augmentation is an effective passive method for de-orbiting n LEO, exploiting the thin atmosphere that still exists below 1000 km.
Drag augmentation
Satellites in this orbit region will decay naturally regardless of mitigation strategy.
Drag augmentation is achieved by deploying a larger structure at the end of the satellite operations - to result in a larger drag surface area.
Resulting in a shorter Decay Time (DT)

## Slide 28
ORIGAMI PATTERN
Miura-Ori
Miura-ori is an example of an origami mosaic pattern
each parallelogram remains flat on top of each other during folding and unfolding.
its final compacted shape is limited only by the thickness of the sheet material.
It also found an application as a meta-material with unusual properties, such as a negative Poisson's ratio.
07/11/2019 INFN, Frascati (Rm)

## Slide 29
ORIGAMI PATTERN
Miura-Ori
Benefits:
It shows a high PR (η=S/V)
It has negative Poisson's ratio
Insert defects may increase material stiffness
Reinforced by a defect
Folded (partially)
Deployed
07/11/2019 INFN, Frascati (Rm)

## Slide 30
ORIGAMI PATTERN
& SAIL SHAPE
Miura-ori
pattern
Rabbit-ears pattern
07/11/2019 INFN, Frascati (Rm)

## Slide 31
ORIGAMI PATTERN
& SAIL SHAPE
With this particular fold configuration, there is only
one way to open/close it:
pulling one (1) corner it opens the whole sail with minimal effort.
The unfolding actuator is greatly simpliﬁed because
only one (1) input is required to deploy 4 sails.
07/11/2019 INFN, Frascati (Rm)

## Slide 32
07/11/2019 INFN, Frascati (Rm)
DEPLOYING ACTUATOR

## Slide 33
DEPLOYING ACTUATOR
The opening mechanism uses a thermally activated Shape Memory Alloy (SMA) actuator consisting of 4 C-shape clamps (C-Clamp), which keep the 2 Retention Plates (RP) locked, exploiting the shape-changing behavior.
 Originally the clamp shape is a rectangular thin plate that is deformed, by two folds, in the shape of a C.
 The plates remain coupled until the C-shaped clamps recover the original shape.
 When a voltage is applied to the C-Clamp, local ohmic heating triggers a martensite-austenite phase change, recovering the annealed shape, opening the C-Clamp, freeing the RPs, thus deploying the sails.
07/11/2019 INFN, Frascati (Rm)

## Slide 34
07/11/2019 INFN, Frascati (Rm)
D
C
B
A
PRELIMINARY DESIGN OF AN ORIGAMI FOLDABLE DEORBITING SAIL FOR A 3U CUBESAT
C. Vendittozzi A, S. Colafranceschi B, S. Bianco C,
G. Saviano D, L. S. L. Barros A, A. V. R. Dias A

## Slide 35
Mimic Nature, seeking for intelligent engineering system
Smart or Intelligent?
An intelligent structure is an adaptive structure, it is defined as a structure that is able to sense external stimuli such as pressure, velocity, density, or temperature change, etc. It can process the information and respond in a controlled manner in real time
Source:
https://www.nasa.gov/centers/langley/news/factsheets/21stcentury.html

## Slide 36
Biological
System
Engineering
System
The concept of biomimetics is applied in the sense of copying the “skeleton” of a
biological nervous system
and
Reproducing it as an array of quasi distributed sensory points (sensors)
Allowing the engineering system to perceive variations in the operating environment and the consequent repercussions on the system.
07/11/2019 INFN, Frascati (Rm)
Mimic Nature, seeking for intelligent engineering system

## Slide 37
Smart Structures being able of
sensing their state in addition to
their surrounding environment
Nerve endings
Spinal cord
Brain
Communication Bus
Processing Unit
Sensors
07/11/2019 INFN, Frascati (Rm)
Mimic Nature, seeking for intelligent engineering system

## Slide 38
07/11/2019 INFN, Frascati (Rm)
Broadband Light Source
(Tunable laser)
Optical Circulator
Data Acquisition
Optical Interrogator
OSA
Optical Spectrum Analyser
Incident Spectrum
Reflected Spectrum
I
l
I
l
lB3
lB2
lB1
lB1
lB3
Mono-mode
Optical Fiber
lB2
PC
Ethernet Cable
Transmitted Spectrum
lB3
I
l
lB2
lB1
FBGs Array
lb=2Ln
FBG Integrated System’s Architecture
… but embedding into the materials is tough!

## Slide 39
Embedded optical fiber in a CFR laminate
Up to 76% of pigtail breaks, exiting the autoclave,
during laminate manufacturing.
Main Issue - Exiting from CFRP parts
New magnetic connector for embedding of optical sensors in composite materials
CFRP Laminate
Pig tail
Entry point
Pig tail
Exit point
Embedded Fiber
FBG
Pigtail
07/11/2019 INFN, Frascati (Rm)

## Slide 40
Exiting from CFRP parts
New magnetic connector for embedding of optical sensors in composite materials
Prof. Ferdinando Felli
Dr. Andrea Brotzu
DICMA
Department of Chemical, Materials and Environment Engineering
Source: 2011 Fifth International Conference on Sensing Technology (ICST):
New magnetic connector for embedding of optical sensors in composite materials
07/11/2019 INFN, Frascati (Rm)

## Slide 41
Extreme Temperatures Applications
Metal Electrodeposition for coating, working at High Temperature (HT)
07/11/2019 INFN, Frascati (Rm)
Cu-Ni Coating
Prof. Ferdinando Felli
ferdinando.felli@uniroma1.it
Dr. Michele A. Caponero
michele.caponero@ênea.it
Prof. Carla Lupi
carla.lupi@uniroma1.it

## Slide 42
Dendrites on Cu ED-Coating
Micro-pitting on Ni ED-Coating
Extreme Temperatures Applications
Metal Electrodeposition for coating, working at High Temperature (HT)
Surface (aesthetic) issues
07/11/2019 INFN, Frascati (Rm)

## Slide 43
Cu-Ni Coating
HT Issues due to
Metal interdiffusion
phenomenum
Extreme Temperatures Applications
Metal Electrodeposition for coating, working at High Temperature (HT)
Internal (severe) issues
Kirkendall Voids
generated over 700 °C
07/11/2019 INFN, Frascati (Rm)

## Slide 44
Cu-Ni Coating on
commercial FBG
reaching 1000 °C
07/11/2019 INFN, Frascati (Rm)
Extreme Temperatures Applications
Metal Electrodeposition for coating, working at High Temperature (HT)

## Slide 45
07/11/2019 INFN, Frascati (Rm)
How to move from a smart structure to an intelligent one?
Adaptive Structures
SHAPE MEMORY MATERIALS
Compliant Mechanisms
4D PRINTING
Embedded sensors array (FBG)
Embedded Actuators
Biomimetics' suggestions

## Slide 46
The purpose is to integrate a sensors network into the engineering system, enabling the system to perceive the variations taking place in its operating environment.
This sensory array must be able to monitor:
in real time
multiple physical quantities (T, P, RH%, etc.) and then send the information collected to the CPU.
simultaneously
in continuous
during the entire lifetime of the system
This CPU will evaluate the collected information and send appropriate instructions to the network of actuators, also embedded in the materials, or consisting of the materials themselves (such as compliant mechanisms and/or shape memory materials), which will perform a reaction.
Best is yet to come
07/11/2019 INFN, Frascati (Rm)
FINAL REMARKS

## Slide 47
Stay naturally inspired…
… stay foolish!
Keep in touch
vendittozzi@aerospace.unb.br