## Slide 1
Optimization of thermal noise
for ET-LF sensitivity
Keiko Kokeyama
University of Birmingham
ET meeting @ Jena, Germany, 1-3 March 2010

## Slide 2: Contents
Thermal Noise (TN) Estimation
  1. Suspension TN
    Thermal conductivity of silicon fiber
    Including the coating TN, optimization of temperature and fiber diameter
    Optimization of suspension length
  2. Thermoelastic Noise
    arm cavity power
Summary
0/13

## Slide 3
Suspension TN estimation
1/13
Mathematical formula of suspension TN
d (suspension fiber diameter) appears as a cross section area
d has to be enough strong
Fibers have to take away the heats due to the arm power
Heat flow depends on d, T
  Arm power 20kW
  Coating absorption
  1ppm
  Heat flow
  20 mW
d: fiber diameter
T: temperature of the test mass
lsus: suspension length
Notes:   n, E wire , lsus, phi wire are the number of wire, Young‘s modulus, suspension length, loss angle.
  E.g., when the arm cavity of 20 kW and the absorption of the coating is 1ppm, the fibers must bring 20 mW
  Thermal flow of the fiver depends on thermal conductivity, etc.

## Slide 4
To choose fiber diameter
2/13
c.f.) experimental data of sapphire is available
We need thermal conductivity k of silicon
Heat flow:
We drive thermal conductivity k analytically using Debye model
k should depend on a fiber diameter, as well as the temperature, and it has not been measured experimentally yet (Experimental data of k is available only for bulk silicon)
Notes: K is the thermal flow
How much K required is determined by the arm power and the coating absorption as I showed in the last page
K depends on d square and the thermal conductivity, and the thermal conductivity also depends on d.
Experimental data is not available yet
We derive kappa from debye model

## Slide 5
Debye Model
Phonons of crystal get scattered by several reasons and the scatterings disturb the thermal propagation inside the material
When scatterings are big, heat propagation is prevented
Thermal conductivity
3/13
Phonon scattering (high temperature)
Impurity scattering (low temperature)
Boundary Scattering
In this model, mean free times are shorten by…
Thermal conductivity by Debye model
[1]
[1] D. Morelli et al, Phys. Rev. B, 66, 195304 (2002)
Notes: τC, τN, … are the mean free times. This relaxation time is affected by scattering between phonons of silicon crystal. (Heat can propagate when phonon scatterings are low) Mean free times are shorten by various scattering source
1. Normal Scattering … phonons are collide with low kinetic momentum
2. Umklapp Scattering … phonons collisions with high kinetic momentum
3. Isotope Scattering … isotope atoms occurs scattering
4. Boundary Scattering … phonons are scattered by the walls of fiber. When the low temperature and other scattering are small, the boundary scattering comes to be dominant. It fiber diameter dependence

## Slide 6
10 20 30 100 200
1000
Temperature [K]
500 um
1 mm
2 mm
5 mm
2000
100
10
Thermal conductivity [W/K/m]
Scatterings and k
This is a theoretical model. It will be replaced by experimental data.
4/13
Notes: is Glasgow doing?
Assuming 1.2mm and 12K lower mass temperature, th hermal flow of 20mW is accomplish -> 1ppm

## Slide 7
10 20 30 100 200
1000
Temperature [K]
500 um
1 mm
2 mm
5 mm
2000
100
10
Thermal conductivity [W/K/m]
Scatterings and k
This is a theoretical model. It will be replaced by experimental data.
4/13
e.g. 12K, 2mm  20mW extraction
We start the parameter optimization.
Heat flow

## Slide 8
Optimization – temperature
Parameter tradeoff:
When T is increased, K becomes larger – d can become smaller – suspension TN is decreased
On the other hand, the coating TN is increased by temperature increasing
20kW, 1m suspension TN + coating TN
12K
16K
20K
24K
28K
32K
1 10 100
10-24
10-23
10-22
10-25
Frequency [Hz]
Sensitivity [1/sqrtHz]
5/13
suspension TN
coating TN

## Slide 9
Optimization scale
We used a range for 200-solarmass black hole binary as a scale
6/13
When lsus=1m
Inspiral Range [Gpc]
15 20 25 30 35 40
Temperature [K]
16K is the best
Notes: 20 kW

## Slide 10
Optimization scale
We determine the temperature by a range for 200-solarmass black hole binary
6/13
16K is the best
smallest d is chosen
When lsus=1m
Inspiral Range [Gpc]
15 20 25 30 35 40
Temperature [K]
Notes: 20 kW

## Slide 11
QN
1 10 100
10-24
10-23
10-22
10-25
Frequency [Hz]
Sensitivity [1/sqrtHz]
Optimization – Length
7/13
20kW, 16K
coatingTN
Suspension length should be changed
16K, 1.44mm, 1m

## Slide 12
Optimization – Length
QN
lsus=3m
1 10 100
10-24
10-23
10-22
10-25
Frequency [Hz]
Sensitivity [1/sqrtHz]
16K, 2.14mm
3m suspension is ok compared with QN
8/13
20kW
16K, 1.44mm, 1m

## Slide 13
Optimal temperature for best inspiral range considering suspension and coating TN
smallest fiber diameter is chosen
Suspension length not to disturb QN
Thermoelastic noise
has to be taken into account
Small summary and a next step
Procedure to choose suspension + coating TN parameters
9/13
Notes: because when you increase the arm power, the heat flow to be extracted will become bigger – higher temperature may be employed -> thermo elastic noise may become high

## Slide 14
Thermal expansion data
0 50 100 150 200 250 300
2.5 10-6
2.0 10-6
1.5 10-6
1.0 10-6
5.0 10-7
0
-5.0 10-7
Tenperature [K]
Thermal expansion rate
10/13
Thermoelastic noise formula [2]
[2] M. Cerdonio et al, Phys. Rev. D, 63, 082003 (2001)
Thermo Elastic Noise

## Slide 15
11/13
Sensitivity Curves
20 kW
S+C TN 3m 16K
TEN 16K
SQL
1 10 100
10-24
10-23
10-22
10-25
10-26
Sensitivity [1/sqrtHz]
Due to the small thermal expansion rate,
thermoelastic noise is good at 16 K
Different an arm cavity power?

## Slide 16
1 10 100
10-24
10-23
10-22
10-25
10-26
Sensitivity [1/sqrtHz]
Frequency [Hz]
200 kW
SQL
S+C TN 3m 32K
TEN 32K
Arm cavity power
should be optimized
considering QN
Sensitivity Curves
20 kW
S+C TN 3m 16K
TEN 16K
SQL
1 10 100
10-24
10-23
10-22
10-25
10-26
Sensitivity [1/sqrtHz]
12/13

## Slide 17
Summary
For ET-LF
We discussed how to choose the optimal TN parameters for d, T, lsus
  200 MS BH binary inspiral range as a scale to choose T
  d was optimized for the chosen T
  lsus was chosen not to disturb QN
Arm cavity power has to be chosen including QN
Other aspect
  Ribbon suspension can be an alternative as it can have a lager cross section area the more heat flow may be accomplish
13/13
Notes:   3m monolithic fiber may not be available

## Slide 18
Thank you.

## Slide 19
Fiber diameter requirement satisfying a thermal flow for 20 kW arm power and strength requirement
Fibediameter [mm]
a
10 20 30 40 50
0.4
1.2
0.8
1.0
0.6
1.4
Temperature [K]
20 kW
Strength limit
Wire diameter from
thermal flow requirement

## Slide 20
Ribbon

## Slide 21
Thermo Elastic Noise
Thermoelastic noise Formula [1]
[1] M. Cerdonio et al, Phys. Rev. D, 63, 082003 (2001)
J(Ωc)
Ωc
11/14
J(Wc) can be approximated;