## Slide 1
Luca Serafini – INFN-Milan and University of Milan –
on behalf of MariX-C.D.R. Collaboration
The Challenge: sustainable CW coherent X-ray FEL & ICS
MariX: Conceptual Design Report of a Multi-disciplinary Advanced Research Infrastructure for the generation and application of X-rays
MariX Seminar – Laboratori Naz. Frascati - INFN - Dec. 2nd, 2019
multi MW electron beams with
recovery/recirculation to keep
power consumption / radio-protection
below 100 kW

## Slide 2
Linea ferroviaria Mi-Torino
Autostrada A7 Como-Varese
MIND : Milan INnovation District
A Multi-disciplinary Advanced Research Infrastructure for the Milan metropolitan area

## Slide 3
Scientific Case for a low jitter CW FEL was conceived by Giorgio Rossi, Giacomo Ghiringhelli, Ezio Puppin, Francesco Stellato/Silvia Morante, Bruno Paroli, Martino Bolognesi: Linear Spectroscopy in 0.2-8 keV at femtosecond time scale
Clinical Case for ICS monochromatic X-ray Source delineated by metropolitan Milan Hospitals: San Raffaele, Niguarda, Istituto Naz. dei Tumori, in collaboration with Ferrara and Naples Univ.
Design of a High Sustainability CW combined FEL & ICS X-ray Source for UniMi Scientific Campus spanning 0.2-180 keV (delivering 200kW to 2 MW sustainable beam power to client, cfr. Fermi 100 W, EupraXia 30 W, LCLS 2 kW )
Multi-disciplinary Advanced Research Infrastructure
for the generation and application of X-rays: MariX C.D.R.

## Slide 4
Compton X-ray photon beam: 1012 - 1013 hn/s (@ 100 MHz) in 5% Dn/n, 20-180 keV, tunable, polarized, st = 2 psec, 10 mm round source spot size, mrad divergence
FEL fully coherent diffraction limited X-ray photon beam: 108-10 hn/pulse @ 1 MHz
in 0.05% Dn/n, 0.2-8 keV, st < 50 fsec, 1016 hn/s
FEL Spectrum
2.5 GeV, lw=12 mm
Compton spectrum
FP @ 400 kW, 10 mA,
e- beam 1 MW
2.6.1012 photons/s
The Mission: coherent femto-second X-rays @ (0.2-8) keV, and ultra-high brilliance hard X-rays @ 20-180 keV
LCLS, 1 Angstrom
15 GeV, lw=2.5 cm

## Slide 5
After 1 year of hard work...
CDR has been published and
available for download at
www.marix.eu
The Product: Conceptual Design Report

## Slide 6
MariX Seminar – Laboratori Naz. Frascati - INFN - Dec. 2nd, 2019

## Slide 7
Executive Summary
published on NIM-A

## Slide 8
Machine Team: A. Bacci, A. Bosotti, F. Broggi, S. Cialdi, C. Curatolo (INFN-PD), S. DiMitri (ST),
I. Drebot, A. Esposito (LNF), D. Giove, G. Galzerano (PoliMi/CNR), P. Michelato, L. Monaco,
R. Paparella, V. Petrillo, F. Prelz, E. Pinotti (PoliMi), M. Placidi (Univ. BO), E. Puppin (PoliMi),
A.R. Rossi, D. Sertore, V. Torri
Fellows: D. GiannottiINFN, L. FaillaceINFN, M. Rossetti ContiINFN, S. CapraUniMi
PhD/Master Students: F. Canella, M. Opromolla, C. Paulin, M. RuijterINFN,
S. SamsamICTP, E. Suerra

## Slide 9
Synchrotron Radiation sources
500 MHz repetition
nJ pulse energy; ≈50ps
105-6 photons x (5)x108pulses
Linear response regime:
Imaging and spectroscopy (perturbation theory)
Free Electron Laser sources
10Hz-27kHz repetition
mJ pulse energy; ≈50fs
1012-13 photons x
101-3-(6)pulses
Ultrafast Non-linear response regime
Imaging, flash+destroy
Laser-HHG UV-Soft X
MARIX+FEL (10 keV)
1 MHz repetition
100nJ pulse energy; ≈50fs
108-11 photons x 106pulses
Ultrafast Linear response
Courtesy Giorgio Rossi
DLSR: vertical emittance 2-8 picorad,
horizontal emittance 200-300 picorad
MariX: vertical/horizontal
emittance 45 picorad
⇒ Round vs. Flat beams

## Slide 10
High resolution low dose Radio-logical Imaging (<100 mm) with mono-chromatic X-rays up to 150 keV: mammography, 2 color angiography, radio-therapy with auger electrons on cis-platine, CAT 3D imaging of Cult.Herit./Archeological/Paleontological samples
Time resolved spectroscopy with fs coherent X-rays up to 8 keV @ 1 MHz rep rate: catalisys and chemistry in solvents, structure of nano-objects from coherent diffraction, bio-chemistry @ atomic and fs scale, pump&probe spectroscopy of strongly correlated materials, magnetism, superconductivity, topological materials, materials under strong spin-orbit interaction. Protein Crystallography with single-shot imaging (flash-and-destroy)
Scientific/Clinical Case: 2 Research Fields
enabled by MariX originality (Compton+FEL in CW)

## Slide 11
Courtesy Giorgio Rossi
MariX Seminar – Laboratori Naz. Frascati - INFN - Dec. 2nd, 2019

## Slide 12
Comparison between X-FELs
Electron Beam Energy to radiate at ~ Angstrom
FEL | Radiation Wavelength (A) | Electron Beam Energy (GeV) | Linac Length (m)
LCLS | 0.5 | 14.3 | 1000.
PSI | 1.0 | 5.8 | 500.
EuXFEL | 0.15 | 17.5 | 1700.
LCLS II | 2.4 | 4.0 | 650.
MariX | 1.5 | 3.8 | ???? < 200
lR = lw (1+aw2)/ 2g2 , lw ÷ 1.2-3 cm
MariX Seminar – Laboratori Naz. Frascati - INFN - Dec. 2nd, 2019

## Slide 13
Injector
Superconductiong Linac: 13 XFEL crio-modules Compr Undulator
100 MeV 1.6-1.8 GeV
Traditional
FEL layout
l=7 Ang
MariX
layout
Arc
compr
Injector
Linac1: 11 XFEL crio-modules
3.4-3.8 GeV 2.8-3.2 GeV 1.4- 1.6 GeV
l=1.5 Ang
Linac2
0
100m
200m
300m
400m
500m
dV/dz=17 MV/m
In quest of High Sustainability we had to conceive a new kind of machine:
the Two-Way Linac (TWL)
All Accelerators are one way – the beam propagates in one direction (ERL too)
MariX uses the CW Linac twice – forward and backward
Only Standing Wave RF Cavities can accelerate particles in both directions!

## Slide 14
Acceleration in opposite directions through a Linac
(two-way acceleration)
is possible if:
RF fields can accelerate in both directions
(Standing Waves can do it)
2) Focusing effective in both directions and weakly energy dependent
(RF focusing and/or solenoids)
3) No bunch crossing –> Twice the Linac Length < Bunch separation
4) RF fields must be on for a time longer than
bunch back-and-forth travel time (CW recommended)
5) Orbit position must not be dependent on magnetic rigidity
(no two-way through dipoles, except bifurcations)
MariX Seminar – Laboratori Naz. Frascati - INFN - Dec. 2nd, 2019

## Slide 15
Modo risonante TM010-p ad Onda Stazionaria
k
phase velocity = c
n=1.3 GHz ; l=0.23 m
Standing RF Waves
9 celle = 4.5 l = 1.04 m
MariX Seminar – Laboratori Naz. Frascati - INFN - Dec. 2nd, 2019

## Slide 16
E0 sin(kz)cos(wt-f0) =
(1/2) E0 sin(kz-wt+f0) + (1/2) E0 sin(kz+wt-f0)
standing wave
forward traveling wave,
synchronous to z = ct
backward traveling wave,
synchronous to z = -ct
ampiezza della componente
di onda viaggiante sincrona
rispetto all’elettrone
MariX Seminar – Laboratori Naz. Frascati - INFN - Dec. 2nd, 2019

## Slide 17
RF Focusing effective only in Standing Wave RF Cavities
a lesson we learned long time ago
RF transport matrix

## Slide 18
RMS Envelope Equation for laminar beams: a path towards the Invariant
Envelope Theory for High Brightness el. beams (1997, L.S and J.Rosenzweig)
1.1
Cauchy

## Slide 19
RF (ponderomotive) Focusing
~ 1 Standing
~ 0 Traveling

## Slide 20
Two-pass 2-way region
The Super Conductive Main Linac
Ten Tesla like cryomodules: max grad 16 MV/m, 8 cavity per cryomodules
Chirp for AC-compression is given injecting @ + 6° from RF crest.
5 T solenoid
We rely only on second order focusing, symmetric back-and-forth: Rf focusing and solenoid foc.
Notes: Adiabatic focsing

## Slide 21: Source layout 5: The arc compressor
One DBA
14 Double Bending Achromats Elettra-like
30°
R=41 m
R56=35 mm
dipole
quad
sextupole
Study of the arc compressor done by
M. Rossetti Conti
MariX Seminar – Laboratori Naz. Frascati - INFN - Dec. 2nd, 2019

## Slide 22
ISR and CSR through Arc Compressor
MariX Seminar – Laboratori Naz. Frascati - INFN - Dec. 2nd, 2019

## Slide 23
10 quads matching line with two different objectives:
The forward traveling bunch is matched to the BAC (in first DBA bending).
The bunch traveling back divergence is controlled to avoid strong degradation by chromatic effects in the SC solenoid.
Bubble Arc matching line
Forward
Backward
Notes: The matching line is composed by 10 Quads and its design is complicated since this line have two objectives. the forward…
The divergence of the backward have to be controlled To avoid emittance deg. By chromatic effects that can occur in the SC solenoid if the bunch tranverse dimensions are too high.

## Slide 24
Beam parameters in BAC
Projected εn,x increase by CSR
Ipeak x 100
CSR and LSC: on
Notes: The main parameters of the bunch in the BAC are shown In this picture, looking at the green line in the upper plot we can clearly see the linear compression of the bunch. At the end of the line the peak current is multiplied by a factor of 1 hundred.
The effects of the CSR kick on the bunch slices are visible at the end of the line in the increase of the projected emittance. However, this effect is not strong as it may seem, in fact we will see that the slice emittance is low. In all the bunch

## Slide 25: Beam dynamics 1: before the arc, Q=50 pC
Longitudinal phase space
here
<E>=1.5 GeV
Ipeak=16 A
sz=360 mm
DE/<E>=7 10-4
enx,y=0.2 mm
sx=6 mm
Transverse phase space
Beam dynamic study made by A. Bacci
MariX Seminar – Laboratori Naz. Frascati - INFN - Dec. 2nd, 2019

## Slide 26
Beam dynamics 2: after the arc, Q=50 pC
here
Ipeak=1600 A
sz=20 mm
DE/<E>=3.6 10-4
sx=52mm
en,x=1 mm
sy=14.5 mm
en,y=0.2 mm
Longitudinal phase space
Transverse phase space
Centro Brasileiro de Pesquisas Fisicas, Rio de Janeiro, May 2nd, 2019

## Slide 27
MariX Seminar – Laboratori Naz. del Sud - INFN - Nov. 13th, 2019

## Slide 28
CSR compensation
Two main factors contribute in CSR compensation:
Current profile shaping (injector) reduce CSR kick.
The HHL in acc. phase (+100 MeV) increases LPS curvature compensating the distorsion induced by CSR.
Forward
Backward
HHL
Notes: The preservation of the slices quality is achieved thanks to two factors
1- the current shaping performed in the injector reduce the CSR kick at maximum compression.
2- the HHL positioned before the matching line is used to increase the curvature of the beam as can be seen in the picture in the bottom left. This is done to compensate the distortion induced by the CSR emission, the effect is clearly seen comparing the shape of the final LPS with the cavity turned off (in red) and on (in blue). This increase significantly the peak current the distribution

## Slide 29
Beam dispersion damping
The CSR kick induces dispersive effects on the beam:
Increase η and η’, <x> and <x’> and spoils FEL emission
Modified last DBA
QUADS
STEERINGS
Projected εn,x decreased by 30%
Beam centered on axis
Notes: Another effect of the CSR kick is the induction of residual dispersion on the beam. This can be quantified using the eta and eta’ parameters or looking at the centroids displacement.
To compensate this effect we modified the last DBA adding 2 Quads and a couple of steering magnets, we used these parameters to minimize eta and eta’ nda the centroids displacements from the axis.
As result we obtained a decrease in the projected emittance by 30% and centered back the beam on axis.

## Slide 30: beam dynamics w/o optimization in last DBA with special lay-out
Linac 1 1st pass TL Arc compressor TL Linac 1 2nd pass Linac2
Envelopes
Emittances
All the beam dynamics simulations have been done with ELEGANT by
Alberto Bacci and Marcello Rossetti Conti
MariX Seminar – Laboratori Naz. Frascati - INFN - Dec. 2nd, 2019

## Slide 31
The Bunch
Beam Propagation
Notes: This is the final LPS of the beam, it is interesting to note that the beam tail is the most populated part of the bunch.
Looking at this PS we see a really weak gain of the MBI induced by CSR.

## Slide 32
T [s]
Par. | Full Beam | Cut
Qtot | 50 pC | 30 pC
Ipeak | 1580 A | 1500 A
σE | 1.6 MeV | 750 keV
σE/E | 1.0 10-3 | 4.7 10-4
εn,x | 1.01 µm | 0.29 µm
Desired Max Slice εn,x = 0.5 mm mrad
The Bunch
0.71
0.71
0.24
Notes: This is the slice analysis of the bunch, that shows a peak current of 1.6 kA . It’s interesting to note that the minimum of the emittance is in the position of the maximum of the current - really high peak brightness 9 10^16
The main beam parameters are shown in this table, a beam cut of the portion that we expect will contribute more to the FEL emission shows 30 pC charge, really low emittance and energy spread and high current

## Slide 34
MAC-INFN LASA, Giugno 2019
estratto dal report:
MariX Seminar – Laboratori Naz. Frascati - INFN - Dec. 2nd, 2019

## Slide 35
MariX Seminar – Laboratori Naz. del Sud - INFN - Nov. 13th, 2019

## Slide 36
MariX Seminar – Laboratori Naz. Frascati - INFN - Dec. 2nd, 2019

## Slide 37
500 m
Next generation CW FELs like LCLS-II are km-long: not enough space in new UniMi Campus

## Slide 38
100
200
300
400
m
MariX Seminar – Laboratori Naz. Frascati - INFN - Dec. 2nd, 2019

## Slide 39
Ezio Puppin – CDR convener for Civil Engineering and
Infrastructure Systems
MariX Seminar – Laboratori Naz. Frascati - INFN - Dec. 2nd, 2019

## Slide 40
200 kW underground beam dump @ 3.8 GeV
MariX Seminar – Laboratori Naz. Frascati - INFN - Dec. 2nd, 2019

## Slide 42
UliX1 l=2.8 cm aw<2.5
from 100 eV to 4KeV
General considerations on MariX FEL
UliX2 l=1.2 cm aw<0.8
from 2 KeV to 8 KeV
ULIX2
ULIX1
1) For emitting with continuity from 100 eV to 8 KeV:
Lmod=2.8 m
Ldrift=56 cm
Undulator
module
Quadrupole
BPM
Phase Shifter
Lquad=20 cm
Beam
pipe
Lmod=1.2 m
Ldrift=24 cm
Undulator
module
Quadrupole
BPM
Phase Shifter
Lquad=8 cm
Beam pipe
Nominal electron beam
MariX Seminar – Laboratori Naz. Frascati - INFN - Dec. 2nd, 2019

## Slide 43
SASE3: single shot imaging (1.5 Å), ULIX2, 1.2 cm
Growth
Spectrum
60 m
Power
60 m
e-En (GeV) | 3.8
Und (cm,m) | 1.2 60
Ph-en (keV) | 9.25
Rep rate | 1 MHz
Energy | 3.3 uJ
Numb per shot | 2.5 109
Bandwidth (%) | 0.3
N/ s (s-1) | 2.5 10 15
Spectral dens(N/shot/1%bw) | 0.8 109
Radiation size mm | 0.1
Divergence mrad | 15 10-3
Tot. spect dens. (N/s/1%bw) | 8 10^14
Coherence | SASE
Q=50 pC, SASE
I=1.5 kA
emit=0.35 um
DE/E=3.6 10-4
aw=0.64
dt=10 fs
SASE spikes undersampled
in the graph (but not in the calculus)
MariX Seminar – Laboratori Naz. Frascati - INFN - Dec. 2nd, 2019

## Slide 44
SASE1: water window (2.77 nm) ULIX1, lw=2.8 cm
I=1.5 kA
emit=0.35 um
DE/E=3.6 10-4
aw=2.5
dt=10-3 fs
Spectrum
30 m
 | 16pC | 50 pC
e-En (GeV) | 3.2 | 3.2
Und l_w, L(cm,m) | 3 , 25 | 5, 25
Ph-en (keV) | 0.45 (2.8nm) | 0.45 (2.8nm)
Rep rate | 1 MHz | 1 MHz
Energy | 21 mJ | 156 mJ
Numb per shot | 3 1011 | 2.2 1012
Bandwidth (%) | 0.1 | 0.15
Pulse duration (fs) | 3 | 10
N/ s (s-1) | 3 1017 | 2.2 1018
S dens(N/shot/%bw) | 1.7 1012 | 1.5 1013
Radiation size mm | 0.15 | 0.07
Divergence mrad | 2.5 10-2 | 1.810-2
Tot. S. d. (N/s/%bw) | 1.7 1018 | 1.5 1019
Coherence | Single Spike | SASE
Power
30 m
Q=16 pC
Q=50 pC
Growth
Q=50 pC
SASE
Q=16 pC
Single Spike
MariX Seminar – Laboratori Naz. Frascati - INFN - Dec. 2nd, 2019

## Slide 45
FEL simulations
With ELEGANT simulations we obtained
an electron beam with parameters very
similar to the nominal ones
0.5-0.35
Sirius like, ESRF-upgrade like

## Slide 46
Seeded pulses for linear spectroscopy (3-6 Ang):
three options
Multi-Cascade Seeded by HHG in gas at 13 nm
Multi-Cascade seesed by a FEL Oscillator at 13 nm, MoSi mirrors
Regenerative Amplifier with diamond mirrors
1 MHz, Optical line by Alberto Tagliaferri
Possible only at low repetition rate
Possible at 0.5 MHz
MariX Seminar – Laboratori Naz. Frascati - INFN - Dec. 2nd, 2019

## Slide 47
3° option: Regenerative amplifier at 4 Ang with Diamond mirrors
SASE
Spectrum
Temp. distr.
Reg. amplifier
l(nm)
s(mm)
Round trip number
Round trip number
MariX Seminar – Laboratori Naz. Frascati - INFN - Dec. 2nd, 2019

## Slide 48
Comparison between X FELs, photons per second,
Electron Beam Energy to radiate at ~ Angstrom
FEL | Pulse per second
LCLS | 120 Hz
SACLA | 30-60 Hz
FERMI | 10-50 Hz
PAL | 30-60 Hz
PSI | 100 Hz
EuXFEL | 27 kHz
LCLS II | 1 MHz
MariX | 1MHz
lR = lu / 2g2
MariX Seminar – Laboratori Naz. Frascati - INFN - Dec. 2nd, 2019

## Slide 50
BriXS: an example of high sustainability. High power 2 MW beam delivered to user with only 200 kW power consumption/dissipation with outstanding beam quality (larger than storage rings, same current)
Great advantage of BriXS ERL vs. storage ring based ICS: we do not care about electron beam quality preservation after collision (tighter focusing, round beam) – we just need to recover its kinetic energy by deceleration

## Slide 51
4th order variational expansion over rms phase space distribution of e-hn colliding beams

## Slide 53
Inverse Compton Sources rivaling in Average Brightness with Synchrotron Light Sources at photon energies above 80-100 keV
I.C.S.
STAR
ELI-NP-GBS

## Slide 54
Fonte dei grafici: SwissFEL Science Case
BriXS Compton Source
Clinical/Scientific Case
enrolling
Ercolano’s
papyri

## Slide 56
MariX-RAD CSN5-INFN (FE, MI, NA)
Resp. Naz. Paolo Cardarelli - Univ. di Ferrara and INFN-FE

## Slide 58
≈ 6 M€, TDR preparation approved by INFN within mid 2020
20 mA, 100 MHz, 10 MeV
> 60% energy recovery

## Slide 59
MariX 2-Phases (M€)
BriXS 82.5
MariX-FEL 685.3
cmp. LCLS-II > 1 G€
XFEL > 1 G€
MariX Seminar – Laboratori Naz. Frascati - INFN - Dec. 2nd, 2019

## Slide 60
Operational Costs (M€/year) Footprint (m2) (€/kwh)
MariX 45.5 (18 A/C) 35.000 0.234
LCLS 110
XFEL 120
SIRIUS 35 68.000 0.11
MariX Seminar – Laboratori Naz. Frascati - INFN - Dec. 2nd, 2019

## Slide 61
MariX/BriXS/BriXSino – the Italian way towards sustainable high power e- (e+) accelerators (MW and multi-MW class)
A new genetic line in accelerator zoology (2-way 2-pass)
Both are strategic motivations for INFN (BriXSino aims at filling an Italian void in this field)
Why Milano: unique overlap among expertise in accelerator & laser physics and technology, like High Brightness Beams/FEL/ICS Physics - SC/RF technology - High QE photocathodes - High Power Optical FP cavities, and a qualified User Community in Synchro-tron Light and FELs, with the endorsement in MariX-CDR and BriXS-EoI from IRCCS San Raffaele, Niguarda, Istituto Nazionale dei Tumori
conclusions
MariX Seminar – Laboratori Naz. Frascati - INFN - Dec. 2nd, 2019

## Slide 62
An Arc Compressor at Eupraxia@SPARC-Lab?
A better footprint sustainability, additional space for a 60 m long undulator
Courtesy Andrea R. Rossi
MariX Seminar – Laboratori Naz. Frascati - INFN - Dec. 2nd, 2019

## Slide 63
MariX Seminar – Laboratori Naz. del Sud - INFN - Nov. 13th, 2019