## Slide 1: Algoritmi di denoising innovativi basati su deep learning per la riduzione del rumore in immagini NMR in Fluoro 19
Alessandro Sbandi

## Slide 2: Objective and strategy
Testing denoising algorithms based on deep learning.
Compare results with traditional methods.
Three different neural network architectures:
-Denoising Autoencoder (DAE)
-Variational Autoencoder (VAE)
-Denoising Convolutional Neural Network (DnCNN)

## Slide 3: Dataset 1
Signal Signal+Rician Noise
Signal = 1000
Sigma = 700
Image Size = 512x512
Blobsize = 10.
Nseeds = 3
Generation parameters:

## Slide 4: First analysis
Signal
Background

## Slide 5: Results dataset 1
 | PSNR (dB) | Dice coefficient
Noised Images | 5.863 ± 0.332 | 0.334 ± 0.008
Denoising autoencoder | 17.039 ± 1.433 | 0.959 ± 0.010
Variational autoencoder | 13.989 ± 1.101 | 0.905 ± 0.018
Wiener filter | 16.701 ± 0.875 | 0.973 ± 0.006
DAE VAE WIENER+OFFSET

## Slide 6: Results dataset 1
 | PSNR (dB) | Dice coefficient
Noised Images | 5.863 ± 0.332 | 0.334 ± 0.008
Denoising autoencoder | 17.039 ± 1.433 | 0.959 ± 0.010
Variational autoencoder | 13.989 ± 1.101 | 0.905 ± 0.018
Wiener filter | 16.701 ± 0.875 | 0.973 ± 0.006
DAE VAE WIENER+OFFSET
Best performance

## Slide 7: Dataset 2
Generation parameters:
Signal = 1000
Sigma = 700
Image Size = 256x256
Blobsize = 1
Nseeds = 1
Gaussian Filter
Signal Signal+Rician Noise
10000 images:
7200 train set
1800 validation set
1000 test set
Using the same architectures used for dataset 1
Fixed shape and Rician noise
Can DAE denoise it? Like a Wiener filter?
Can a generative model (VAE) do the ‘‘same’’ task?

## Slide 8: Denoising autoencoder results
 | PSNR (dB) | Dice Coeff.
DAE | 35.920 ± 2.283 | 0.829 ± 0.020
Loss
Epochs

## Slide 9: Denoising autoencoder results with an offset
 | PSNR (dB) | Dice Coeff.
DAE | 35.920 ± 2.283 | 0.829 ± 0.020
DAE with offset | 21.507 ± 1.305 | 0.878 ± 0.016
GT PREDICT PREDICT+OFFSET

## Slide 10: Variational autoencoder results
 | PSNR (dB) | Dice Coeff.
VAE | 26.985 ± 3.637 | 0.810 ± 0.040
Loss
Epochs

## Slide 11: Variational autoencoder results with an offset
 | PSNR (dB) | Dice Coeff.
VAE | 26.985 ± 3.637 | 0.810 ± 0.040
VAE with offset | 14.619 ± 1.576 | 0.768 ± 0.066
GT PREDICT PREDICT+OFFSET

## Slide 12: Using Wiener filter+offset+median filter
 | PSNR (dB) | Dice Coeff.
Wiener filter | 17.433 ± 1.405 | 0.828 ± 0.064
TEST WIENER FILTER MEDIAN FILTER GT

## Slide 13: Results dataset 2
 | PSNR (dB) | Dice coefficient
Noised Images | 5.863 ± 0.332 | 0.334 ± 0.008
DAE | 35.920 ± 2.283 | 0.829 ± 0.020
DAE with offset | 21.507 ± 1.305 | 0.878 ± 0.016
VAE | 26.985 ± 3.637 | 0.810 ± 0.040
VAE with offset | 14.619 ± 1.576 | 0.768 ± 0.066
Wiener filter with offset | 17.433 ± 1.405 | 0.828 ± 0.064
DAE VAE WIENER+OFFSET
The denoise is good as a Wiener filter ✓
For a generative model performance are lower as expected ✓

## Slide 14: Dataset 3
Test the reconstruction: do DAE and VAE generalize the reconstruction of signals with different shapes?
Generation parameters:
Signal = 1500
Sigma = 900
Image Size = 64x64
Blobsize = 0.3
Nseeds = 1
7000 train set
3000 validation set
3 test set
10003 images:

## Slide 15: Results dataset 3
DAE/VAE don’t generalize in reconstruction ✗
Two possible strategies:
a) DAE/VAE trained with deformed signals shapes.
b) try with a different network DnCNN.

## Slide 16: Dataset 4
Generation parameters:
Signal = 1500
Sigma = 900
Image Size = 64x64
Blobsize = 0.2/0.5
Nseeds = 1
Gaussian filter
Elastic deformation
Signal Signal+Rician Noise
7000 train set
3000 validation set
3 test set
10003 images:

## Slide 17: Denoising autoencoder results
 | Shannon Entropy
MRI 1 | 11.996
MRI 2 | 11.995
MRI 3 | 11.997
Loss
Epochs

## Slide 18: Variational autoencoder results
 | Shannon Entropy
MRI 1 | 11.982
MRI 2 | 11.981
MRI 3 | 11. 988
Loss
Epochs

## Slide 19: Results dataset 4: A plan
Reconstructions are a little bit better then before ✓
But not so good, I need greater dataset for an appropriate generalization ✗

## Slide 20
Input Layer (64, 64, 1)
Conv2D(64)
Conv_block
Conv2D(1)
Conv2D(64, (3,3))
BatchNormalization((2,2))
Conv_block
…
x15
Output=Input-Conv2D(1)
Forces to learn noise
Dataset 4: B plan
Try with a different network, DnCNN.
DnCNN needs fewer data then AE to generalize.
Used as denoiser with residual learning configuration.

## Slide 21: Results of DnCNN
 | Shannon Entropy
MRI 1 | 11.996
MRI 2 | 11.995
MRI 3 | 11.999
Loss
Epochs
DnCNN results are good as the best DAE (the one with infinite power generalization) and of the Wiener filter ✓
DnCNN generalizes better with different shapes ✓

## Slide 22: Results dataset 4
DAE
MRI
VAE
DnCNN
Wiener
Shannon Entropy | MRI 1 | MRI 2 | MRI 3
DAE | 11.996 | 11.995 | 11.997
VAE | 11.982 | 11.981 | 11. 988
DnCNN | 11.996 | 11.995 | 11.999
Wiener | 11.999 | 11.999 | 11.999

## Slide 23: Conclusions...
Denoising is good, but DnCNN and Wiener work better then DAE/VAE.
Wiener eliminates the noise, but produces artifacts. Maybe others non-Rician noise sources.
DnCNN produces really good results in 2/3 MRI. Statistic is too low, but could be different acquisition conditions or problematics.
Tested three different deep neural network architectures for denoising:
- DAE: works well in recognizing and removing the noise, needs large data- augmented samples in order to not learn shapes in the training set.
- VAE: as expected underperform with the DAE but can be used to produce large samples for training of the DAE/DnCNN.
- DnCNN: best results, same level as Wiener filter, in terms of noise removal and good generalization to different shape (need to be quantitatively assessed).

## Slide 24: ...and further steps
Try to add a residual layer in DAE/VAE.
Improve plots and quantitative measures between different methods.
High statistic test with simulated data with different shape (to quantify generalization power).
High statistic test with simulated data adding Rician noise + other noise components.
Completing the study and wrapping up for the thesis (deadline for submission end of december).