## Slide 1
Vladimir Shiltsev (Fermilab)
eeFACT’22 – 65th ICFA BD Workshop (INFN Frascati, Sep 12-15, 2022)
12 September 2022
Realization, Timeline, Challenges and Ultimate Limits of Future Colliders

## Slide 2: Content (Plan)
Snowmass’21 Accel. Frontier (4 slides)
Implementation Task Force (7 slides)
On Limits of Colliders (17 slides)

## Slide 3: https://www.snowmass21.org/
Snowmass’21 Discussions (incl. colliders)
“Snowmass is a particle physics community study”
Snowmass
P5
DOE/NSF
1.5-2 yrs
~ 1 yr
~7 yrs of
hard work
Organized by APS DPF, DPB, et al
Snowmass provides input to P5 (Particle Physics Project Prioritization Panel)
which develops
a 10-20 yrs strategy for
the US HEP program
  Particle Physics is global
Particle Physics is not isolated
Particle Physics
Project Prioritization Panel

## Slide 4: Snowmass’21 Accelerator Frontier Conveners
Steve Gourlay (LBNL)
Tor Raubenheimer (SLAC)
Vladimir Shiltsev (FNAL)
Topical Group |  | Topical Group co-Conveners |  |  | 
AF01 | Beam Phys & Accel. Education | Z. Huang (Stanford) | M. Bai (SLAC) | S. Lund (MSU) | 
AF02 | Accelerators for Neutrinos | J. Galambos (ORNL) | B. Zwaska (FNAL) | G. Arduini (CERN) | 
AF03 | Accelerators for EW/Higgs | F. Zimmermann (CERN) | Q. Qin (ESRF) | G.Hoffstaetter (Cornell) A.Faus-Golfe (IN2P3) | 
AF04 | Multi-TeV Colliders | M. Palmer (BNL) | A. Valishev (FNAL) | N. Pastrone (INFN) J.Tang (IHEP) | 
AF05 | Accelerators for PBC and Rare Processes | E. Prebys (UC Davis) | M. Lamont (CERN) | Richard Milner (MIT) | 
AF06 | Advanced Accelerator Concepts | C. Geddes (LBNL) | M. Hogan (SLAC) | P. Musumeci (UCLA) | R. Assmann (DESY)
AF07 | Accelerator Technology R&D |  |  |  | 
 | Sub-Group RF | E. Nanni (LBNL) | H.Weise (DESY) | S. Belomestnykh (FNAL) | 
 | Sub-Group Magnets | G. Sabbi (LBNL) | S. Zlobin (FNAL) | S. Izquierdo Bermudez (CERN) | 
 | Sub-Group Targets/Sources | C. Barbier (ORNL) | Y. Sun (ANL) | Frederique Pellemoine (FNAL) | 

## Slide 5: AF Report: Exec. Summary
“Intro”:
  Since last P5, this Snowmass’21 process
“Future Facilities”:
  TBD by P5 – accelerator/people need to be part of P5; ITF analysis can greatly help
  Multi-MW FNAL complex upgrade will be priority for NF in 2030 (AF ready)
  Many opportunities for Rare Processes (AF ready), incl. PAR and utilize what we have
  Several Higgs/EW factories are feasible: FCCee, C3 and HELEN to be explored
  O(10 TeV/parton) needed for >2040’s, muon colliders to be explored/ pre-CDR by 2030
  Need an Integrated Future Colliders R&D program in OHEP to provide design reports by next Snowmass/P5’2030 and engage internationally (FCC, ILC, IMCC)

## Slide 6: Multi-MW targets: - 2.4 MW for PIP-III - 4-8 MW for muon collider
Magnets for
colliders and RCSs: - 16T dipoles
- 40T solenoids - 1000 T/s fast
cycling ones
…coordinated
with US MDP
Wakefields: - collider quality beams
- efficient drivers and staging
- close coordination with Int’l (Euro Roadmap, EUPRAXIA,..)
SC/NC RF: - 70-120 MV/m C3
- 70 MV/m TW SRF
new materials, high Q0
efficient RF sources
Accelerator R&D: Next Decade
Accelerator & Beam Physics
    High intensity/brightness beams acceleration and control
    High performance computer modeling and AI/ML approaches
    Design integration and optimization, incl energy efficiency
Full AF “final draft” report available and via https://snowmass21.org/accelerator/start

## Slide 7: Part II
Collider Implementation Task Force
(Snowmass’21 Accelerator Frontier)

## Slide 8: Implementation Task Force
The Accelerator Frontier Implementation Task Force (ITF) is charged with developing metrics and processes to facilitate a comparison between collider projects:
  Higgs/EW factories (focus of slides below)
  Lepton colliders with 3 TeV cme
  Lepton and hh colliders 10+ TeV cme
  FNAL site-fillers and eh colliders
ITF addressed (four subgroups):
  Physics reach (impact), beam parameters
  Size, complexity, power, environment
  Technical risk, readiness, and R&D required
  Cost and schedule
Steve Gourlay (LBNL)
Tor Raubenheimer (SLAC)
Vladimir Shiltsev (FNAL)
Thomas Roser (BNL, Chair)
Jim Strait (FNAL)
John Seeman (SLAC)
Philippe Lebrun (CERN)
Katsunobu Oide (KEK)
Reinhard Brinkmann
(DESY)
Spencer Gessner (SLAC)
Marlene Turner (LBNL)
Sarah Cousineau (ORNL)
Liantao Wang (U.Chicago)
Meenakshi Narain (Brown U.)
Dmitry Denisov (BNL)
REPORT
https://arxiv.org/abs/2208.06030
Below I mostly follow T.Roser presentation in Seattle

## Slide 9: Proposals – Higgs/EW Physics

## Slide 10: 250 GeV cme Fermilab Site-Fillers
https://arxiv.org/abs/2203.08211
https://arxiv.org/abs/2203.08088
CCC
HELEN
16-km collider e+e- ring
cool- or SC-RF e+e- linear colliders
7-km for 250 GeV, 12-km 0.5+ TeV
https://arxiv.org/abs/2110.15800

## Slide 11
Fermilab
site-fillers
ITF Report – T.Roser, et al, arXiv:2208.06030

## Slide 12: Cost Estimates for Higgs Factories
ITF Report – T.Roser, et al, arXiv:2208.06030

## Slide 13: ITF Technical Risk Registry
ITF Table 14: "Design Status": I - TDR complete, II - CDR complete, III - substantial documentation; IV - limited documentation and parameter table; V - parameter table. Overall risk tier category ranging from Tier 1 (lower overall technical risk) to Tier 4 (multiple technologies that require further R&D).
ITF Report – T.Roser, et al, arXiv:2208.06030

## Slide 14: Luminosity per Power
Circular ee
ERL based ee
Linear ee
Muon coll
Wakefield
Hadron pp
ITF Report – T.Roser, et al, arXiv:2208.06030
Once again: luminosity and power consumption values have not been reviewed by ITF - we used proponents’ numbers.

## Slide 15: Part III
Limits of Colliders
(as discussed at the Snowmass’21 Accelerator Frontier Topical Group 1 Workshop “Physics Limits of Ultimate Beams”, Jan. 2022;
mostly following
V.Shiltsev, Proc. IPAC’21, WEPAB017)

## Slide 16: How ultimate colliders might look like?
BASED ON EXISTING TECHNOLOGIES ?
  Circular ee
  Linear ee/γγ
  Circular pp
  Circular μμ
BASED ON EMERGING TECHNOLOGIES ?
  ERL ee/γγ
  Plasma ee/γγ
  Linear μμ / Plasma μμ
EXOTIC SCHEMES ?
  Crystal linear μμ/ττ
  Crystal linear ττ
  Crystal circular pp

## Slide 17
ITF’s Look Beyond Higgs Factories
 | CME (TeV) | Lumi per IP (10^34) | Years, pre-project R&D | Years to 1st Physics | Cost Range (2021 B$) | Electric Power (MW)
FCCee-0.24 | 0.24 | 8.5 | 0-2 | 13-18 | 12-18 | 280
ILC-0.25 | 0.25 | 2.7 | 0-2 | <12 | 7-12 | 140
CLIC-0.38 | 0.38 | 2.3 | 0-2 | 13-18 | 7-12 | 110
HELEN-0.25 | 0.25 | 1.4 | 5-10 | 13-18 | 7-12 | 110
CCC-0.25 | 0.25 | 1.3 | 3-5 | 13-18 | 7-12 | 150
CERC(ERL) | 0.24 | 78 | 5-10 | 19-24 | 12-30 | 90
CLIC-3 | 3 | 5.9 | 3-5 | 19-24 | 18-30 | ~550
ILC-3 | 3 | 6.1 | 5-10 | 19-24 | 18-30 | ~400
MC-3 | 3 | 2.3 | >10 | 19-24 | 7-12 | ~230
MC-10-IMCC | 10-14 | 20 | >10 | >25 | 12-18 | O(300)
FCChh-100 | 100 | 30 | >10 | >25 | 30-50 | ~560
Collider-in-Sea | 500 | 50 | >10 | >25 | >80 | »1000
17
ITF Report – T.Roser, et al, arXiv:2208.06030

## Slide 18: Factors and Limits
Main factors to consider feasibility of future colliders used to be
  Feasibility of Energy
  Feasibility of Luminosity
  Feasibility of Cost
The European Strategy (2019) and Snowmass’21 discussions revealed additional limits:
  Time to construct and commission
  Societal limits: # of experts, size of facility, radiation, etc
  Environmental impacts: power consumption, carbon footprints, scarcity of resources (He, Nb, W, etc), excavated materials, etc
Here we will only briefly touch some important points

## Slide 19: Limits on Energy
Synchrotron radiation defines linear vs circular if USR < E
for e-/e+:
for muons:
for protons:
;
where is the lifetime, for muons…
requires fast acceleration
for muons
for τ-leptons
Production and survival: unstable particles such as muons
  Circumference 100 km , B<16 T , E <50 TeV
  Circumference 40,000 km, B=1 T, E <1.3 PeV
  Length 50 km , G<0.1 GV/m, E <5 TeV
  Length 10 km, G<1 TV/m, E <10 PeV
Staging efficiency (losses) per stage for M stages ≥
Technology within limited space /area:

## Slide 20: Limits on Luminosity (some)
General Equation
  sheer beam power
  e/p SR rad. power
  μν radiation dose
  LC power, BS, jitter
flux dilution factor

## Slide 21: αβγ vs ITF 30-parameter cost model
ITF Report - Figure 7: Ratio of the estimates of the three-parameters αβγ Model (#2) and Model 3 to the 30-parameter cost Model 1 for future collider projects vs ECM.
ITF Report – T.Roser, et al, arXiv:2208.06030
Higher energy  usually bigger size, more power and higher costs:
  Where is the societal limit on the cost of colliders?
  Cost ranges estimates – detailed vs parametric models
The αβγ cost model (2014): Cost(TPC)= α L1/2 + β E1/2 + γ P1/2
α≈ 2B$/sqrt(L/10 km) for tunnel/civil
β ≈ 10B$/sqrt(E/TeV) for SC/NC RF
β ≈ 2B$ /sqrt(E/TeV) for SC magnets
β ≈ 1B$ /sqrt(E/TeV) for NC magnets
γ≈ 2B$/sqrt(P/100 MW) for site power
αβγ model – V.Shiltsev, JINST 9 T07002 (2014).

## Slide 22: Accelerators Timeline X+Y+Z ≤ ?
Bigger size and cost  longer:
  Pre-project R&D X years
    Depends on novelty
  Construction project Y years
    Annual peak <0.5B$/year ?
    “Oide law”: need ~1 expert to spend (intelligently) 1 M$/year
    NB: <4500 experts worldwide
  Commissioning Z years
    Depends on complexity
    Past large colliders:
    5 yrs
Katsunobu Oide - KEK
+4 (SLC, DAFNE, BEPCII)
-3 (PEP-II, Tevatron-I, LEP-II)
~SQRT(Cost)?

## Slide 23: Construction Time… ~SQRT(Cost)?
Peak spending rate depends on $$/yr limit and on # of available
experts …currently, btw 0.2 to 0.5 B$/yr (total World’s HEP ~4B$)
ITF Report - Figure 11: Construction time for recent large accelerator projects in the US and Europe.

## Slide 24: Circular e+e- Colliders
Let’s skip them… dead end… SR power
E.g. >0.5 TeV ring will be
  Big (>200-300 km?)
  Low luminosity O(10 fb-1/yr)
  A lot of RF  expensive >1.5-2 LHCU

## Slide 25: Circular pp Colliders
Can use Tevatron and LHC as reference point
Parameter sets exist for SSC, FCC-hh, SppC, VLHC, Coll-Sea, Eloisatron, CCMoon
Major advantages:
  known technology and physics
  good power efficiency ab-1/TWh
Major limitations:
  Size (magnetic field B)
  Power
  Beam-beam, burn-off, instabilities
  Synchrotron radiation
  Cost
Texas 90 km
China 100 km

## Slide 26: pp Colliders: Lumi and Cost vs Energy
  Circular pp
7 TeV
70 TeV
700 TeV
70 PeV
10 ab-1/yr
1 ab-1/yr
0.1 ab-1/yr
0.01 ab-1/yr
1 fb-1/yr
7 PeV
B=4.5 T, 6 km, P=0.3 TWh
Cost=~0.5 LHCU
LHC
VLHC
UELN
Globe
Sea
FCC
Tevatron
B=8 T, 27 km, P=1.1 TWh
Cost=1 LHCU
B=16T, 100 km, P=2.5-3 TWh
Cost=3-5 LHCU
ELN
B=10T, 233 km, P=1.5-3 TWh
Cost= 3.8? LHCU
B=3.2T, 1900 km P=>5 TWh
Cost>8 LHCU
B=1T, 40000 km, P> 30 TWh
Cost> 30 LHCU
B=10T, 300 km
P=2-3 TWh
Cost=3-5 LHCU
B=20T, 1600 km, P=10? TWh
Cost > 6 LHCU
B=20T, 11000 km, P> >10 TWh
Cost> 40 LHCU
Collider on Moon

## Slide 27: MC: Lumi and Cost vs Energy
  Circular μμ
1 TeV
10 TeV
100 TeV
10 PeV
MC-1.5
MC-6
MC-14
10 ab-1/yr
1 ab-1/yr
0.1 ab-1/yr
0.01 ab-1/yr
1 fb-1/yr
1 PeV
B=10 T
6 km, Ф=1
P=1.3 TWh
Cost=0.7-1 LHCU
B=10 T, 2.5 km, Ф=1
P=1 TWh
Cost=0.5 LHCU
B=10 T, Ф=1
27(14) km
P=1.5-2TWh
Cost=1-2 LHCU
B=10 T, Ф=10
27 km
P=2 TWh
Cost=1.6-2.5 LHCU
B=10 T, Ф=100
100 km
P=3.5? TWh
Cost=3-5 LHCU
B=10 T, Ф=100
300 km
P=5 ? TWh
Cost=>5 LHCU
B=10 T, Ф=100
1000 km
P=9 ?TWh
Cost=>8 LHCU

## Slide 28: Linear RF and Plasma: Lumi and Cost vs Energy
  Linear ee/γγ
1 TeV
10 TeV
100 TeV
10 PeV
ILC-1
CLIC-3
PWFA-10
10 ab-1/yr
1 ab-1/yr
0.1 ab-1/yr
0.01 ab-1/yr
1 fb-1/yr
1 PeV
40 km
P=1.5 TWh
Cost=1.5-2 LHCU
50 km
P=3 TWh
Cost=2-3 LHCU
LWFA-30
DLA-30
Ult.Plasma-1
Ult.Plasma-0.1
18 km
P=3-4 TWh
Cost=2-5 LHCU
20-50 km
P=6-15? TWh
Cost=4-8 LHCU
30-100 km
P=2.5 TWh
Cost=5-10 LHCU
~200-500 km
P=2.5 TWh
Cost=15-30 LHCU

## Slide 29: Exotic Colliders
Acceleration in structured media, eg CNTs or crystals ( only muons!!! )
Major advantages:
  solid density  1-10 TV/m gradients
  continuous focusing and acceleration (no cells, one long channel, particles get strongly cooled betatron radiation)
  small size promises low cost
Major limitations:
  “blue sky”, O(10) papers, plans for proof-of-principle experiment E336 @FACET-II (S.Corde, T.Tajima, et al)
  how to drive Xtals? lasers, beams?
  Cost is unknown, power is unknown, luminosity - (how low?)
Acceleration in Xtals book (T.Tajima, et al 2020)

## Slide 30: Xtal Collider
1 PeV = 1000 TeV
V.Shiltsev, Phys. Uspekhy 55 965 (2012)
n~1022 cm-3, 10 TeV/m 
n ~1000, nB ~100, frep ~106 L ~1030-32

## Slide 31: XtalC Luminosity
Considerations :
  Angstrom size at IP
  Muons/bunch < Xtal electrons excited
  Employ many channels
  Limit beam power O(10MW)
  Combine n_channels to gain L
  via crystal funnel (? Is it possible)

## Slide 32: Xtal Colliders: Lumi and Cost vs Energy
  Linear Xtal μμ
1 TeV
10 TeV
100 TeV
10 PeV
XC-1
XC-0.1
10 ab-1/yr
1 ab-1/yr
0.1 ab-1/yr
0.01 ab-1/yr
1 fb-1/yr
1 PeV
G=1 TV/m
0.1-1 km
P=< 1TWh
Cost=<1 LHCU?
XC-10
G=1-10 TV/m
0.1-1 km
P=< 1TWh
Cost=<3 LHCU?
G=1-10 TV/m
1-10 km
P=< 2TWh
Cost=<10 LHCU?

## Slide 33: Main Conclusions:
For ultimate high energy colliders:
  Major thrust is Energy
  Major concern/limit is Cost
  Main focus is Luminosity and Power
  There are other important factors (CO2 footprint, etc)
Cost:
  Critically dependent on core acceleration technology
  Existing injectors and infrastructure greatly help
High Energy means low Luminosity :
  Don’t expect more than 0.1-1 ab-1/yr at 30TeV - 1 PeV
  Assume Power limited to 1-3 TWh/yr (1-3 x LHC)

## Slide 34: Main Conclusions (2):
For considered collider types:
  Circular pp – limit is ~100 TeV (14 TeV cme per parton)
  Circular ee – limit is ~0.4-0.5 TeV
  Circular μμ – limit is between 30 and 100 TeV
  Linear RF ee/γγ – limit is between 3 and 10 TeV
  Plasma ee/γγ
  Exotic crystal μμ – promise of 0.1-1 PeV, low Luminosity
Muons are particles of the future
  Helpful/cited references (next slide)

## Slide 35: (Some Useful) References:
ITF Report – T.Roser, et al, arXiv:2208.06030
RMP Colliders – V.Shiltsev, F.Zimmermann, Rev.Mod.Phys. 93, 015006 (2021); see also arxiv
αβγ model – V.Shiltsev, JINST 9 T07002 (2014).
Ultimate Limits of Colliders – V.Shiltsev, Proc. IPAC’21, WEPAB017 (2021).
Nature Physics MC – K.Long, et al, Nature Physics (2021), see also arxiv
Eloisatron – W.Barletta, in AIP Conference Proceedings, vol. 351, no. 1, pp. 56-67(1996).
Xtal collider – V.Shiltsev, Physics Uspekhi, v.55 (10), p.1033 (2012).
F.Zimmermann – NIMA 909 (2018): 33-37; see also ARIES Workshops summary
T.Raubenheimer - Phys. Rev. ST Accel. Beams 3, 121002 (2000).
D.Schulte Plasma Colliders – Rev.Accel.Sci.Tech. 9 (2016): 209-233.
2019 Crystal Workshop - eds. T.Tajima, et al, Beam Acceleration in Crystals and Nanostructures (World Scientific, 2020)
CPT-theorem – V.Shiltsev, Mod. Phys. Lett. A, vol. 26, No. 11 (2011) pp. 761-772.

## Slide 36
Special thanks to
  My AF co-conveners S.Gourlay and T.Raubenheimer, and AF3 conveners - Angeles, Qing Qin, Frank Z and Georg H.
  Marica and Organizers of the eeFACT’22 Workshop
… as final note, tons of material (all reports, etc) available at:
https://snowmass21.org/accelerator/start
Thanks for your attention!

## Slide 37
Back up slides