## Slide 1: EIC MDI & IR Magnet Design
Holger Witte
Head Magnet Systems, L3 IR
eeFACT 2022
September 13th 2022

## Slide 2: EIC IR: Overview
Forward
Rear
Hadron storage ring (HSR): 4 yellow and 2 blue RHIC arcs
Add electron storage ring (ESR) in existing tunnel (and the RCS)
IR location: IR6

## Slide 3: EIC IR: Forward Direction
Interleaved magnet scheme
  Adding magnets is challenging
Why are these magnets difficult?
  Required field
  Aperture
  Geometric constraints
Hadron forward magnets: collared magnets
  Large apertures: physics
Electron forward magnets/B0pF: direct wind magnet
All magnets NbTi, 2K (Q0eF: 4K)
Two cryostats
Name | R1 | length | B | grad | B pole
 | [m] | [m] | [T] | [T/m] | [T]
B0ApF | 0.043 | 0.6 | -3.3 | 0 | -3.3
Q1ApF | 0.056 | 1.46 | 0 | -72.608 | -4.066
Q1BpF | 0.078 | 1.61 | 0 | -66.18 | -5.162
Q2pF | 0.131 | 3.8 | 0 | 40.737 | 5.357
B1pF | 0.135 | 3 | -3.4 | 0 | -3.4
IP
Cryostats
Name | R1 | length | B | grad | B pole
 | [m] | [m] | [T] | [T/m] | [T]
Q0eF | 0.025 | 1.2 | 0 | 13.5 | 0.4
Q1eF | 0.063 | 1.61 | 0 | 8.1 | 0.5
Electrons
Hadrons

## Slide 4: Hadron Forward - Apertures
To optimize aperture: magnets tilted and displaced
Verified with two codes
  BMAD – general purpose tracking code
  Geant4 (friends from Physics)
B0pF
B1ApF
pt=1.3GeV
Generate cone for particles with pt=1.3GeV
Rendered in CAD program with magnet apertures
Neutron cone

## Slide 5: EIC IR: Rear Direction
2-in-1 magnets
  Common yokes
Main issue: space between magnets
  Crossing angle
Large aperture due to synrad fan
  Comes from low-beta quads
All magnets NbTi, 4.2K
All magnets direct wind
Three cryostats
Name | R1 | R2 | length | grad | B pole
 | [mm] | [mm] | [m] | [T/m] | [T]
Q1ApR | 20 | 26 | 1.8 | 78.4 | 2.0
Q1BpR | 28 | 28 | 1.4 | 78.4 | 2.2
Q2pR | 54 | 54 | 4.5 | 33.8 | 1.8
Name | R1 | R2 | length | B | grad | B pole
 | [mm] | [mm] | [m] | [T] | [T/m] | [T]
Q1eR | 66 | 79 | 1.8 | 0 | 14 | -1.1
Q2eR | 83 | 94 | 1.4 | 0 | 14.1 | 1.3
(B2eR) | 97 | 139 | 5.5 | 0.2 | 0 | 0.2
B2AeR | 90.45 | 90.45 | 2.0 | 0.192 | 0 | 0.192
B2BeR | 111.45 | 111.45 | 3.45 | 0.238 | 0 | 0.238
Cryostats
IP
B2eR: split into two magnets, not shown in figure
Electrons
Hadrons

## Slide 6: IR Magnets – Fabrication Techniques
10 Direct Wind Magnets (S-MD)
Patterns: serpentine and CCT
5 Collared Magnets
1 Special Magnet (also direct wind)
Three groups of superconducting magnets
  All NbTi

## Slide 7: B0pF Forward Spectrometer
Beams share magnet aperture
  Hadrons: 1.3T field
  Electrons: 14T/m gradient
Implementation: combined function magnet
  Large aperture quadrupole; zero field axis shifted with dipole
Space constraints/large aperture
  Requires 2K
Courtesy of B. Parker (BNL)
Courtesy of
K. Hamdi (BNL)
Electron Coils
Hadron Coils
Common Yoke

## Slide 8: Hadron Forward Cable Magnets Status
Re-design for 2K
  4K did not converge
  Better margins
  Risk reduction
New cable geometry: LHC style, 15mm wide
  Two keystones
  Similar to LHC cable
  28 strands
2D work complete
  3D work ongoing
  Structural analysis
15.1mm
1.984mm
1.816mm
15.1mm
2.01mm
1.79mm

## Slide 9: 2D Cross-Sections
2D cross-sections for all collared magnets
Sufficient field quality and temperature margin at 2K
Iron yoke – magnetization management
Q2pF
Q1ApF
Q1BpF
B1pF
B1ApF
Courtesy of BNL SMD

## Slide 10: 3D Designs
Preliminary designs for all magnets
  Minimized peak field in ends
  Good harmonics
Sufficient margin (>30%)
B1pF
B1ApF
Q1BpF
Courtesy of BNL SMD

## Slide 11: Direct Wind Magnets - Status
Preliminary magnet designs complete
Recent changes
  B2eR split into two magnets to optimize magnet aperture/cost
  B0pF length reduction
Implementation of correctors
B2AeR
B2BeR
2m
3.45m
Q2pR
Courtesy of B. Parker (BNL)

## Slide 12: Detector Solenoid Compensation
Need four skew quadrupole magnets
  0.6T/m over 1.8m (assuming 3T solenoid)
Possible locations
  Hadrons: B0ApF, Q1ApR
  Electrons: Q1eF, Q1eR
    Q0eF: technically possible, but cuts into acceptance

## Slide 13: B0ApF – Corrector Dipole
Normal dipole
4 layers skew dipole
2 layers skew quadrupole
Wire dia: 0.25mm
B0ApF: 1.55mm dia
Horizontal corrector, 3.3T, 0.6m long
  Reason: B0pF is fixed field magnet
  Different energies: different orbits
  B0ApF and B1(A)pF: same orbit
Also: vertical corrector
  Detector solenoid compensation
Also: possible location for skew quadrupole
He space

## Slide 14: Skew Quad, Hadron Forward
Normal dipole
Implementation: CCT
  Serpentine pattern could be more efficient
Sufficient margin for all multipoles at 2K
Lower detector solenoid field: margins will increase
Skew dipole
Skew quad

## Slide 15: Q1ApR/Q1eR Tapered Quads
Tapered CCT FF quadrupole magnets
Clear apertures
  Q1eR: IR 47.6... 55.7 mm
  Q1ApR: IR 20…26 mm
Gradient
  Q1ApR: 78T/m
  Q1eR: 14T/m
Harmonics: <0.25 units
Q1ApR
Q1eR
Q1eR
Normal harmonics
Q1eR
Skew harmonics

## Slide 16: Progress – Integration to IR
IP magnets & ancillary detectors fully simulated in GEANT including all beam effects
developed software for proto-collaborations to account for crossing angle and other beam effects in MC
to be published http://www.eicug.org/web/sites/default/files/Accelerator_and_beam_conditions_critical_for_EIC_simulations.pdf
Courtesy of E. Aschenauer & group (BNL)
PbWO4
PbSi
PbScint
ECAL
HCAL

## Slide 17: Synchrotron Radiation
Extensive simulations of SR by dedicated working group
  Including photo desorption
  SR photon spectrum provided to collaborations
Two separate codes with good agreement
  Synrad3D
  SYNC_BKG (Mike Sullivan)
Focus on
  Central chamber
  Lumi window
  Polarimeter
  Heat loads inner IR
  Spin rotators/crab cavities
Courtesy of C. Hetzel (BNL) / M. Sullivan (SLAC)

## Slide 18: Collimators
IR2 - Horizontal
IR4 – Vertical
ESR
  Planned in IR2 & 4
  2-sided prim. + 2 sec. for cleaning and flexibility with phase advances and optics
Courtesy of A. Drees (et. al.)

## Slide 19: Overview
Sector 12 H Momentum Collimation (D7 ‘dummy’)
IR12 e Injection absorbers
IR4 e Vertical + Momentum Collimation
IR2 e Horizontal Collimation
& Abort System
H Injection protection
(note: not actual inj. location)
electron : 6+1 collimators
Hadrons : 6+1 collimators
+absorbers and masks
Sector 12 H Betatron Collimation (both planes)
Hadron Abort System (already there)
Masks
Collimator efficiency tracking studies ongoing

## Slide 20: Summary
IR design is mature
Collared magnets: preliminary design complete
  2D/3D
  2K operation
Most magnets: direct wind manufacturing technique
  Preliminary designs complete
  Including corrector magnets into designs
Synchrotron radiation
Detector integration
Collimator design progressing

## Slide 21: Acknowledgements
BNL
J. Adam, M. D. Anerella, E.C. Aschenauer, J. Avronsart, A. Ben-Yahia, J.S. Berg, M. Blaskiewicz, A. Blednykh, W. Christie, J. Cozzolino, A. Drees, D. Gassner, K. Hamdi, C. Hetzel, H.M. Hocker, D. Holmes, A. Jentsch, A. Kiselev, P. Kovach, M. Kumar, F. Kurian, H. Lovelace III, Y. Luo, G. Mahler, A. Marone, G. McIntyre, C. Montag, R.B. Palmer, B. Parker, S. Peggs, S. Plate, V. Ptitsyn, G. Robert-Demolaize, J. Rochford, C. Runyan, J. Schmalzle, K.S. Smith, S. Tepikian, R. Than, P. Thieberger, J. Tuozzolo, F.J. Willeke, H. Witte, Q. Wu, Z. Zhang
JLAB
M. Stutzman, R. Gamage, P. Ghoshal, T. Michalski, W. Wittmer
SLAC
M. Sullivan, Y. Nosochkov, A. Novokhatski
ORNL
V. Morozov
… and many more!

## Slide 22: Additional Slides

## Slide 23: Forward Hadron Magnets
 | Length | IR1 | Pole tip field R1 | Dipole Field | Gradient
 | m | cm | T | T | T/m
B0pF | 1.2 | 17 |  | -1.3 | 
B0ApF | 0.6 | 4.3 |  | 3.3 | 
Q1ApF | 1.46 | 5.6 | 4.07 | 0 | -77.903
Q1BpF | 1.61 | 7.8 | 5.16 | 0 | -63.028
Q2pF | 3.6 | 11.3 | 5.36 | 0 | 39.736
B1pF | 3 | 13.5 |  | 3.4 | 
B1ApF | 1.5 | 16.8 |  | 2.7 | 
IR1: inner radius (= clear aperture) at coil beginning
Pole tip field R1: IR1*gradient
Collared coils, apart from B0pF and B0ApF (direct wind)

## Slide 24: Forward Electron Magnets
 | Length | IR1 | IR2 | Pole tip field R1 | Pole tip field R2 | Gradient
 | m | cm | cm | T | T | T/m
Q0eF | 1.2 | 2.5 | 2.5 | 0.4 | 0.4 | 13.5
Q1eF | 1.61 | 6.3 | 6.3 | 0.5 | 0.5 | 8.1
All direct wind coils
IR1: inner radius (= clear aperture) at coil beginning
IR2: inner radius (= clear aperture) at coil end
Pole tip field R1: IR1*gradient
Pole tip field R2: IR2*gradient

## Slide 25: Rear Hadron Magnets
 | Length | IR1 | IR2 | Pole tip field R1 | Pole tip field R2 | Gradient
 | m | cm | cm | T | T | T/m
Q1ApR | 1.8 | 2.0 | 2.56 | 1.56 | 2. | 78
Q1BpR | 1.4 | 2.8 | 2.8 | 2.184 | 2.184 | 78
Q2pR | 4.5 | 5.4 | 5.4 | 1.84 | 1.84 | 34
IR1: inner radius (= clear aperture) at coil beginning
IR2: inner radius (= clear aperture) at coil end
Pole tip field R1: IR1*gradient
Pole tip field R2: IR2*gradient
All direct wind coils
Q1ApR: tapered

## Slide 26: Rear Electron Magnets
 | Length | IR1 | IR2 | Pole tip field R1 | Pole tip field R2 | Dipole Field | Gradient
 | m | cm | cm | T | T | T | T/m
Q1eR | 1.8 | 4.76 | 5.57 | 0.67 | 0.78 | 0 | 14
Q2eR | 1.4 | 6.43 | 6.43 | 0.91 | 0.91 | 0 | 14.1
B2AeR | 2.0 | 90.45 | 90.45 | 0.192 | 0.192 | 0.192 | 0
B2BeR | 3.45 | 111.45 | 111.45 | 0.238 | 0.238 | 0.238 | 0
IR1: inner radius (= clear aperture) at coil beginning
IR2: inner radius (= clear aperture) at coil end
Pole tip field R1: IR1*gradient
Pole tip field R2: IR2*gradient
All direct wind coils
Q1eR: tapered double-helix coil

## Slide 27: Abort systems: HSR & ESR
ESR:
Plan to use an unused spectrometer tunnel in IR2 which will allow extracting the 300-kJ beam away from other IR2 users. It features 6 x 2-mrad vertical kickers, a 2° Lamberton magnet & a 50m-long transfer line with 6 warm quads.
HSR:
The plan is to keep the current RHIC system w. necessary upgrades
27
27
Top view
Lambertson magnet
kickers
dump

## Slide 28: Forward Side, Two Cryostat Layout
B0 Cryostat Inside Detector Hall
Forward Cryostat Inside Tunnel

## Slide 29: Hadron Forward - Apertures
275 GeV
41 GeV
100 GeV
Magnet aperture optimization:
Magnets tilted and displaced
Magnets split in two (e.g. Q1A and Q1B)
275 GeV
41 GeV
100 GeV
275 GeV +1.3 GeV px
275 GeV -1.3 GeV px

## Slide 30: Q1ABpF – New Magnet Concept
275 GeV
41 GeV
100 GeV
275 GeV +1.3 GeV px
275 GeV -1.3 GeV px
New magnet – Q1ABpF
Advantages: No end plates, making use of additional space between magnets
Smaller aperture at IP side
Recombining Q1ApF and Q1BpF

## Slide 31: Q1ABpF: Implementation
Q1ABpF
Q1eF
R=50mm
CCT
  Allows to cancel unwanted harmonics
  Modulation of gradient
Frontloading of gradient
Helps crosstalk / field quality
  Better utilization of space
  Can tailor maximum gradient
Challenges
  Need to prove that this works mechanically
  No collar
100 → 50 T/m
J1
J2
JΣ

## Slide 32: Mechanical Analysis
Ongoing work
  2D/3D
Modeling details 3D
  Opera 3D: Forces
  CATIA: Geometry and fill
  COMSOL: Structural analysis
  Complexity: 1TB RAM
COMSOL 2D
  Contact elements
  Pre-stress, cooldown and Lorentz force

## Slide 33: Tapered Double Helix Magnet
Tapered double helix demonstrator
4 layer coil, NbTi, 4.2K
  Aperture: 60..80mm
  L=0.4m
Tested successfully 7/16/2020
  40 T/m, no quench up to short sample
Constant gradient despite taper
H. Witte et al. http://dx.doi.org/10.1109/TASC.2019.2902982
940A/0.6mm2=1567A/mm2

## Slide 34
Different constraints:
  Different loss behavior for protons/ions
  Cold ring requires good cleaning efficiency in the arcs
  More flexibility on the optics
We can benefit from RHIC and LHC experience.
Planned in IR12 :
  issues with other users due to radiation
  switchyard doubles the second secondary
  Real estate
Momentum collimators are planned for the sector 12 ”D7” dummy.
  Requires cryo-bypass!
Courtesy of G. Robert-Demolaize
HSR Collimators