## Slide 1: Beam Physics Frontier Problems in 25 minutes
Frank Zimmermann
eeFACT’22 ICFA Workshop
13 September 2022
many thanks to Prof. Jie Gao and the Program Committee

## Slide 2
synchrotron radiation
bending magnetic field
accelerating gradient
(rare) particle production – e+ and m
cost and sustainability
exploring novel directions
major beam frontier challenges

## Slide 3
challenge #1: synchrotron radiation (SR)
energy loss per
particle per turn
SR power
e±: 23 MW for LEP (former e+e- collider in the LHC tunnel),
100 MW for FCC-ee (imposed as design constraint),
protons: 0.01 MW for LHC,
5 MW for FCC-hh – this requires >100 MW cryoplant power
circular colliders
L. Rivkin

## Slide 4
SR in the arcs: possible mitigations (challenge #1)
mitigations:
large bending radius r
  → large circular collider
linear collider
  - ”almost” no arcs, but beamstrahlung
muon collider
- m 200 heavier than e± → 109x less radiation
at same energy and radius, but m’s decay
shaping beam vacuum chamber or the beam itself
- tiny vacuum chamber in large ring, with d: pipe diameter
- beam shaping to suppress radiation; a DC beam does not radiate!
explored in EU projects ARIES & I.FAST
→ next slide
→ next next slides
→ later
→ later

## Slide 5
365 GeV c.m.
↔
100 km
cost-optimized
circumference
SR → size of circular e+e- colliders (challenge #1)
Data points from
S. Myers, “FCC - Building on the Shoulders of Giants”,
submitted to EPJ+ (2021)
B. Richter, “Very High Energy Electron-Positron Colliding Beams for the Study of Weak Interactions”, NIM 136 (1976) 47-60
Serendipitously, 90-100 km is exactly the size required for a 100 TeV hadron collider and optimum tunnel size in the Lake Geneva basin !
circular colliders

## Slide 6
SR → linear collider beam delivery (challenge #1)
linear colliders
Historical footprints of CLIC 3-TeV and 500-GeV beam delivery systems (M. Aleksa et al., 2003, CLIC-Note-551 )
SR in bending magnets caused a factor 2 loss in luminosity in 2003 CLIC BDS design at 3 TeV; similarly for the SLC at 91 GeV c.m. (!)
SR in bending magnets of the beam-delivery system
SR in final quadrupole magnet
(“Oide effect”) limits collision spot size
Other footprints of CLIC 3-TeV and 500-GeV beam delivery systems (G. Zamudio, R. Tomas, 2011, CLIC-Note-882 )
K. Oide, Phys. Rev. Lett. 61, 1713 (1988)
g
final quadrupole lens
e-
e-
beam delivery tunnel should be compatible w. future beam energies

## Slide 7
challenge #1: synchrotron radiation - cont’d
linear colliders
synchrotron radiation in the strong field of the opposing beam (=“beamstrahlung”) degrades the luminosity spectrum
H. Abramowicz, et al
- arXiv:1807.02441
CLIC at 380 GeV: 60% of total luminosity within 1% of target energy
CLIC at 3 TeV: only 33% of total luminosity within 1% of target
e+e- collisions in linear colliders lose their distinct energy precision
D. Schulte

## Slide 8
suppressing synchrotron radiation: shaping the beam?
DC beam does not radiate
suppression of shot noise and reduced radiation demonstrated at SLAC NLCTA, D. Ratner et al., PRST-AB 18, 050703 (2015)
1 D crystalline beam (acceleration by induction acceleration)?
Synchrotron radiation of crystallized beams, Harel Primack and Reinhold Blümel, Phys. Rev. E 60, 957 (1999)
N~106
particles uniformly
distributed
→
factor 50 reduction
in total SR power

## Slide 9
suppressing synchrotron radiation: tailoring boundary?
tailoring the boundary
large bending radius + small chamber size provide shielding
  - effect seen at RHIC
HTS coating for small (mm/micro/nano-) chamber?
hollow channel shield?
Examples:
h=w=1 cm, r=1 km → l >600 nm (2 eV)
h=w=1 mm, r=10 km → l >0.6 nm (2 keV )
h=w=0.1 mm, r=10 km → l >2 pm (600 keV )
h: full chamber height
w: full chamber width
r: bending radius
N. P. Abreu et al.,
EPAC’08
first experimental evidence for suppression
of incoherent synchrotron radiation,
above plasma frequency: index of refraction < 1 : phase velocity
of light > 1 suppression of
synchrotron emission
“Razin-Tsytovich effect”
SR suppression in plasma

## Slide 10
challenge #2: bending magnetic field
Record fields attained with dipole magnets of various configurations and dimensions, and either at liquid (4.2 K, red) or superfluid (1.9 K, blue) helium temperature.
Nb-Ti
Nb3Sn
Superconducting wire critical current density versus magnetic field.
Nb-Ti
Nb3Sn
HTS
L. Bottura
P. Lee
→ hadron collider energy reach

## Slide 11
US – MDP: 14.5 T magnet tested at FNAL
15 T dipole demonstrator
Staged approach: In first step pre-stressed for 14 T
Second test in June 2020 with additional pre-stress reached 14.5 T
60-mm aperture
4-layer graded coil
84% on the laodline at 1.9 K
92% on the loadline at 4.2 K
cosq dipole

## Slide 12
CERN Nb3Sn progress: FRESCA2 & eRMC
Block dipoles
FRESCA2 (4-decks, 100 mm), 14.6 T
RMC/eRMC (2-decks, no aperture), 16.5 T
Luca Bottura

## Slide 13
Chart: Bore field (T)
| 9 | 12 | 12 | 13.7 | 14.6
 | 18590 | 33 | 182.4 | 2.46 | 1
Exploration of new concepts and technologies
Development of robust and cost-efficient processes
HL-LHC 11T
Fresca2
MDPCT1
LHC
HTS
Robust Nb3Sn
D20
HL-LHC QXF
Ultimate Nb3Sn
Logical step for a next phase (2027-2034)
High-Field Magnets - R&D Program Goals
Luca Bottura

## Slide 14
Nuclear Fusion Magnet R&D Progress
September 2021
HTS material:
REBCO
toroidal model coil
important synergies with magnet development for fusion projects

## Slide 15
challenge #3: accelerating gradient
RF Accelerators
> 30,000 operational – many serve for Health
30 million Volt per meter
RF: 90 years of success story for society
Plasma Accelerators
first user facility to be realized
100,000 million Volt per meter
Added value
new RI’s due to compactness and cost-efficiency
bringing new capabilities to science, institutes, hospitals, universities, industry, developing countries.
400 m
60* m
*realistic design including all required infrastructure for powering, shielding, …
R. Aßmann
Gradient growth Superconducting RF linac accelerating gradient achievements and applications since 1970. CERN Courier 2020
R. Geng

## Slide 16
High-Gradient Acceleration (Plasma/Laser)
R. Assmann

## Slide 17
plasma acceleration of positrons ? (required for e+e- collider)
“ballistic injection”: a ring-shaped laser beam and a coaxially propagating Gaussian laser beam are employed to create donut and center bubbles in the plasma, resp.
Z.Y. Xu

## Slide 18
challenge #4: particle production – e+, m
required for top up
routinely
achieved
being
commis-
sioned
positron rates [1010e+/s]
required at IP
Lemma scheme
>1016 e+/s
muon rates [105m/s]
existing
required for
m collider
x100
x10,000
x1000
> x100,000

## Slide 19
failure of SLC e+ target after 5 years of operation (challenge #4)
SLC target analysis at LANL: Failed SLC positron target was cut into pieces and metallographic studies were carried out to examine level of deterioration of material properties due to radiation exposure.
even achieving SLC e+ rate is not trivial

## Slide 20
particle production: Gamma factory (challenge #4)
resonant scattering of laser photons off partially stripped heavy-ion beam in LHC (or FCC): high-stability laser-light-frequency converter
proposed applications:
intense source of e+ (1016-1017/s) , m (1011-1012/s), p, etc. – sufficient for LEMMA type m collider
doppler laser cooling of high-energy beams
HL-LHC w. laser-cooled isocalar ion beams
Pb+81 beam lifetime
38 hours (and first electrons in the LHC…)
W. Krasny
Gamma Factory could provide e+ rate required for LEMMA m collider

## Slide 21
1.6x109 x less SR than e+e-, no beamstrahlung problem
two production schemes proposed
m‘s decay within a few 100 - 1000 turns:
→ rapid acceleration
(perhaps plasma?)
→ n radiation hazard
(limits maximum m energy)
US-MAP (2015) p-driven
Italian LEMMA (2017) e+-annihilation
needs large 45 GeV e+ ring like FCC-ee, possible upgrade path to FCC-mm
solution beyond 10 TeV unclear
Bruce King 1999
Muon Collider schemes & challenges

## Slide 22
post FCC-ee option: feeding 14 TeV m collider
F. Zimmermann 2018 J. Phys.: Conf. Ser. 1067 022017
P. Raimondi, M. Antonelli, M. Boscolo.
M. Antonelli, et al., NIM A 807, 101 (2016)
M. Boscolo et al., PRAB 23, 051001 (2020)

## Slide 23
after FCC-hh: FCC-mm, a 100 TeV m collider?
F. Zimmermann 2018 J. Phys.: Conf. Ser. 1067 022017
PSI: partially stripped ion (“Gamma Factory”)
https://arxiv.org/abs/1511.07794
W. Krasny,

## Slide 24
simulated of plasma target response for FCC-mm
Transverse profiles of the plasma electron density as the positron bunch passes through the plasma, simulated with LCODE (K.V. Lotov) for the initial bunch distribution. The mean density over different distances behind the head of the beam are shown over a radial distance of up to 100 𝜇m from the beam (a) and a zoom over 1 𝜇m around the beam (b).
Electron density at the entrance of the plasma as a function of radial position for different time steps, simulated by RFTRACK, with only positron fields acting on electrons; during 3.3 ps the positron bunch advances by 1 mm.
J. Farmer
A. Latina
energy loss mechanisms inside the plasma ?
F. Zimmermann et al., Proc. IPAC’22, p. 1691

## Slide 25
challenge #5: cost / sustainability
total cost Ecm0.28
P. Lebrun, RFTech 2013
1959
1971
2008
cost per collision energy greatly reduced
new
concepts
and
new
technologies

## Slide 26
more efficient RF power sources
more efficient SC cavities
twin aperture dipoles for FCC-ee
A. Grasselino
I. Syratchev
A. Milanese
CCT HTS quadrupoles & sextupoles for FCC-ee
M. Koratzinos
“green” energy efficient technologies

## Slide 27
Energy Recovery Linacs (ERLs) – Landscape
ERL Panel
V. Litvinenko, T. Roser, M. Chamizo
test Facility PERLE at IJClab
(high current, multi-turn)
would complement MESA, CBETA,
bERLinPRO and EIC cooler
M. Klein, A. Hutton, et al.

## Slide 28
Possible Future Colliders based on ERLs
A. Hutton, M. Klein
cost, power & feasibility of ERLC & CERC
being analysed by expert sub-panel

## Slide 29
Maury Tigner, “A Possible Apparatus for Clashing-Beam Experiments”, Nuovo Cimento 37, 1228 (1965)
Ugo Amaldi, “A possible scheme to obtain e-e- and e+e- collisions at energies of hundreds of GeV”, Physics Letters B61, 313 (1976)
early linear-collider proposals
these early proposal always
recovered the energy of the spent beam!
reappraisal of historical ERL collider proposals
300 GeV c.m.
1-6 GeV c.m.

## Slide 30
V. Shiltsev
protons per pulse
challenge
power efficiency challenge
Fermilab & J-PARC Power Upgrades
efficiency and upgrade of super-beam facilities

## Slide 31
challenge #6: exploring novel directions
J. Beacham, F. Zimmermann, 2022 New J. Phys., https://doi.org/10.1088/1367-2630/ac4921
Very large hadron collider on the Moon (CCM), 11 Mm, Ec.m.14 PeV (1000x LHC’s), 6x105 dipoles with 20 T field, either ReBCO, requiring ~7-13 k tons rare-earth elements, or IBS, requiring a million tons of IBS. Many of the raw materials required to construct machine, injector complex, detectors, and facilities can potentially be sourced directly on the Moon. 11000-km tunnel a few 10 to 100 m under lunar surface to avoid lunary day-night temperature variations, cosmic radiation damage, and meteoroid strikes. Dyson band or belt to continuously collect sun power. Required: <0.1% sun power incident on Moon surface.

## Slide 32
storage rings as tools to detect or generate gravitational waves
J. Ellis et al (2021), https://arxiv.org/abs/2105.00992
ARIES workshop 2021
Accelerators meet gravitational waves – CERN Courier
Sources and sensitivities GW sources (shaded) and detector sensitivities (lines), incl. space-based interferometer LISA, ground-based LIGO and Einstein Telescope. Accelerator-based detection methods and sources are superimposed based on optimistic assumptions.
challenging, but maybe not hopeless -
note: earlier studies in 1980’s and 90’s, e.g.
G. Diambrini Palazzi, D. Fargion, P. Chen, D. Zer-Zion,
J. Van Holten, H. Schmickler, A. Jansson, M. Lindroos,...

## Slide 33
Tusculanae Disputationes, 45 BC: series of dialogues that take place during five days at Cicero’s villa at Tusculum (now the town of Frascati near Rome) – Might the Frascati eeFACT’22 proceedings (5 days of talks!) become equally famous?!
Marcus Tullius Cicero,
106-43 BC
This is the place to make progress !