## Slide 1
IR Optics design for the FCC-ee
s-channel monochromatization scheme
H. Jiang A. Faus-Golfe, F. Zimmermann, K. Oide, Z. Zhang
15 September, 2022
IJCLAB IN2P3-CNRS

## Slide 2: Outline
Introductions
The trade-off between energy spread and luminosity
The standard FCC-ee IR Optics design
The IR optics for the monochromatization scheme
The continuing optimization of the mono-scheme

## Slide 3: Introduction: FCC-ee collider
FCC-ee modes:
  The FCC-ee standard modes:
    Four different energy operation modes:
    Z, WW,H(ZH) and ttbar
  The optional fifth mode: s-channel Higgs production mode
    The measurement of the electron Yukawa coupling, in dedicated runs at 125 GeV with center-of-mass (CM) energy spread(5-10 MeV). But the natural collision energy spread, due to the synchrotron radiation, is about 50MeV.
Requirements:
  reduce the CM energy spread from 50MeV to 5MeV, which is comparable to the resonant width of the standard model Higgs Boson itself (4.2MeV) [1]
[1]Abada, A., Abbrescia, M., AbdusSalam, S.S. et al. FCC-ee: The Lepton Collider.
2 IPS

## Slide 4: FCC-ee Parameters (including s channel mode)
FCCWEEK22, K. Oide, D. Shatilov

## Slide 5: The transverse monochromatic scheme
The transverse monochromatic scheme(Guinea-Pig simulation results)
Monochromatization:
D*x=±0.2m
c.m. Energy spread
6.9MeV
Standard:
D*x=0
c.m. Energy spread
46MeV

## Slide 6: Example IP parameters for monochromatization scenario for FCC-ee
The example IP parameters and performance for typical monochromatization scenario for FCC-ee
The correlation D*x and Mono-factor |  |  |  | 
 | ±0.1m | ±0.2m | ±0.3m | ±0.4m
 | 3.6 | 7.0 | 10.4 | 13.9
The correlation D*x and Mono-factor |  |  |  | 
 | ±0.1m | ±0.2m | ±0.3m | ±0.4m
 | 3.6 | 7.0 | 10.4 | 13.9
The monochromatization factor:

## Slide 7: The trade-off between luminosity and center-of-mass energy spread
The monochromatic scheme reduces the c.m. energy spread but decreases the luminosity.
Guinea-pig simulations:
The relationship between luminosity and c.m. energy spread for different
Dx*= 0.1, 0.2, 0.3, 0.4m
The initial beam distribution:
Generated by mathematica with parameters shown in FCC-ee parameters table and different Dx*

## Slide 8: The trade-off between luminosity and center-of-mass energy spread
Dispersion | 0.1m | 0.2m | 0.3m | 0.4m
RMS energy spread with crab cavities | 12.8 MeV | 6.9 MeV | 4.6MeV | 3.6 MeV
RMS energy spread without crab cavities | 30.6 MeV | 21.1MeV | 14.8MeV | 11.6MeV
Luminosity(1035cm-2s-1) | 2.6 | 1.25 | 0.84 | 0.63
Monochromatization factor | 3.3 | 6.1 | 9.1 | 12
The relationship between dispersion and luminosity and c.m. energy spread
Significance(left) and associated upper limits contours on the electron Yukawa ye. (Right) in the c.m. energy spread vs. integrated luminosity[1]

## Slide 9: FCC-ee Standard IR optics design
FCC-ee IR geometry
Crossing angle:30mrad

## Slide 10: The baseline S-channel standard IR Optics
The asymmetric Standard mode IR Optics (from dispersion-free to dispersion-free region)

## Slide 11: The Preliminary IR Optics for transversal mono-schemes
Before the Interaction Point: D*x=±0.1m After the Interaction Point:

## Slide 12: Next steps
Dx* scanning and limits
Redesign and Correction of local chromaticity correction (LCC system)
Beam dynamic aperture (DA) analysis
Beam-beam effects

## Slide 13: Thanks for your attention!
Bled lake, Slovenia
e+
e-