## Slide 1: Timepix Neutron Beam Monitor at nTOF
In 2018 a beam monitor based on 2 Quad Timepixes
has been installed in nTOF EAR1
It as been used for the beam alignment and will be used for flux measurements in 2021
We propose to realize a second system in EAR2 for beam alignment
Beam image
nTOF EAR1

## Slide 2: Borated GEM: multiborated head-on converter
In three years several attempts have been made in collaboration with Milano Bicocca, CERN and ESS Liopking
and now a new etching and Boron deposition procedure has been defined
The borated GEM was proposed for the first time by Cascade project
but problems on boron deposition stability
and GEM reliability.
We are assembling a detector for the first characterization.
Good prospective for high efficiency thermal neutron imaging for nTOF.

## Slide 3: Borated GEM for high efficiency thermal neutrons detector
The GEMPix detector allows to develop and optimize a new thermal neutron detector based on GEM technology.
A collaboration between CERN ESS INFN has recently develop a new procedure to realize borated GEM.
A detector efficiency 7 times the single foil has be reached on a uniform big surface (3x3 cm2)
with high time (10 ns) and spatial resolution (50 mm) with Timepix electronics.
F.Murtas, R.De Oliveira, C.Lai, G.Croci, A.Muraro

## Slide 4: Production of 10 Borated GEM foils 10x10 cm2
10 GEM foils (10x10 cm2) have been borated
in Sweden on February 15th
They are at CERN ready for
the final etching (Rui’s Laboratory)
Two detectors we’ll be built in Frascati
before September.
Electronics readout ready :
- 256 pads 6x6 mm2
- Gemini32 boards and FPGA board

## Slide 5: Financial requests
1 FTE
50 % FM
20 % Tonino Pietropaolo ENEA
30 % Gerardo Claps ENEA
Financial requests :
9 Keuro Beam Monitor (for 2 quad Timepix, 2 readout system, 2 movable stage)
6 Keuro Thermal neutron detector for new 10x10 cm2 Borated GEM
Missions :
5 Keuro for installations and collaboration meetings
LNF Facility : clean room