## Slide 1: Simulation of 4He events @ 700 MeV/u
Milano group

## Slide 2
In view of the call of GSI BioPac for 2021/2022 beam time, FOOT we are reiterating and improving the proposal already presented in 2017.
One of the major points is to apply for ion beams which are difficult to obtain outside GSI: in particular 4He and 16O.
The case of 4He 0.7 GeV/u is considered for space radioprotection
Motivations (see slides from Meeting of March 4th)

## Slide 3
Using 4He projectiles, the only final state channels (excluding target fragmentation) are:
n + 3He + X’
p + t + X’
d + d + X’
n + p + d + X’
n + n + p + p + X’
4He + X*
X* → X + g
X* → target fragm. channels
4He + X →
Favourable case study for both Z & A identification
Maximum overlap of ECC and Electronic Apparatus
~as many 3He as t are expected
Physics Channels (see slides from Meeting of March 4th)

## Slide 4: Proposed Geometry
Longer level arm to allow a better resolution for ToF measurement.
The higher energy also allows a narrower angular cone to contain secondary products.
In view of a run at GSI Cave A, the same Taget-TW distance used in GSI 2019 has been considered
shift of TW+Calo to compensate for bending
Setup produced within SHOE master branch using –exp HE_MC
180.25 cm
Also a small shift in the non-bending view to avoid particles sailing through the space between crystals
C target
5 mm

## Slide 5: Compensation for bending
As expected, at this energy, calorimeter cannot achieve full containment. Furthermore, hadronic showering takes place
In geomaps/HE_MC/FOOT_geo.map:
TofWallBaseName: "TW"
TofWallPosX: 5.5 TofWallPosY: 0.5 TofWallPosZ: 180.25
TofWallAngX: 0. TofWallAngY: 0. TofWallAngZ: 0.
CaloBaseName: "CA"
CaloPosX: 5.5 CaloPosY: 0.5 CaloPosZ: 194.55
CaloAngX: 0. CaloAngY: 0. CaloAngZ: 0.

## Slide 6: Transv. view

## Slide 7: Simulated Data (FLUKA pro Version 2020.0)
/gpfs_data/local/foot/Simulation/newgeom_v1.0/HE_MC
4He_C_270_1.root (5 106 primaries, 46689 ev.)
4He_C_200_2.root (5 106 primaries, 46178 ev.)
As usual, a «software trigger» in implemented to write only events in which there was at least one inelastic interaction of primary in target

## Slide 8: A few very preliminary plots: multiplicity per event at TW
Multiplicity of charged particles arriving at TW
All charged, produced everywhere
Charged from primary fragmentation on target

## Slide 9: Multiplicity per event at TW - 2
Multiplicity including neutrons
(no energy cuts)
produced everywhere
from primary fragmentation on target: ~no low energy neutrons

## Slide 10: (Total) Energy of secondaries from projectile fragm. arriving at TW
p
d
t
3He

## Slide 11: (Total) Energy of secondaries from projectile fragm. arriving at TW - 2
4He
C* → more complex target fragm. channels where projectile excites a higher energy level in target nucleus
C* → C + g
12C* → 11C + n
12C* → 4He+ 4He+ 4He
…..
Target excited to 1st excited nuclear energy level.
Charged fragments usually not escaping from target
These processes also are tagged in MC as inelastic interactions

## Slide 12: (Total) Energy of secondaries from projectile fragm.: neutrons arriving at TW
n from everywhere

## Slide 13: (Total) Energy of secondaries from projectile fragm.: neutrons arriving at TW
n from everywhere
n from fragmentation of primary (~ as p)

## Slide 14: Arrival time at TW of neutrons
n from everywhere

## Slide 15: Arrival time at TW of neutrons
n from everywhere
n from fragmentation of primary (~ as p)

## Slide 16
The end