SuperB Drift Chamber mechanical structure: preliminary considerations
G. Finocchiaro
INFN-LNF
and on behalf of
M.A. Franceschi
T. Napolitano
A. Saputi
INFN-LNF
Servizio Sviluppo e Costruzione Rivelatori

---
Current BABAR design
Total wire load about 3.5tons
Flat Al end-plates
Backward:	24mm (27% X0)
Forward:	24mm for R<47cm, 12mm (13% X0) for R>47cm
Max. plate deflection under wire load ~2mm

---
Options for Carbon-Fiber end plates
3 options considered for the end-plates
Flat
Spherical
Reduce thickness
Conical
Reduce occupancy
in forward direction
For all options, the E.P.'s are only constrained at the OUTER radius
Disclaimer: what follows is VERY preliminary

---
Option(s) #1: flat CF end-plates
25mm thick CF sandwich of
2mmCF + 21mm honeycomb + 2mm CF
~0.015X0, max deformation dmax~1 mm
10mm thick CF sandwich of
2mmCF + 6mm honeycomb + 2mm CF
~0.015X0, dmax~7 mm
20mm thick CF
~0.075X0, dmax~1 mm
10mm thick CF
~0.04X0, dmax~6 mm

---
Option #2: spherical end-plates
Thickness O(4mm), or 0.015 X0
sagitta=200 mm dmax200≤0.5mm
sagitta=100 mm dmax100~2xdmax200

---
Spherical EP concept proved in the KLOE DC
Rmax ~ 2m
52,140 wires
total load ~ 3.5 tons
EP thickness 9 mm
Plate deformations recovered with CF “stiffening ring”
Given the smaller radius of the SuperB DCH, we can probably avoid this complication

---
Option #3: conical end-plates
Expect high particle flux in forward direction. Conic-shaped EP's might
help reducing occupancy in inner layers.
Thickness O(4mm), or 1.5% X0 (perp. to walls)
dmax~0.5mm

---
Option #3: conical end-plates (cont.)
Besides the trickier structural analysis, conical end-plates would pose several problems though:
drilling the holes at a very small angle
ensuring a flat seat for the feed-throughs
stringing the wires in the conical section
a lot of material seen by electrons tangential to the cone ⇨a lot of background produced
None of the above (excluding 4), which needs careful investigation) looks unsurmountable, but we should be aware that conic end-plates are not exempt from issues.

---
An alternative: variable-gain sense wires
Electron amplification at the sense wire is obtained by the very high electric field due to the small wire diameter (~20mm)
If we could vary the wire diameter, we could tune the amplification along the wire length.
The big question is HOW
With a dedicated extrusion, or coating process?
Replies from wire-drawing company experts were not encouraging
Alternatively, one could just stop the electron drift before amplification starts
Encapsulating part of the wire in a tiny plastic tube?
With a layer of insulator, ~100mm thick?
All of the above is clearly very non-standard and still in a pre-preliminary stage, but worth being pursued, IMHO.

---
Summary and outlook
Once more – no detailed calculation (e.g. of restraints), or FEA performed yet.
All options considered for a drift chamber with carbon-fiber mechanical structure seem feasible from the structural point of view, allowing CF thickness O(few %) with deformations < 1mm.
The spherical EP solution has been successfully demonstrated to work.
Conical EP solution has still many unknowns (both known and unknown) at this point.