## Slide 1: ASTENA
Advanced Surveyor of Transient Events and Nuclear Astrophysics
M. Moita(1), L. Ferro(1), E. Virgilli(2), P. Rosati(1), F. Frontera(1), E. Caroli(2),
N. Auricchio(2), J. B. Stephen(2), S. del Sordo(3)
HPXM2021 Conference
1 – University of Ferrara, Dept. of Physics and Earth Science 2 – INAF/OAS Bologna 3– INAF/OAS Palermo

## Slide 2: Advanced Surveyor of Transient Events and Nuclear Astrophysics (ASTENA)
ASTENA is a new high energy mission concept that has been proposed within the context of the European project AHEAD.
Submitted to ESA for the Voyage 2050 long-term plan
Narrow Field Telescope:
  Board band (60-600 keV)
  Large collection Area
  Focusing optics: LAUE lens
Wide Field Monitor
  Imager; Spectomer
  Broad energy passband (1keV - 20 MeV)
Notes: that aims the promotion of synergies between the distinct national efforts in high-energy astrophysics and propose the next generation of gamma-ray observatories.
A view of the inner accommodation of the ASTENA payload before the launch. Right panel: ASTENA spacecraft in the fairing of the Soyuz launcher. Also the fairing of the Vega C launcher can host ASTENA.

## Slide 3: NFT – Laue Lens
Hard X-soft Gamma ray optics based on Bragg’s Law of Diffraction
Large number of crystals disposed in a spherical cup that concentrate the incident radiation onto a common focal spot
Inner crystals – higher energies
Outmost crystals – lower energies
Notes: A Laue lens is made of a large number of crystal tiles in transmission configuration, that are disposed in such a way that they concentrate the incident radiation onto a common focal spot.
Thus the highest energies are diffracted from the nearest crystals and the lowest energies from the farest crystals to the lens axis.

## Slide 4: NFT – Laue Lens ASTENA Configuration
∼19500 bent crystal tiles of Si(111) and Ge(111)
20 m focal length
Crystal dimensions: 30 x 10 mm2
43 Rings (R in/out: 18 cm /149 cm)
Total Geometric Area ~ 7 m2
Pass-band: 60 – 600 keV
FOV ~ 4 arcmin
Angular Resolution ~ 0.5 arcmin
Notes: A Laue lens is made of a large number of crystal tiles in transmission configuration, that are disposed in such a way that they concentrate the incident radiation onto a common focal spot.
Thus the highest energies are diffracted from the nearest crystals and the lowest energies from the farest crystals to the lens axis.

## Slide 5: NFT – Focal Plane Detector
4 layers of CZT
Layer dimensions: 80 mm x 80 mm x 20 mm
Detection efficiency: > 80% @ 600 keV
Fine spectroscopy response: 1% @511 keV
3-D position resolution: 300 μm (x, y, z direction)

## Slide 6: NFT – Expected Performances
NFT continuum sensitivity at 3 σ confidence level 105s observation time, with ∆E = E/2
Expected line sensitivity at 3 σ confidence level 105s observation time
Unprecedented sensitivity - up to two orders of magnitude better than that of NuSTAR in the common energy band
One order of magnitude better then the SPI at 511 keV

## Slide 7: NFT – Polarization
Minimum Detectable Polarization (MDP)
6 energy ranges
Tobs: 100 ks; 1Ms
Flux: 100 mCrab; 1 Crab
Full Band (65 - 600 keV)
MDP ~1.3%, 100 ks, 10mCrab

## Slide 8: Wide Field Monitor (WFM-IS)
Array of 12 units
2 units on each side of the hexagon surrounding the NFT
15 deg offset
Position Sensitive Detector (PSD)
  4 x 8 Modules
  43 × 42 cm cross section
Square coded mask

## Slide 9: WFM-IS Module
10 rows of hexagonal scintillator bars CsI
  Distance between hexagon flat sides of 5 mm;
  5 cm length
  205 bars total
Top - Linear multi-anode SDDs
Bottom - Hexagonal single anode SDDs
Notes: working principle of a SDD coupled with a CsI scintillator crystal. The soft X-rays interact directly in the SDD while high energy photons pass through the SDD and are absorbed in the scintillator. Secondary photons are then detected with the SDD.
﻿The operating principle (see Fig. 32 right) is the following. The top SDD-PD, facing the X-/gamma-ray entrance window, is operated both as X-ray detector for low energy X-ray photons interacting in Silicon and as a read-out system of the scintillation light resulting from X-/gamma-ray interactions in the scintilla- tor. The bottom SDD-PD at the other extreme of the crystal bar operates only as a read-out system for the
scintillators. The

## Slide 10: WFM-IS Module Operating Principle
Similar to that adopted for the X-Gamma-ray Imaging Spectrometer (XGIS) aboard the THESEUS mission
Top SDD-PD
  X-ray detector for low energy X-ray photons
  Read-out system of the scintillation light
Bottom SDD-PD
  Read-out system for the scintillators
Broad passband (2 keV–20 MeV)
3-D position sensitivity
Hexagonal cross section – improve polarimetric capabilities
Notes: working principle of a SDD coupled with a CsI scintillator crystal. The soft X-rays interact directly in the SDD while high energy photons pass through the SDD and are absorbed in the scintillator. Secondary photons are then detected with the SDD.
﻿The operating principle (see Fig. 32 right) is the following. The top SDD-PD, facing the X-/gamma-ray entrance window, is operated both as X-ray detector for low energy X-ray photons interacting in Silicon and as a read-out system of the scintillation light resulting from X-/gamma-ray interactions in the scintilla- tor. The bottom SDD-PD at the other extreme of the crystal bar operates only as a read-out system for the
scintillators. The

## Slide 11: WFM-IS - Image Capabilities
Double scale coded mask
  Low energy photons (mainly < 30 keV) that lose their energy in the SDD alone.
    Point Source Location Accuracy (PSLA): 1 arcmin
  High energy photons (30–150 keV) that lose their energy in the scintillator bars
    79×79 elements
    Fully Coded Field of View: 0.27 sr
    Point Source Location Accuracy: 5 arcmin
Compton Imager (>150 keV)
  Compton kinematics reconstruction
  Source location accuracy @ 1 MeV:10 - 35 deg
  Use total number of units – triangulation
Lateral passive shield for the imager system (1–30 keV) and as a FOV delimiter at energies >150 keV.

## Slide 12: WFM-IS – Expected Performances
Energy pass-band | 2 keV – 20 MeV
Total useful area | ~ 5800 cm2 (<30 keV) ∼ 6700 cm2 (30–150 keV) ∼ 13800 cm2 (>200 keV)
Field of View | 2 sr
Angular resolution | 6 arcmin
Point source localization accuracy | 1 arcmin (<30 keV) 5 arcmin (30–150 keV)
Continuum sensitivity of the WFM-IS in three energy bands

## Slide 13: WFM-IS – Polarimetric Capabilities
Left: Scattering map obtained with a 500 keV, 100% polarized far field source, using the WFM-I/S Monte Carlo model.
Right: Comparison of the modulation curve obtained with a hexagonal shape and square shape scintillators for the same source characteristics.
Minimum Detectable Polarization (MDP)
6 energy ranges
Tobs: 100 ks; 1Ms
Flux: 100 mCrab; 1 Crab

## Slide 14: ASTENA Scientific Cases

## Slide 15: Gamma-ray Bursts
WFM-IS - Unprecedented performances for the detection, characterization and localization within few arcmin of all classes of GRBs
  GRB spectra, light curves and polarization over an energy band (2 keV – 20 MeV)
  Large effective area and excellent energy and time resolution
NFT: High energy spectrum and polarization of the GRB afterglow emission
Multi-messenger Astrophysics: Electromagnetic counterparts of Gravitational Wave events (NS–NS merging)
Notes: The ASTENA WFM-IS, thanks to its specific capability as a polarimeter (see below), its very large detection area and broad passband, is expected to provide secure information about the polarization level of a large sample of GRBs, also determining its temporal and energy dependence.
thanks to the unprecedented sensitivity of the Narrow Field Telescope (NFT) (see below), will be capable to measure the high energy spectrum and the polarization of the afterglow emission of a large sample of GRBs, and thus to establish the underlying physics and the emission mechanisms at play (e.g., synchrotron photon energy, presence of a Compton or pair pro- duction component in addition to the synchrotron) and the cor- responding parameters.

## Slide 16: Nuclear Astrophysics
NFT Measurements with unprecedented sensitivity and angular resolution of the 511 keV annihilation line from the Galatic Center
  Difuse emission made up of a population of discrete unresolved sources?
Line emission from radioactive nuclei produced in Type-Ia supernovae and core-collapse SN explosions
Weidenspointner et al. 2018
Notes: The ASTENA WFM-IS, thanks to its specific capability as a polarimeter (see below), its very large detection area and broad passband, is expected to provide secure information about the polarization level of a large sample of GRBs, also determining its temporal and energy dependence.
thanks to the unprecedented sensitivity of the Narrow Field Telescope (NFT) (see below), will be capable to measure the high energy spectrum and the polarization of the afterglow emission of a large sample of GRBs, and thus to establish the underlying physics and the emission mechanisms at play (e.g., synchrotron photon energy, presence of a Compton or pair pro- duction component in addition to the synchrotron) and the cor- responding parameters.

## Slide 17: Optimisation & Performance evaluation
NFT Laue Lens
  Ray tracing program to optimise mainly the PSF, the efficiency, and the FOV of the Laue Lens optics
  The TRILL project: building a first prototype of broadband Laue lens.
    Lisa Ferro, 10/07, 11h
NFT Focal Plane detector
  MEGAlib model of the CZT 3D spectro-imager focal plane

## Slide 18: Optimisation & Performance evaluation
WFM
Development of a MEGAlib model of one WFM
Evaluate performance
  Sensitivity
  Polarimetric capabilities
  Mask design
  Operating parameters (e.g. spatial and energy resolution, background)
Optimization detector geometry & material
THESEUS Mission

## Slide 19: Thank you for your attention!
Contact us!
Dott. Miguel Moita: mmoita@fe.infn.it
Dott. Lisa Ferro: lisa.ferro@unife.it
Dott. Enrico Virgilli: enrico.virgilli@inaf.it
Prof. Piero Rosati: rosati@fe.infn.it
Prof. Filippo Frontera: frontera@fe.infn.it