## Slide 1
PADME status report
Mauro Raggi, Sapienza Università di Roma e INFN Roma 59th meeting of the LNF Scientific Commitee

## Slide 2: Outline
Consequences of COVID-19 on PADME plans
Planning for the PADME detector commissioning
Tentative 2020 run plan
RUN-1 data analysis status
Expected publications 2020 - early 2021

## Slide 3: Mid-term scicom plan 2020 and COVID
Plan of the last meeting of the SciCom
Original plan
  15-30 April PADME beam commissioning
  Start data taking first week of May
Beginning of March COVID-19 emergency started
Beginning of May COVID phase II start (~ 60 days complete shutdown)
Normal operating conditions?
Normal operating conditions??
COVID-19 emergency
COVID-19 phase II

## Slide 4: COVID-19 INFN protocol May 5th

## Slide 5: Impact on PADME restart activities
Almost no hardware preparation activity during COVID-19 phase I
  Need to perform some repairs and small improvements
Activity during phase II limited to RM1 and LNF personnel only
  Only travels from Rome to LNF
  No help in preparation activities from Lecce, Sofia and Torino
COVID-19 rules limit personnel access in BTF area, control room, etc.
  Not possible to parallelize interventions in BTF area
  Access to the area should be coordinated with accelerator division operators
Restart operations much longer wrt to normal operating conditions
COVID-19 rules will also affect RUN-2 operations (e.g. use of control rooms)

## Slide 6: Tentative BTF schedule
see L. Foggetta’s talk for details

## Slide 7: The PADME detector 1 slide
Active target
Lecce & University Salento
Veto scintillators
(University of Sofia, Roma)
Dipole magnet
(CERN TE/NSC-MNC)
C-fiber window
TimePIX3 array
(ADVACAM, LNF, RM1)
PbF2 calorimeter
(MTA Atomki, Cornell U., LNF)
BGO calorimeter
(616 L3 endcap crystals: Roma, Cornell U., LNF, LE)

## Slide 8: Planned hardware operation
F. Ferrarotto: 2 days/week (PADME LAB)
G. Piperno: 2 days/week (BTF)
M. Raggi: 2 days/week (PADME LAB-BTF)
P. Valente: 1 day/week (BTF)
F. Ferrarotto: 2 days/week (BTF)
G. Piperno: 2 days/week (PADME CR)
E. Leonardi: 1 day/week (PADME CR)
M. Raggi: 2 days/week (BTF)
P. Valente: 1 day/week (PADME CR)

## Slide 9: Ecal ventilation system
In July ‘19 test-run temperature of ECal was critical
  PMT box T ~14º higher than BTF hall
Light-tight ventilation system designed and built to improve air exchange:
  All component available at LNF
  Top part already in place
  Need testing the fan controls (PADME Lab)
  Install air inlets and controls in BTF (1d 2P)
Can profit from shutdown period to test Ecal temperature during June

## Slide 10: ECal new cosmic rays trigger
Improve efficiency and uniformity of cosmic rays trigger
New scintillating tiles ready and tested
  Electronics is on board and polarity reversed
Need to be installed in BTF on ECal
  Needs connection to PADME DAQ system
Estimated effort 1d 2P in BTF
  installation and integration in DAQ
Calibrate Ecal with cosmics from early June
70 cm
23 cm

## Slide 11: Ecal temperature monitoring system
Status before lockdown
  Properly shielded flat cables with new copper shielding tape
  Grounded copper shielding to Ecal metal frame
  Tested with DAQ and still having noise problem
  Keysight power from far away power line (near servers)
  New version of ECAL thermocouples readout program (loop every 120 sec and read 1 channel only each 2 sec)
  Not yet tested if noise problem solved by these last changes
To do in BTF/Control room :
  Test new version of readout with all boards and DAQ components UP and RUNNING
  ??? Try other solutions ????
  If nothing else works: Read temperature at run start and end only (and possibly make shorter runs)
Temperature sensors readout ADC crashing the DAQ system (noise on the VMEbus to the digitizers)
  Crucial to measure temperature of the BGO crystals, especially during RUN-2 spanning summer period
Estimated effort 2d 2P (F. Ferratotto + E. Leonardi)

## Slide 12: Ecal not working scintillating units
Estimated effort (2d 2P)
  Need to open Ecal back cover
  Extract and plug back units
  Close again the back cover
An electronic technician needed
SU 91834 already fixed: software and cabling configuration issue
SU 2105124: broken signal cable connector, need fixing cabling and test
SU 2104022, SU 2104032 “clocked” divider: Extract the divider, check its integrity and reconnect it. Not an easy task due to density of cables in the ECal back region.

## Slide 13: 22Na based Ecal calibration system
Moving 22Na crystal calibration system
  Check stability of the crystals response in addition to cosmic
  Now in PADME Lab to check moving software and motors
Mounting the bars on the Ecal structure
  Test and install the motorized system
Estimated effort 2d 2P in BTF for hardware installation
  F. Ferrarotto + E. Capitolo

## Slide 14: Ecal fine alignment
Effort (1d 2P): LNF alignment service in BTF
Present survey has shown millimetre scale misalignment of Ecal
  3,8 mm too high and 3.1 mm too much on the BTF wall direction
Can refine the alignment at the sub millimetre level
  Can check better the rotation angle, if any

## Slide 15: Intervention on DAQ system
Estimated effort (1d 2P): E. Leonardi + 1
One V1742 CAEN board from ECal readout has oscillating pedestal
  Remove the 32 channels cables and connection to DAQ
  Need to dismount the board and cable back 32 channels
  Test the DAQ system with the new board.

## Slide 16: Intervention on the diamond target
Apparently no damages during BE window accident
  Target never operated again
  Readout need to be moved to allow BTF2 installation
Operations can be performed without experts from Lecce
  Estimated effort: (1d 2P)

## Slide 17: “Smart running” PADME from remote
Running PADME during summer 2020 will be an important effort
  No possibility of having shifters at LNF from outside Rome area
  Losing Sofia, Lecce, US contribution.
  30% less man power expected for shifts
  Possibility of new restrictions on the mobility due to COVID-19 crisis
PADME can be operated remotely thanks to our web based online monitor
  During RUN-1 night shift were performed mainly from remote
  Efficiency similar or even slightly higher than day shifts
Day 7-15
Afternoon 15-23
Night 23-7

## Slide 18: Run 1 Data analysis status
SM Brems.: e+N->e+Ng
g
e+
SM annih. e+e-->gg(g)
g
g
e+
2g in Ecal in time with E1+E2 = Ebeam
e+ in veto +g in SAC in time with Ee++Eg = Ebeam

## Slide 19: gg signal selection
Two photons in Ecal DT<10. ns

## Slide 20: gg signal selection
Two photons in Ecal DT<10. ns
Df < 20 deg.

## Slide 21: gg signal selection
Taglio temporale 10. ns Df < 20°
gg Center Of Gravity < 2. cm

## Slide 22: gg signal selection
> 5000 events gg in (DATA & MC)
- Potential statistical error: ~1-2 %
- Good data MC agreement
- Rescaled MC beam time structure using SAC time measurement
Taglio temporale 10. ns Df < 20°
gg Center Of Gravity < 1. cm
s~4.8%
Bunch time structure

## Slide 23: e+e- -> gg next to leading order
NLO calculation needed to compare PADME to SM at % level
Many thanks to C. Carloni Calame for adapting Babayaga to fixed target and PADME energy scale.
  Very good agreement <1% at tree level with Calchep calculations
  NLO correction ~5%
  Event generator for PADME MC
  Allows correct acceptance calculation

## Slide 24: PADME veto used as spectrometer
Impact point of particles in veto can be used to measure |P|
beam
Good correlation around fingers 20-70
  In region >70: beam halo pile-up
  in the region <15: particles from interaction with vacuum chamber
Region covered by fingers 15-70 corresponds to energy range
  Emin > 50 MeV and Emax < 350 MeV

## Slide 25: Bremsstrahlung spectrum in PVeto
a) In red in the plot
Beam
Target
b) In black in the plot
Beam
No Target
Difference in rate observed in data MC
  Due to non perfect beam shape simulations
  Significant difference target On-Off beam radiation!
a) target - b) no target data in the region 15-70
  Bremsstrahlung spectrum is obtained
  Very good data-MC agreement in large energy range
  Higher finger index region: disagreement due to inefficiency in data reconstruction for higher pile up
a) – b) data
a) – b) MC
Rate is very well reproduced
  Bremsstrahlung cross section well understood in PADME
  Means luminosity measurement is working
  Correlation of different detector works

## Slide 26: SM and beyond in ee collisions

## Slide 27: searching for DH in multi leptons
Extended dark sector with a dark Higgs h’
  Minimal suppression: only e2aD
  BR(A’->ee=1)
Main production mechanism: higgs-strahlung
  Main decay of h’: h’→A’A’
  Assuming A’ → e+e-
  Can produce e+e- → e+e-e+e-e+e-

## Slide 28: Summary of multi-lepton events
In Events/y column 1y=100 days at 100% efficient data taking
  The dark sector related calculation are for e2=1E-6 and aD=0.1
In the Acc/y a cut on the Emin>50 MeV is applied
  4e scales down by ~2000 (Calchep), 6e scales by only ~100 (phase space)
  DH scales by 0.6 (phase space)
Seem that DH contribution to 6 leptons production cross section could be sizable, even with e2 as low as 10-6
Final state | s in pb | PADME lumi | Events/s | Events/day | Events/y | Acc/y
e+e-→4e± | 1.32E8 | 1.2E-8 pb-1 | ~ 1.6 | ~ 136K | ~ 13.7M | ~ 6400
e+e-→wDwD | 6E3 | 1.2E-8 pb-1 | ~7E-5 | ~ 6 | ~ 600 | ??
e+e-→6e± | 2.0E4 | 1.2E-8 pb-1 | ~ 2.4E-4 | ~ 20.7 | ~ 2.07E3 | ~ 20
e+e-→h’A’ | 485 | 1.2E-8 pb-1 | ~ 6e-6 | ~ 0.5 | ~ 50 | ~ 30
PADME luminosity assuming (24.5K x 49) =1.2E6 POT/s

## Slide 29: Publications detector during 2020
Three papers are in preparation and likely will be submitted within next SciCom meeting (Nov.2020):
Presents the performance of the PADME detectors obtained with the data collected from Sep.2018 to Feb.2019, the software algorithms employed to reconstruct physics objects, and the calibration procedures adopted [NIM A or JINST].
Reviews each step of the construction of ECal, from the initial L3 crystal recovery, to the final assembly. The trigger, DAQ unit equalisation and energy calibration are described [NIM A or JINST].
A first technical paper on target performance has been published:
Development and deployment of the Trigger and Timing System.
https://doi.org/10.1016/j.nima.2019.162354
NIMA Volume 958, 1 April 2020, 162354

## Slide 30: Physics papers in early 2021
Paper on 2018-2019 data set
  Measurement of the ee -> gg cross section with the PADME experiment
Phenomenological papers on PADME physics (preparation of RUN II)
  A next to leading order e+e- -> gg generator for the PADME experiment
  PADME sensitivity to multi-lepton final states
  Searching for ALPs at PADME

## Slide 31: Conclusions
COVID-19 emergency has significantly delayed the expected restart of the experiment data taking wrt to last mid-term meeting plan.
The PADME restart program has been established
  Hardware fixes and small upgrade are foreseen in May to mid June
First sample of 5000 clean ee->gg candidate identified
  Working hard to improve Data-MC comparisons to extract acceptance
  Next-to-leading order generator obtained
First solid evidence of the Bremsstrahlung process has been extracted
Beam expected for beginning of July
  2 month of physics-grade data are expected to be delivered to PADME by the end of the 2020.
Data reconstruction quality much higher wrt to RUN1- will allow faster and better feedback in the beam commissioning phase.

## Slide 32
SHERPA “Slow High-efficiency Extraction from Ring Positron Accelerator” CSN5 grant, P.I.: Marco Garattini (LNF-INFN)
R&D study to extract a high-quality e+ beam from the DAΦNE ring
The idea is to use a bent crystal to steer the positron beam
VS
Current BTF spill parameters:
Energy spread: Δp/p < 0.5 x 10-2
  Emittance: ε < 10-5 rad⋅m
  Length: Δt < 200 ns
Target spill parameters:
Energy spread: Δp/p < 10-3
Emittance: ε < 10-6 rad⋅m
Length: ms < Δt < s
Channeling
e+
DAΦNE
BTF
Bent crystal
With the SHERPA beam, PADME could increase the statistics by a factor 104 and its sensitivity by a factor ~102, largely extending the discovery potential
2 year grant (120K) by CSN5 to realize a proof of principle and a realistic design

## Slide 33: backup slides

## Slide 34: A’ visible decays at PADME
Process | Name | aX | Fin. state | Detectors | Main BG | Sens. Est.
1.e+N→e+NA’→e+Ne+e- | A’-stra. | 3 | e+e+e- | Vetos | PileUp+Trident | None
2.e+e-→gA’→ge+e- | 2g-ann | 2 | ge+e- | Ecal+Veto | Rad-BhaBha | 
3.e+e-→A’→e+e- | Res.an | 1 | e+e- | Vetos | BhaBha | X boson
A-stra.: Production cross section high, but very high background from QED
  Need to measure e+e- invariant mass distribution.
  Strong competition from electron based experiment A1, APEX, HPS.
  In principle masses up to >100 MeV are accessible
2g-annihilation: lower cross section but can use Ecal to measure A’ mass.
  Bump hunt possible by computing missing mass to the recoil g
  Helps in rejecting radiative BhaBha, g-conversion and trident BG.
  Mass reach limited to 23.7 MeV for 550MeV beam
Resonant Annihilation: very high cross section but a very narrow mass region
  Need to know the particle mass in advance. (Xboson)
1.
2.
3.

## Slide 35: Novità da Torino
Gruppo di Numen interessato ad entrare in PADME
  Primi contatti allo scorso PADME collaboration meeting
Il gruppo è del politecnico ed è composto da
  Iazzi Felice PO, Pinna Federico RTDa, Capirossi Vittoria PHD
Interesse a lavorare nei rivelatori di fascio al silicio di PADME
  TimePix e Mimosa primi contatti e raccolta di informazioni
Sarebbero anche interessati a partecipare al RUN di quest’anno
  Inclusi nello sblocco di SJ di 120gg

## Slide 36: Due diversi tipi di fascio e di fondo
LINAC
wall
LINAC wall
Secondario
Primario
BTF target in
BTF target out
DHSTB001
DHSTB002
DHSTB002
DHSTB001
BeW 250mm
BeW 250mm
1E9 e- 750 MeV
1E5 e+ 500 MeV
1E4 e+ 550 MeV
1E4 e+ 490 MeV

## Slide 37: Origine del fondo
Fascio secondario
  1E9 e- generano e+ e fotoni di qualunque energia.
  Fotoni creati al collimatore in uscita dal primo magnete colpiscono il secondo magnete creando un fondo diffuso di fotoni ~7 GeV su ECAL dovuti a sciami sul secondo magnete
  Se si spegne il secondo magnete si vede ancora molto fondo quindi fondo dominato dal collimatore
Fascio primario
  Niente bersaglio BTF
  Molti meno primari e tutti dell’energia giusta passano attraverso la linea senza creare fondi importanti
  All’attraversamento della finestra di Be si creano piccole code di positroni fuori energia che colpiscono la parte interna del magnete creando fondo nel calorimetro
  Questo fondo può essere mitigato migliorando il fascio e spostando la finestra

## Slide 38: Beam background PADME
Fondo fascio secondario
  Background ~7 GeV for DHSTB001 and DHSTB002 ON
  Background ~5.5 GeV for DHSTB001 On and DHSTB002 OFF
  Background ~0.2 GeV for DHSTB001 OFF and DHSTB002 OFF
Fondo con fascio primario
March 2019
July 2019 run
24/07/2019 ore15

## Slide 39: Nuovo layout della linea
Vecchia Linea
Nuova Linea
BeW 250 mm
Mylar
Mylar
125mm

## Slide 40: SAC calibration status
SAC calibration beam
SAC cosmic rays
CR results on calibration are encouraging:
- better with a fixed-energy source beam
- need data for all the 25 crystals (9 so far)
Positron runs with the beam into each crystal is needed
Parasitic secondary beam in Ok for this task
9 crystals few hours
- 1-2 days of data taking should be enough

## Slide 41: A’ decay modes MeV-GeV scale
A’->𝓁+𝓁-
e+e- m+m- decay allowed
If 1MeV <MA’< 2mc dilepton “visible” decays (at PADME energy just ee)
  Min MA’>1MeV lifetime depends mostly on e2 long lived
2mc<MA’ dark matter decays “invisible” decays
  Min MA’<1MeV lifetime depends mostly on aD2 short lived
Decays in 3g are not interesting for the accelerator searches
MA’
Mc
long lived A’->ggg
2me
Visible A’->𝓁+𝓁-
MA’=2mc
Invisible A’-> cc
(Visible A’->𝓁+𝓁-
suppressed by e2)
MA’
Mc
long lived A’->ggg
2me
A’->𝓁+𝓁- e+e- only region
Heavy DM c>GeV light mediator
Light DM c and light mediator
2mm

## Slide 42: X17 dal 8Be al 4He
arXiv:1910.10459v1
23 Oct 2019

## Slide 43: The 8Be nucleus
Can excite the 8Be(18.15 MeV) by using proton capture Ep=1030 KeV
The Be is a peculiar nuclei having high energy transitions to the ground state
  1+0 T=0 has 18.15 MeV if it goes directly to ground state 0+0 Ep= 1030 KeV
  1+0 T=1 has 17.64 MeV if it goes directly to ground state 0+0 Ep= 441 KeV
IPC
EM
HAD
8Be decay
Resonant proton capture

## Slide 44: On resonance measurements
Deviation from IPC
Ep=1.10 MeV
Ep=1.04 MeV

## Slide 45: Scanning the resonance with Ep
Experimental angular e+e− pair correlations measured in the 7Li(p,e+e−) reaction at Ep=1.10 MeV with -0.5< y <0.5 (closed circles) and |y|>0.5 (open circles). The
results of simulations of boson decay pairs added to those of IPC pairs are shown for different boson masses.
y=

## Slide 46: The 4He anomaly
Resonant proton capture
3H
4He*
The investigated 0− state overlaps with the first ex-
cited state in 4He (J=0+, Ex=20.21 MeV, G=0.50 MeV), which was also excited but but give only a managable background to the e+e− spectra.
Ep=900 keV
The 3 H(p,γ )4 He reaction at Ep =900 keV bombarding energy was used to populate the wide (G = 0. 84 MeV) 0− second excited state in 4He, located at Ex = 21.01 MeV.
The 3H was absorbed in a 3 mg/cm2 thick Ti layer evaporated onto
a 0.4 mm thick Mo disc. The density of the 3H atoms was 2.66x1020 atoms/cm2. The disk was cooled down to liquid N2 temperature to prevent 3H evaporation.

## Slide 47: The 4He anamaly peak
External pair creation
IPC e+e− pairs crated in the J =0+ -> 0+ gs E0 transition
The data measured for the background
were fitted by a 4-th order exponential polynomial, and the result is shown in a blue full curve. This blue curve was rescaled to fit the background of the angular correlation shown in red in the range of 40◦ < θ < 90◦ .

## Slide 48: Comparing anomaly peaks
8Be anomaly (18MeV to GS)
4He anomaly (21MeV to GS)
MX=17.00 ± 0 .13 ± 0 .2 MeV
7.2s
MX =16.70±0.35.stat.± 0.5.syst. MeV
Γ𝑋=ΓγxBx=1.9x6x10-6 eV= 1.2x10-5 eV
Γ𝑋= 3.9x10-5 eV
6.8 s

## Slide 49: The experimental constraints A’
Na64 no beam up to end of 2021
Mesa no beam before 2024
Interesting target for PADME mass is within reach.
  Unfortunately PADME is not designed to search for visible decay.

## Slide 50: Veto di PADME
PADME spectrometer inside the vacuum chamber from the calorimeter point of view
Electron Veto system
(EVeto)
Active diamond target
Positron Veto system
(PVeto)

## Slide 51: the acceptance of the veto
Particle with momentum <50 MeV do not enter the PADME vacuum chamber due to bending of the fringe field of the magnet