## Slide 2: Preliminary Fluka Geometry for MDI Studies of the 1.5 TeV Muon Collider
Alessio Mereghetti

## Slide 3: Outline
Introduction
  LineBuilder and FLUKA Element DataBase
Application of LB/FEDB to MC MDI Studies
  Building the FLUKA Geometry
Conclusions and Outlook

## Slide 4: Introduction
In a high-luminosity, high-intensity muon collider (MC) ring, high background is expected in the experimental apparatus due to muon decays in the circulating beam;
  Measures to lower the background in the detector may also impact the design of the accelerator in the vicinity of the detector;
  It is essential to have a flexible simulation set up, in order to:
    Estimate the background induced by the machine / circulating beam;
    Feed the design of the machine back with results from Monte Carlo (MC) simulations about the detector background;
At CERN, studies where a similar flexibility is needed are conducted daily;
  Optics/Lattice design: MADX;
  Energy deposition / particle fluences / etc… (MC): FLUKA;
  From the lattice structure (MADX) to MC geometry (FLUKA): LineBuilder (LB) and FLUKA Element DataBase (FEDB);
Accelerator lattice design and optics calculation
Detector background estimation (MC)
LB and FEDB: from the lattice structure to the FLUKA geometry

## Slide 5: LineBuilder and FLUKA Element DataBase
The FLUKA Element DataBase (FEDB) is a collection of FLUKA geometries of accelerator / beam lines elements:
  Full description of each object: bodies, regions, material assignments;
  Each object is described in its own reference system, independently of the other elements  easy to modify / update / debug;
  Any type of element can be described: magnets, collimators, interconnects, monitors, etc…;
The LineBuilder (LB) is a python program capable of producing complex accelerator geometries in FLUKA:
  Lattice structure and powering of magnets is taken from output files of optics codes (e.g. MAD-X);
    Twiss file: lattice structure, powering of magnets and linear optics  generation of the geometry + check of optics;
    Survey file: beam position throughout the beam line in a global 3D reference system  check of orbit;
  Geometries of accelerator elements are taken from the FEDB;
  User directives, to customize the geometry: which portion of accelerator/beam line, further manipulation to lattice structure, tunnel geometry, detailed position of monitors, etc…

## Slide 6: Application of LB/FEDB to MC MDI Studies
Set up LB/FEDB for MC MDI studies: complications due to:
  lattice/optics has been studied with MAD-8: peculiar format of files, that could not be modified!
  Naming convention of elements completely different from that used at CERN – e.g. elements cannot be uniquely identified by their names;
  Very limited use of MARKERs – e.g. separation between arcs and long straight sections (LSS);
Usual tasks when a new machine has to be built:
  Build the FEDB + tunnel geometries;
  Customize the geometry construction;
Script to convert MAD-8 output files into MAD-X format (crunched by LB);
General tool, inserted in LB code repo (MR), crunches both twiss and survey files;
Customization of crunching twiss sequence by LB + further manipulation;
Building the FLUKA geometry of the MC was also the occasion for fixing a couple of bugs in LB (MR);

## Slide 7: Building the FLUKA Geometry
View of the MC FLUKA geometry from top;
Used MAD-8 output files describing half-ring;
  Entire ring cannot be really built, since all the MB kicks sum to >2p…
  Visible already in the part of beam line close to the second IP;
Half-ring is presently the largest MC geometry that we can build for the time being;
  Used to verify that the set-up is sound;
  Production of simulation results will come with a smaller portion of beam line – typically, few hundreds meters downstream of IP;
Tried to come up with something usable by others ASAP:
  F. Collamati, C. Curatolo and P. Sala can proceed with missing points in simulation set-up (e.g. scoring, physics cards, relevant details of geometry of cavern/detector);
  A. Mereghetti can have some more detailed checks on correctness of geometry;
450 m
750 m
1300 m

## Slide 8: Building the FLUKA Geometry (II)
View of the MC FLUKA geometry from top;
Very essential geometry at the detector location and in the region of the magnets immediately next to it;
  To be developed, following geometry used by N. Mokhov;
Created the muoncollider_mdi_flukageo group on gitlab.cern.ch, collecting the git repos of the FEDB and geometry for MDI studies (+config files);

## Slide 9: Building the FLUKA Geometry (III)
A very basic FEDB (for the time being):
Only dipoles and quadrupoles;
  To be enriched with missing elements (e.g. sextupoles);
All quads / dipoles have same cross section, and lengths as per each family;
  Is this true? From comments in the MAD-8 input files this seems not to be the case…
Dimensions / shapes based on my personal experience on LHC studies;
  Are these adequate for the MC MDI studies?
Using materials pre-defined in FLUKA (i.e. no SC coils, SS collars / beam pipe, etc…);
  We should check that this is acceptable for our studies…

## Slide 10: Building the FLUKA Geometry (IV)
3D view of the MC FLUKA geometry experimental cavern towards machine tunnel;

## Slide 11: Conclusions
The necessary set-up to create FLUKA geometries of the MC ring with LB and FEDB based on MAD-8 output files is now available;
  Tried to have something usable ASAP;
  Git repos on gitlab.cern.ch, such that work can progress in parallel;
For the time being:
  Used MAD-8 output files describing half-ring;
    Largest geometry possible, to verify that set up is solid;
    For the actual simulations, only some hundreds of meters around the detector will be needed;
  Created (not so) dummy geometries of SC magnets;

## Slide 12: Outlook (for discussion)
Detailed verification of machine geometry:
  Add missing models of SC magnets – mainly sextupoles (A. Mereghetti, F. Collamati, C. Curatolo);
  Verify that the design closed orbit and linear optics is reproduced with acceptable accuracy (A. Mereghetti);
  Check that models of SC magnets are actually representative of what was used by N. Mokhov et al. (F. Collamati, C. Curatolo);
    SC material, dimensions, opening, etc…
  Improve geometry of experimental cavern: nozzle, tunnel around final focusing, etc… (F. Collamati, C. Curatolo);
Collect relevant physics cards (F. Collamati, C. Curatolo, A. Mereghetti, P. Sala) and set up suitable scoring;
Run!