## Slide 1: Progress on the FTM prototype

## Slide 2: Measurements - Setup
Main goal to measure the effective gain
  Estimation of the ionization current
Setup
  CAEN 1471H
  has 50pA current
  Resolution
    Able to scan low
    amplification fields
Amptek Ag X-ray gun
Prototype
Gas Inlet
Gas Outlet
Connector to drift foil
Connector to FTM foil
Connector to Anode foil
CAEN 1471H
2 GΩ
1 GΩ
2 GΩ

## Slide 3: Ongoing Tests
From the previous meetings
  Agreed to perform effective gain measurements also with different gas mixtures
    Ar/CO2 70/30
    Ar/CO2 93/7
    Ar/CO2/CF4 45/15/40
  We faced proble with the gas mixing system capable to mix 3 gas components
    Issue was resolved in August
  Performed Effective Gain measurement tests  Only conductive foil (the resistive is defective)
  Outstanding issues have risen

## Slide 4: Eff. Gain tests
After fixing the gas mixing system
  Performed test with Ar/CO2/CF4 45/15/40
  First test performed using only the CAEN 1471H power supply
    i.e. Monitoring the current from all the three layers
The behavious is differet from the
”flat” region that we were expecting

## Slide 5: Eff. Gain tests
Comparing the two gases (and the two mixing systems) shows this strange behaviour

## Slide 6: Eff. Gain tests
Ar/CO2 70/30 performed with the same mixing system as in the Ar/CO2/CF4
Performed Ar/CO2 93/7 with the standard gas mixer (the one used for the GE1/1 project)
The results were interesting
  The plot depicts only the Anode current in absolute value (normally the values are negative)

## Slide 7: Eff. Gain tests
For completeness, I plotted also the FTM and the Drift currents in the standard values

## Slide 8: Eff. Gain tests
During a discussion with Marcello we have observed what the plots show
  i.e. maybe this methode
It is observed that the collected current in the drift is constant while due to low collection efficiency the anode current is only a fraction is collected  reformulate?

## Slide 9: Eff. Gain tests
Since signal is observed  shifted the eff. Gain to a QC5 like test (assuming a # of primaries 346 – just like in the GE1/1)
The photopeak was visible for quite high voltages > 140 kV/cm
  Gas Ar/CO2/CF4 45/15/40
  X-rays: 40kV/5μA

## Slide 10: Eff. Gain tests
In the plot there is a small plateau region
Similar is the case for the Ar/CO2 70/30 situation

## Slide 11: Eff. Gain tests