## Slide 1
Development and Characterization of Plasma Sources for Plasma-based Accelerators
Sahar. Arjmand
Prof. Massimo Ferrario
Dr. Angelo Biagioni
On behalf of SPARC_LAB
collaboration
Sahar.Arjmand@lnf.infn.it
Laboratori Nazionali di Frascati
INFN

## Slide 2
Outline
  Motivations:
    Plasma Accelerators
    Accleration Scheme
    Importance of Plasma Properties
  Plasma Module:
    Experimental Setup
    Plasma Sources
    Plasma Diagnostics
  Plasma Characterization Results:
    Longitudinal Density Profiles
    Plasma Ramps Study
    Stability with Laser Trigger Technique
  Future Frontiers
L = 30 mm
Electrode
H2 inlets
Ø = 1 mm
L = 30 mm
Plasma Capillary
Sahar.Arjmand@lnf.infn.it

## Slide 3
Motivations: Plasma Based Accelerators
Sahar.Arjmand@lnf.infn.it
High accelerating gradients ∼ 100GeV/m
Compactness
COMB Chamber

## Slide 4
Motivations: Acceleration Scheme
Driver bunch
Witness bunch
λp
PWFA and Importance of the Plasma Prameters
Sahar.Arjmand@lnf.infn.it
The plasma density regulates the accelerating field, thus is a crucial point to implement plasma based devices and has to be finely tuned.

## Slide 5
Motivations: Acceleration Scheme
High Accelerating Gradient
Active Plasma lens
90 μm
25 μm
Focusing the beam
Bφ > 500 T/m
Sahar.Arjmand@lnf.infn.it
Driver bunch
Witness bunch
High Quality Beam
To strongly focus an electron beam, squeezing its size down to few microns. The gas is ionized into a plasma by a current-discharge flowing through the capillary itself. The discharge induces an azimuthal magnetic field whose strength is directly proportional to the flowing current.
Magnetic Field
(Compactness)
Replacing Solenoids/Quadrupoles

## Slide 6
Plasma Module: Experimental Setup
Capillary shapes:
Length (Energy)
Radius (Density)
Spectrometer:
Grating
Optical alignment
Camera timing:
Delay time
Gate time
Timing:
Valve opening time
Voltage delay time
Trigger of ICCD camera
Sahar.Arjmand@lnf.infn.it
Experimental Setup
H2 inlets
Ø = 1 mm
Vacuum:
10-7 mbar
Gas injection system: 3 ms
Capillary 30mmx1mm
Double inlets
Voltage 20kV
Current 550A
Discharge circuit
Gas injection frequency: 1-10Hz

## Slide 7
Plasma Module: Plasma Sources
Sahar.Arjmand@lnf.infn.it
Plasma Sources:
Linear Spacer/Standard Capillary/Spacer with deflectors
Table of all tested Sources |  | 
Capillary |  | 
Length | Diameter | Inlet
20 mm | 1 mm | Single
20 mm | 2 mm | Single
30 mm | 1 mm | Single
30 mm | 1 mm | Double
50 mm | 1 mm | Double
100 mm | 1 mm | Double
200 mm | 1 mm | Double
Spacer: A 10mm elongation located at the capillary’s exterimities, near the electrodes to stabilize the plasma ramps.

## Slide 8
Stark Broadening Method
Electrode shadow
Plasma plume
Plasma channel
Plasma Module: Plasma Diagnostics
Sahar.Arjmand@lnf.infn.it
Balmer beta line Bβ due to transitions from the outer orbit n=4 to the orbit n=2
< Balmer Lines >
Alpha: n 3 2 656 nm
Beta: n 4 2 486 nm
By using the Stark Broadening method we measure the plasma densities as a function of the delay time from the zero-time of the current pulse. For each delay time we obtain a longitudinal profile of the density.
The results below have obtained:
The larger is the Balmer line (Δλ)
The higher is the plasma density.
Plasma density depends on the enlargement of Balmer lines so the measuring Balmer lines are as following.

## Slide 9
Plasma density inside and outside the capillary changes during the current pulse: such a behaviour it is essential for injecting the electron bunch at the right time.
Position (mm)
λ (nm)
Electrode
Plasma
Channel
Plasma Plume
Δλ
Balmer β line
Capillary
Sahar.Arjmand@lnf.infn.it
Plasma Density
Plasma Module: Plasma Diagnostics
Capillary 30mmx1mm
Double inlets
Voltage 20kV
Current 550A

## Slide 10
Plasma Charecterization Results: Density Measurement
Capillary 20mmx1mm
Single inlet
NO SPACERS
Sahar.Arjmand@lnf.infn.it
1
Longitudinal Plasma Density Profile
Capillary 20mmx2mm
Single inlet
NO SPACERS
Diameter Configuration
Voltage: 9 kV
Current: 300 A
Pressure: 300 mbar
Reduction of 65 %
Reduction of 75 %
2×1017
3.5×1017
1×1017
6×1016

## Slide 11
Plasma Charecterization Results: Density Measurement
Capillary 30mmx1mm
Single inlet
NO SPACERS
Voltage: 9 kV
Current: 300 A
Pressure: 300 mbar
Inlet Configuration
Sahar.Arjmand@lnf.infn.it
2
Capillary 30mmx1mm
Double inlets
NO SPACERS
Longitudinal Plasma Density Distribution

## Slide 12
Plasma Charecterization Results: Plasma Ramps
Sahar.Arjmand@lnf.infn.it
Ramps Comparison of:
Capillary with Linear Spacer
Standard Geometry
Capillary with Spacer and deflector
3

## Slide 13
Sahar.Arjmand@lnf.infn.it
Plasma Charecterization Results: Plasma Ramps
Ramps Stabilization
Spacers _3ms_delay2000ns_Pressure -0.2
No spacers _3ms_delay2000ns_Pressure -0.2
Plasma plume
Plasma discharge

## Slide 14
Plasma Charecterization Results: Laser Trigger Technique
Sahar.Arjmand@lnf.infn.it
4
Laser Trigger Setup
Capillary
30mmx1mm
2 inlets
By applying laser at the one entrance of
the capillary, it is possible to stabilize
the plasma formation, depending on:
Voltage
Pressure
Laser energy
Laser spot position along the capillary
Density measures
Voltage: 5.5 kV
Laser: 80 mJ
Current: 110 A
Laser:
80 mJ
11 ns
100 um
Lens to change the focal spot
Discharge Capillary
Plasma Light

## Slide 15
Sahar.Arjmand@lnf.infn.it
Instability without laser (50 shots)
(relative standard deviation reaches 25%)
Stability with laser (50 shots)
(Relative standard deviation 10-12%)
Plasma Charecterization Results: Laser Trigger Technique
The laser trigger technique used to reduce the plasma instabilities within the discharge capillaries, on the area close to the electrodes and has shown that could remove the current oscillations around the peak value.
Capillary
30mmx1mm
2 inlets
Voltage: 5.5 kV
Laser: 80 mJ
Current: 110 A
Longitudinal Shot-to-shot Stability of the Plasma Formation
Reduction of ∼ 15-13 %

## Slide 16
Future Frontier
Sahar.Arjmand@lnf.infn.it
200 mm - 1 mm
To be Tested
200 mm
400 mm
1. Shortly, an investigation of the new capillaries up to 400 mm that will be placed in the novel acceleration machine related to the EuPRAXIA project would be feasible.
2. For capillaries in higher lengths, the length will be segmented, and the voltage will be forced to each part separately to ionizing the gas inside the entire plasma tube.
3. Characterization of the transverse plasma density distribution.
The maximum accelerating filed is depend on the the plasma density, for this reasoan the length of capillary get increased to increase the accelerating energy while the gradient remains constant.

## Slide 17
Do appreciate your attention!
Sahar.Arjmand@lnf.infn.it
Laboratori Nazionali di Frascati
INFN