## Slide 1: Multi-bunch longitudinal beam-dynamics code for the DAFNE rings
D. Quartullo
Acknowledgements: S. Caschera, G. Franzini, A. Gallo,
A. Ghigo, M. Migliorati, C. Milardi, D. Pellegrini, M. Zobov

## Slide 2
Introduction (1/2)
DAFNE is an electron-positron collider in operation at LNF for physics experiments since 1999.
  It is composed of two rings, one per type of beam, and operates with (usually) 105 bunches at 510 MeV nominal energy.
Due to the high circulating beam-current and the presence of HOMs in the RF accelerating cavity, longitudinal coupled-bunch instabilities can severely limit the performance of the machine.
  These instabilities grow exponentially with time and can lead to losses of entire bunches in a few thousands of turns.
A significant damping of the HOMs was achieved in the 1990s by opening slots onto the cavity-surface and conveying (coupling) the HOMs fields out of the cavity with waveguides terminated onto 50 external loads.
  This solution, although important, couldn’t prevent the occurrence of coupled-bunch instabilities at high beam-currents.
Therefore a bunch-by-bunch longitudinal feedback was installed in each DAFNE ring and became operational since 1998.
  The active element of this feedback is a broadband cavity-kicker which provides voltage corrections to the bunches.
  This feedback system strongly contributed to the achievement of the 1.4 A – 2.4 A beam currents available today.
In the 1990s, M. Migliorati developed for his PhD thesis a Fortran code able to simulate the longitudinal beam-dynamics of DAFNE bunches in the presence of synchrotron radiation, HOMs induced-voltage and feedback corrections.
  Each bunch is represented by just one macroparticle, therefore only oscillations of the bunches centroids can be studied.
    However this type of oscillations is the main issue as concerns the coupled-bunch instabilities.
  The code accurately models the HOM induced-voltages, the complete bunch-by-bunch feedback system and even the additional RF feedback able to counteract the beam-loading voltage in the accelerating cavity.

## Slide 3
The studies performed with the Fortran code provided useful indications for stable machine operation, such as expected grow rates of coupled-bunch instabilities and optimal feedback parameters to counteract them.
  The code was rarely used after the 1990s and in particular it was never benchmarked with measurements.
The code is relatively fast and easy-to-use. This recently motivated the desire to make it usable again, both for accelerator physicists and operators who can use it in (almost) real time to better understand the beam-dynamics under observation.
  The code is modular and can be easily customized, therefore it can also be applied to other accelerators.
Recently, the Fortran code was rewritten entirely in Python, which is an open-source high-level programming language.
  Pros of using Python: less lines of code for a given task, better code-readability, easier production of data and plots.
  Cons of using Python: execution speed. However this can be solved by converting the most time-consuming Python routines into the C++ language and embedding them into the Python code (as done e.g. for the CERN BLonD code).
During the code conversion from Fortran to Python, some routines were generalized or improved, some minor bugs were fixed and new functionalities were added.
Three types of content are included in this presentation.
  Essential theoretical concepts, which are needed to understand the principles behind the code, are covered in detail.
    Complete derivations are presented to make the presentation as self-contained as possible.
  Several important code-routines are described and explained in depth.
  The code-capabilities are illustrated by numerous examples.
Introduction (2/2)

## Slide 4
Contents
Introduction.
Single-particle longitudinal beam-dynamics with synchrotron radiation.
  Equations of motion, synchrotron radiation, small-amplitude synchrotron oscillations, …
Longitudinal beam-dynamics with synchrotron radiation and Higher Order Modes (HOMs).
  HOM induced voltage, synchronous phase shift, HOM initial conditions, coupled-bunch instabilities, …
Longitudinal beam-dynamics with synchrotron radiation, HOMs and bunch-by-bunch feedback.
  Models of the feedback components, grow and damping-rates, cavity-kicker, ideal and real corrections, …
Conclusions and suggested next steps.
Appendices.
  Execution of the new-Python and old-Fortran codes, structure of the code, exponential fits in Python, …
References.

## Slide 5
Single particle equations of motion: energy equation (1/5)
We call the length of the RF cavity.
We assume that the particle traverses the RF gap along its central axis.
We assume that the electric field (s) seen by the particle in the RF gap is purely longitudinal and given by
  where is the design amplitude of the electric field;
  and are respectively the RF angular frequency and phase of ;
  v is the particle speed assumed constant during the passage (in DAFNE v c).
RF cavity
()

## Slide 6
Let’s assume that the circulating particle has charge .
The energy gain of the particle after it has crossed the gap one time is
Therefore
  where the peak RF voltage and the transit time factor are given by
0 < <1
Single particle equations of motion: energy equation (2/5)

## Slide 7
We suppose that the nominal energy is constant, i.e. no acceleration, such as in the DAFNE case (=510MeV).
From we compute the reference revolution period . We use to define the external clock
We call the arrival-time of the particle at the RF cavity (supposed point-like).
We define the particle arrival time with respect to the reference clock as
0
Absolute time
Single particle equations of motion: energy equation (3/5)

## Slide 8
The energy gain of the particle at the crossing time is
  where
This is multiple of , and therefore irrelevant, only if ( is the harmonic number).
  This condition isn’t satisfied e.g. when beam-based LLRF loops, such as phase and radial loops, modify the RF frequency to damp the bunch oscillations.
It can represent e.g. constant phase offsets or the injection of RF noise in the RF cavity for controlled emittance blow-up.
Single particle equations of motion: energy equation (4/5)

## Slide 9
In DAFNE, supposing , we have
Choosing =, we have
After crossing the cavity, the particle energy is
Defining
we obtain the energy equation of motion
Single particle equations of motion: energy equation (5/5)

## Slide 10
Using the definitions given previously we can write
  where is the nominal revolution frequency and is the particle revolution frequency.
It can be proven that
  where
    and are respectively the nominal momentum and relativistic beta;
    = - , = - ;
    and are respectively the momentum and energy of the circulating particle.
In DAFNE
(510 MeV) = 0.999999498 1
Single particle equations of motion: time equation (1/4)

## Slide 11
From the previous slide
  where the are called the slippage factors.
The slippage factors are defined through the momentum compaction factors , which are constant numbers for a given machine and depend on the optics.
  For instance
  where is the nominal relativistic gamma.
The such that = 0 is called transition gamma
In DAFNE , = 998 and . Since the beam is ‘above transition energy’.
Single particle equations of motion: time equation (2/4)

## Slide 12
When , one can take just the first term of the expansion, i.e.
  In DAFNE, since ,
  Therefore
    A particle with has . Indeed above transition energy the particle speed is essentially equal to the light speed and more energy corresponds to more mass and inertia, forcing the particle to travel on a longer orbit.
Therefore
Single particle equations of motion: time equation (3/4)

## Slide 13
Since then
Therefore the time equation of motion is
To summarize, the two equations of motion are
  The particle-tracking starts at the exit of the accelerating cavity.
    The particle drifts along the ring, then it receives an energy-kick by the cavity, then it drifts along the ring with the new energy, etc.
Particle-drift along the ring
RF voltage-kick to particle
Single particle equations of motion: time equation (4/4)

## Slide 14
Equations of motion in the code (only RF)
Using the coordinates
the equations of motion become
In the code each bunch is described by only one macroparticle.
  The above equations imply that the evolution of each bunch is independent from the evolutions of the other bunches.
    As shown later, each bunch is tracked in the code with a more complicated version of these equations.
These equations of motion can be seen as a map between coordinates at consecutive turns.
It can be easily verified that the Jacobian of is one, i.e.
  This implies that the phase-space area enclosed by the bunch (particle) trajectory is preserved over time.

## Slide 15
Let’s assume that a particle with charge and relativistic factor follows a curved trajectory with bending radius .
  It can be proven that the power lost by synchrotron radiation (SR) is given by
    where is the free-space permittivity.
If the particle is on the nominal orbit then
  where is the bending radius corresponding to the nominal orbit.
If the lattice is isomagnetic, i.e. if , the SR energy-loss per turn for a particle on the nominal orbit is
What is the SR energy-loss for a particle with energy different from ?
Synchrotron radiation (1/6)

## Slide 16
Synchrotron radiation (2/6)
From the following drawing, we can derive the relations
We know from transverse beam-dynamics that the horizontal displacement of an off-energy particle can be written as
  where is the dispersion function of the lattice.
Therefore
Nominal trajectory
Generic trajectory

## Slide 17
Synchrotron radiation (3/6)
The energy-loss per turn for the off-energy particle is the integral of the radiated power around the off-energy orbit
Equating the magnetic Lorentz-force acting on the particle with the centripetal force we derive the magnetic rigidity formula
  where is the dipolar magnetic field bending the particle.
The following proportionality relations can be deduced
Therefore can be written as a function of energy and transverse displacements
  is the power radiated at the position s of the design orbit, where the dipolar field is .

## Slide 18
Synchrotron radiation (4/6)
Expanding linearly we have
Therefore, keeping only the linear terms in ,
Expanding also linearly we have
Since the integral of is then

## Slide 19
Synchrotron radiation (5/6)
We define the focusing parameter for gradient fields as
Therefore
  where is the damping coefficient and, since ,

## Slide 20
Synchrotron radiation (6/6)
The quantity K is entirely described by integrals of lattice functions
Contributions to come only from bending magnets and wigglers, where 1/.
  For parallel-edged bending magnets at the entrance and exit of the magnet.
    This exactly compensates the term 1/ above, so that K = 0.
  For sector bending magnets if the focusing isn’t performed by the bending magnets but by dedicated quadrupoles.
In DAFNE there are parallel-edged magnets, sector magnets and wigglers.
  Using data from M. Migliorati PhD thesis, and = 9.3 keV.
    Assuming = 510 MeV, we can derive an estimation for
  Therefore can be neglected in

## Slide 21
Equations of motion in the code (RF+SR)
Including the synchrotron-radiation effect, the equations of motion become
The Jacobian becomes
  The phase-space area enclosed by the bunch (particle) trajectory decreases with time.
    This is due to the radiation damping, as shown later.
Also these equations of motion are decoupled for the different bunches.
  Each bunch can be tracked independently of the others.

## Slide 22
The synchronous particle is the ideal particle which travels along the design (central) orbit at each turn.
  For this particle at each turn and the corresponding phase is called synchronous phase.
  The subscript SR indicates that the synchronous phase is evaluated considering the synchrotron radiation.
  = (=0) = = 1.571 rad is the synchronous phase without considering the synchrotron radiation.
Synchronous phase
0
, since the corresponding RF voltage must be positive in order to compensate for the energy lost by synchrotron radiation.
In DAFNE, using = 8.88 keV and = 130 kV, we have
As shown later, changes when induced voltages are added to the equations of motions.
= 1.502 rad
[rad]
[1]
Example of difference between and in DAFNE

## Slide 23
Small-amplitude synchrotron frequency and damping rate (1/3)
We first derive the continuous version of the equations of motion assuming that in the derivative.
We expand around and we assume that the phase displacement is small.
Since we have
And deriving again

## Slide 24
Therefore
  where and are given by
The eigenvalues of this differential equation are
  therefore the solution is
decays exponentially oscillating. The small-amplitude damping-rate and synchrotron-frequency are given respectively by
Small-amplitude synchrotron frequency and damping rate (2/3)
and are constants
( if = 0, i.e. no damping)

## Slide 25
  depend on the initial conditions and
If for instance we assume that then
  or
  therefore, using the relation between and , we obtain
The constants A and B in
Small-amplitude synchrotron frequency and damping rate (3/3)

## Slide 26
Comparison between simulation and analytical formula (1/2)
Comparison between evolutions from single-bunch simulation () and analytical formula ().
Used parameters:
  = 9.3 keV, = 510 MeV, = 260 kV, = 0.02;
  rad, ;
  200000 turns are simulated.
The two curves have the same amplitude of oscillations (exponential envelope).
  However the phase-difference between the two curves can be large.
    The curves are out of phase by almost at 15 ms.
This phase-difference comes from the fact that the equations of motion in the code are discrete while the analytical formula is continuous.
  The equations of motion are correct, the analytical formula is an approximation.
  As shown later, the phase-space orbits associated to the equations of motion are tilted ellipses, while the analytical formula provides non-tilted ellipses.
For example, the error can decrease by just decreasing .
  decreases, therefore the discretized curve converges to the smooth one.
Error curve
Evolution of and
Zoom
Zoom
Discrete
Zooms
15 ms
Smooth
Discrete
Smooth

## Slide 27
is decreased from 0.02 to 0.002.
  The phase difference is barely visible. The maximum error is reduced from to .
is decreased from even more, from 0.002 to 0.0002.
Comparison between simulation and analytical formula (2/2)
Evolution of and
Zoom
Error curve
18 ms
  The phase difference isn’t visible anymore. The maximum error is reduced from to .
Evolution of and
Zoom
Error curve
17 ms

## Slide 28
We start from the discrete equations of motion
We change variable + --> and we linearly expand around for small
Amplitude of motion for small oscillations (1/2)

## Slide 29
We can write these two equations in matrix form
The 2x2 matrix can be written as
  where
This matrix representation indicates that the phase-space orbits are tilted ellipses with equations
  and the amplitude of motion is proportional to
Amplitude of motion for small oscillations (2/2)
This idea of matrix representation comes from transverse beam dynamics, where is the phase advance and , , are the Twiss parameters.
This formula is used in the code to evaluate how the bunch amplitude of motion evolves with time.

## Slide 30
Example: amplitude of motion for small oscillations
Single-bunch simulations are performed with the code to verify that the bunch-orbits in phase-space are indeed titled ellipses.
  Parameters used in simulations: = 510 MeV, = 0.02, rad, = 260 kV.
Unrealistically we increase the voltage to = 26 MV to see better that the ellipses are tilted.
turn 0
turn 12500
turn 25000
turn 50000
turn 100000
= 260 kV
= 260 kV
Ellipse-point with largest
Ellipse-point with smaller
Simulated bunch at
Non-damped motion, slightly tilted ellipse
Damped motion, slightly tilted ellipses
Non-damped motion, very tilted ellipse
Damped motion, very tilted ellipses
= 26 MV
= 26 MV

## Slide 31
Example: bunch profile (delta) performing synchrotron oscillations
Simulation of a Dirac-delta bunch-profile performing synchrotron oscillations in DAFNE.
  Used parameters: = 510 MeV, = 9.3 keV, = 130 kV, = 0.018, initial oscillation-amplitude of 0.1 rad.
  From these parameters we derive = 3.07 MHz, = 368.26 MHz and = 28.69 kHz.
  The inverse of the synchrotron tune 107 corresponds to the number of revolution turns necessary to perform one synchrotron period in phase space.
  We simulate exactly one synchrotron period.
What is the spectrum of a bunch-profile performing synchrotron oscillations?
  Doing numerically a Discrete Fourier Transform (DFT) of the time-domain bunch-profile is computationally expensive.
  We can recur to analytical evaluations.
Zoom

## Slide 32
Spectrum of one bunch performing synchrotron oscillations
We need these three general properties, two concerning the Dirac-delta function and the last one related to a series-expansion of a complex exponential.
Dirac comb
Period
-th Bessel function of the first kind
The bunch-spectrum is therefore discrete and its lines are at .
We assume that the bunch-profile is a delta arriving at a given machine-spot at time , integer.
  is the synchrotron-oscillation amplitude, which we assume constant (no synchrotron radiation).
  The bunch current and spectrum can be written as

## Slide 33
Example: spectrum of bunch performing synchrotron oscillations
We consider again the last example, where the simulated bunch-profile was a delta performing synchrotron oscillations.
  Parameters: 1/ 107, = 28.69 kHz, = 3.07 MHz, = 368.26 MHz, = 0.1 rad/.
We can use Python to evaluate the bunch spectrum
Given a frequency in , the spectrum-amplitudes strongly decrease as increases.
  As an example, the zoom shows that the spectrum-amplitudes for are essentially zero in the range .
[a.u.]
[a.u.]
Zoom
Bunch spectrum versus frequency
The spectrum is discrete, although it looks continuous.

## Slide 34
Contents
Introduction.
Single-particle longitudinal beam-dynamics with synchrotron radiation.
  Equations of motion, synchrotron radiation, small-amplitude synchrotron oscillations, …
Longitudinal beam-dynamics with synchrotron radiation and Higher Order Modes (HOMs).
  HOM induced voltage, synchronous phase shift, HOM initial conditions, coupled-bunch instabilities, …
Longitudinal beam-dynamics with synchrotron radiation, HOMs and bunch-by-bunch feedback.
  Models of the feedback components, grow and damping-rates, cavity-kicker, ideal and real corrections, …
Conclusions and suggested next steps.
Appendices.
  Execution of the new-Python and old-Fortran codes, structure of the code, exponential fits in Python, …
References.

## Slide 35
If =1, each HOM of the accelerating cavity can be treated as a parallel RLC circuit driven by a point charge current.
  charges the capacitance with the charge at = 0.
  This leads to a voltage across the capacitance.
  Applying the Kirchhoff’s law to the currents flowing across the three branches of the circuit
  Deriving
HOM induced voltage (derivation)
(is the Dirac delta function)
: shunt impedance
L: inductance
C: capacitance
: voltage across the capacitance at time t
: current in the inductance at time t

## Slide 36
HOM induced voltage (derivation)
  The eigenvalues are
  The solution of the differential equation gives free oscillations of the kind
  and are respectively the angular resonant frequency and the quality factor of the HOM.
The current in the inductance satisfies the equation
  direct verification shows that is of the kind

## Slide 37
HOM induced voltage (derivation)
We need to find the constants , , and .
  and are immediately computed
  As for
  As for
The solution is therefore

## Slide 38
HOM induced voltage (derivation)
In matrix form
Let’s suppose that the HOM is unloaded at t = , i.e. and .
  Let’s suppose that a charge crosses the accelerating cavity at t=0. The charge induces the voltage on the HOM
  According to the beam-loading theorem, the energy change of the particle due to the voltage induced by itself is
  The bunch therefore loses energy due to the HOM.
  The current does not change at t=0 and therefore ,

## Slide 39
HOM induced voltage (derivation)
Let’s suppose that a second charge crosses the accelerating cavity at .
  The voltage and current of the HOM at are
  The voltage seen by the particle at is
Let’s suppose that a third charge crosses the accelerating cavity at .
  The voltage and current of the HOM at are
  The voltage seen by the particle at is
And so on for the other charges…

## Slide 40
Note 1:
  The voltage of the HOM is discontinuous at the times of passage of the charges
  The current of the HOM is continuous everywhere but not differentiable at the times of passage of the charges
  Example on the right: DAFNE case, one HOM.
HOM induced voltage (notes)
Note 2: propagation property of the matrix. If and are positive, then
  This property is useful to keep track of the HOM voltage and current as bunches travers the cavity at different times.

## Slide 41
HOM induced voltage (notes)
Note 4: if the HOM is unloaded and a charge passes through the accelerating cavity at , then, before the passage of the second charge, we have
  This expression is the well-known one. Why we need to also consider the HOM current and the matrix propagation?
    If the matrix is not used, then another method is to consider the first row of the expansion in Note 3, i.e. to add the freely oscillating voltages produced by the previous charges. This is inefficient as the number of charges increases.
    Another possibility is to save into memory the future voltage as the sum of the past and current voltages. A voltage decay-time must be defined (first approximation) and interpolations are needed (second approximation).
Note 5: if we have more HOMs, then each HOM is treated separately, i.e. the traversing charge drives separately each HOM.
  Since we suppose that the HOMs are in series, the traversing charge sees the sum of the HOM voltages.
Note 3: if the HOM voltage and current are freely oscillating at due to the passage of the first bunch at and if the second bunch arrives at time , then, using Note 2,
  The voltage and current at time can be decomposed as sum of two free oscillations: the first comes from the first bunch (free oscillation for ), the second comes from the second bunch (free oscillation for ).
  This can be generalized to the passage of more than two bunches.
contribution from first bunch
contribution from second bunch

## Slide 42
Equations of motion in the code (RF+SR+HOM)
The equations of motion for the bunch become
  where is the number of HOMs,
  where is the residual voltage present in the HOM and which the bunch sees at turn
voltage induced by the charge on the HOM
time distance between the bunches and ( is the distance in buckets)

## Slide 43
Equations of motion in the code (RF+SR+HOM)
voltage induced by the charge on the HOM
time distance between the bunches and , at turn n and n+1 respectively ( is the distance in buckets)
  where derives from the beam loading theorem: the charge k sees half of the voltage that the charge itself induces on the HOM j

## Slide 44
Synchronous phase considering also the HOMs
Imposing , the synchronous phase is the solution of
  if all the HOM voltages are zero, i.e. , then
  if all the HOM residual voltages are zero, i.e. , then
    note that , indeed the RF cavities must now compensate for plus the energy lost by the particle due to the beam loading theorem
  we need an iterative procedure to find in the general case, see below.

## Slide 45
In the code the HOMs can be either ‘unloaded’ or ‘loaded’.
  Unloaded: the HOM residual voltage and current are both zero at the start of the simulation.
    Useful to study transient effects, however in this case the injection process has to be simulated as well.
  Loaded: the HOM voltage and current satisfy a stationarity condition, as if the bunches were already circulating for a long time in the ring at the start of the simulation.
    Useful to neglect the injection and transient phases, allowing at the same time perturbative studies where the bunches are positioned close to their synchronous phases in phase-space.
Stationarity condition for a loaded HOM:
  When a charge traverses the RF cavity, the induced must compensate the decay of V(t) during the previous period , while the current must remain constant. Normalizing with respect to , this condition reads
Solving with respect to and )/, we obtain
HOM initial conditions (unloaded vs loaded)

## Slide 46
HOM initial conditions (unloaded vs loaded)
In order to start the tracking of the bunches in the code, we need
  The initial phases of the bunches
  The energy-deviations of the bunches
  The residual voltage and current of the HOM when the first bunch traverses the RF cavity.
Case of unloaded HOM.
  The Fortran code allows to set the initial phases of the bunches to values close to
  The Fortran code allows to set the initial energy-deviations of the bunches to values close to 0
  The residual voltage and current are 0 for the first bunch at turn 0
  NOTE 1: if intensity effects are large, then the difference between and is large, therefore the bunches close to (,0) are far from their equilibrium positions and can display unwanted large initial dipole oscillations.
  NOTE 2: even if bunches are at (,0), dipole oscillations are still visible since the HOM is unloaded and assumes that the HOM is loaded. However these dipole oscillations are lower than the ones obtained when the bunches are at (,0).

## Slide 47
HOM initial conditions (unloaded vs loaded)
Case of loaded HOM.
  The Fortran code allows to set the initial phases of the bunches to values close to .
  The Fortran code allows to set the initial energy-deviations of the bunches to values close to 0.
  In the Fortran code, the residual voltage and current for the first bunch at turn 0 are computed as
    This equation represents the sum of residual voltages and currents generated by the bunches during the last turn.
    As desired, this equation implies that the HOM voltage and current are -periodic for each bunch (see below).
    The sum in the equation should be extended to all the previous turns, however the propagation properties of W listed above and the stationarity condition allow to restrict the sum to just the last revolution period.
    NOTE 1: a strong assumption was made, i.e. that all the bunches are in , with time distances which are multiple of . However the actual equilibrium phases are and the time distances aren’t multiple of .
  NOTE 2: if intensity effects are large, then the difference between and is large, therefore the bunches close to (,0) are far from their equilibrium positions and can display unwanted large initial dipole oscillations.
-> is the time distance between the bunch at the previous turn and the bunch 1 at the current turn.
-> is the distance in number of buckets between the first and the bunches.

## Slide 48
-periodicity of voltage and current for loaded HOMs
By definition, the voltage of a loaded HOM are - periodic if there is only one bunch in the ring.
The -periodicity works also for more bunches.
  Example: two bunches on a h=3 ring with one HOM.
t [s]
[1]
(n-1)
n
(n+1)
perturbation from second bunch
perturbation from first bunch
perturbation from second bunch
- periodicity is verified.

## Slide 49
Example of simulation using unloaded and loaded HOMs
DAFNE case: = 510 MeV, = 9.3 keV, = 260 kV, 14 HOMs, 100 bunches with = 15 nC in buckets 1, 2, …, 100.
The initial phases and energy-deviations are respectively and .
We plot the dipole oscillations for the bunches 1, 50 and 100 along 10000 turns.
We plot the HOM voltages seen by the bunches along 10000 turns.
Unloaded HOMs
Loaded HOMs
Bunch 1
Bunch 50
Bunch 100
The dipole oscillations remain practically the same when the HOMs are loaded.
The voltages seen by the bunches when the HOMs are unloaded converge rapidly to the voltages seen by the bunches when the HOMs are loaded.
We need a better algorithm to compute the stationary voltages of loaded HOMs.
  The stable phases are and not and so the time-distances between bunches are not multiple of .
  Finding allows also to position the bunches close to their equilibrium points at turn 0.
Bunch 1
Bunch 50
Bunch 100

## Slide 50
Improvement of the loaded-HOM algorithm
= =
,
error =
=
for = 1, …,
return , , , , ,
-> First guess for and
-> is the chosen number of iterations
Compute residual voltage and current for first bunch
Compute updated values for and
Example with only two bunches and one HOM.
The routine provides as output , , , , , .
The routine is an iterative algorithm: at each iteration the error is expected to diminish.
The routine is launched one time before the main tracking loop.
Idea behind the algorithm:
  Guess and
  and are determined
  and are determined …
The routine can be also used to compute and for unloaded HOMs.
The Fortran loaded-HOM routine is obtained setting =1 and = for all the bunches.
-> First guess for and
Compute residual voltage and current for second bunch
-> norm
=
= = 0
= , =
-> save voltages to compute error at iter. j+1
-> outputs

## Slide 51
Previous simulation using improved routine for loaded HOMs
DAFNE case: = 510 MeV, = 9.3 keV, = 260 kV, 14 HOMs, 100 bunches with =15 nC in buckets 1, 2, …, 100.
The initial phases and energy-deviations are respectively and .
Unloaded HOMs: .
  As desired, the dipole oscillations are significantly lower than the ones obtained when .
Loaded HOMs: and come from the outputs of the improved routine.
  As desired, there are no dipole oscillations and the voltages seen by each bunch are constant in time.
Unloaded HOMs (improved routine)
Bunch 1
Bunch 50
Bunch 100
Loaded HOMs (improved routine)
Loaded HOMs (Fortran routine)
Bunch 1
Bunch 50
Bunch 100
Bunch 1
Bunch 50
Bunch 100

## Slide 52
Effects of the bunch length on HOM-voltage computations
In the code, each bunch is represented by just one macroparticle.
How to take into account the actual bunch length in the HOM voltage calculations?
  In the code, the of each HOM is multiplied by and then computations are done as for a single particle. Why?
If is the longitudinal line-density of a particle-bunch crossing the RF cavity, then the residual voltage in the cavity is given by
  where [V/C] is the wakefield of the HOM.
In general, given an arbitrary , the residual voltage in the RF cavity is given by the convolution of and
  where is the charge at which affects the charge at . The particles at the head of the bunch have lower .
  The formula is indeed true if
NOTE: is called wake function or wake potential

## Slide 53
Effects of the bunch length on HOM-voltage computations
Applying the Fourier transform and using its inverse we obtain
  where is the bunch spectrum and Z is the longitudinal coupling impedance of the HOM
  The formula is indeed true if
  If is Gaussian, then
) or
Is this approximation ok?

## Slide 54
Let’s check if the following approximation can be done
We take as an example one HOM of the DAFNE RF cavity and we consider a Gaussian bunch with = 30 mm ().
or or
Green and magenta lines overlap
Close to , since the HOM bandwidth is small.
Far from , significantly differs from , but
Effects of the bunch length on HOM-voltage computations
[1]
[1]

## Slide 55
DAFNE example with one Gaussian bunch ( = 30 mm) and one HOM:
  Grad/s
Very good agreement in 0 and above between wake from Gaussian bunch and wake from single charge with correction.
There is significant disagreement if the wake from single charge is used.
We suppose that the actual bunch is Gaussian with a constant bunch-length and that all the charge is at the bunch centre.
Wake from Gaussian bunch
Wake from single charge
Wake from single charge with correction
-
Effects of the bunch length on HOM-voltage computations
[1/ns]
[1/ns]
[1/ns]
beam-loading theorem

## Slide 56
Let’s suppose to have equally-spaced bunches, each with charge , circulating in a ring with circumference .
  We assume that each bunch is described by only one macroparticle.
For each bunch , the continuous equations of motion are
  where is the induced-voltage seen by the bunch and induced by all the charges circulating in the ring.
Deriving and substituting
Changing variable from to , and then from to , we obtain
Coupled-bunch instabilities (1/12)

## Slide 57
can be obtained summing wake-function contributions over all the past revolution turns and over all the bunches
  where for and the are mod(2).
The must be all equal due to the symmetrical position of the full buckets in the ring. We call the common value.
Therefore, expanding linearly with respect to the equilibrium positions , we obtain
  where
Coupled-bunch instabilities (2/12)
We linearly expand the accelerating voltage as well
  and

## Slide 58
Substituting into the differential equation we obtain
Therefore
  where, setting for instance = 0 due to the symmetry of the charge distribution,
  and
Coupled-bunch instabilities (3/12)
For we obtain the zero-intensity zero-amplitude synchrotron frequency with synchrotron radiation
This equation can be used to compute .

## Slide 59
Coupled-bunch instabilities (4/12)
We have to solve a system of coupled second-order differential equations with the forcing term being a linear combination of the solutions themselves computed at different times.
We find a solution of the type
  with and complex quantities to be determined.
Substituting into the differential equation we obtain
  where the sum over could be extended for negative values since if .
From the definition of the longitudinal coupling impedance we have

## Slide 60
Coupled-bunch instabilities (5/12)
Multiplying by the exponential, summing over and using one property of the delta function, we have
Substituting
Defining

## Slide 61
Coupled-bunch instabilities (6/12)
  we obtain the system of linear equations
  where we imposed that all the are equal, calling the common value.
From linear algebra, we know that this system of equations has complex eigenvalues , .
  A set of eigenvectors ( ) is associated to each .
The square matrix is said circular since it satisfies the property
Since is circular, then the eigenvalues are given by

## Slide 62
Coupled-bunch instabilities (7/12)
If is a multiple of ( integer), then the last sum is equal to , otherwise
Therefore the eigenvalues are
  where is called coupled-bunch mode.
Given a certain , an important property of the corresponding eigenvectors can be obtained from
It follows that

## Slide 63
Coupled-bunch instabilities (8/12)
Given , the solutions of the original differential equation are
  where we highlighted the dependency of from , since is the solution of
  If e.g. , then and all the bunches oscillate in phase (“0 mode”);
  If e.g. with even, then and pairs of consecutive bunches oscillate in antiphase (“ mode”);
  For , it occurs that mod().
Example of “ mode” scheme for 3 bunches:
Turn 0
Turn
  If is complex with negative imaginary part, then grows exponentially in time and the bunch is unstable.
Given , the phase-shift between consecutive bunches is given by

## Slide 64
Coupled-bunch instabilities (9/12)
To estimate the grow-rates of the unstable bunches, we assume that .
Therefore, rearranging the terms,
Taking the real and imaginary parts of
The imaginary part of the impedance leads only to a shift of the angular frequency of the bunch oscillation.
Since for all frequencies, the bunch instability is caused by the real part of the impedance with .

## Slide 65
Coupled-bunch instabilities (10/12)
To summarize, for a given , we have
The bunches are unstable if and only if
If is given by a resonator impedance, then
  Therefore we can compute numerically limiting the sum to indices , with sufficiently large.
  After having computed with the formula shown earlier, can be evaluated with

## Slide 66
Coupled-bunch instabilities (11/12)
The expression for assumes that each bunch is represented by just one macroparticle.
  This assumption is also done in the macroparticle code and therefore there is consistency.
  However, as explained earlier, all the HOM shunt-impedances were rescaled in the code to take into account that bunches have a Gaussian profile.
  To have again consistency, we need to correct assuming that bunches have a Gaussian profile.
    All the steps done previously to arrive at can be repeated changing
    where is the voltage induced by a Gaussian bunch at a distance from its centre of mass.
Therefore the can be corrected as
  This expression can be refined even more using a correction factor involving a Bessel function (derivation from Vlasov equation).
    However, the proposed exponential factor is more consistent with the type of shunt-impedance rescaling done in the code.
The assumption that in the argument of can be strong since varies rapidly with frequency due to the high .
  If the beam-spectrum couples with at essentially just one frequency, then we can solve directly the equation for .
or equivalently

## Slide 67
Indeed, calling the index associated to the unique coupling frequency, the equation to solve is
Assuming that and that , the impedance term can be expressed as
Therefore
  where the complex constants , and are
Rearranging the terms we obtain this quadratic equation in
  and the desired is the smallest solution in absolute value. The grow-rate is the imaginary part of .
Coupled-bunch instabilities (12/12)
where

## Slide 68
Coupled-bunch oscillations: beam spectrum (1/2)
We fix the coupled-bunch mode and we assume that each bunch-profile is a delta function.
At turn , the bunch arrives at a fixed point of the ring at time
  where we assume that all the bunches have the same oscillation amplitude .
The beam current can be written as

## Slide 69
Coupled-bunch oscillations: beam spectrum (2/2)
Therefore the beam spectrum can be written as
The beam spectrum is discrete and its lines are situated at .
  If , then and the lines are at .
We saw that, for bunches having a delta profile, the grow-rate of the coupled-bunch instability is
  The electromagnetic interaction between the different bunches is due to the multiplication of the beam coupling-impedance with the beam spectrum with .
    Only the beam spectrum-lines with (dipolar motion) are significant to evaluate the coupled-bunch instability.
    This is consistent with the adopted macroparticle model, where each bunch has no internal structure and therefore the spectrum lines with (quadrupolar motion etc.) can’t be excited.

## Slide 70
, keV, kV, MHz, MHz, kHz.
4 equally-spaced bunches, bunch-current = 15 mA, = 20 mm.
4 coupled-modes . The phase between consecutive bunches is .
One HOM of the accelerating cavity has MHz, k,
  We want to excite a certain coupled-bunch mode with this HOM.
    and are always kept constant, whereas is shifted to obtain the desired coupling between beam-spectrum and impedance.
The critical frequencies which can lead to instability are negative and given by
  We want to excite only the mode through the line at , with .
    Since is symmetric with respect to the axis , and assuming that , we set at
  is the line-frequency closest to and some coupling could occur, although the is quite large.
    In any case and therefore the mode (mod 4) is damped and not excited.
Example for the DAFNE ring: coupled-bunch instability (1/7)
Accelerating cavity
Scheme of 4 equally-spaced bunches in the ring

## Slide 71
Example for the DAFNE ring: coupled-bunch instability (2/7)
We want to excite .
  If , then MHz.
  The high leads to a small coupling (damping) of .
At turn 0, the four bunches start with different initial conditions.
  The maximum oscillation amplitude is 0.3 mrad = 0.13 ps.
Frequency [MHz]
[k]
Zoom
Bunch 1
Bunch 31
Bunch 61
Bunch 91
Phase oscillations of the four bunches along the first 100000 turns
Zoom (0-200 turns)
Zoom (14.75k-15k turns)
Real part of the HOM longitudinal impedance
Exponential growth of oscillations in the first roughly 15000 turns, then convergence to an equilibrium due to wake-field/RF-voltage non-linearities and synchrotron radiation.
At equilibrium the four bunches oscillate with roughly the same amplitude of 1.32 rad = 570 ps.
  The instability is fast and strong.
After a certain transient time and during the exponential growth, the bunches oscillate in phase, i.e. .
  The bunches aren’t in phase anymore at equilibrium.
Zoom (99.75k-100k turns)

## Slide 72
Example for the DAFNE ring: coupled-bunch instability (3/7)
We want to excite .
  If , then MHz.
  The high leads to a small coupling (damping) of .
The initial conditions of the bunches are the same as those chosen for (the maximum oscillation-amplitude is 0.3 mrad = 0.13 ps.)
Frequency [MHz]
[k]
Phase oscillations of the four bunches along the first 100000 turns
Zoom (0-200 turns)
Zoom (14.75k-15k turns)
Real part of the HOM longitudinal impedance
Exponential growth of oscillations in the first roughly 12000 turns, then convergence to an equilibrium due to wake-field/RF-voltage non-linearities and synchrotron radiation.
At equilibrium the four bunches oscillate with roughly the same amplitude of 1.40 rad = 604 ps.
  Instability even faster and stronger than for .
After a certain transient time, consecutive bunches oscillate in quadrature, i.e. .
  This phase difference isn’t preserved at equilibrium.
Zoom (99.75k-100k turns)
Bunch 1
Bunch 31
Bunch 61
Bunch 91
Zoom

## Slide 73
Example for the DAFNE ring: coupled-bunch instability (4/7)
We want to excite .
  If , then MHz.
  The high leads to a small coupling (damping) of .
The initial conditions of the bunches are the same as those chosen for (the maximum oscillation-amplitude is 0.3 mrad = 0.13 ps.)
Frequency [MHz]
[k]
Phase oscillations of the four bunches along the first 100000 turns
Zoom (0-200 turns)
Zoom (14.75k-15k turns)
Real part of the HOM longitudinal impedance
Exponential growth of oscillations in the first roughly 15000 turns, then convergence to an equilibrium due to wake-field/RF-voltage non-linearities and synchrotron radiation.
At equilibrium the bunches 61 and 91 have the largest oscillation amplitude of 1.31 rad = 566 ps.
  Instability comparable to that obtained for .
After a certain transient time and during the exponential growth, the bunches oscillate in antiphase, i.e. .
  This phase difference isn’t preserved at equilibrium.
Zoom (99.75k-100k turns)
Bunch 1
Bunch 31
Bunch 61
Bunch 91
Zoom

## Slide 74
For each analysed case (, 1, 2) we plot the longitudinal phase space for the first 15000 turns.
  The oscillation amplitudes grow exponentially (the value-limits on the axes are modified every 5000 turns for better visualization).
  All the phases are mod so that the evolution of the different bunches can be seen on the same bucket.
After a certain number of turns:
  : Consecutive bunches oscillate in phase () and the four bunches are superimposed.
  : Consecutive bunches oscillate in quadrature () and the four bunches coincide with vertices of squares.
  : Consecutive bunches oscillate in antiphase (), bunches 1 and 61 are superimposed, bunches 31 and 91 are superimposed.
Example for the DAFNE ring: coupled-bunch instability (5/7)
mod 2 [+1.5 rad]
mod 2 [+1.5 rad]
mod 2 [+1.5 rad]

## Slide 75
Example for the DAFNE ring: coupled-bunch instability (6/7)
Finally we compute in simulation the grow-rate of bunch oscillations and compare them with analytical estimations.
  As an example we consider the following six cases in simulation.
Bunch 1, fit from turn 4k to 15k
Bunch 1, fit from turn 0 to 10k
Bunch 1, fit from turn 7k to 15k
Time [s]
mod 2 [rad]
Time [s]
mod 2 [rad]
Time [s]
mod 2 [rad]
Bunch 31, fit from turn 4k to 15k
Time [s]
mod 2 [rad]
Bunch 31, fit from turn 0 to 10k
Bunch 31, fit from turn 7k to 15k
Time [s]
mod 2 [rad]
Time [s]
mod 2 [rad]
  As expected from theory, given a certain the grow-rates are practically the same for all the bunches.
  As already seen, the largest grow-rate occurs for , whereas the grow-rates for and are essentially the same.
The analytical damping-rate due to synchrotron radiation is 1/s ( turns).

## Slide 76
Example for the DAFNE ring: coupled-bunch instability (7/7)
To analytically estimate the total grow-rate (including synchrotron radiation) we use the two formulas discussed earlier
  ‘Explicit’ formula
  ‘Implicit’ formula
Comparison of values from simulations and analytical estimations.
 | [1/s] for | [1/s] for | [1/s] for
From simulation | 1588, 1583 | 1642, 1639 | 1589, 1584
Analyt. explicit | 1542 (2.8%) | 1588 (3.3%) | 1542 (2.8%)
Analyt. implicit | 1636 (3.1%) | 1631 (0.6%) | 1635 (3.0%)
From simulation | 1588, 1583 | 1642, 1639 | 1589, 1584
Analyt. explicit | 1542 (2.8%) | 1588 (3.3%) | 1542 (2.8%)
Analyt. implicit | 1636 (3.1%) | 1631 (0.6%) | 1635 (3.0%)
The explicit formula confirms that is the largest for and that is the same for and .
  These values are lower than those found in simulations by just 3%.
The implicit formula provides essentially the same for each .
  The maximum discrepancy with simulations is just 3%.
The discrepancies between from simulations and analytical estimations are in %.
Why the implicit formula, expected to be precise, overestimate if or ?
  If then and if then , so the implicit formula neglects the line at positive frequencies which contributes to a small damping of the mode and to a decrease of .
  If then , so in this case the neglected damping refers to mode 3 and therefore doesn’t affect the mode 1.
If the implicit formula has to consider also the line at positive frequencies, then a cubic equation in must be solved.
The with the smallest magnitude is considered
It’s safe to set 100 since the critical is -66

## Slide 77
Contents
Introduction.
Single-particle longitudinal beam-dynamics with synchrotron radiation.
  Equations of motion, synchrotron radiation, small-amplitude synchrotron oscillations, …
Longitudinal beam-dynamics with synchrotron radiation and Higher Order Modes (HOMs).
  HOM induced voltage, synchronous phase shift, HOM initial conditions, coupled-bunch instabilities, …
Longitudinal beam-dynamics with synchrotron radiation, HOMs and bunch-by-bunch feedback.
  Models of the feedback components, grow and damping-rates, cavity-kicker, ideal and real corrections, …
Conclusions and suggested next steps.
Appendices.
  Execution of the new-Python and old-Fortran codes, structure of the code, exponential fits in Python, …
References.

## Slide 78
Bunch-by-bunch longitudinal feedback
Let’s suppose that
  We have only one bunch circulating in the DAFNE ring.
  The bunch intensity is very low, so that the induced voltages can be neglected.
  The bunch is injected into the ring with a phase error of 0.23 rad with respect to .
Simplifying a lot, the DAFNE bunch-by-bunch longitudinal feedback
  measures the last synchrotron oscillation of the bunch phases;
  shifts this synchrotron oscillation by - to obtain a sinusoidal function in anti-phase with respect to the oscillation.
  applies this shifted synchrotron oscillation as an energy correction to the bunch during the next synchrotron oscillation.
Turn [1]
Phase [rad]
0.1
0.0
-0.1
Phase [rad]
[%]
The particle performs synchrotron oscillations in phase space.
The phase and energy oscillations are sinusoidal functions with initial phases which differ by
How to actively damp these phase and energy oscillations?
[%]

## Slide 79
Bunch-by-bunch longitudinal feedback in DAFNE
The energy correction is provided by a so-called kicker, which can be an RF cavity, as in DAFNE, or a stripline structure.
Here is a simplified scheme of the bunch-by-bunch longitudinal feedback used in DAFNE.
  When multiple bunches circulate in the ring, the feedback acts on each bunch independently from the other bunches.
Longitudinal pickup
(wide-band between 4 and 6)
Cavity-kicker
Comb-filter generator
(used to minimize the noise and tuned at 4 or 6)
Local oscillator (LO)
(signal at 4 or 6 and in quadrature with respect to the bunch-signal)
Bunch
Mixer
(used to mix the bunch and LO signals)
Low pass filter
(used to obtain the low-frequency content of the signal)
FPGA
(uses digital filters to shift the phase oscillation by -).
ADC
(conversion from analog to digital signal).
DAC
(conversion from digital to analog signal).
Beam orbit
The phase oscillation is obtained when the low pass filter is applied.
The shift of this oscillation by - is done in the FPGA using a digital filter.
The shifted oscillation is converted back to analog and provided to the kicker.
Amplifier
Amplifier
Attenuator
Attenuator
Amplifier
Amplifier

## Slide 80
Longitudinal pickup: special-button BPM
The Beam Position Monitors (BPMs) are the main diagnostic tools in DAFNE.
  They consist of four “button” electrodes mounted flush with the vacuum pipe.
In each DAFNE ring, special-button BPMs can measure individual time offset on a bunch-by-bunch basis, i.e. without memory of the preceding bunch.
These special-button BPMs must
  have a reasonably high transfer impedance and shouldn’t have narrow-band resonances in the frequency-range of interest:
    in DAFNE the frequencies of interest are between 4 = 1.47 GHz (30 bunch operation) and 6 = 2.21 GHz (120 bunch operation);
    the necessary design value of is in the region GHz.
  keep the beam coupling impedance and parasitic losses within acceptably low values.
  NOTE: in general these two impedances grow together (e.g. with the increase of the button radius), so a compromise must be found.
For the longitudinal feedback, one special-button BPM is chosen out of two available.
  this BPM measures the bunch current summing together the signals coming from the four button electrodes.

## Slide 81
Analytical formulae for the electrode impedances
The transfer impedance of a button electrode is the complex ratio between the voltage induced by a centred beam at the external termination of the detector circuit and the beam current.
  where is the so-called coverage factor, with and the button and beam-pipe radii;
  is the characteristic impedance of the coaxial cable connecting the button to the detector circuit;
  , with the electrode capacitance; is the inverse of the electrode traversal time.
The frequency response of is of the high-pass type since
In first approximation, the coupling impedance is simply
Multiplication by .
The electrode acts like a time differentiator.
The asymptotic response is purely resistive.
The electrode voltage is in phase and proportional to the beam current.
For low frequencies
  For high frequencies

## Slide 82
Longitudinal pickup: transfer and coupling impedances
Frequency [GHz]
[]
The coupling impedance is indeed roughly proportional to the transfer impedance.
In the working region the button transfer impedance is sufficiently flat with a satisfactory value of 0.43 .
The button low-frequency impedance is relatively small and is acceptable from the beam dynamics point of view.
The first stronger HOM at 5.2 GHz is not dangerous to the multibunch instabilities due to its low .
F. Marcellini et al. (1996)
Working region
Button transfer impedance from the HFSS code
F. Marcellini et al. (1996)
Frequency [GHz]
Re []
BPM coupling impedance from the HFSS code
First stronger HOM
Simulations were performed in 1996 to estimate the transfer and coupling impedances of the DAFNE special-button BPMs .

## Slide 83
Phase detection for a signal coming from the pickup
The analog front-end of the longitudinal feedback is designed to measure , which is the time of arrival of each bunch relative to the RF master oscillator clock.
  Equivalently, the goal is to measure , i.e. the difference between the bunch phase and the synchronous phase.
The bunch-signal coming from the pickup is a short differentiated pulse.
  We can numerically reproduce the electrode transfer function and apply it to the typical DAFNE bunch current.
If such a short pulse is used for phase detection, the obtained signal will be also a short baseband pulse.
  The sampling of this signal by the ADC clock will be very sensitive to pulse and clock timings.
Simulated Gaussian bunch with = 20 mm
Grad/s
The low frequency regime (differentiation) dominates

## Slide 84
Stripline comb generator
Measured BPM signal (8 bunches) and comb output (8
4-cycle tone bursts at 6) at PLS, South Korea
To avoid this sampling sensitivity, the pickup signal is ‘lengthened’ by feeding it into a comb generator.
  Planar stripline circuit made from a copper-clad teflon material and then gold plated to lower the losses.
The comb generator converts the pickup signal of a bunch into a tone burst of a few cycles at an harmonic of .
When the bunch-spacing is , 4-cycle tone bursts at 6 are often used (as in PEP-II, PLS).
  The tone burst must be shorter than the bunch spacing to minimize the interbunch crosstalk.
  Some margin is left since the actual bunch-spacing can be less than : adjacent bunches
    have non-zero bunch length;
    can oscillate not in phase.
When a burst is phase-detected, the baseband phase-signal has a rectangular envelope with duration equal to that of the input burst.
  The sampling of the phase-signal is less sensitive to pulse and clock timings.
J. D. Fox et al. (2007)
4-cycle comb generator at 6 used for PEP-II
Signal from PU
Comb output
J. Y. Huang,
M. Kwon (2000)
Differentiated Gaussian bunch

## Slide 85
Stripline comb generator at 4: measurements (1/2)
Measurements of the frequency response of DAFNE comb-generators were performed at INFN using a VNA (G. Franzini, D. Pellegrini, D. Quartullo).
  Considered frequencies between 300 kHz and 8.5 GHz (maximum possible).
First measured comb generator: 5-tone-burst at 4 = 1.47 GHz.
The frequency response is made of sinc-like functions at 1.50 GHz (), 4.47 GHz ( = 4.42 GHz), 7.44 GHz ( = 7.37 GHz).
We reproduce in simulation the comb-filter in time and frequency domain.
  We suppose that the comb-filter in time domain is ‘a smoothing’ of the derivative of a 1.47 GHz square-wave.
    Sinc functions at 4(2+1) (=0,…) in frequency domain.
Good agreement between measurements and simulations.
5-cycle comb generator at 4
Measured frequency response
Simulated comb-filter in time domain at
Time [ns]
Comb filter [a.u.]
Frequency [GHz]
Simulated comb-filter in frequency domain at
Comb filter [a.u.]

## Slide 86
Measurements of the response of the comb-generator in time domain were then performed.
  An impulse-generator and an oscilloscope were used.
A pulse of 456 ps length was generated and sent to the comb-generator.
  It was not possible to have shorter pulses without decreasing the signal amplitude.
  The pulse length was 2/3 of the square-wave period (equal to 680 ps).
The oscilloscope provides as output a sine-like 5-cycle tone burst with period of 678 ps or frequency of 4.
This output is reproduced in simulation convolving the reconstructed pulse with the comb-filter in time domain.
  The pulse acts like a low-pass filter which keeps only the sinc at 4.
Impulse of length 456 ps
Setup with generator (down), comb (middle), oscilloscope (top)
Zoom on the output of the oscilloscope
Time [ns]
Pulse [a.u.]
Simulated pulse with
456 ps end-to-end length
Convolution between simulated pulse and comb filter in time domain
680 ps
Time [ps]
Pulse spectrum [a.u.]
456 ps
Frequency [GHz]
Comb filter, product [a.u.]
Simulated pulse spectrum, comb filter and their product
Convolution [a.u.]
Stripline comb generator at 4: measurements (2/2)

## Slide 87
5-cycle comb generator at 6
Measured frequency response
Measurements were then repeated for another comb generator: 5-tone-burst at 6 = 2.21 GHz.
The frequency response is made of sinc-like functions with frequencies at 2.27 GHz (), 6.76 GHz ( = 6.64 GHz).
We reproduce in simulation the comb-filter in time and frequency domain.
  We suppose that the comb-filter in time domain is ‘a smoothing’ of the derivative of a 2.21 GHz square wave.
    Sinc functions at 6(2+1) (=0,…) in frequency domain.
Good agreement between measurements and simulations.
Simulated comb-filter in time domain at
Time [ns]
Comb filter [a.u.]
Frequency [GHz]
Simulated comb-filter in frequency domain at
Comb filter [a.u.]
Stripline comb generator at 6: measurements (1/2)

## Slide 88
Impulse of length 456 ps
Setup with generator (down), comb (middle), oscilloscope (top)
Zoom on the output of the oscilloscope
Time [ns]
Pulse [a.u.]
Simulated pulse with
456 ps end-to-end length
Convolution between simulated pulse and comb filter in time domain
453 ps
Time [ps]
Pulse spectrum [a.u.]
456 ps
Frequency [GHz]
Comb filter, product [a.u.]
Simulated pulse spectrum, comb filter and their product
Convolution [a.u.]
Measurements of the response of the comb-generator in time domain were then performed.
A pulse of 456 ps length was generated and sent to the comb-generator.
  The pulse length was comparable to the square-wave period (equal to 452 ps).
The oscilloscope provides as output a sine-like 5-cycle tone burst with period of 439 ps or frequency of 6.
This output is reproduced in simulation convolving the reconstructed pulse with the comb-filter in time domain.
  The pulse acts like a low-pass filter which keeps only the sinc at 6.
Good agreement between measurements and simulations, as for the case of the comb at 4.
Stripline comb generator at 6: measurements (2/2)

## Slide 89
Comb-generator as a filter
The simulated comb-filter, confirmed by measurements (see before), was applied in simulation to the signal coming from the pickup.
  As an example, we considered a 4-cycle comb-filter at 6.
The bandwidth of a sinc is equal to
Simulated comb-filter in time-domain
Simulated comb-filter in frequency-domain
4.5
Therefore in DAFNE the actual bunch current ( Gaussian) is filtered first by the pickup and then by the comb generator.
7.5
6
6
6
1
1
1
  The signal coming from the pickup acts as a band-pass filter which keeps only the sinc at 6.

## Slide 90
We consider one synchrotron period in DAFNE and we simulate the output-signal coming from the comb-generator.
  Three different input-signals are used.
  The macroparticle code is not used here. Synchrotron oscillations are obtained by simply shifting the input signal by
First example: We obtain by convolving the numerically reconstructed comb-filter in time domain with a delta signal arriving at time .
Time signal before and after the comb generator (1/3)
[a.u.]
[a.u.]
  The output from the comb generator is the filter itself shifted by .
  The relative phase between and is preserved over time.
    Required for phase detection.
  This model is not realistic since the signal entering the comb-generator is not a delta function, as shown before.
= cos(
: oscillation amplitude = 0.1 rad
: turn number

## Slide 91
Second example: The input signal is Gaussian with mean and with = 20 mm or 30 mm.
  We obtain by convolving this signal with the comb-filter in time domain
  The output of the comb generator is sinusoidal with frequency 6.
    The filter sinc-functions at higher frequencies are made negligible by the Gaussian spectrum.
  The relative phase between and is preserved over time. This is essential for phase detection.
    With respect to the mean of , this phase difference is equal to and is larger for longer bunches.
  For large , is amplitude-modulated in correspondence of the first and fourth periods (amplitude ).
  This better model is not realistic yet since the comb-generator input is not Gaussian, but a differentiated Gaussian.
[a.u.]
Time signal before and after the comb generator (2/3)
[a.u.]
[a.u.]
( = 20 mm)
( = 30 mm)
[a.u.]
[a.u.]

## Slide 92
Third example (realistic): The input signal is a differentiated Gaussian.
  This signal is obtained by applying to a Gaussian profile with mean and with = 20 mm or 30 mm.
  We obtain by convolving the input signal with the comb-filter in time domain.
  has essentially the same features of the computed for Gaussian inputs (second example).
    It is sinusoidal with frequency 6.
    The phase difference between and the mean of the Gaussian profile is and constant over time.
    extends to the adjacent bucket, leading to possible coupling between phases of consecutive bunches.
Time signal before and after the comb generator (3/3)
[a.u.]
[a.u.]
, [a.u.]
+
+
= 20 mm
= 30 mm
, [a.u.]

## Slide 93
Voltage from the comb generator
The signal exiting the comb generator goes through an attenuator, which is followed by an amplifier.
Characterizing better the proportionality factor, is equal to:
  is proportional to:
    the total bunch current ;
    the magnitude of the button transfer impedance , which is constant (= 0.43 ) in the working region, i.e. around 4 or 6;
    the coefficient , accounting for the attenuation provided by the pickup-attenuator, which is able to control the level of signal measured by the pickup;
    the coefficient , which accounts for the attenuation-level provided by the comb-generator and the attenuator placed after it;
    the gain of the amplifier placed after the comb generator;
    the amplitude modulation , which can be different from 1 in correspondence of the first and fourth periods of the sinusoidal tone burst.

## Slide 94
Local oscillator and mixer
The local oscillator is locked to the ring RF clock and produces a sinusoidal signal with frequency 6
  where is adjusted by using a phase shifter (servo), so that
    is in quadrature with respect to the sinusoidal ;
    is the phase advance of the comb-voltage relative to the bunch centre of mass minus the synchronous phase
Therefore
and are multiplied together in the mixer

## Slide 95
Low-pass filter
A low-pass filter is then applied to to eliminate the high-frequency component of the mixer output
More in general we have
  where is the conversion efficiency of the mixer;
  where or 6 depending on the DAFNE operation mode;
  where
    being an error phase accounting for the possible coupling between consecutive bunches when a tone burst reaches the adjacent bucket (as shown earlier);
    being an error phase present when the phase advance of the comb-voltage relative to the bunch centre of mass is not compensated (as shown earlier);
    being a phase offset which one can adjust to compensate the other phase errors.
For small phases

## Slide 96
Example continued: mixer
DC component (signal average)
High-frequency component at 1
6
1
  Qualitatively
[a.u.]
Frequency [GHz]
, , [a.u.]
Third example continued: is the comb-generator output when the input is a differentiated Gaussian signal, = 20 mm.
  We suppose first that the local oscillator can’t compensate for .
  We compute numerically and its Fourier transform along one synchrotron period.
[ns]
DC component
3

## Slide 97
Example continued: low-pass filter
  Qualitatively
We apply a Bessel low-pass filter to in order to obtain only the DC component of .
  A baseband Bessel low-pass filter was used at PEP-II.
  In simulation the filter has order 4 and the gain magnitude is -3 dB at 3.
6
, , , [a.u.]
[ns]
||[a.u.]
1
3
1
Frequency [GHz]
  doesn’t oscillate around zero due to the lack of compensation for .
  extends to the adjacent bucket, leading to potential coupling in phase detection.
, [a.u.]
DC component
+

## Slide 98
  Qualitatively
  At each turn, the time-span where is constant is relatively large thanks to the tone-burst technique.
    In this time-span (no amplitude modulation in ), therefore we assume that .
    The ADC clock could for instance sample in correspondence of the orange line at each turn.
  still extends to the adjacent bucket, leading to potential coupling in phase detection.
Example continued: phase compensation
If the reference signal from the local oscillator can compensate for the phase error then oscillates around zero and consequently the phase detection is correct.
6
, , , [a.u.]
[ns]
1
3
Frequency [GHz]
DC component
, [a.u.]
||[a.u.]
+
ADC clock

## Slide 99
Phase detection and input for ADC
In the macroparticle code is already known at each turn,
  is known from the tracking and the constant can be easily computed.
  The signal manipulations shown in the last slides (Gaussian profile, button transfer impedance, comb-generator, etc.) can’t be directly applied in the code since each bunch is represented by just a macroparticle.
    However the Python routines able to perform these signal manipulations are available for separate analysis.
In the code we directly compute
  where phase errors can be included through (bunch coupling) and (phase advance of the comb-voltage).
If intensity effects are large, then the synchronous phase is and this shift can’t be neglected. Therefore, from
  we see that, even when , we have to compensate the synchronous-phase shift due to the HOMs.
    This can be done in the code since can be computed with the new Python routine;
    In operation, an input-offset can be set in the phase-servo-loop panel in order to obtain the desired compensation.
Before entering into the ADC, passes through an amplifier with gain .
  Noise can also be added in the code and the input voltage for the ADC is , where is a sample from a Gaussian distribution with mean 0 and rms .

## Slide 100
ADC processing
Let’s suppose that the number of bits for the ADC is .
With we can represent the signed numbers
The ADC converts a mixer-voltage (real number) into an output (integer number)
Calling the maximum input voltage for the ADC
For other values of , we divide the interval into sub-intervals with length

## Slide 101
Therefore we have the correspondences
The relations are
If , then the above relation yields a non-integer number and we take the integer part of it
In DAFNE and therefore the conversion formula is
NOTE: bug in the Fortran code, the formula on the left is used even when
ADC processing

## Slide 102
ADC processing: DAFNE examples
Simulation of an oscillating bunch. Phase amplitude of 0.1 rad, no intensity effects, no action of the feedback.
  We plot the voltage signal entering the ADC and the ADC output ( = 200 mV).
Phase oscillations around
[rad]
Input voltage for ADC between 200 mV
Turn [1]
Turn [1]
Turn [1]
[V]
[1]
ADC output between -127 and 128
[V]
Turn [1]
[1]
Saturated
Not saturated
Turn [1]
Too high gains can lead to signal saturation in the ADC.

## Slide 103
FPGA: introduction
The ADC output is processed by the FPGA (Field Programmable Gate Array), which is a configurable integrated circuit.
The goal of the FPGA is to shift the signal by , so that the output signal is in anti-phase with respect to the energy oscillation of the bunch.
The shift by is performed applying a FIR (Finite Impulse Response) filter to the signal.
  FIR: the filter is not recursive, i.e. the output is not used in the input.
Different filters can be programmed in the FPGA, although the sinusoidal one is generally used in DAFNE operation.
Xilinx FPGA used in DAFNE
A. Drago (2007)
Concerning the sinusoidal filter, a convolution is performed between the signal, evaluated along the last synchrotron period, and the sinusoidal function with angular frequency and phase . At time , the FPGA output is
  where is the gain of the FPGA;
  are equidistant bunch arrival-times when the feedback operates (we call the time interval);
  is the number of filter taps and is such that .

## Slide 104
FPGA: shift of the input-signal using a convolution
Why this convolution is able to shift the signal by ? We start from the expression
If is small, this expression can be approximated with an integral
  where is the number of synchrotron periods along which and are evaluated;
  where and are respectively the amplitude and phase of .
Therefore we have the transformation
  if = 0, then is shifted by as desired.

## Slide 105
FPGA: frequency response of the sinusoidal filter
We compute the frequency response of the filter, assuming an arbitrary small time-step.
  We take as an example DAFNE with = 28.72 kHz. The filter has phase = 0.
Frequency [kHz]
Frequency [kHz]
[a.u.]
Phase of [rad]
-
Frequency [kHz]
Frequency [kHz]
[a.u.]
Phase of [rad]
The absolute value of the filter Fourier-transform is a sinc-like function.
  The maximum value occurs at and approaches as increases.
The phase decreases linearly with frequency and has discontinuities where = 0.
  The phase is - in correspondence of as expected.
If the input signal has , then the phase has to be as close as possible to - .
  is preferable to since the phase slope is higher.
-

## Slide 106
FPGA: down sampling factor (1/5)
Let’s suppose that the feedback operates every turns. is an integer called down-sampling factor.
Using a down-sampling factor larger than 1 has pros and cons.
Advantage: the number of operations per unit-time performed in the FPGA is reduced by factor .
  Computations on 1/ of the original data, moreover the time available to do the computations is times longer.
  The saved computational time can be used to do more complicated filter-calculations and/or treat more bunches.
Disadvantage: the feedback doesn’t provide the proper correction at each revolution turn, but just every turns.
  The last computed correction is given until a new correction is evaluated.
In theory, according to the Nyquist theorem, can be as low as in order to properly reconstruct the sinusoidal synchrotron oscillation of the bunch.
  Two samples per period ( = 2) are sufficient to detect amplitude and phase of the synchrotron oscillation.
In practice, the synchrotron oscillations are not perfectly sinusoidal, for instance when the bunch is far from the synchronous phase or when intensity effects are high.
  Moreover, the two samples are useless if they are close to zero.
    This can happen when the sampling times are close to the zero crossings of the sine function.
Usually in operation .

## Slide 107
FPGA: down sampling factor (2/5)
As seen earlier, is shifted by - when convolved with .
  Both signals should extend over one synchrotron period and should be zero.
Using taps means to divide the synchrotron period into intervals, each with length .
1/ is the number of revolution turns necessary for a particle to perform one synchrotron period.
  Assuming that 1/ is an integer multiple of , then
Therefore the following three expressions are all equivalent
When (as usual) 1/ isn’t an integer multiple of , we use the first of these three expressions.
  The time step of is , which is also the time step of . This is required to perform a proper convolution.
  However it’s usually not possible to cover exactly one using this expression, as instead it occurs using the third one.

## Slide 108
FPGA: down sampling factor (3/5)
The previous formula doesn’t take into account the following two delays.
  Feedback delay: the feedback-correction computed at turn is not provided to the bunch at turn .
    In the macroparticle code we assume that this correction is given at turn .
  Hold-buffer delay: The feedback-correction computed at turn is the one given to the bunch for all the times between and .
    The feedback-correction at turn is computed as if the turn is not but + .
The filter sinusoidal function has to compensate these two delays with a constant phase offset
The filter sinusoidal function is not supposed to add DC components to the output signal.
  Even if the integral of the sine function on one period is zero, discretizations can add a non-zero DC component.
  Therefore the average of the filter-coefficients is subtracted from each .
Therefore we have
Feedback delay
Hold-buffer delay

## Slide 109
There is still one correction to be added to .
To see this, we compute again the frequency response of the sinusoidal filter.
  This time we take into account the two delays in and the fact that the samples are taken every turns.
  Used parameters in this example: from DAFNE, = 28.7 kHz, , = 16, .
FPGA: down sampling factor (4/5)
[a.u.]
Phase of [rad]
Phase of [rad]
Frequency [kHz]
Frequency [kHz]
Turn [1]
[a.u.]
Frequency [kHz]
-
-
- +
Frequency response: phase
Zoom on the phase plot
  is due to two independent reasons:
    the filter function can’t cover exactly one ( even if ideally the time step is arbitrarily small);
    the time step is not arbitrarily small ( even if ideally one is exactly covered)
Phase error
Filter coefficient
Frequency response: modulus
Zoom
(0 DC)

## Slide 110
FPGA: down sampling factor (5/5)
Iterative procedure in the new Python code to compensate for this phase error:
  Iteration 1: is subtracted from , i.e. the new is .
    In this way the phase frequency-response at becomes as desired.
    However, since the time step is not arbitrarily small, changing leads to a non-zero DC component.
  Iteration 2: the average of the filter coefficients is subtracted from the coefficients themselves.
    In this way the DC component is zero.
    However, this subtraction changes the phase frequency-response at which is not anymore.
  Iteration 3: the new is subtracted from , i.e. the new is .
  Iteration 4: …
The iterations repeat until the filter has zero DC component and the phase frequency-response at is sufficiently close to .
  Usually few iterations are needed to reach convergence.
    In our example 10 iterations diminish the phase error from 5.6 rad to 1.3 .
Turn [1]
[a.u.]
[a.u.]
Phase of [rad]
Frequency [kHz]
Frequency [kHz]
[a.u.]
Phase of [rad]
Frequency [kHz]
Frequency [kHz]
Zoom
on abs plot
Zoom
on phaseplot

## Slide 111
DAC processing and ideal voltage
The DAC (digital-to-analog converter) converts the digital output of the FPGA into analog values.
  The inputs of the DAC must be integers between and , where is the number of bit for the DAC (in DAFNE ).
  As a function of time, the output of the DAC is a continuous piecewise-constant function.
    The discontinuities are located in correspondence of the bunch arrival-times when the feedback operates, i.e. those times which are multiple of .
If represents the maximum voltage which the cavity-kicker can provide to the bunch, then the analog values given by the DAC represent the fractions of which the cavity-kicker should provide to the bunch to damp its oscillations.
  The feedback provides the values of the requested voltages, whereas the actual voltages are produced by the cavity kicker and its generator.
  We denote the voltage values requested by the feedback with .
    As shown later, these values are ideal since the bunch can see in reality only approximations of them.
The output of the DAC and are given by
  where is the gain of the DAC and the operator int() takes the integer part of ;
  if , then ;
  if , then .

## Slide 112
If we assume that the cavity-kicker can provide exactly the voltage requested by the feedback, the equations of motion are
Equations of motion in the code: RF+SR+HOM+FB (simplified)
Small bug in the Fortran code: the kicker voltage applied to the last bunch is wrong if the first bucket is empty.
Accelerating cavity (RF + HOMs)
Ideal kicker (correction)
  where is the voltage provided by the kicker to the bunch at turn .
    usually changes from bunch to bunch and, for a given bunch, changes every turns.
    If for instance , then is evaluated using and not since the feedback-kicker system acts with a delay of one turn.
The equations of motion assume that the two cavities are point-like and placed at the same spot in the ring. The bunch starts at the exit of the accelerating cavity and in order
  drifts along the ring (first equation of motion);
  loses energy by synchrotron radiation;
  receives the energy-kick from the cavity-kicker;
  receives the energy-kicks (accelerating and HOM-induced) from the accelerating cavity.
Synchrotron radiation

## Slide 113
Small amplitude synchrotron frequency with SR and FB (1/3)
We neglect collective effects and we assume that
  ;
  the feedback-kicker system acts with no delay;
  is small relative to .
The discrete equations of motion can be made continuous as
Deriving again with respect to time
Expanding around we have

## Slide 114
Small amplitude synchrotron frequency with SR and FB (2/3)
Simplifying and rearranging the terms we obtain
We assume that the feedback shifts by as desired.
  This requires that no saturation has to occur in the feedback, i.e.
    The input of the ADC is always in the range .
    The input of the DAC is always in the range
  Grouping all the feedback gains in one expression, we have
  where is the total gain of the feedback in volt units
Phase detection
ADC
FPGA
DAC
Kicker max voltage
Note 1: although should have rad units, in this case is dimensionless since derives from
Note 2: if then, at least in first approximation, the FPGA term should be divided by ( = in the convolution)

## Slide 115
Small amplitude synchrotron frequency with SR and FB (3/3)
The differential equation becomes
As expected, the feedback affects the damping-rate of the bunch oscillations. This rate becomes
On the contrary, the feedback doesn’t affect the frequency of the oscillations
The solution of the differential equation is
If, for instance, and then

## Slide 116
Assuming = 8.88 keV, = 510 MeV, = 130 kV and = 0.018, then 1/ = 106.95.
In DAFNE can vary from 1 to 32, whereas can vary from 1 to 16.
  We assume that the maximum number of taps is used, i.e. = 16.
  In principle the optimal can be either 6 or 7 since
We do single-bunch simulations without intensity effects to find which leads to the most efficient feedback-response.
  At turn 0 the bunch-phase is displaced by 0.1 rad with respect to . 100000 turns are simulated.
FPGA: DAFNE example (1/5)
.
[1]
  When , then and cover less than one synchrotron period (.
  When , then and cover more than one synchrotron period (.
Turn [1]
Turn [1]
[1]
[1]
: filter with = 16 and first 16 samples of
(no feedback-correction applied to the bunch)
: filter with = 16 and first 16 samples of
(no feedback-correction applied to the bunch)
[1]

## Slide 117
FPGA: DAFNE example (2/5)
We compare the frequency-response of the filter when and .
[a.u.]
Phase of [rad]
Frequency [kHz]
[a.u.]
Phase of [rad]
Frequency [kHz]
Frequency [kHz]
Frequency [kHz]
: frequency response of the filter
: frequency response of the filter
is equal to 0.235 rad when , 0.264 rad when .
The modulus frequency-response around is lower when .
-
-

## Slide 118
[1]
[1]
Turn [1]
[1]
Turn [1]
: and
We analyse the evolution of and without applying the feedback-correction to the bunch.
  The linear interpolations between consecutive points are plotted only to facilitate the visualization.
  The decay of the oscillations is due to synchrotron radiation.
Zoom 1 (0-150 turns)
Zoom 2 (850-1000 turns)
  The shaded regions cover the first 1 = 15 samples of . Here is in transient regime (hold-buffer not full yet).
  The amplitude is lower when . This is due to the lower modulus of the frequency-response around .
Turn [1]
Turn [1]
Turn [1]
Turn [1]
[1]
[1]
[1]
[1]
[1]
[1]
[1]
[1]
FPGA: DAFNE example (3/5)
[1]
: and
Zoom 1 (0-150 turns)
Zoom 2 (850-1000 turns)

## Slide 119
We analyse the evolution of , and when the feedback-correction is applied to the bunch.
[1]
Turn [1]
[1]
FPGA: DAFNE example (4/5)
: evolution of , and
[1]
[1]
: evolution of , and
Turn [1]
Zoom
(99500-100000 turns)
Zoom
(99500-100000 turns)
  When , faster exponential decay of (black and orange dashed lines) due to the larger amplitude of and .
  At the end of the simulations, takes 0 and 1 values, whereas is sinusoidal like with .
  In this example = 0.5, therefore = 0 if , and this occurs after about 10000 turns.
  There is a transient period of about 100 turns for .
Turn [1]
[V]
Zoom
(0-500 turns)
Zoom
(0-10000 turns)
Zoom
(0-500 turns)
Zoom
(0-10000 turns)
Turn [1]
[V]

## Slide 120
FPGA: DAFNE example (5/5)
Turn [1]
[rad]
  The simulated damping-rates are if , if .
  The analytical damping-rates are if , if (good agreements with simulations).
    The analytical damping-rate assuming is (, ).
This example shows that should be preferred to (an equal is obtained by increasing by 14% when ).
We analyse the evolution of the bunch-phase when the feedback-correction is applied to the bunch.
Turn [1]
[rad]
Turn [1]
[rad]
[rad]
Turn [1]
Here the envelope is not exponential due to the transient period of
Here the envelope is not exponential due to the transient period of
Zoom
Zoom

## Slide 121
Cavity kicker in DAFNE: introduction
The active element of the longitudinal feedback-system is the cavity-kicker.
  One kicker per DAFNE ring.
The kicker is a special ‘overdamped’ pill-box cavity:
  The pill-box cavity is 72 mm long and has a diameter of 200 mm (the diameter of the beam-pipe is 88 mm).
A large bandwidth is obtained by loading the pill-box cavity with 6 ridged waveguides followed by broadband transitions to standard coaxial cables.
  The 6 waveguides are placed symmetrically on the pill box, 120° apart from each other.
3 waveguides (ports) are used to inject power into the kicker, the other 3 are terminated onto 50 termination loads.
  Thanks to the symmetry of the waveguides and the fact that the power dissipated on the loads is much larger than the one dissipated on the cavity walls, the system is in theory perfectly matched at the resonant frequency (zero reflected power by the input ports).
There is no need to tune the kicker in operation due to the large bandwidth and no need to cool the kicker since most of the power is dissipated on the loads.
The strong waveguide-coupling leads also, as a by-product, to a significant damping of all the kicker HOMs.
Cavity kicker for the DAFNE positron ring
A. Drago (2018)
CAD view of the cavity kicker
A. Gallo (1995)

## Slide 122
Kicker parameters (1/3)
The kicker must be able to damp the coupled-bunch instabilities due to the HOMs (mostly those of the accelerating RF system).
It was shown that, in the presence of coupled-bunch instabilities, the beam-spectrum lines which can be excited are situated at
  where , is the oscillation mode and is the coupled-bunch mode.
We suppose that the machine is full, i.e. , and that , since the dipolar mode is usually the most critical for coupled-bunch instabilities. This leads to
  with (in DAFNE they differ by about factor 100).
To be able to damp every coupled-bunch mode, it is sufficient that the kicker bandwidth covers for each at least one line .
  We want to find the minimum bandwidth able to do this: larger bandwidths would unnecessarily lower the kicker shunt impedance and this, as shown later, would decrease the available kicker-voltage for a given amplifier power.
Neglecting in the analysis which is relatively small, and considering that can be positive and negative, it can be easily verified that the minimum required bandwidth is
  as long as the resonant frequency is placed at
or

## Slide 123
In DAFNE the following resonant frequency was chosen
  Since the pillbox cavity is operated in the fundamental mode, the diameter of the pill box cavity can be estimated as
The constraints on the kicker bandwidth and the quality factor are given by
  In DAFNE the measured and simulated kicker bandwidth and quality factor are
  Since each waveguide covers 11% of the available cavity surface, the number of waveguides could be increased to 8 leading to a larger bandwidth.
    This was not done since the constraints are already satisfied (with some margin) using 6 waveguides.
MHz
Kicker parameters (2/3)
Kicker shunt-impedance reproduced in simulation with some spectrum lines (see next slide for the definition of ), kHz
Zoom 1
Zoom 2
Bandwidth covers at least = 60,…,119
Bandwidth covers at least = 0,…,60

## Slide 124
The frequency-dependent kicker shunt-impedance is defined as
  where , and are respectively the kicker gap-voltage phasor, the forward-power at the kicker input and the gap length;
  where and are respectively the amplitude and phase of the longitudinal electric-field evaluated on the beam axis and expressed as a phasor:
was computed by integrating on the beam-axis the -field distribution given by a 3D electromagnetic simulation of the kicker.
Simulations, and also measurement, showed that .
  The maximum power provided by the kicker amplifiers is 600 W.
    One 200 W power-amplifier for each input-waveguide.
  The available gap-voltage when the kicker-generator works at is
Frequency [MHz]
[]
A. Gallo (1995)
Shunt-impedance obtained from an electromagnetic simulation of the kicker model
It turns out that , where is the beam-coupling impedance of the kicker.
  The kicker, in addition to providing the voltage-correction to each bunch, contributes as a resonant impedance with parameters
  This impedance, not included in the Fortran code, was added in the new Python code.
Kicker parameters (3/3)

## Slide 125
As shown, the HOMs shunt-impedances were rescaled by an exponential factor to consider the Gaussian profile of the bunches.
  We show now that this technique can’t be properly used for the kicker fundamental-mode due to its relatively small .
We consider the parameters of the kicker fundamental-mode , , and a Gaussian profile of rms .
The kicker wake-potential induced by the Gaussian profile at distance from its centre can be computed analytically as
  where is the complementary error function and
  This formula is obtained through profile and wake-function convolution using algebraic routines from the Mathematica software.
  This formula is valid for every resonator impedance.
    A plot of has already been shown to verify that the HOM shunt-impedance rescaling was possible.
As concerns the kicker impedance, we want to compare with two rescaled wake-functions:
  : the rescaling is done by using the exponential factor already adopted for the HOMs;
  : the rescaling factor is such that .
Kicker coupling-impedance in the code (1/3)
where

## Slide 126
Kicker coupling-impedance in the code (2/3)
We show the three potentials for the DAFNE case, using mm.
Wake potentials and bunch profile
Zoom 1
Zoom 2
Zoom 3
decays to zero after essentially 3 RF periods.
At 0 ns the amplitudes of and differ by 7%.
After roughly 0.2 ns:
  there is a time-shift of 2.7 ps between and ;
  the amplitudes of and are the same.
At 0 ns the and amplitudes coincide by construction.
After roughly 0.2 ns:
  there is a time-shift of 2.7 ps between and ;
  the amplitudes of and differ by 7%.
As for the beam dynamics, we expect that the approximation using is stronger than the one using .
  Error using : always 15 V/nC;
  Worst-case error using : 7% of 150 V/nC + 7% of 25 V/nC = 12 V/nC.
  If the bunch distances are (e.g. in stable conditions), the error using is just 7% of 10 V/nC. Indeed the bunch sees zero potential from the last bunch due to the fact that .
and are among the best possible fits for .
  In any case the constant time-shifts can’t be compensated changing the resonator parameters.
  This proves that no resonator can properly fit .
, , [V/nC]
, , [V/nC]
, , [V/nC]
, , [V/nC]
7%
2.7 ps
0%
2.7 ps
7%
150
25
0
10

## Slide 127
Kicker coupling-impedance in the code (3/3)
Being the resonator-fits unprecise, the kicker-impedance contribution was added in the energy equation of motion using directly .
    Here the phases aren’t meant mod 2, i.e. is the distance between the bunches and .
    As shown, the kicker induced-voltage decays after 3 RF periods, so the contributions from the last 3 bunches are enough.
Oscillations of bunch 80,
matching with just HOMs
Initial amplitude 20 mrad
Initial amplitude 1 mrad
Initial amplitude 0.03 mrad
DAFNE example with 105 contiguous bunches, mA, HOMs + kicker impedances during tracking, feedback off, bunch starts at .
  Although it’s an approximation, the matching with HOMs + provides a negligible initial oscillation-amplitude for all bunches (as the number 80 here shown).
  The matching with HOMs + provides less satisfying results, as expected from the observations given in the previous slide.
Since the kicker induced-voltage isn’t negligible, it was also necessary to add the kicker-impedance in the beam-matching routine.
  This was done by simply adding the resonator to the HOMs during the matching procedure.
Oscillations of bunch 80,
matching with HOMs+
Oscillations of bunch 80,
matching with HOMs+
  where the kicker induced-voltage is given by the sum of the instantaneous voltage and the voltage induced by the last 3 bunches

## Slide 128
We now describe the second voltage-contribution of the kicker, i.e. the voltage-corrections given to the bunches.
The final part of the feedback block-diagram shown earlier can be expanded (and simplified) as
Kicker correction-voltage
Cavity-kicker
(it provides the actual correction-kicks to the bunches)
DAC (it provides the values of the ideal correction-voltages)
Mixer or amplitude modulator
(it multiplies the QPSK signal with the values provided by the DAC)
QPSK
(it shifts the phase of the signal by 90° every )
RF generator
(it produces a sine wave with frequency = 3.25, phase = 0 and amplitude 1 V)
The DAC provides the values of the voltages which should be given to the bunches to have optimal corrections.
The generator produces a sine wave with frequency , which is the resonant frequency of the kicker.
  If this signal is equal to 0 at , then a bunch crossing the kicker at sees the maximum of the sine wave, as desired.
  However, a second bunch crossing the kicker at sees zero voltage and therefore no correction is applied to that bunch.
  To solve this problem, the QPSK (Quadrature Phase-Shift Keying) modulation is used to shift the signal by 90° every .
The mixer multiplies the signal coming from the QPSK with the values provided by the DAC.
  The resulting signal is a piece-wise sinusoidal signal with amplitudes given by the values .
The cavity-kicker, being a resonator with its filling time, modifies the signal coming from the mixer.
  Because of this, even if everything is perfectly synchronized, the bunches can see just an approximation of the ideal kicks .

## Slide 129
Example: voltage signal from generator to mixer
Let’s suppose that the bunches 1, 2, 3 and 4 circulate in DAFNE ( ns).
  At a certain turn the values of the ideal correction-voltages are 2, -0.5, -2.5, 4 respectively for the bunches 1, 2, 3 and 4.
  The kicker is crossed by the bunch at , .
The mixer-signal is given by the QPSK-signal, which never changes along the turns, multiplied with the DAC signal, which changes every turns.
  The voltage from the mixer is discontinuous at the times which are multiple of .
  As shown later, the voltage-signal from the kicker is continuous at all times and bunches arriving slightly late can still get a proper correction.
Voltage from the generator
Voltage [V]
Time [ns]
Voltage [V]
Time [ns]
Time [ns]
Voltage [V]
Time [ns]
Voltage from the QPSK
Signal from the DAC at turn
Voltage from the mixer at turn
[1]
0
2
3
4
0
2
3
4

## Slide 130
Kicker correction-voltage in the code (1/6)
The cavity-kicker is modelled as a parallel RLC resonant circuit. This allows to take into account the finite filling-time of the kicker.
The kicker is excited by the circulating beam-current and by the kicker RF-generator .
  The generator has angular frequency = and is amplitude-modulated with the values coming from the DAC.
  The generator has inner resistance equal to the shunt impedance of the kicker divided by the coupling factor
  As observed earlier, we assume that the generator-kicker system is perfectly matched when the generator works at , therefore = 1.
Since we expect that the bunches cross the kicker at times , after the passage of the bunch at the generator-amplitude suddenly changes to the value pertaining to the bunch . The QPSK shifts the generator-phase by 90° at times .
Cavity-kicker
Generator
Beam
: voltage across the capacitance at time t
Sources
Unknown
Ohmic power-losses due to the non-perfectly conductive walls of the kicker.
‘External’ power lost through the waveguides (power-couplers).
In the following derivation we neglect the beam current () since the corresponding (induced) voltage was already considered.

## Slide 131
The generator-voltage in the time interval is given by
  where we consider the more general case with .
Applying the Kirchhoff’s law for currents, we have
Deriving one time
The associated homogenous differential equation is
Its eigenvalues are
Its solution is
Kicker correction-voltage in the code (2/6)
  where the constant and depend on and .

## Slide 132
The forcing term of the inhomogeneous equation is
Therefore we find a particular solution of the type
  where is a complex constant.
Inserting and into the inhomogeneous differential equation we obtain
Solving for
  where
Kicker correction-voltage in the code (3/6)

## Slide 133
Substituting
Therefore all the solutions of the inhomogeneous differential equation are given by
is determined by
is determined by
Kicker correction-voltage in the code (4/6)

## Slide 134
Substituting we finally obtain
  where
Deriving we obtain
  where
Kicker correction-voltage in the code (5/6)

## Slide 135
Similar to what done for the RLC circuit for the HOMs discussed earlier, in the code and are computed using the matrix expression
Kicker correction-voltage in the code (6/6)
It decays exponentially with time and accounts for the emptying-process of the kicker.
It oscillates with time and accounts for the generator-voltage and the filling-process of the kicker.
If the RF generator is perfectly synchronized with the synchronous arrival times of the bunches, then and
If , as it occurs when the QPSK is active and there are no frequency errors, then , and
If and (ideal case), then
Filling-process term decaying exponentially with time
,
Desired voltage-kick
Error term due to filling-process
(since )

## Slide 136
Example continued: voltage signal from mixer to kicker
Voltage [V]
Time [ns]
Voltage from the mixer at turn
0
2
3
4
Kicker voltage at turn
0
2
3
4
Voltage [V]
Time [ns]
We assume that and . The voltage from the mixer and the actual kicker-voltage are given respectively by
  The voltage from the mixer coincides with the amplitude-modulated generator voltage defined for the kicker circuit-model.
  The kicker-voltage is a continuous function of time, as opposed to the mixer-voltage which is discontinuous at .
  The kicker-voltages at , and are visibly lower than the corresponding .
  In this example, being at turn 1, there isn’t residual voltage in the kicker at , therefore for .
Voltage [V]
Time [ns]
Kicker voltage at turn
Voltage [V]
Time [ns]
At least for times close to , a frequency error of 5% is essentially equivalent to a shift of the phase by .
Kicker voltage at turn

## Slide 137
Kicker-voltage evaluation for bunches
The code takes into account the fact that bunches perform synchrotron oscillations around their corresponding synchronous phases.
  The times , when the QPSK acts, correspond to the of the different buckets: a bunch arriving at has phase .
Given , , and , the matrix equation previously derived can be expressed in functional and compact form as
  where , , and is the ‘propagation’ function.
If the bunch is in advance with respect to , then the kicker-voltage seen by the bunch is given by
If the bunch is late with respect to , then we need first to update the initial conditions and then compute
If there are empty buckets between two bunches, then the initial conditions must be updated iteratively before computing .

## Slide 138
Example continued: kicker-voltage seen by bunches
We consider again the case , and we assume that the four bunches traverse the kicker respectively at times (in advance), (late), (late), (in advance), with .
Kicker voltage at turn
0
2
3
4
Voltage [V]
Time [ns]
+
Being the first turn, the kicker residual-voltage is zero at
can be computes as
  To compute we need to update the initial conditions twice
+
+
  To compute and we need to update the initial conditions one time more

## Slide 139
Another example: residual voltage and kicker efficiency (1/3)
Let’s suppose that
  120 bunches in DAFNE perform coupled-bunch motion with ;
  the phase-shift between consecutive bunches is ;
  the oscillation-amplitudes and are the same for all the bunches
    at turn , the bunches 1, 5, 9, … have coordinates (0,), the bunches 2, 6, 10, … have coordinates (+ , ) etc.;
    the feedback ideal-corrections are , , , .
mod 2
1,5,…
2,6,…
3,7,…
4,8,…
(+, )
(-, )
At turn
()
Voltage [V]
Time [ns]
Kicker voltage at turn ()
1
2
3
4
5
6
7
8
9
10
11
12
13
14
15
We assume that and are small so that each bunch sees essentially the corresponding .
  The bunches 1, 5, … see -1.733 V instead of -2 V.
    Error 14.3%.
  The bunches 2, 6, … see -0.05 V instead of 0 V.
    Error 0.05 V.
  The bunches 3, 7, … see 1.733 V instead of 2 V.
    Error 14.3%.
  The bunches 4, 8, … see 0.05 V instead of 0 V.
    Error 0.05 V.

## Slide 140
Another example: residual voltage and kicker efficiency (2/3)
Let’s now suppose that
  the 120 bunches perform coupled-bunch oscillations with () and that at turn the coordinates of all bunches are (0,);
  the feedback ideal-corrections are all .
mod 2
1,2,…
At turn
()
Kicker voltage at turn ()
Voltage [V]
Time [ns]
1
2
3
4
5
6
7
8
9
10
11
12
13
14
15
We assume again that are are small so that each bunch sees the corresponding .
  All the bunches see -1.70 V instead of -2 V.
    Error 16.2% (instead of 14.3% obtained for ).
This example indicates that the kicker is more efficient (smaller differences between ideal and actual kicks) when . Why?

## Slide 141
Second explanation (time domain): let’s suppose that after the bunch 9 traverses the kicker, so that we can examine the evolution of the residual voltage as a function of time.
  is zero when the bunches 10 and 12 cross the kicker, whereas is a local maximum when the bunch 11 arrives.
    = 30: agreements with =0, =2.
    = 0: disagreements with = -2.
Another example: residual voltage and kicker efficiency (3/3)
First explanation (frequency domain): the resonant frequency of the kicker is , therefore the shunt-impedance (kicker-efficiency) has its maximum at .
  As already seen, if we consider negative frequencies, - corresponds to , so we expect a better kicker-efficiency for .
  decreases as the distance from the resonant frequency increases, so we expect a worse kicker-efficiency for .
Kicker shunt-impedance
9
Voltage [V]
Time [ns]
Frequency [GHz]
9
Voltage [V]
Time [ns]
Residual voltage after the bunch 9 transit, =30 (top), =0 (bottom)
0, it AGREES with
max, it AGREES with
0, it AGREES with
0, it DISAGREES with
max, it DISAGREES with
0, it DISAGREES with

## Slide 142
Including the actual corrections given by the kicker, the equations of motion become
Equations of motion in the code: RF+SR+HOM+FB+BBZ
Accelerating cavity (RF + HOMs)
Kicker (correction + impedance)
Synchrotron radiation + broad-band impedances
  where is the actual voltage provided by the kicker to the bunch at turn . As we saw, depend on
    the ideal voltage-correction evaluated at turn ;
    the kicker parameters , and ;
    the frequency and phase of the kicker-generator;
    the arrival time of the bunch at turn , or .
The effects of broad-band impedances which don’t couple consecutive bunches can be simply included in the energy equation of motion as instantaneous voltages .
  Usually these impedances (e.g. resistive wall) are due to non-resonant devices and are spread all along the ring.
  depend on the bunch charge .
    If all the charges are equal, then is constant for all bunches and all turns.

## Slide 143
Example 1: coupled-bunch instability damped by the kicker (1/2)
We assume the DAFNE parameters = 8.88 keV, = 510 MeV, = 130 kV and = 0.018.
Moreover we assume that
  three equally-spaced bunches with mA, mm circulate in the machine.
    At turn 0 the bunches are displaced by 0.25 mrad with respect to (equal for all the bunches due to symmetry).
  an HOM excites the coupled-bunch mode , .
    , ;
    An instability is obtained if , . We choose , therefore MHz.
We first simulate the three bunches without the feedback correction for 200000 turns. The kicker impedance is added to the HOM.
  The oscillation-amplitudes are essentially the same for the three bunches.
    The grow-rate computed analytically is 247.4 1/s which is in very good agreement with the one computed numerically.
  As expected, the phase changes by 120° for consecutive bunches.
Phase evolution of bunch 1 and grow-rate from the exponential fit
Zoom on the phase evolutions of the three bunches
Bunch 1
Bunch 41
Bunch 81

## Slide 144
Example 1: coupled-bunch instability damped by the kicker (2/2)
We then include the voltage corrections of the kicker, first assuming that the bunches see the ideal kicks .
  The feedback acts only from turn 40000 onwards and produces essentially the same damping behaviour for the three bunches.
    = 16, = 6. The total feedback gain isn’t too high, so that enough phase oscillations can be used to perform a proper fit.
  The analytical damping rate of the feedback is 4536 1/s.
    The total analytical damping rate is (4536-247) 1/s = 4289 1/s, which is in very good agreement with the numerical one.
As expected, the damping rate decreases when the bunches see the real voltage-corrections, which in general are lower than the ideal ones.
Phase evolution of bunch 1 and grow-rate from the exponential fit.
Voltage kicks for the bunch 1.
The bunch sees ideal kicks
The bunch sees real kicks
Ideal kicks
Real kicks

## Slide 145
Example 2: coupled-bunch instability damped by the feedback (1/2)
Main beam and machine parameters
As a second example we use operational/expected parameters for a DAFNE typical run.
  Bunch current, length and peak RF voltage are taken from 2014 measurements.
Measurements of bunch length vs intensity
C. Milardi (2014)
We choose for instance this point in simulations
Parameters | Values
Harmonic number | 120
Ring circumference | 97.587 m
Mom. compaction factor | 0.018
Nominal energy | 510 MeV
Revolution frequency | 3.07 MHz
RF frequency | 368.65 MHz
Synchr. radiation energy loss | 8.88 keV
Peak RF voltage | 130 kV
Zero-amplitude synchr. freq. | 28.72 kHz
Beam filling pattern | 105 contiguous bunches
RMS bunch length | 19 mm
Bunch current | 19.5 mA
Parameters | Values
 | 120
 | 97.587 m
 | 0.018
 | 510 MeV
 | 3.07 MHz
 | 368.65 MHz
 | 8.88 keV
 | 130 kV
 | 28.72 kHz
Beam filling pattern | 105 contiguous bunches
 | 19 mm
 | 19.5 mA
Parameters | Values
ADC number of bits | 8
Max. ADC voltage | 200 mV
Number of taps | 16
Down sampling factor | 6
Kicker resonant frequency | 3.25
Kicker quality factor | 5.45
Kicker shunt impedance | 750
Max. kicker voltage | 950 V
Parameters | Values
 | 8
 | 200 mV
 | 16
 | 6
 | 5.45
 | 950 V
Some important feedback parameters
Beam-coupling impedances (HOMs + kicker)
 | [MHz] | [] | 
1 | 746 | 1120 | 70
2 | 797 | 105 | 210
3 | 1024 | 81 | 90
4 | 1121 | 90 | 300
5 | 1176 | 54 | 90
6 | 1201 | 36 | 180
7 | 1369 | 340 | 170
8 | 1432 | 550 | 550
1 | 746 | 1120 | 70
2 | 797 | 105 | 210
3 | 1024 | 81 | 90
4 | 1121 | 90 | 300
5 | 1176 | 54 | 90
6 | 1201 | 36 | 180
7 | 1369 | 340 | 170
8 | 1432 | 550 | 550
Parameters of waveguide-damped HOMs
Kicker
HOMs
Bunch current [mA]
RMS bunch length [cm]

## Slide 146
Min, mean and max bunch phase along 100000 turns
100000 turns are simulated, the maximum running time is just 16 minutes.
The simulation outcomes depend on the bunches initial conditions.
  Here the bunches start in (,0), so very small initial displacements due to non-perfect matching routine.
Without feedback all the bunches are unstable and the maximum oscillation amplitude is essentially an increasing function of the bunch number.
  The oscillation amplitude of the most unstable bunch (105) is half bucket at turn 17000, then non-linearities damp the growth.
With feedback the oscillations are damped for all the bunches.
  The feedback responds differently with different bunches.
Min, mean and max bunch phase along 100000 turns
Phase evolution for the bunch 105
Kicker voltage evolution for the bunches 1 and 105
Without feedback
Without feedback
With feedback
Phase evolution for the bunch 105
The mean corresponds essentially to .
half bucket
Example 2: coupled-bunch instability damped by the feedback (2/2)
Much more voltage is needed for bunch 1 than bunch 105.
Phase evolution for the bunch 1
Very small initial oscillations damped after 500 turns.
Larger initial oscillations damped after 600 turns.
With feedback
With feedback
With feedback

## Slide 147
Contents
Introduction.
Single-particle longitudinal beam-dynamics with synchrotron radiation.
  Equations of motion, synchrotron radiation, small-amplitude synchrotron oscillations, …
Longitudinal beam-dynamics with synchrotron radiation and Higher Order Modes (HOMs).
  HOM induced voltage, synchronous phase shift, HOM initial conditions, coupled-bunch instabilities, …
Longitudinal beam-dynamics with synchrotron radiation, HOMs and bunch-by-bunch feedback.
  Models of the feedback components, grow and damping-rates, cavity-kicker, ideal and real corrections, …
Conclusions and suggested next steps.
Appendices.
  Execution of the new-Python and old-Fortran codes, structure of the code, exponential fits in Python, …
References.

## Slide 148
Conclusions
The new Python code is ready to be used for longitudinal beam-dynamics simulations of the DAFNE accelerator.
  The current version is able to simulate coupled-bunch instabilities and the effects of the bunch-by-bunch feedback.
  Some important improvements to the code can still be done (see next slide).
This presentation covered in detail all the features of the code.
  The theoretical principles required to fully understand the code were explained in depth.
  Numerous examples with plots and animations were provided to demonstrate the code capabilities.
Several benchmarks between simulations and analytical formulas were performed to prove the code reliability.
  In particular we found good agreements concerning grow-rates of coupled-bunch instabilities and feedback damping-rates.
Some additional functionalities were added to the new code, for instance
  Computation of the synchronous phases taking into account the beam-induced voltages. This allows for instance
    the matching of the beam with respect to the induced voltages;
    the feedback compensation of the synchronous-phase shifts due to induced-voltages.
  Inclusion of the cavity-kicker beam-coupling impedance in simulation.
Some new studies were performed, for example
  Accurate models of the signal manipulations performed by the feedback-system (pickup, comb generator, mixer, …).
    In particular, measurements of the comb-generator transfer-function were needed to properly model the bursts generation.
  Optimized design of the FPGA sinusoidal filter and determination of the optimal down-sampling-factor.
Preliminary simulations of DAFNE operational scenarios were performed confirming the importance of the feedback for beam stability.

## Slide 149
Suggested next steps
The work presented here isn’t definitive, in particular the following next steps can be done.
Implementation in the Python code of the RF feedback for the compensation of beam-loading in the accelerating cavity.
  This feedback is required to reduce the significant beam-coupling impedance of the fundamental mode.
  This feedback is already implemented in the Fortran code and its effects have already been studied in simulation in the past.
    Simulations without this feedback assume that the beam-loading is perfectly compensated.
Time [ps]
Normalized kicker voltage [V]
Extension of the code to represent each bunch with millions of macroparticles so that more realistic simulations can be performed.
  The effects of arbitrary beam-coupling impedances could be studied.
  Other types of instabilities, already observed in measurements, could be seen also in simulation, for instance
    Microwave: it’s caused by short-range wakefields with wave-lengths much shorter than the bunch length. It leads to bunch-lengthening and beam-quality degradation.
    Longitudinal quadrupole (q-pole): it’s probably caused by the broadband machine-impedance and can be cured delaying the kicker correction signal with respect to the bunch passage.
  However multi-bunch simulations with 105 bunches are cumbersome.
    The code must be optimized and parallelized following for instance the example of the CERN BLonD code.
A. Drago
et al. (2003)
Feedback-timing versus bunch-passage in the kicker
Optimal bunch phasing for dipole instability
Optimal bunch phasing for q-pole instability
Benchmarks between simulations and beam measurements taken during the next 2021 DAFNE run.
  This would confirm that the models and assumptions used in the code are accurate enough.

## Slide 150
Contents
Introduction.
Single-particle longitudinal beam-dynamics with synchrotron radiation.
  Equations of motion, synchrotron radiation, small-amplitude synchrotron oscillations, …
Longitudinal beam-dynamics with synchrotron radiation and Higher Order Modes (HOMs).
  HOM induced voltage, synchronous phase shift, HOM initial conditions, coupled-bunch instabilities, …
Longitudinal beam-dynamics with synchrotron radiation, HOMs and bunch-by-bunch feedback.
  Models of the feedback components, grow and damping-rates, cavity-kicker, ideal and real corrections, …
Conclusions and suggested next steps.
Appendices.
  Execution of the new-Python and old-Fortran codes, structure of the code, exponential fits in Python, …
References.

## Slide 151
Computation of the decay rate of an oscillating function (1/3)
Python is used to evaluate the grow-rate of an oscillating increasing or decreasing function
  The first used routine scipy.signal.find_peaks is able to find all the local maxima of a given signal.
  The second used routine scipy.optimize.curve_fit is able to fit the local maxima with an exponential function.
Example: our original signal is made of samples from
  The envelope traversing the local maxima of has equation
The first step is to find the local maxima of with the find_peaks routine. The output arrays are and (length ).
  A check has to be done on which can belong to the envelope or not depending on the specific case.
    If and , then belongs to the envelope (as in our example).
Original signal with local maxima detected
The second step is to fit the points with the curve_fit routine, aiming at finding , and of .
  The exponential function to be used for the fit is
    where , and are the three parameters to be determined.
We assume that and aren’t known. The goal is to find the decay rate of the signal, i.e. the value = -1.1.

## Slide 152
The curve_fit routine needs as input the initial guesses for , and , which we call , and
  If these guesses are too far from , and , then the routine provides unacceptable results.
  First method to find , and :
    , where is the mean of the array. Indeed, for large , and also .
    and are easily found solving the system
  Second method to find , and (from Jacquelin J. “Regressions et equations integrals”, 2014):
    More general method which doesn’t need the array but only and .
Computation of the decay rate of an oscillating function (2/3)
,
1)
2)
3)
4)

## Slide 153
Original signal
Local maxima
Envelope
Fit ( method)
Computation of the decay rate of an oscillating function (3/3)
Zoom on
Zoom on
Aiming at finding , , , the curve_fit routine provides as results
  method: , ,
  method: , ,
Both methods provide initial guesses relatively close to , and .
  This allows the curve_fit routine to work properly and provide results very close to , and .
Note that the envelope doesn’t cross the local maxima but it crosses points at the right of them.
  The fit, which tends to be close to the local maxima, is below the envelope. This explains why is slightly smaller than .
, ,
, ,

## Slide 154
The open-source Anaconda Python distribution with its Spyder editor can be used. The following instructions are for Windows 10, 64 bit.
Go to https://www.anaconda.com/products/individual.
In the ‘Anaconda Installers’ section, in the ‘Windows’ column, click on ’64-Bit Graphical Installer’ and download the executable of around 500 MB.
During the installation procedure
  Select the ‘Destination Folder’, e.g. ‘ProgramData\Anaconda3’.
  In ‘Advanced Options’, mark only ‘Register Anaconda…’ and click Install.
Python code: download and installation of the Anaconda distribution

## Slide 155
Python code: creation of a new Spyder project and import
After the Anaconda installation, the Spyder editor is available.
Search for Spyder in your PC typing ‘Spyder (Anaconda 3)’ into the search box.
  When found, you can also pin it to the Taskbar with a right click for an easier access.
Open Spyder and go to ‘Projects -> New Project…’.
  Mark ‘Existing directory’.
  Click on the folder icon in the field ‘Location’ and select the ‘python_code’ folder.
    The ‘python_code’ folder can be anywhere.
  Leave ‘Empty project’ in the ‘Project type’ field and click on Create.
All the files of the Python code are now accessible inside Spyder from the Management panel on the left.
  In general Python files can be easily run clicking on the green-triangle icon.
Management panel
Button to run Python files

## Slide 156
Python code: structure
The folder ‘analysis’ contains several Python files useful to perform analyses and computations.
  Example of file: signal manipulations from the longitudinal pick-up to the mixer.
  Each file can be run independently of the others.
  All these files are like ‘add-ons’ with respect to the main code: they aren’t essential to launch simulations with the main code and they don’t affect the main code.
The folder ‘saved_main_files’ contains main-files which the user saved in order to be able to relaunch the corresponding simulations later on.
  Example of saved main-file: simulation of a certain coupled-bunch instability for three equally-spaced bunches in DAFNE.
The file ‘functions.py’ contains several essential routines which are called and used in the main files and also in the files contained in the ‘analysis’ folder.
  Examples of functions: generation of beam matched with collective effects, computation of kicker voltage-corrections and of voltages due to the HOMs.
  All these functions aren’t supposed to be run directly.
The file ‘main.py’ is the main-file which should be run to perform a simulation.
  Once a simulation is well set up, the user can decide to copy this file into the ‘saved_main_files’ folder and rename the copied file with a more significant name.
  The input-parameters for the simulation should be specified directly in this main-file.
  This main-file directly provides all the simulation outputs.

## Slide 157
Python code: example of input-parameters in the main file
Essentially four types of input-parameters must be set in the main file:
  Machine parameters: harmonic number, circumference, momentum compaction, nominal energy, peak RF voltage, …
  Beam properties: filling scheme, bunch charge and standard-deviation, initial displacements with respect to the synchronous phases.
  Impedance parameters: boolean variables to include HOMs and kicker impedances in simulation, parameters of the HOMs, possibility to match with collective effects either the entire beam or all the bunches except one for injection-transient studies, …
  Bunch-by-bunch feedback parameters: boolean variable to turn the feedback on, how many turns to wait for the feedback action, different gains, computation of optimal filter coefficients, possibility to apply the ideal or the real voltage-corrections to the bunches, …

## Slide 158
Fortran code: download of Code Blocks
The open-source Code Blocks can be used as editor. The following instructions are for Windows 10, 64 bit.
Go to http://www.codeblocks.org/, click on ‘Downloads’, then on ‘Download the binary release’.
We need a version which contains the compiler MinGW, i.e. ‘codeblocks-20.03mingw-setup.exe’.
Click on FossHUB and download the ‘Code Blocks Windows 64 bit (including compiler)’ version.

## Slide 159
Fortran code: installation of Code Blocks
Now we need to install Code Blocks. Click on the downloaded executable of around 150 MB.
If possible, install all the components (Full).
Choose the destination folder (Program Files is OK)
Open Code Blocks at the end of the installation.

## Slide 160
Inside Code Blocks, go to ‘Settings -> Compiler…’.
Choose ‘GNU GCC Compiler’ in ‘Selected compiler’.
Go to ‘Toolchain executables’.
In ‘Compiler’s installation directory’, type the path of the ‘MinGW’ subfolder present in the Code Blocks installation directory.
Click on ‘Auto-detect’. A window appears reporting that the ‘GNU GCC Compiler’ has been found. Click OK.
Fortran code: setting of the GNU GCC compiler

## Slide 161
Fortran code: setting of the GNU Fortran compiler
Choose ‘GNU Fortran Compiler’ in ‘Selected compiler’.
Save the applied changes when asked.
Go to ‘Toolchain executables’.
In ‘Compiler’s installation directory’, type the path of the ‘MinGW’ subfolder present in the Code Blocks installation directory.
Click on ‘Auto-detect’. A window appears reporting that the ‘GNU Fortran Compiler’ has been found. Click OK and again OK.

## Slide 162
Inside Code Blocks, go to ‘File -> New -> Project…’
In ‘Category’ select Fortran and click on Fortran application.
In the ‘Fortran application’ window,
  choose the name of the project in ‘Project title’, e.g. ‘fortran_code’.
  choose the folder where to store the project and click Next.
  In ‘Compiler’ select ‘GNU Fortran Compiler’ and mark ‘Create “Debug” configuration’. Click on Finish.
Fortran code: creation of a new project

## Slide 163
Fortran code: import, build-targets and simulation run
Copy all the files from the folder ‘fortran_code_original’ into the folder ‘fortran_code’ just created.
  Delete the file main.f90 from the folder ‘fortran_code’.
Inside Code Blocks, in the Management panel -> Projects,
  Right click on main.f90 and ‘Remove file from project’.
  Right click on ‘fortran_code’ and ‘Add files recursively…’.
  Select the folder ‘fortran_code’.
  Select all the files and click OK.
‘fortran_code’ folder
Inside Code Blocks, in the Management panel -> Projects,
  Right click on ‘fortran_code’ and ‘Properties…’.
  Go to the tab ‘Build targets’.
  In the ‘Build target files’ part, select only ‘simul2.f’.
  Click OK.
Open ‘simul2.f’ from the Workspace in the Management panel and click on the icon ‘Build and run’.

## Slide 164
Contents
Introduction.
Single-particle longitudinal beam-dynamics with synchrotron radiation.
  Equations of motion, synchrotron radiation, small-amplitude synchrotron oscillations, …
Longitudinal beam-dynamics with synchrotron radiation and Higher Order Modes (HOMs).
  HOM induced voltage, synchronous phase shift, HOM initial conditions, coupled-bunch instabilities, …
Longitudinal beam-dynamics with synchrotron radiation, HOMs and bunch-by-bunch feedback.
  Models of the feedback components, grow and damping-rates, cavity-kicker, ideal and real corrections, …
Conclusions and suggested next steps.
Appendices.
  Execution of the new-Python and old-Fortran codes, structure of the code, exponential fits in Python, …
References.

## Slide 165
References (1/2)
Analog Devices, “Mixers and modulators”, MT-080 Tutorial, 2008.
Analog Devices, “Multiplier application guide”, 1978.
S. Bartalucci et al., “Analysis of methods for controlling multibunch instabilities in DANE”, Particle Accelerators, 1995.
M. Bassetti et al., “A time domain simulation code of the longitudinal multibunch instabilities”, DANE technical note G-19, 1993.
M. Bassetti et al., “DANE longitudinal feedback”, LNF-92-033-PG, 1992.
R. Boni et al., “A waveguide overloaded cavity as longitudinal kicker for the DANE bunch-by-bunch feedback system”, Particle Accelerators, 1996.
D. Briggs et al., “Computer modelling of bunch-by-bunch feedback for the SLAC B-factory design”, SLAC-PUB-5466, 1991.
D. Briggs et al., “Prompt bunch-by-bunch synchrotron oscillation detection via a fast phase measurement”, SLAC-PUB-5525, 1991.
A. Drago, “Diagnostica e misure 2 (anelli)”, corso per la formazione di operatori e conduttori di macchine acceleratici, 2007.
A. Drago, “Longitudinal feedback systems at the lepton collider DAFNE”, Joint ARIES Workshop on Electron and Hadron Synchrotrons, 2018.
A. Drago et al., “Longitudinal quadrupole instability and control in the Frascati DANE electron ring”, Phys. Rev. STAB, 2003.
P. Forck, P. Kowina, and D. Liakin, “Beam position monitors”, Synchrotron Radiation News, 2008.
J. D. Fox et al., “Feedback implementation options and issues for B factory accelerators”, SLAC-PUB-5932, 1992.
J. D. Fox et al., “Stripline transversal filter techniques for sub-picosecond bunch timing measurements”, SLAC-PUB-12631, 2007.
G. Franzini et al., “Feedback layout at DANE”, DAFNE Machine Development Meeting, 2020.
A. Gallo et al., “An overdamped cavity for the DANE longitudinal feedback”, DANE technical note RF-17, 1995.
A. Gallo, M. Migliorati and L. Palumbo, “Efficiency of the broadband RF cavity longitudinal kicker in DANE”, NIM, 1998.
A. Gallo, F. Marcellini and M. Migliorati, “Implementation of the fast RF feedback on the DANE beam … ”, DANE technical note RF-14, 1994.
A. Gallo et al., “Simulations of the bunch-by-bunch feedback operation with a broadband RF cavity …”, DANE technical note G-31, 1995.
General Radio Company, “The frequency spectrum of a tone burst”, engineering department instrument notes, 1965.
A. Ghigo et al., “Kickers and power amplifiers for the DANE bunch-by-bunch longitudinal feedback system”, LNF-96-033-PQ, 1996.
H. Hindi et al., “Down sampled signal processing for a B factory bunch-by-bunch feedback system”, SLAC-PUB-5772, 1992.
J. Jacquelin, “Regressions et equations integrales”, engineering department note, 2014.
E. Jensen, “RF cavity design”, CERN Yellow Report CERN-2014-009, 2014.

## Slide 166
References (2/2)
S. Khan, “Collective phenomena in synchrotron radiation sources”, Springer, 2006.
I. S. Ko, Y. Kim and J. Y. Huang, “Status of longitudinal feedback system for the PLS storage ring”, PAC, 1999.
A. Latina, “Introduction to transverse beam dynamics”, JUAS, 2016.
F. Marcellini, M. Serio and M. Zobov, “DANE broad-band button electrodes”, DANE technical note CD-6, 1996.
M. Migliorati and L. Palumbo, “Multibunch and multiparticle simulation code with an alternative approach …”, Phys. Rev. STAB, 2015.
M. Migliorati, “Past collective effects studies for DAFNE”, CERN ICE meeting, 2012.
M. Migliorati, “Effetti collettivi nella dinamica dei fasci in una macchina acceleratrice circolare con applicazioni …”, PhD thesis, 1996.
M. K. Park et al., “Longitudinal feedback control system for the PLS”, EPAC, 2000.
S. Prabhakar, “New diagnostics and cures for coupled-bunch instabilities”, SLAC-Report-554, 2001.
C. Sanelli and M. Preger, “The DANE main ring magnet prototypes”, EPAC, 1996.
H. Schmickler, “Multi-bunch feedback systems”, CAS, 2015.
D. Teytelman, “Architectures and algorithms for control and diagnostics of coupled-bunch instabilities …”, SLAC-Report-633, 2003.
D. Teytelman et al., “Design and testing of Gproto bunch-by-bunch signal processor”, EPAC, 2006.
D. Teytelman, “FBE-368L longitudinal RF signal processor”, technical user manual, 2012.
D. Teytelman, “iGp-120F signal processor”, technical user manual, 2008.
D. Teytelman and J. Fox, “Set-up of PEP-II longitudinal feedback systems for even/odd bunch spacings”, SLAC-PUB-9217, 2002.
K. A. Thompson, “Simulation of longitudinal coupled-bunch instabilities”, Asymmetric B-Factory Collider note, 1991.
R. P. Walker, “Radiation damping”, CAS, 1994.
L. Wu-Bin et al., “A waveguide overloaded cavity kicker for the HLS II longitudinal feedback system”, Chinese Physics C, 2014.
A. Young, J. Fox and D. Teytelman, “VXI Based Multibunch Detector and QPSK Modulator for the PEP-II/ALS/DAFNE …”, SLAC-PUB-7485, 1997.
M. Zobov et al., “Collective effects and impedance study for the DANE -factory”, LNF-95/041, 1995.