## Slide 1
Ph.D. school on Accelerator Physics, XXXIII cycle
Targets for Laser Plasma Acceleration at SPARC_LAB
Gemma Costa

## Slide 2
Plasma wakefield acceleration:
  Advantages and techniques
  FLAME laser@SPARC_LAB
Experiment:
  Guiding process, experimental parameters and setup
  High repetition rate laser guiding tests
  Spectroscopic plasma density measurements and plasma simulations
  Guiding pulse experiment in a plasma density hollow profile
  Curved capillary for the Camel project
Conclusions and future perspectives
Outline:

## Slide 3
Plasma module:
E [GV/m ] = 96 (ne [cm-3])1/2
range mm - cm
Motivation to plasma based accelerators
Conventional RF structures:
(20 – 40) MV/m
range m - km

## Slide 4
Plasma frequency
⍵p = (ne e2/ε0 me)1/2
Laser pulse I = 1018 W/cm2 and cτ < λp/2
Plasma based acceleration:
Tajima and Dawson (1979)
Self-injection a0 = 0.85 10-9 λ0 I1/2 > 1 wave breaking
External-injection a0 ≃ 1 linear regime

## Slide 5
High-power Ti:Sa based laser, ultra-short CPA based pulse
FG Bisesto, G Costa, et al., doi:10.1016/j.nima.2018.02.027
external-injection
Interaction point
self-injection
Nozzle for gas jet
The FLAME laser at SPARC_LAB
Peak power | 250 TW
Energy on target | 7 J
Rep. rate | 10 Hz
Temporal length | 25 fs
FW 1/e2 @ focus | 20 μm
Intensity | 1019 W/cm2
Contrast-ratio | 1010
CPA
G Costa, et al., doi:10.1016/j.nima.2018.02.008

## Slide 6
Laser guiding in a capillary discharge waveguide:
e- energy gain ∝ Acceleration field × Acceleration length
optical guiding in plasma
λ0 = laser wavelength
rm = matching radius
re = e- radius
n0 = plasma density on the axis
nd = density difference axis-walls
Rayleigh length
=> Diffraction
gaussian intensity laser pulse
parabolic density distribution plasma channel
if waist radius

## Slide 7
Diameter: 500 µm
Length: 3 cm
Plastic 3D printed
Discharge: 20 kV
H pressure: 1.9 bar
Plasma density: 1018 cm-3
Repetition rate: 1 Hz
Vacuum: 10-7 mbar
Oscillator: 80 MHz, 220 mW
Probe: 10 mJ, 50 fs, 120 µm focus FW1/e2
Experimental parameters

## Slide 8
Experimental Setup at SPARC_LAB
Laser guiding experiment
Longitudinal and transverse plasma density diagnostic
beam profile imaging
beam signal and timing
plasma density diagnostics
beam alignment

## Slide 9
G Costa, et al., doi:10.1088/1742-6596/1596/1/012044
Oscillator and probe pulses guiding – 1st test

## Slide 10
Spectroscopic plasma density measurements
G Costa, et al., under publication
Stark Broadening:
= FWHM Hβ
H= 486 nm
= const.
theoretical value 2.3 1018 cm-3 experimental value 2.5 1018 cm-3, statistical error 8%
Hβ
H
1D theoretical model
at thermic equilibrium
theoretical value 0.58 1018 cm-3 experimental value 0.6 1018 cm-3, statistical error 5%

## Slide 11
Ionization level distribution for plasma density
Notes: NA Bobrova, AA Esaulov, J-I Sakai, PV Sasorov, DJ Spence, Arthur Butler, Simon Mark Hooker, and SV Bulanov. Simulations of a hydrogen-filled capillary discharge waveguide. Physical Review E, 65(1):016407, 2001. Modello all’equilibrio

## Slide 12
Pulse guiding in a plasma density hollow profile
G Costa, et al., under publication
150 µm focus FW1/e2
guiding transmission ⁓ 90%

## Slide 13
Guiding tests for different capillary geometry
transmission ⁓ 60%
transmission ⁓ 70%

## Slide 14
Plasma generation in a curved capillary
Curved multistage plasma channel for electron acceleration
Removal of a laser beam after its interaction with the plasma

## Slide 15
FLAME main high power pulse
300 µm diameter plasma channel
Discharge current ⁓ 500 A
High power laser guiding

## Slide 16
Nozzle design for supersonic gas jets generation
Gas jet target study and measurements for self-injection experiment
Fluid dynamics simulations of neutral gas flow in various types of target
Capillary design for uniform longitudinal profile of plasma density
Low power pulse guiding in a plasma transverse hollow profile
Online measurements of longitudinal and transverse plasma density
Comparison of guiding and density measurements for capillaries with different diameters and geometries
Ongoing project:
Plasma generation and laser pulse guiding
in curved capillary channels
High power laser guiding for external-injection
experiment at SPARC_LAB
Conclusions:

## Slide 17
Publications:
Costa, G., et al. "Plasma density profile measurements for ultra-short high power laser beam guiding experiments at SPARC _LAB." Journal of Physics: Conference Series. Vol. 1596. No. 1. IOP Publishing, 2020.
G Costa, et al., Characterization of self-injected electron beams from LWFA experiments at SPARC_LAB, Nuclear Instruments and Methods in Physics Research Section A: Accelerators, Spectrometers, Detectors and Associated Equipment (Feb 5, 2018).
FG Bisesto,… G Costa, et al., The FLAME laser at SPARC_LAB, Nuclear Instruments and Methods in Physics Research Section A: Accelerators, Spectrometers, Detectors and Associated Equipment (Feb 9, 2018).
A. Biagioni,… G Costa, et al., Temperature analysis in the shock waves regime for gas-filled plasma capillaries in plasma-based accelerators, Journal of Instrumentation, Volume 14, March 2019.
Curcio, A.,… G Costa et al. "Modeling and diagnostics for plasma discharge capillaries." Physical Review E 100.5 (2019): 053202.
Pompili, R.,… G Costa et al. "Energy spread minimization in a beam-driven plasma wakefield accelerator." Nature Physics (2021): 1-5.
R Pompili,… G Costa, et al., Focusing of High-Brightness Electron Beams with Active-Plasma Lenses, Physical Review Letters 121.17 (2018): 174801; doi:10.1103/PhysRevLett.121.174801.
V Shpakov,… G Costa, et al., Longitudinal phase-space manipulation with beam-driven plasma wakefields, Physical Review Letters 122, 114801 (2019).
Assmann, R. W., … G Costa et al. "EuPRAXIA Conceptual Design Report." The European Physical Journal Special Topics 229.24 (2020): 3675-4284.
M Ferrario,… G Costa, et al., EuPRAXIA@SPARC_LAB Design study towards a compact FEL facility at LNF, Nuclear Instruments and Methods in Physics Research Section A: Accelerators, Spectrometers, Detectors and Associated Equipment (Mar 1, 2018).
E Chiadroni,… G Costa, et al., Overview of plasma lens experiments and recent results at SPARC_LAB, Nuclear Instruments and Methods in Physics Research Section A: Accelerators, Spectrometers, Detectors and Associated Equipment (Feb 7, 2018).
FG Bisesto,… G Costa, et al., Innovative single-shot diagnostics for electrons accelerated through laser-plasma interaction at FLAME, Proc. SPIE 10240, Laser Acceleration of Electrons, Protons, and Ions IV, 102400K (May 7, 2017).

## Slide 18
Targets for self-injection experiments
Gas jet flow within a supersonic nozzle
A = nozzle area
A*= throat nozzle area
= ratio of specific heats
M = Mach number
Relations between temperature, pressure and density
Mach number ∝ flow velocity
+ area ratio
the exit velocity of the nozzle
Notes: Il fascio viene focalizzato tramite uno specchio parabolico sul target della camera di interazione, gas-jet, struttura metallica che trasporta gas nella camera di interazione, in vuoto. Il gas viene iniettato in modo sincrono con l’impulso laser in modo tale che quando l’impulso arriva, può ionizzare il gas portandolo in uno stato di plasma e generare il campo accelerante.
Gas-jet supersonico: sulla valvola del gas è presente un ugello che permette di avere un profilo netto del gas. Elio o Azoto.
Parametri esperimento: 300 mJ => 2x10^18 e a0 circa 1
Numero Mach = rapport tra velocità del flusso e velocità del suono nel mezzo, se M>1 supersonico

## Slide 19
Plasma density interferometric measurements
Path difference between probe and reference laser
Mach Zehnder interferometer:
interference fringes
Plasma refractive index
ne = e- plasma density
nc = critical e- density
Notes: Metodi interferometrici usano la dipendenza dell’indice di rifrazione eta dalla densità del mezzo, in questo caso il plasma, nc è la denistà critica degli elettroni che dipende dalla lunghezza d’onda del laser. La variazione dell’indice di rifrazione può essere rilevata misurando lo sfasamento di un fascio che propaga nel plasma.
Il passaggio attraverso il plasma genera una variazione che dà luogo allo shift delle frange, e questo permette di ricavare lo sfasamento (variazione di fase creata dalla differente velocità di fase con la quale il probe passa). Questo produce interferogramma, cioè delle frange risultanti dall’interferenza costruttiva e distruttiva, che vengono visualizzate su una CCD.
Analisi: ricostruzione interferogramma tramite algoritmo che fa inversione di Abel, suppongo di avere simmetria cilindrica e proietto su una superficie piana che è quella della CCD, ricavo lo sfasamento dalla trasformata di Fourier.

## Slide 20
Plasma density interferometric measurements
G Costa, et al., doi:10.1016/j.nima.2018.02.008
⁓2.5 × 1018 cm-3
⁓1 × 1018 cm-3
Low quality of produced and accelerated electron bunches
divergence
energy spread
diffraction
depletion
Notes: Metodi interferometrici usano la dipendenza dell’indice di rifrazione eta dalla densità del mezzo, in questo caso il plasma, nc è la denistà critica degli elettroni che dipende dalla lunghezza d’onda del laser. La variazione dell’indice di rifrazione può essere rilevata misurando lo sfasamento di un fascio che propaga nel plasma.
Il passaggio attraverso il plasma genera una variazione che dà luogo allo shift delle frange, e questo permette di ricavare lo sfasamento (variazione di fase creata dalla differente velocità di fase con la quale il probe passa). Questo produce interferogramma, cioè delle frange risultanti dall’interferenza costruttiva e distruttiva, che vengono visualizzate su una CCD.
Analisi: ricostruzione interferogramma tramite algoritmo che fa inversione di Abel, suppongo di avere simmetria cilindrica e proietto su una superficie piana che è quella della CCD, ricavo lo sfasamento dalla trasformata di Fourier.