## Slide 1
Piero Rapagnani
GWADW 2021
17/05/2021

## Slide 2
The Amaldi Research Center (ARC) (https://www.phys.uniroma1.it/fisica/arc_amaldi_research_center) is an interdisciplinary Center for Gravitational Physics and Astrophysics dedicated to Edoardo Amaldi and financed with 10 M€ by MIUR, the Italian Ministry for University and Research, in the framework of the “Dipartimenti di Eccellenza” initiative.
The research activities of the Amaldi Research Center are organized into the following research areas:
Gravitational physics and astrophysics
LIGO-Virgo gravitational-wave data analysis
Multi messenger astronomy
Quantum technologies for gravitational-wave detection
Material science for 3G interferometers
3G gravitational-wave lab
All the experimental activities of the ARC are dedicated to R&D on technologies crucial for 3G Gravitational Wave detectors:
Improvement of optical coatings of mirrors
Development of quantum noise reduction strategies
Cryogenics for cooling down mirrors of 3G gravitational wave detectors

## Slide 3
Quantum technologies for gravitational-wave detection
Faculty Members:
Fabio Sciarrino (Group Leader), Nicolò Spagnolo
Post Docs:
Iris Agresti, Mariana Berros, Gonzalo Carvacho, Valeria Cimini, Taira Giordani, Emanuele Polino
Machine learning for quantum sensing
Platform for squeezing generation
Machine learning for CV quantum sensing
Advanced protocols in the multiparameter regime
Development of experimental platform for continous-variable (CV) quantum sensing
Application of machine learning in the CV regime for quantum sensing
Machine learning for quantum sensing
ADAPTIVE PROTOCOLS FOR PHASE ESTIMATION
CALIBRATION OF QUANTUM SENSORS
A. Lumino, et al., Phys. Rev. Applied 10, 044033 (2018);
K. Rambhatla, et al, Phys. Rev. Research 2, 033078 (2020).;
M. Valeri, et al., npj Quantum Information (in press, 2020).
V. Cimini, et al., Phys. Rev. Lett. 123, 230502 (2019)
Bounds and protocols for quantum sensing
V. Cimini, et al., Phys. Rev. Applied 13, 024043 (2018);
E. Polino, et al, AVS Quantum Sci. 2, 024073 (2020).;
A. Z. Goldberg, et al., Phys. Rev. A 102, 022230 (2020).
Ongoing work
Future work:
https://www.phys.uniroma1.it/fisica/arc_quantum_technologies_for_gw_detection

## Slide 4
5 A. Paolone, et al. Effects of the annealing of amorphous Ta2O5 coatings produced by Ion Beam Sputtering concerning the effusion of argon and the chemical composition
Journal of non crystalline solids 557 (2021) 120651
SMART LAB
M. G. Betti, C. Mariani, M. Felici,
E. Placidi, M. Sbroscia,
A. Polimeni, P.Postorino, R. Trotta
https://www.phys.uniroma1.it/fisica/arc_material_science_for_3g_interferometers

## Slide 5
Payload Development and Test Area (LF Payload – Real size)
With ARC funds, we are preparing a lab for low temperature tests on a real size prototype of an ET LF-Payload
Pulse Tube Cooling Station
Cryogenic Tests Area:
Test Cryostat for a full size LF-Payload, cooled by two PT (~Ø 3 m x 3.5 m):
- 2 thermal shields in insulation vacuum
- 1 experimental chamber with separated vacuum
3G Gravitational-Wave Lab

## Slide 6
Lab ready beginning of 2022
Payload Development and Test Area (LF Payload – Real size)
2 tons crane
16 tons crane
Pulse Tube Cooling Station
Cryogenic Tests Area:
Test Cryostat for a full size LF-Payload, cooled by two PT (~Ø 3 m x 3.5 m):
- 2 thermal shields in insulation vacuum
- 1 experimental chamber with separated vacuum
3G Gravitational-Wave Lab

## Slide 7
Amaldi Research Center
ET Cryogenics Test Lab

## Slide 8
Amaldi Research Center
ET Cryogenics Test Lab

## Slide 9
2 PTs in counterphase (CUORE like)
with thermal links in Al5N and Al6N
Cryogenic cooling lines suspensions
(VIRGO like)
Soft thermal links
(KAGRA like)
Call for tender started. Construction starting in June 2021.
First phase:
for ET LF-Payload Test Cryostat
Design by Antonio Marra, Franco Bronzini:
Cryogenic Test Chamber:
Cooling efficiency,
Residual vibrations,
Sensing and actuators testing
Pulse Tube Cooling Station

## Slide 10
With the funds of ARC we have already bought two Pulse Tube Cryomech PT400 (1.8 W @ 4.2 K). They are being used for thermal tests in a temporary test lab in Rome La Sapienza.
Note: development of a good, damped, thermal link technology is essential in any cryogenic system configuration.
Pulse Tube Station for ET LF-Payload Test Cryostat

## Slide 11
Low vibration PT test facility for sensor and actuators at low temperature: VFC
RSI 77(9):095102 - 095102-7 · 2006
In our main lab in Rome, we use our low vibration cryogenic setup to develop cryogenic sensing of position/velocity/acceleration, in collaboration with KAGRA, and, since this year, also with CUORE.
Active System for Pulse Tube Vibrations Attenuation
For instance:
Design, assembly, calibration of low frequency Vertical Accelerometers for cryogenic operations (feedback control)
Vibration measurements of KAGRA cryostats: vacuum chamber and inner radiation shield @ University of Tokyo (ICRR), at Toshiba Keihin (Yokohama), JP., and at KAGRA site
Development of cryogenic sensors and actuators is crucial for payload design.

## Slide 12
Cryocoolers facilities for thermal conduction measurements
We plan to use it mainly for developing the thermal links for Payload cooling
In our Lab in Rome we have also a Cryomech PT dedicated to thermal resistance measurements, both on conductive links, and silicon or sapphire semples bonded with a monolithic bonding technique.
Recently, we gained access also to a facility for thermal conductivity measurements at INFN Laboratori Nazionali del Gran Sasso.

## Slide 13
ET Amaldi Research Center Lab
Program outline
2021:
Tests on high conductivity thermal links (ongoing)
Construction of prototype PT Cooling Station (call for tender started)
Design of test cryostat (starting)
2022:
Construction of test cryostat begins
Tests on dummy ET-LF payload at room temperature:
- frequencies, sensing & actuation, assembly procedure
2023:
- Tests on prototype payload at low temperature in test cryostat

## Slide 14
END
Thank you for your attention