## Slide 1
News from CERN
Alberto Mengoni
Meeting della Collaborazione nazionale n_TOF
26 marzo 2021

## Slide 2
n_TOF target III & facility upgrades
target installation started (target lowered into the pit for a test of positioning)
beam starts: W29 (19 July 2021)
beam ends: W45 (14 November 2021) and resumes W5 (31 January, TBC) in 2022
INTC meeting coming up on 23-24 June
LOI on HPGe “in beam” test
LOI on the X17 setup test
n_TOF Phase-2021

## Slide 3
150 mm
50 mm
Al-6082-T6 supporting structure
(anti-creep and N2 cooling channels)
Target design report: EDMS 2154581
n_TOF Target III

## Slide 4
After 5 years and 5 project reviews, the n_TOF Target #3 is ready to be installed in the area where it will stay at least until LS4.
The project is on track; commissioning with beam will start in July 2021.
Cold tests on final target assembly successful:
  Pressure test: 2.5 barg (moderators) and 0.715 barg (N2 vessel)
  Operating water circuits and N2 circuit tested up to 1000 m3/h
  All 6 thermocouples properly working with online recording and monitoring on NXCALS/TIMBER
  Pressure drop at the target experimentally validated (10 kPa max. at 1000 m3/h)
  Target deformations experimentally validated by DIC (max. displacement: 0.55 mm)
  Target vibrational behavior validated by accelerometers
n_TOF Target III

## Slide 5
n_TOF Phase-2021
Main activities going on at CERN
full fledged FLUKA simulations (Massimo B)
test of the new SiMON chamber (Oliver A & Massimo B)
test/setup L6D6 detectors (Javier P & two PhD students)
DAQ commissioning (DAQ team with Massimo B)

## Slide 6
For your reference, by Javier Praena

## Slide 7
n_TOF Phase-2021
useful links:
Index of documents for the Commissioning (Phase-2021)
Local Team @ CERN
n_TOF twiki

## Slide 8
Slides di Massimo B

## Slide 9
Update on the Fluka simulations for the new target performances and for the NEAR Station
n_TOF Collaboration Board Meeting, March 2021

## Slide 10
Collimator
Rabbit 3
Endoscopes
Rabbit 2
Rabbit 1
RP
Simulations for R2M
M. Barbagallo, Report on fluka simulations, n_TOF Collaboration Board Meeting, March 2021

## Slide 11
M. Barbagallo, NEAR Simulation, January 2021
Shelf top
Shelf bottom
Rabbit 3
Rabbit 2
Rabbit 1
Neutrons distribution (n/cm2/pulse)
‘’Old’’ reduced calculations
Same order of magnitude at different heights
Upstream side of the target area slightly higher neutron density

## Slide 12
M. Barbagallo, NEAR Simulation, January 2021
Shelf top
Shelf bottom
Rabbit 3
Rabbit 2
Rabbit 1
Gammas distribution (g/cm2/pulse)
Same order of magnitude at different heights
Upstream side of the target area slightly higher gamma density (in particular on the right side wrt to p beam positive direction)
‘’Old’’ reduced calculations

## Slide 13
Updated facility Fluka model (includes shelves for R2M samples and NEAR moderator (if any), holes for rabbit)
Quantities scored: Dose (total and EM), spatial distributions of n, g, p, e, m, p, k, HEH
M. Barbagallo, Report on fluka simulations, n_TOF Collaboration Board Meeting, March 2021
neutrons
Summary of simulation status for NEAR
Available upon request

## Slide 14
M. Barbagallo, Report on fluka simulations, n_TOF Collaboration Board Meeting, March 2021
Beam profile at scoring plane

## Slide 15
M. Barbagallo, Report on fluka simulations, n_TOF Collaboration Board Meeting, March 2021
Beam profile at scoring plane

## Slide 16
m profile projection
M. Barbagallo, March 2021