## Slide 1: Timepix Neutron Beam Monitor at nTOF
In 2018 a beam monitor based on 2 Quad Timepixes has been installed in nTOF EAR1
It has been used for the beam alignment and could be used for flux measurements in 2021-2022
LNF proposed in 2019 to realize a second alignment system in EAR2 (financial requests for 2020)
2 silicon quad are in wire bonding phase here at CERN
Beam image
nTOF EAR1

## Slide 2
Tests on MBGEM neutron detector

## Slide 3: Borated GEM: MultiBorated head-on converter
In three years several attempts have been made in collaboration with Milano Bicocca, CERN and ESS Liopking
and now a new etching and Boron deposition procedure has been defined
The borated GEM was proposed for the first time by Cascade project
but problems on boron deposition stability
and GEM reliability.
We have assembled two detectors for the first characterization.
Good prospective for high efficiency thermal neutron imaging for nTOF.

## Slide 4: Borated GEM for high efficiency thermal neutrons detector
The GEMPix detector allows to develop and optimize a new thermal neutron detector based on GEM technology.
A collaboration between CERN ESS INFN has recently develop a new procedure to realize borated GEM.
A detector efficiency 7 times the single foil has be reached on a uniform big surface (3x3 cm2)
with high time (10 ns) and spatial resolution (50 mm) with Timepix electronics.
F.Murtas, G.Claps, R.De Oliveira, C.Lai, G.Croci, A.Muraro

## Slide 5: MBGEMPix detector
Active area 3x3 cm2
Characterization with 55Fe source with the aim to uniform the Qion produced by alfas in the different conversion layer
2D images of X ray “beam” through
1 mm hole and spectra
55Fe

## Slide 6: MBGEMPix detector
neutrons
gammas
Linearity up to 1.2 MHz/cm2
with the reactor at 250 kW.
Relative efficiency switching ON the BGEM foils
Neutron gamma discrimination
Measurements at LENA
3He Tube

## Slide 7: MBGEM Spatial Resolution
Sigma: 13.1 pixels
Sigma: 20.0 pixels
140 pixels
20 pixels
Edge sigma <1mm
(1 pixel 55x55 um)
4 Cd disks:
diameter 8 mm, width 1 mm.

## Slide 8: Production of 10 Borated GEM foils 10x10 cm2
10 GEM foils (10x10 cm2) have been borated
in Sweden on February 15th
They are at CERN ready after the etching
(Rui’s Laboratory)
Two detectors we’ll be built in Frascati
before September.
The electronic readout is ready :
- 256 pads 6x6 mm2
8 Gemini32 boards and FPGA board (designed by Corradi Tagnani)
Paid by nTOF-LNF and MIB

## Slide 9: Preliminary results on 10x10cm2 MBGEM
Measurements at LENA
Spectrum with GEMINI chip
2D beam image