## Slide 1: Advanced time-of-flight diagnostics for real-time characterization of ions accelerated by high energy lasers
PhD candidate: Martina Salvadori
Supervisors: Mauro Migliorati, Patrizio Antici, Fabrizio Consoli
Agenzia nazionale per le nuove tecnologie,
L’energia e lo sviluppo economico sostenibile

## Slide 2: Overview
Introducing laser-driven ion acceleration
Advanced Time-Of-Flight (TOF) diagnostic system
From the acquired data to the spectrum reconstruction
Application to different experimetal Scenarios
2
29/04/2021
context and motivation
Methodology
Data Analysis
Results and Discussion

## Slide 3: Introducing Laser driven ion acceleration
A. Macchi et al., Rev. Mod. Phys. 85 (2013) 751, H. Daido et al., Reports Prog. Phys. 75 (2012) 056401 and references there in
3
29/04/2021
Ions+
1. Plasma generation
2. Laser energy absorption by plasma electrons
  Collisional processes (I < 1015 W cm-2)
  Collisionless processes (resonance absorption, vacuum heating, JB heating)
, ps
Ions+
Suprathermal electrons
2.1. electrons transport through the dense target

## Slide 4
4. The oncoming electrons are thus going to be confined under Coulombic forces to a Sheath field, directed as the Target Normal, that extends for a distance and reaches an intensity of the order of TV/m.
A. Macchi et al., Rev. Mod. Phys. 85 (2013) 751, H. Daido et al., Reports Prog. Phys. 75 (2012) 056401 and references there in
4
29/04/2021
Introducing Laser driven ion acceleration: TNSA
3. The escaping electrons will give rise to an electrostatic potential derived by the charge-separation between themselves and the positively charged target.
5. The intensity of this electric field in high enough to ionise the atoms present at the rear surface of the target.
+
6. These ions, which are subjected to an intense electric field, will be then accelerated to the order of MeV energies. Protons, having the highest charge to mass ratio, are in the most favorable condition for Acceleration

## Slide 5
A. Macchi et al., Rev. Mod. Phys. 85 (2013) 751, H. Daido et al., Reports Prog. Phys. 75 (2012) 056401 and references there in
Proton energy up to a few tens of MeV
Short proton bunch duration at the source (fs-ps)
Charge of a few nC
Conical beam of tens of degrees ( 20°)
The spectrum can be approximated with a Maxwellian
detector
5
29/04/2021
Highest energies
Lowest flux
Introducing Laser driven ion acceleration:
ions bunch characteristics
What requirements does it have to satisfy?
+

## Slide 6: Diagnostic system requirements
6
29/04/2021
The ideal diagnostic system should have:
High sensitivity
High energy resolution
and should allow to retrieve:
Spectrum of accelerated ions
Angular distribution of accelerated ions
but it also has to provide:
Electro Magnetic Pulses (EMPs) robustness
Real-time detection and characterization of ions
Layered Imaging systems (RCF, Imaging plates…)
Solid state nuclear track detectors
Thomson spectrometers
Electrostatic-magnetostatic spectrometers
Time Of Flight technique
M. Salvadori et al. Scientific Reports 11, 3071 (2021)

## Slide 7: Diagnostic system requirements
7
29/04/2021
The ideal diagnostic system should have:
High sensitivity
High energy resolution
and should allow to retrieve:
Spectrum of accelerated ions
Angular distribution of accelerated ions
but it also has to provide:
Electro Magnetic Pulses (EMPs) robustness
Real-time detection and characterization of ions
Layered Imaging systems (RCF, Imaging plates…)
Solid state nuclear track detectors
Thomson spectrometers
Electrostatic-magnetostatic spectrometers
Time Of Flight technique
M. Salvadori et al. Scientific Reports 11, 3071 (2021)

## Slide 8: Time Of Flight Technique
Time Of Flight measurements are a powerful and effective method to obtain timely spectra of accelerated particles.
time
Ion, v1
Ion, v2 < v1
Typical signal from Time Of Flight
EMP noise
X-rays peak
(photopeak)
Ion signal
TOF signals have an intrinsic high dynamic range.
It is necessary to develop a technique able to appreciate the full dynamic range
EMP pollution hinders the employment of TOF in high energies facilities
It is necessary to optimize the system to work in these environments
Photons, c
X-rays peak: signal generated by the incoming X-rays produced by the laser-matter interaction.
8
29/04/2021
TNSA: temporal window with pure proton contribution
Or in terms of proton energy:
TOF technique relies on the measurement of the time needed by a particle to travel for a known distance

## Slide 9: Towards the spectrum reconstruction
9
29/04/2021
Energy
estimation
Number
estimation
Signal Acquisition

## Slide 10: Detrimental effect of EMPs on TOF signals: an example
10
29/04/2021
τ = 25 fs
Target : 10 µm Al
M. Salvadori et al., Journal of Instrumentation 15, C10002 (2020)
F. Consoli et al., Scientific Reports 9, 8551 (2019)
Broadband EMP spectra
Associated electric field at 30 cm: 25 kV/m
Coupling with the detection system
Coupling with the acquisition system
FLAME
E = 2.5 J
W

## Slide 11: Avoiding EMP coupling with the detection system (1)
11
29/04/2021
Developing a proper shielding
Compact metallic enclosure: exploting skin effect
Skin depth for aluminum
= 2 mm
M. Salvadori et al. Scientific Reports 11, 3071 (2021)
≈ 2 kHz
resistivity; permeability
The 2 mm Al enclosure attenuate EM waves with frequencies down to 2 KHz

## Slide 12
12
29/04/2021
Exploiting the attenuation provided by waveguides
1. Cutoff frequency
2. Attenuation of the propagating EM waves:
M. Salvadori et al. Scientific Reports 11, 3071 (2021)
Avoiding EMP coupling with the detection system (2)
40 mm Aluminum pipe
Geometrical parameters
Skin depth
Material conductivity

## Slide 13
13
29/04/2021
Long double shielded coaxial cables
  Provide high frequency attenuation,
  Introduce a temporal delay between the TOF signal and the EMP contribution,
  Allow to place the scope far from the experimental chamber.
Scope with minimal bandwidth to reduce coupling with high frequency electromagnetic pulses.
M. Salvadori et al. Scientific Reports 11, 3071 (2021)
Avoiding EMP coupling with the acquisition system
Scattering parameter S21 Transmission coefficient
ù

## Slide 14
14
29/04/2021
Effectiveness of avoiding EMP coupling
M. Salvadori et al., Journal of Instrumentation 15, C10002 (2020)
Raw signal: no numerical filtering technique is used!
Where is the photopeak?
Need an higher dynamic range

## Slide 15: High dynamic range acquisition
29/04/2021
M. Salvadori et al. Scientific Reports 11, 3071 (2021)
15

## Slide 16: Towards the spectrum reconstruction
16
29/04/2021
Energy
estimation
Number
estimation
Signal Acquisition

## Slide 17: Energy Estimation
The temporal position T0 of the photopeak provides a reliable signature of the laser-matter interaction instant
Ion energies are computed evaluating the delay between the signal detection time and
29/04/2021
M. Salvadori et al. Scientific Reports 11, 3071 (2021)
It holds assuming that
one type of ion, of known mass,
is detected
17
T0

## Slide 18: Towards the spectrum reconstruction
18
29/04/2021
Energy
estimation
Number
estimation
Signal Acquisition

## Slide 19: Estimation of the particle number
19
29/04/2021
De-embedding procedure of the signal to retrieve its amplitude at source
Characterization of the detector used for TOF measurements
Particle number estimation from signal amplitude
M. Salvadori et al. Scientific Reports 11, 3071 (2021)

## Slide 20: 1. De-Embedding Procedure
= Fourier Transform, De-embedded signal
20
17/02/2021
WHAT WE HAVE
WHAT WE NEED
M. Salvadori et al. Scientific Reports 11, 3071 (2021)

## Slide 21: 2. Diamond detectors characterization
C. Verona et al. , J. Appl. Phys. 118 (2015) 184503,
R. Sussmann CVD diamond for electronic devices and sensors, Wiley and Sons (2009)
21
29/04/2021
1. Production of free electron-hole pairs ( = 13.1 eV).
Wide bandgap (5.5 eV)
High charge carrier mobility
High breakdown field
Not sensible to visible and IR light High radiation hardness
Fast time response
Low leakage current
Ionizing radiation

## Slide 22
22
29/04/2021
Wide bandgap (5.5 eV)
High charge carrier mobility
High breakdown field
Not sensible to visible and IR light High radiation hardness
Fast time response
Low leakage current
E
(> 1 MV/m)
Ionizing radiation
2. Diamond detectors characterization
Two main characterizing parameters: TIME RESPONSE and CHARGE COLLECTION EFFICIENCY
1. Production of free electron-hole pairs ( = 13.1 eV).
2. Charge collection at the electrodes thanks to the applied electric field
3. Signal Generation according to the collected charge
Charge Collection Efficiency
Carriers drift velocity
mobility, Electric field
C. Verona et al. , J. Appl. Phys. 118 (2015) 184503,
R. Sussmann CVD diamond for electronic devices and sensors, Wiley and Sons (2009)

## Slide 23
23
29/04/2021
2. CVD-DD characterization
50 µm thickness = Protons up to 3 MeV are completely stopped inside their bulk

## Slide 24
24
29/04/2021
2. CVD-DD characterization : Time Response
FWHM = 520 ps
FWHM = 460 ps

## Slide 25
25
29/04/2021
= ≈
2. CVD-DD characterization : CCE
Effect of a thickness-dependent electric field on CCE

## Slide 26
26
29/04/2021
3. Particle number estimation
ti
8
Time step
ti
tf
t
E
Time step = temporal response of the diagnostic system
M. Salvadori et al. Scientific Reports 11, 3071 (2021)
Numerical integration of the signal to retrieve the collected charge

## Slide 27
27
29/04/2021
The final spectrum
Pure proton Contribution
M. Salvadori et al. Scientific Reports 11, 3071 (2021)
Application of suitable filters
helps to down extend
the region of pure proton contribution

## Slide 28: Towards the spectrum reconstruction
28
29/04/2021
Energy
estimation
Number
estimation
Signal Acquisition
Experimental Results

## Slide 29
29
29/04/2021
Experimental results : ALLS facility
S. Vallières, M. Salvadori et al. Review of Scientific Instruments 91, 103303 (2020)
τ = 20 fs
Target : 5 µm Copper
ALLS
E = 2 J
W
ʎ = 800 nm

## Slide 30
30
29/04/2021
Associated estimated electric field at 30 cm: 250 kV/m
Experimental results : PHELIX facility
FWHM = 3.4 ns
CCE ≈ 30 %
15 × 15 mm2 area
τ = 750 fs
Target: 10 µm Titanium
PHELIX
E = 88 J
W
10 µm Al filter
10 µm Al filter
20 µm Al filter

## Slide 31
31
29/04/2021
GSI experimental campaign

## Slide 32: Experimental Validation: GSI experimental campaign
32
29/04/2021

## Slide 33: GSI experimental campaign
33
29/04/2021
Detector inside the experimental chamber 60 cm from target

## Slide 34: Conclusion and Perspectives: a novel detector design
34
17/02/2021
n
M. Salvadori et al. Scientific Reports 11, 3071 (2021)
A layered diamond structure enables:
High sensitivity for a wide range of ion energies
High energy resolution
High radiation hardness
Characterization of diamond detectors exploiting α particles produced by the radioactive decay of Americium
Successful employment of the advanced TOF technique in various experimental campaigns exploiting different laser systems (ABC, ECLIPSE, FLAME, LLC, ALLS, PHELIX)
Spectra reconstruction algorithm
Development of an effective procedure to acquire signals with high signal to noise ratio even in highly EMP polluted environments
Calibration of diamond detectors through the exposition to proton beams of different fluxes and energies
Now ongoing:

## Slide 35
Publications
M. Salvadori, P.L. Andreoli, M. Cipriani, F. Consoli, G. Cristofari, R. De Angelis, G. di Giorgio, D. Giulietti, F. Ingenito, S. Y. Gus’kov, A. A Rupasov, “Laser Irradiated Foam Targets: Absorption and Radiative Properties“, EPJ Web of Conferences 167 (2018)
M. Salvadori, P.L. Andreoli, S. Bollanti, F. Bombarda, M. Cipriani, F. Consoli, G. Cristofari, R. De Angelis, G. Di Giorgio, F. Flora, D. Giulietti, L. Mezi, M. Migliorati, M.A. Alkhimova, S. Pikuz, T. Pikuz, and R. Kodama. “A laser-produced plasma X-ray source for contact microscopy” Journal of Instrumentation 14, C03007 (2019)
M. Salvadori, F. Consoli, C. Verona, M. Cipriani, P. L. Andreoli, G. Cristofari, R. De Angelis, G. Di Giorgio, D. Giulietti, M.P. Anania, F. Bisesto, G. Costa, M. Ferrario, M. Galletti, R. Pompili, A. Zigler, P. Antici, M. Migliorati “Assessment of sensitivity improvement for Time-Of-Flight schemes in experiments with high intensity lasers” Journal of Instrumentation 15, C10002 (2020)
M. Salvadori, F. Consoli, M. Cipriani, M. P. Anania, P. L. Andreoli, P. Antici, F. Bisesto, G. Costa, G. Cristofari, R. De Angelis, G. Di Giorgio, M. Ferrario, M. Galletti, D. Giulietti, M. Migliorati, R. Pompili, C. Verona and A. Zigler, “Accurate spectra for high energy ions by advanced time-of-flight diamond-detector schemes in experiment with high energy and intensity lasers” Scientific Reports 11, 3071 (2021)
S. Vallières, M. Salvadori, P. Puyuelo-Valdes, S. Payeur, S. Formaux, F. Consoli, C. Verona, E. d’Humières, M. Chicoine, S. Roorda, F. Schiettekatte, P. Antici. “Thomson Parabola and Time-of-Flight Detector Cross-Calibration Methodology on the ALLS 100 TW Laser-Driven Ion Acceleration Beamline” review of Scientific Instruments 91, 103303 (2020)
S. Vallières, M. Salvadori , A. Permogorov, G. Cantono, K. Svendsen, Z. Chen, S. Sun, F. Consoli, E. D’Humières, C.-G. Wahlstrom, P. Antici. “Enhanced laser-driven proton acceleration using nanowire targets” Scientific Reports 11, 2226 (2021)
C. Verona, M. Marinelli, S. Palomba, G. Verona-Rinati, M. Salvadori, F. Consoli, M. Cipriani, P. Antici, M. Migliorati, F. Bisesto, R. Pompili. “Comparison of single crystal diamond TOF detectors in planar and transverse configuration” Journal of Instrumentation 15, C09066 (2020)
35
17/02/2021
Publications
S. Vallières, C. Bienvenue, P. Puyuelo-Valdes, M. Salvadori, E. d’Humières and P. Antici. “Low-Energy Proton Calibration and Energy-Dependence Linearization of EBT-XD Radiochromic Films” Review of Scientific Instruments 90 (8) (2019)
S. Vallières, P. Puyuelo-Valdes, M. Salvadori, C. Bienvenue, S. Payeur, E. d’Humières, P. Antici. “The laser-driven ion acceleration beamline on the ALLS 200 TW for testing nanowire targets” Proc. SPIE 11037, Laser Acceleration of Electrons, Protons, and Ions V, 1103703 (2019)
F. Bisesto, M. Galletti, M.P. Anania, M. Ferrario, R. Pompili, M. Botton, A. Zigler, F. Consoli, M. Salvadori, P. Andreoli and C. Verona. “Single-shot and time-resolved detection from high-intensity laser-solid matter interaction at SPARC_LAB” High Power Laser Science and Engineering 7 (2019)
F. Bisesto, M. Galletti, M. P. Anania, G. Costa, M. Ferrario, R. Pompili, A. Poye, F. Consoli, M. Salvadori, M. Cipriani, C. Verona, A. Zigler. “Ultrafast electron and proton bunches correlation in laser-solid matter experiments” Optics Letters 45, 5575 (2020)
F. Bisesto, M. Galletti, M. P. Anania, G. Costa, M. Ferrario, R. Pompili, A. Zigler, F. Consoli, M. Cipriani, M. Salvadori, C. Verona. “Simultaneous observation of ultrafast electron and proton beams in TNSA” High Power Laser Science and Engineering 8, E23 (2020)
G. Di Giorgio, F. Consoli, R. De Angelis, P. Andreoli, M. Cipriani, G. Cristofari, A. Bonasera, M. Salvadori, J. Sura. “Development of advanced Thomson spectrometers for nuclear fusion experiments initiated by laser” Journal of Instrumentation 15, C10013 (2020)
F. Consoli, P. L. Andreoli, M. Cipriani, G. Cristofari, R. De Angelis, G. Di Giorgio, L. Duvillaret, J. Krasa, D. Neely, M. Salvadori, M. Scisciò, R. A. Smith, V. T. Tikhonchuk. “Sources and space-time distribution of the electromagnetic pulses in experiments on inertial confinement fusion and laser-plasma acceleration” Phylosophical Transaction of the Royal Society A Mathematical Physical and Engineering Sciences 379, 20200022 (2021)
F. Consoli, R. De Angelis, P. L. Andreoli, A. Bonasera, M. Cipriani, G. Cristofari, G. Di Giorgio, D. Giulietti, M. Salvadori. “Diagnostic Methodologies of laser-initiated 11B(p,a)2a fusion reactions” Frontiers in Physics 8, 561492 (2020)

## Slide 36
Summer schools
January 2018, Archamps: Attendance at JUAS “The science of particle accelerators”
June 2018, Kudowa: Attendance at Kudowa summer school “Toward Fusion Energy”
September 2018, CLPU Salamanca: Attendance at LaPlaSS “Diagnostic Techniques for Laser-Plasma Experiments”
Poster presentations & Awards
4/10/2018 “Characterization of a X-Ray source for contact-microscopy applications obtained from laser-produced plasma” 5th International Conference Frontier in Diagnostics Technologies, Frascati, Italy. Winner of the Best Poster Award.
8/5/2019 “Determination of accurate spectra for laser-accelerated MeV ions by CVD diamond-detector setups optimized for experiments subject to intense EMPs” 3rd European Conference on Plasma Diagnostics, Lisbon, Portugal. Winner of the Student Poster Award.
23-24 /3/2021 “Advanced Time-Of-Flight methodologies for real time characterization of multi-MeV ions accelerated by high energy lasers” 16th Direct Drive and Fast Ignition workshop, Prague, Czech Republic.
Oral presentations
“Laser Irradiated Foam Targets: Absorption and Radiative Properties“ Plasma Physics by Laser and Application, Messina July 2017
“Advanced methods for the quantitative detection of Laser-Plasma accelerated MeV protons” Plasma Physics by Laser and Applications, Pisa October 2019
“Effective diagnostics of ions accelerated in laser-matter experiments with intense EMPs” EMP satellite workshop, Prague, Czech Republic. March 2021 (held online)
“Time-of-Flight methodologies with large-area diamond detectors for ion characterization in laser-driven experiments” 4th international symposium on High Power Laser Science and Engineering, Suzhou, April 2021 (off-site contribution)
36
17/02/2021

## Slide 37
Thank you for your attention
Any Questions?

## Slide 38
Back Up slides

## Slide 39: The EMPs
C. G. Brown et al., Journal pf Physics conference series 244 (2010) 032001
Electromagnetic Pulses (EMPs) can be destructive for any electronic device
Spectrum defined by the geometry of the target holder
Intensity related to the amount of generated charge
Temporal extension: hundreds of ns
Intensity: hundreds of kV/m
Broadband frequency range
ESD [a.u.]

## Slide 40: Detrimental effect of EMPs on TOF signals: an example
40
17/02/2021
FLAME
E = 2.5 J
W

## Slide 41: Single crystal CVD diamond detector
Charged particles passing through the detector deposit their energy into the material creating free electron-hole pairs
( = 13.1 eV).
Voltage applied to the electrodes of the detector allows for charges collection. The Voltage Amplitude is chosen such to have an electric field E > 1 MV/m in order to operate in electron holes pairs velocity saturation regime.
C. Verona et al. , J. Appl. Phys. 118 (2015) 184503
41
29/04/2021
Wide bandgap (5.5 eV)
High charge carrier mobility
High breakdown field
Not sensible to visible and IR light High radiation hardness
Fast time response
Low leakage current
The Amplitude of the generated signal will be proportional to the amount of charges generated inside the detector, which in turn is related to the impinging particle Energy:
According to the detector characteristics, only a certain amount of the produced charge is going to be effectively collected, this effect is taken into account with the charge collection efficiency CCE. The number of ions generating the signal can be written as:
Diamond detector
Pin-hole
Shielded holder
Flange 40

## Slide 42: Spectra reconstruction
0,8 ns
.
Error on Energy
Error on Number
16/10/2019
= Relativistic parameter
= Ion rest mass = error on time
= )
= error on time measurement
= TOF line length
Example:
FWHM = 0.8 ns
2.31 ± 0.04 MeV
Roughly 2%
FWHM = 3.2 ns
2.7 ± 0.2 MeV
Roughly 7%
Few %

## Slide 43: Spectra reconstruction
Al filter cut
SHOT #5
EL on Target = 2.65 J
Al filter cut
According to the performed SRIM simulations, (10±1.5) µm aluminium filter stops protons up to 750 keV and heavier ions.
16/10/2019

## Slide 44
C. Verona et al. , J. Appl. Phys. 118 (2015) 184503
Polycristalline diamond detector
15 mm
15 mm
Wide active surface:
  Enhanced sensitivity
  More susceptible to direct EMP coupling
150 µm thicnkess:
  Suitable for protons up to 6 MeV
  For higher energies a correction factor must be introduced
Polycristyalline structure:
  Allow to have large area detectors
  CCE lower than single crystal structures
  Lower temporal response than single crystal structures
Type: IIa-Electronic grade

## Slide 45
C. Verona et al. , J. Appl. Phys. 118 (2015) 184503
Polycristalline diamond detector
15 mm
15 mm

## Slide 46
C. Verona et al. , J. Appl. Phys. 118 (2015) 184503
Polycristalline diamond detector
Mounting of the detector
4. Biased grid to deflect electrons
2. Electrical connection optimized to cope with EMPs
3. Possibility to place a filter to cut heavier ion contribution
1. Stainless steel case for proper EMP shielding

## Slide 47
C. Verona et al. , J. Appl. Phys. 118 (2015) 184503
Polycristalline diamond detector
4. Biased grid to deflect electrons
Two grids separated by 40 mm
The first can be biased the second grounded
They provide a static electric field separating the electric component from the ionic one

## Slide 48
Polycristalline diamond detector: charaterization
FWHM = 3.4 ns
CCE ≈ 30 %