## Slide 1: SEM Meeting
INFN-LNF
F. Rosatelli
09/06/2021

## Slide 2
ATLAS ITk – Cabling
Activities:
Update the Layer 2 routing in End caps (WIP). Waiting news from ATLAS collaboration to update Layer 3 and Layer 4.
Align Outer Barrel routing with the last services mapping. There will be small changes.
Preliminary disposition in data Feedthroughs to check the routing outside the PP1.
EC L2 NOW
HV/LV
DATA

## Slide 3
ATLAS ITk – Cabling
Activities:
Preliminary study of data link and power cables disposition on trolley. This respecting the integration sequence and envelope assigned.
Verify if the layout on trolley it’s compatible with the length of the cables in the detector (WIP).
After integration
Z
Before integration
EC envelope
AFTER
EC
EC
OB
OB

## Slide 4
ATLAS ITk –Leak test
Activities:
Full scale Outer system feedthrough ready for filling process. Data link 2484.
Test the behaviour of different compounds for filling.
1:1 SCALE FEEDTHROUGHT OS
FLANGE
VESSEL
FEEDTHROUGHT WITH DATA LINK
PREPARATION OF COMBS
U-BENDED CABLES (INSIDE)

## Slide 5
ATLAS ITk –Leak test
Activities:
O-ring Leak check test performed. Radiation dose 3,5 MGy.
Design a new prototype to test a new batch of compressed O-ring (Shieldseal® 663), up to 6 MGy.
4MGy
6MGy
4MGy
6MGy
Prototype tested
New prototype

## Slide 6
CYGNO - LIME
Activities:
New bellow for camera.
Regulation system for camera lens (WIP).
Support to the experiment.