Results from
TB 2020-07 HOTNES
(planar cathode + mesh)
21/05/2021 – uRANIA
Matteo

---
The same must
be done with
Li ions
[by Lia]

---
Data from Lia (2020/05/14)
[by Lia]

---
Analysis flow
Resistive Current
Ionizzation
α/Li from simulation
Efficiency
α/Li from simulation
From Cathode
From Cathode
N from
i=eNRG
From Mesh to up
From Mesh to up
From Mesh to dw
From Mesh to dw
\epsilon = \epsilon_\text{from simulation} \frac{\widetilde{N}_\text{from measure}}{\widetilde{N}_\text{from simulation}}

---
Results of the Source test
CAT / [um]	MESH / [um]	type	Ed/Et / [kV/cm]	G	iRes / [nA]	Transp.	SIM / %	Eff / %
2.5			3.5	700	4.1	1	1.8	2.2 ± 0.4
2.5	NO	Cu66	0.2 | 2.7	420	1.5	0.97	1.7	1.9 ± 0.4
NO	2.5	Al33	0.1 | 2.7	420	2.4	0.5	2.7	4.7 ± 1.0
2.5	3.5	Al33	0.1 | 4.0	420	2.3	0.55	4.4	4.6 ± 1.0
2.5	1.5	Al33	0.1 | 4.0	434	1.1	0.55	4.4	2.1 ± 0.5

---
Results of the Source test
CAT / [um]	MESH / [um]	type	Ed/Et / [kV/cm]	G	iRes / [nA]	Transp.	SIM / %	Eff / %
2.5			3.5	700	4.1	1	1.8	2.2 ± 0.4
2.5	NO	Cu66	0.2 | 2.7	420	1.5	0.97	1.7	1.9 ± 0.4
NO	2.5	Al33	0.1 | 2.7	420	2.4	0.5	2.7	4.7 ± 1.0
2.5	3.5	Al33	0.1 | 4.0	420	2.3	0.55	4.4	4.6 ± 1.0
2.5	1.5	Al33	0.1 | 4.0	434	1.1	0.55	4.4	2.1 ± 0.5
Questi valori sono sensati

---
Results of the Source test
CAT / [um]	MESH / [um]	type	Ed/Et / [kV/cm]	G	iRes / [nA]	Transp.	SIM / %	Eff / %
2.5			3.5	700	4.1	1	1.8	2.2 ± 0.4
2.5	NO	Cu66	0.2 | 2.7	420	1.5	0.97	1.7	1.9 ± 0.4
NO	2.5	Al33	0.1 | 2.7	420	2.4	0.5	2.7	4.7 ± 1.0
2.5	3.5	Al33	0.1 | 4.0	420	2.3	0.55	4.4	4.6 ± 1.0
2.5	1.5	Al33	0.1 | 4.0	434	1.1	0.55	4.4	2.1 ± 0.5
Tira davvero troppa corrente
Considerata la trasparenza
???
La corrente tirata da questa camera
È sospettosamente poca