## Slide 1: uRANIA a mRwell Advanced Neutron Identification Apparatus
G. Cibinetto (INFN Ferrara)
on behalf of the uRANIA collaboration
International Conference on Technology and Instrumentation in Particle Physics
May 24-28, 2021

## Slide 2: Outline
Neutron Detection
micro-RWELL Technology
The uRANIA Project
Development of a Simulation Toolkit
Proof of Concept
Ongoing and Future Studies
Technology Transfer to Industries

## Slide 3: Reasons to go for Neutrons
PROBING STRUCTURE AND MOTION
HIGH PENETRATION
A PRECISE TOOL
HIGH SENSITIVITY AND SELECTIVITY
A UNIQUE PROBE FOR MAGNETISM
A PROBE OF FUNDAMENTAL PROPERTIES
ESS Technical Design Report S. Peggs (ESS, Lund)(ed.), 2013

## Slide 4: Few Applications relevant to our project
Radiation Portal Monitor (RPM) for homeland security
diffracted image
Radioactive waste monitoring (PuO2 or PuF4)
Complementary to X-ray imaging
Neutron diffraction imaging

## Slide 5: Neutron Detection in a Nutshell
High energy: Hadron Calorimeter
  measure energy deposited in form of hadronic shower
Moderate energy: np-Scattering
  scattering with protons from material containing appreciable amounts of hydrogen
Low energy: Exoergic Nuclear Processes
  Use converter medium with large capture cross-section
Helium-3 shortage calls for alternatives
Mod. Phys. Lett. A 28 (2013) 1340025
Dana A. Shea, D. Morgan (2010)
Notes: X section increase with the time the neutron is close to the absorbing nucleus
high energy little effect of the neutrality of the particle
low energy: for slow neutrons; capture process results in unstable nuclei ... Subsequent decay products give a detectable signal ...

## Slide 6: u-RWELL Advanced Neutron Imaging Apparatus (uRANIA)
  Applications in grain mapping of structural and functional materials, characterization of protein crystals at spallation sources
  Applications to homeland security  RPM portals
Development of an innovative neutron detector based on micro-Resistive WELL technology: a compact, spark-protected, single-amplification stage MPGD
funded by
https://phase1.attract-eu.com/showroom/project/u-rwell-advanced-neutron-imaging-apparatus-urania/
JINST_10_P02008 (2015)
Boron-coated cathode PCB

## Slide 7: m-Resistive Well Detector
Single amplification stage resistive MPGD composed of
  μ-RWELL_PCB
  drift/cathode PCB defining the gas gap
μ-RWELL_PCB
  ampl.-stage
  res.-layer
  r/out PCB (with suitable segmentation)
Large area & flexible geometry
Comes in two flavors: low rate and high rate
The “WELL”, suitably polarized applying HV between top and DLC, acts as a multiplication channel for the ionization produced in the gas
JINST 14 P05014 (2019)
easy assembly
and HV supply

## Slide 8: Neutron capture through Boron coating
B4C enriched with 97% of 10B sputtered on a copper surface at the ESS Coating Workshop in Linköping (Sweden) with direct current magnetron sputtering technology
About 94% of the time the recoiling 7Li ion is produced in an excited state and de-excites in flight, emitting a 477 keV g ray
a particle and a 7Li ion are produced back-to-back, only one enters the gas volume and produces detectable signal
chemically stable
not too expensive
adherence to substrate
low impurity level uniform sputtering thickness on large surface

## Slide 9: Neutron Converter Simulation
Simulation is used to optimize the detector and to extract the detection efficiency from the current measurement
Gas mixture ionizing energy ~ 31.5 eV
Particles range < 6 mm of gas
  all the energy released in the gas
  ~104 number of primaries
Neutron source energy distribution and divergence considered in the simulation
7Li ions
a particles
Energy release for different Boron thickness
1 mm of B
2 mm of B
3 mm of B
4.7 mm of B
1 mm of B
2 mm of B
3 mm of B
4.7 mm of B

## Slide 10: Source test facility: Hotnes (ENEA)
Detector characterization done @ ENEA (Frascati, Italy)
HOmogeneous Thermal NEutron Source (HOTNES) – 241Am-B source
Thermal fluence rate about 750 cm−2 s−1
Shadow bar to stop photons
Energy spectrum peaks at 100 meV (FWHM ~290 meV)
NIMA 843 (2017) 18–21

## Slide 11: Proof of concept with planar cathode
Efficiency for thermal neutrons (25 meV)
about twice the values of the Hotnes setup
due to the source energy distribution
with Hotnes n source
1
NOT IN SCALE

## Slide 12: Boron-coated mesh
Adding a boron-coated mesh to increase the efficiency
Different contributions studied independently with simulation and source test
1
2
4
3
Preliminary results show
about a factor 2 efficiency increase
negligible dependance on the Boron thickness
importance of optical transparency tuning
material | wire diameter [um] | pitch [um] | opt. transparency
Copper | 56 | 190 | 60%
Aluminum | 53 | 74 | 33%
1
2
3
4
NOT IN SCALE

## Slide 13: Grooved cathode
1
Grooved cathode can also increase the efficiency
Different geometries under study
For each layout, the energy deposit has been considered on the spacings, slopes and peaks
A factor ~2 of increase in the efficiency can be achieved
with respect to planar cathode
NOT IN SCALE

## Slide 14: Counting mode electronics
Readout large fraction of the chamber with one channel
Developed for large area application where position information is less relevant (RPM, RWM)
Two readout under testing
  CAEN A1422-based - gain ~0.2 mV/fC - noise ~20 mV - signal duration ~5 um
  CREMAT CR110-based - gain ~0.5 mV/fC - noise ~20 mV - signal duration ~5 um
Detector
Input
Anode signal
TOP signal
reference PMT
test with m.i.p.
signal waveform acquired with a Picoscope for amplitude analysis

## Slide 15: Counting mode electronics
First validation done with Hontes source
Signal amplitude from neutron conversion (top) is compared with simulation (bottom)
Simulation reproduces the same features of the data down to the noise level
Edep from simulation (a+7Li)
a particles step
7Li ions step
Signal amplitude spectrum from data
(CREMAT CR-110 readout)

## Slide 16: All in all
mRWELL_PCB
HV and filtering
Anode readout connectors
Counting mode electronics
External shielding
2
3
4
1
5

## Slide 17: Technology transfer: m-RWELL_PCB @ELTOS
The ELTOS company (Arezzo, Italy) performs the coupling of the DLC-foil with the readout PCB (only for low-rate layout)
The max size of the m-RWELL-PCB that can be produced by ELTOS is about 600x700 mm2. Up to 8 PCBs of such a size can be manufactured at the same time
The PI etching to be done @ CERN
33x33 cm2 active area LR - RWELL
INFN and ELTOS participate to the
AIDAinnova project for further TT
https://cordis.europa.eu/project/id/101004761

## Slide 18: Summary and Conclusions
The m-RWELL technology, robust, easy to assemble and relatively cheap MPGD, can be a valuable alternative for neutron detection
m-RWELLs have been successfully tested for thermal neutron detection with a 10B layer as converter
  Source test data confirms simulation studies with good accuracy
Efficiency improvement by means of grooved cathode, converting mesh and other detector layout
  10-20% efficiency can be achievable with a single detector for 25 meV neutrons
  higher efficiency with multiblade or multi-stack configurations
For neutron imaging applications standard MPGD electronics can exploit the high spatial resolution of the m-RWELL detector
For Radiation Portal Monitors counting electronics under development will reduce the costs
Technology Transfer is ongoing
  large area m-RWELL_PCB can be produced by industries (except for the Kapton etching)