## Slide 1
A mechanical design proposal for the CMD-3 drift chamber

## Slide 2
The mechanical design development of the CMD3 drift chamber.
Cell structure
Sector A: jet-cells with wires arranged axially.
From inside to outside, marked with black circle:
inner cylinder
middle cylinder
outer cylinder
Red circles show the different sectors in which the chamber is conceptually divided.
Sector B, C, D: single-wire cells with the wires arranged in stereo angle configuration.

## Slide 3
DIMENSIONS
Along beam axis ( distance between end-cap calorimeter) = 484 mm
Transverse direction (diameter) = 609 mm
Inner shell= 41 mm
The size along beam will be change not more than 5-15 mm, due to the optimization of BGO electronics.
655
550
150
609
41
602
1092
1469
1600
1800.5
Vacuum chamber
DC
BGO
Z-CHAMBER
CsI barrel calorimeter
Liquid Xe calorimeter
Superconducting solenoid
Iron yoke
Dimensions in mm

## Slide 4
Sector A: 24 spokes-48 PCBs
The construction of the chamber is driven by two main purposes:
The high transparency
The mechanical stability of the whole structure
Support for PCB
Wire PCB for sector B
PCB for sector A
Each spoke will be inserted inside the inner cylinder
The spoke will be fixed with a tiny pin
Tie-rod
The spider web structure will be built in carbon fiber.

## Slide 6
Details about the positioning of PCBs in sector A
At the intermediate ring, supports will be built with a suitable shape to host the PCBs.
At the inner ring, we will insert a wedge-shaped locking plate.

## Slide 7
Tie rod to prevent deformations
Due to the wire loads, (≈20 kg per spokes), the end-plates are affected by deformations.
We intend to install an appropriate number of tie rods per spoke to minimize the deformations due to the wire load.
C-fiber (low modulus, 133 GPa) 4.8 mm deflection
Al 9.4 mm deflection
Ss 3.3 mm deflection

## Slide 8
back to back spokes
Single tie rod per spokes
Three tie rod per spokes
Just by adding symmetry reduces to 2.2 mm deflection
Single tie-rod at inner radius loaded with 450 N at 10°: max deflection < 300 μm
Three tie rods loaded with : 140 N at 10°, 240 N at 14°, 200 N at 21°: max defection <±25 μm

## Slide 9
Possible ways to attach the tie rods on the spokes
First proposal:
create buttonholes, insert an eyelet and hook the tie rod.
Second proposal: create two buttonholes, insert an eyelet and hook the tie rod.
Third proposal:
use a “cart”, like the mast of a sailboat

## Slide 10
Conclusion
We started a collaboration with the technicians from University and Polytechnic of Bari, planning the following steps:
Finite elements simulation of the inner cylinder and spokes
Analysis and choice of suitable materials
Building of a prototype
We accept any suggestion, criticism and doubt!