## Slide 1: Single shot diagnostics for plasma accelerated beams
Ph.D. in accelerator physics, thesis discussion, Sapienza, 30/06/2021
Candidate:
Matteo Cesarini
Advisors:
Prof. Massimo Ferrario
Prof. Alessandro Cianchi

## Slide 2
Introduction
  The plasma acceleration
OTR based diagnostics
  OTR: theory and diagnostic applications
  Angular distributions measurement
  Emittance measurement
A new innovative scheme: concept and simulation
  The micro-lenses array for the correlation term
  Theorical single-shot measurement setup
  The need of a polarizer
The measurement
  Experimental setup at SPARC_LAB
  Case of study: simulation
  Data analysis
  Results
Conclusions

## Slide 3
Introduction
  The plasma acceleration
OTR based diagnostics
  OTR: theory and diagnostic applications
  Angular distributions measurement
  Emittance measurement
A new innovative scheme: concept and simulation
  The micro-lenses array for the correlation term
  Theorical single-shot measurement setup
  The need of a polarizer
The measurement
  Experimental setup at SPARC_LAB
  Case of study: simulation
  Data analysis
  Results
Conclusions

## Slide 4
The plasma acceleration

## Slide 5
The plasma acceleration
The diagnostics are required to be as compact as possible.
There is the need to use diagnostics that allow a single shot characterization of the beam.
The plasma acceleration leads to a reduction of the machine dimensions.
The first plasma based accelerators suffer from instability.

## Slide 6
Introduction
  The plasma acceleration
OTR based diagnostics
  OTR: theory and diagnostic applications
  Angular distributions measurement
  Emittance measurement
A new innovative scheme: concept and simulation
  The micro-lenses array for the correlation term
  Theorical single-shot measurement setup
  The need of a polarizer
The measurement
  Experimental setup at SPARC_LAB
  Case of study: simulation
  Data analysis
  Results
Conclusions

## Slide 7
A charged particle passing through the boundary between two media with different optical properties generates transition radiation. For beam diagnostics purposes, only the visible part of the radiation is used.
The backward radiation, produced by a thin metallic foil is normally used to measure the beam spot, by means of an imaging system.
The main advantage of OTR is the instantaneous emission process which makes it suitable for single shot diagnostic measurements.
The main drawback is the low radiation intensity, with respect for example to the scintillator screens, widely used for the beam spot measurement.
OTR: theory and diagnostic applications

## Slide 8
Angular distributions measurement
The angular distribution of a single particle can be expressed in the relativistic limit as:
In a beam, each particle emits radiation at a different angle.
The overall angular distribution is the sum of these different radiations; the resultant distribution loses the properties of the single particle one.
The central minimum is no more null; actually the minimum raising contain information about the beam divergence. It can be retrieved evaluating this increase.
The overall distribution is well described by the following formula, i.e. the convolution of the OTR angular distributions and a gaussian beam profile:

## Slide 9
Emittance measurement
The geometrical r.m.s. emittance is expressed as:
When the beam emits OTR in its waist, the correlation term is null. Thus measuring spot and angular distribution provides an emittance measurement.
Experimentally, the spot is measured by the detector in the image plane of a lens. Whereas the angular distribution can be observed placing the camera in the lens focal plane.
Beam spot
OTR angular distribution

## Slide 10
Introduction
  The plasma acceleration
OTR based diagnostics
  OTR: theory and diagnostic applications
  Angular distributions measurement
  Emittance measurement
A new innovative scheme: concept and simulation
  The micro-lenses array for the correlation term
  Theorical single-shot measurement setup
  The need of a polarizer
The measurement
  Experimental setup at SPARC_LAB
  Case of study: simulation
  Data analysis
  Results
Conclusions

## Slide 11
The micro-lenses array for the correlation term
For the correlation term of the r.m.s. emittance, the measurement of the divergence in different transverse positions of the beam is needed.
A micro-lenses array accomplishes this feature: each lens provides an angular distribution of the light from different transverse parts is directed on it.
In order to compute the divergence in the proper transversal position, an image of the beam OTR on the micro-lenses array is created by using a lens.
The overall profile obtained is analyzed to retrieve the term.

## Slide 12
Theorical single-shot measurement setup
Electron beam
Metallic screen
Beam splitter
Beam splitter
Lens for
beam imaging
CCD
Lens for
angular distribution
CCD
Imaging lens
Microlenses array
Imaging lens for the microlenses focal plane
CCD
Spot
Divergence
Correlation

## Slide 13
The need of a polarizer
The OTR angular distribution has in the inner hole the contribution of the both transverse planes.

## Slide 14
The need of a polarizer
The OTR angular distribution has in the inner hole the contribution of the both transverse planes.
The use of a polarizer let us to retrieve the divergence related to one of the two planes.

## Slide 15
Introduction
  The plasma acceleration
OTR based diagnostics
  OTR: theory and diagnostic applications
  Angular distributions measurement
  Emittance measurement
A new innovative scheme: concept and simulation
  The micro-lenses array for the correlation term
  Theorical single-shot measurement setup
  The need of a polarizer
The measurement
  Experimental setup at SPARC_LAB
  Case of study: simulation
  Data analysis
  Results
Conclusions

## Slide 16
Experimental setup at SPARC_LAB
Motorized stages allow to switch optical transfer line to chose which one acquire and to take control of the optical line itself.
A polarizer beam splitter let us have the separation between the two transverse plane; moreover an interferential filter reduce the blurring of the distribution.
A Micro-Channel Plate is used to amplify the signal collected by a CMOS based fast camera.
The acquisition of OTR angular distribution with the single lens and with the microlenses array is not simultaneous.
Imaging lens
f=400 (m.l.)
mirror
Beam splitter
OTR single lens
f=200 (s.l.)
Filter
500+-40 nm
PBS (hor.)
Imaging lens
f=200 (s.l.)
Microlenses array (m.l.)
Imaging lens
f=50 (m.l.)
MCP + camera

## Slide 17
Experimental setup at SPARC_LAB
The acquisition of OTR angular distribution with the single lens and with the microlenses array is not simultaneous.
This is the optical line for the
divergence measure.
Imaging lens
f=400 (m.l.)
mirror
Beam splitter
OTR single lens
f=200 (s.l.)
Filter
500+-40 nm
PBS (hor.)
Imaging lens
f=200 (s.l.)
Imaging lens
f=50 (m.l.)
MCP + camera
Microlenses array (m.l.)

## Slide 18
Experimental setup at SPARC_LAB
The acquisition of OTR angular distribution with the single lens and with the microlenses array is not simultaneous.
This is the optical line for the
correlation measure.
Imaging lens
f=400 (m.l.)
mirror
Beam splitter
OTR single lens
f=200 (s.l.)
Filter
500+-40 nm
PBS (hor.)
Imaging lens
f=200 (s.l.)
Microlenses array (m.l.)
Imaging lens
f=50 (m.l.)
MCP + camera

## Slide 19
Case of study: simulation
Spot:
Divergences:
Correlations:
  𝜌(x) = 0.90
  𝜌(y) = 0.95
Normalized emittance:
  𝜀x = 3.4 mm mrad
  𝜀y = 2.9 mm mrad

## Slide 20
Case of study: simulation
Spot:
Divergences:
Correlations:
  𝜌(x) = 0.90
  𝜌(y) = 0.95
Normalized emittance:
  𝜀x = 3.4 mm mrad
  𝜀y = 2.9 mm mrad
Simulations results: |  | 
: | 0.0998 mrad | (diff: ̴0.2%)
: | 0.0023 mm mrad | (diff: ̴3%)
𝜀x : | 3.0 mm mrad | (diff: ̴10%)
Simulations results: |  | 
 | 0.0998 mrad | (diff: ̴0.2%)
 | 0.0023 mm mrad | (diff: ̴3%)
𝜀x : | 3.0 mm mrad | (diff: ̴10%)

## Slide 21
Data analysis
Spot and angular distribution of both single lens and micro-lenses have been acquired.
For each one, 20 images of signal and background have been acquired, filtered, subtracted each other and then analyzed.
In order to improve the results, mean and std. deviation are computed.

## Slide 22
Data analysis
Spot and angular distribution of both single lens and micro-lenses have been acquired.
For each one, 20 images of signal and background have been acquired, filtered, subtracted each other and then analyzed.
In order to improve the results, mean and std. deviation are computed.

## Slide 23
Data analysis
Spot and angular distribution of both single lens and micro-lenses have been acquired.
For each one, 20 images of signal and background have been acquired, filtered, subtracted each other and then analyzed.
In order to improve the results, mean and std. deviation are computed.

## Slide 24
Results
Quadrupole scan results:

## Slide 25
Introduction
  The plasma acceleration
OTR based diagnostics
  OTR: theory and diagnostic applications
  Angular distributions measurement
  Emittance measurement
A new innovative scheme: concept and simulation
  The micro-lenses array for the correlation term
  Theorical single-shot measurement setup
  The need of a polarizer
The measurement
  Experimental setup at SPARC_LAB
  Case of study: simulation
  Data analysis
  Results
Conclusions

## Slide 26
The Ph.D. thesis work has been aimed at the study and the characterization of this innovative OTR based diagnostics.
The simulations has highlighted some crucial aspects, such as the need of a polarizer to select one polarization.
The experimental results have shown the compatibility between the emittance value measured with this technique and the one obtained with the classical reliable quadrupole scan method.
Conclusions

## Slide 27
Backup Slides

## Slide 28
To remove the X-ray spikes on the acquired picture, an hampel filter is used.
It checks and remove maximums over 3 over the close pixels average.
Data analysis algorithm
Before hampel filter
After hampel filter

## Slide 29
In the general formula:
a2 = b2 – c2
a compensation of errors made on b and c leads to a better estimation of a when they are correlated.
This happens with emittance.
Errors compensation in emittance-like formula

## Slide 30
The main errors on the parameters estimation done with the simulations are due to the discretization.
Simulations errors

## Slide 31
Divergence resolution
An essential issue of the measurement is the resolution limit of the angular divergence.
The measurement is very efficient for high energy beam, but it can be carried out as well for low energy beam, with a particular attention on the divergence resolution.
At low energy (i.e. low ) it worsens and the divergence has to be higher and higher to be measured.
At SPARC_LAB, the energy can reach energies up to ~ 160 MeV ( ~ 315); hence the beam divergence has to be at least ~ 0.45 mrad .
Angular divergence resolution as function of the relativistic
SPARC_LAB limit

## Slide 32
The second configuration, without the polarizer.
Fit result: σx′ = 0.286 ± 0.006 mrad.
Experimental evidence of the polarizer need
The first configuration, with the polarizer.
Fit result: σx′ = 2.6 ± 0.3 mrad.
Integrated shots of two configurations both with an expected divergence value of σx’ = 0.283 mrad.

## Slide 33
Backtracking
To estimate the expected emittance in the OSE apparatus position, the beam transport along the machine optics is carried out thanks to GPT, that reconstruct the beam dynamics from the Q scan position, up to the OSE setup.

## Slide 34
Parameters of the neglected transversal plane
The angular distribution intensity with the polarizations contributions in Cartesian coordinates is expressed as:
Neglecting the vertical polarization the term disappears only in the numerator.
A simulations scan has been done to test its effect on the measurement.
The term in denominator affects the measurement of the horizontal divergence and hence the emittance.
A clue on an aspect ratio of 5 on the transversal divergences appears from the simulations.